## Slide 1
CLS 332
CLINICAL INSTRUMENTAL ANALYSIS

## Slide 2: A VISIBLE ABSORPTION SPECTROMETER

## Slide 3: Spectrophotometry
One of the simplest and most widely used methods to determine concentration of a substance in solution
  Measures light absorbed by solution at a specific wavelength
Notes: <number>

## Slide 4
In the analysis, the amount of light radiation absorbed by a sample is measured. The light absorption is directly related to the concentration of the coloured compound in the sample.
The wavelength (λ) of maximum absorption is known for different compounds.

## Slide 5
This method is used to determine concentrations of various chemicals which can give colours either directly or after addition of some other chemicals

## Slide 6
Principles of Spectrophotometer A spectrophotometer consists of two instruments
Spectrometer for producing light of any selected color (wavelength),
Photometer for measuring the intensity of light.

## Slide 7
The instruments are arranged so that liquid in a
cuvette can be placed between the
spectrometer beam and the photometer.

## Slide 8
The amount of light passing through the tube is measured by the photometer.
The photometer delivers a voltage signal to a display device, normally a galvanometer.
The signal changes as the amount of light absorbed by the liquid changes.

## Slide 9
Visible light
Is only a small portion of the entire electromagnetic spectrum and it includes the colors commonly observed (red, yellow, green, blue and violet).
The visible spectrum consists of electromagnetic radiation whose wavelengths range from 400 nm to nearly 800 nm

## Slide 10: Visible region wavelength
Color | Wavelength (nm)
Ultraviolet | 400 and under
Violet | 400 - 450
Blue | 450 - 500
Green | 500 - 570
Yellow | 570 - 590
Orange | 590 - 620
Red | 620 - 650
Infrared | 750 & over
Notes: <number>

## Slide 11
100% transmittance means no light is absorbed by the solution so that incident light is 100% transmitted.
100% T = 0A

## Slide 12
The Spectrophotometer Instrument
All spectrophotometer instruments designed to measure the absorption of radiant energy have
the basic components as follows:
1.Light source (tungsten lamp for visible region
The intensity of out put of the lamp varies with the wavelength.

## Slide 13
2. Monochromator (filter );
To isolate a desired wavelength from the source.

## Slide 14
3. Transparent container (cuvette)
For the sample and the blank
4. A radiation detector (phototube)
To convert the radiant energy received to a measurable signal; and a readout device that displays the signal from the detector

## Slide 15
Lamp
Io I
A = 0.012
 l 
Monochromator
Cuvette
Detector
Notes: <number>

## Slide 16
Notification:
Pyrex glass absorbs no light in the visible
region but absorbs almost all the light in the
UV region.
Hence in UV range quartz or silica cuvettes are used

## Slide 17
Procedure:
The general measurement procedure consists of 5 steps:
1. Prepare samples to make coloured compound
2. Make series of standard solutions of known concentrations and treat them in the same manner as the sample for making coloured compounds

## Slide 18
3. Set spectrophotometer to l of maximum light absorption
4. Measure light absorbance of standards
5. Plot standard curve: Absorbance vs. Concentration

## Slide 19: Rules to handle cuvettes:
- Do not handle lower portion of the cuvette.
- Rinse cuvette with two portion of solution.
- Wipe off any liquid drops with a clean lens
paper.
- Insert the cuvette with the index-line facing the front of the instrument.

## Slide 20
Some OPERATING INSTRUCTIONS FOR SPECTROPHOTOMETER
1. Ensure 230V, 50Hz, single-phase power supply is available in the 3 contact 5A
power point.
2. Insert the power cord of the instrument in to a power point.
3. Turn the switch at ‘ON” position.

## Slide 21
4. Warm up the instrument for 15 minutes.
5. Press %T selector switch.
6. Adjust wavelength control to read the wavelength at which the test is desired.

## Slide 22
Lambda max is the wavelength at which the maximum fraction of light is absorbed by a solution
Lambda λ max

## Slide 23: How to calculate λ max:
Materials:
Chromium nitrate.
Blank.
Spectrophotometer.
Wavelengths :400- 800 nm.

## Slide 24
Procedure:
1- Adjust spectrophotometer to zero against blank.
2- Take the readings of chromium nitrate at wavelengths starting from 400 till 800 nm in 50 nm interval (400-450-500-550-........800).
3-Observe the max absorption and take one interval before and one interval after.

## Slide 25
4-Now, take the reading in 10 intervals and
observe the max absorption .
5-Then take the reading in 5 intervals and observe the max absorption.

## Slide 26
6- Take the reading now in 2 intervals and observe the max absorption.
7- Finally ,take the reading in one interval .
8- This is going to be λ max.