## Slide 1: Chapter(16) AASHTO flexible pavement design method

## Slide 2: Determination of the required structural number
  SN = a1D1 + a2D2m2 + a3D3m3 + …
a | = | layer structural coefficient
D | = | layer depth (inches)
m | = | layer drainage coefficient

## Slide 3: Materials of construction (AC surface), a1
Structural number of the AC surface, a1

## Slide 4: Materials of construction (Base course), a2
Structural number of the base course, a2
Use CBR, R-value, or Mr to find a2 values

## Slide 5: Materials of construction (Subbase), a3
Structural number of the subbase, a3
Use CBR, R-value, or Mr to find a3 values

## Slide 6: Definition of drainage quality and finding recommended mi values

## Slide 7: Structural Number (SN):

## Slide 8: Example :-
Design a flexible highway pavement using the AASHTO method of design the traffic is 2x10^6 ESAL in the design lane the asphalt concrete modulus E= 450,000 psi for base and subbase is 25000 psi and 12000 psi , subgrade 6000 . In addition the following information are psi = 4.0 ,Pt =2.5 ,SD = 0.3 , R= 95%

## Slide 9
Solution :-
Reliability =95%
Standard deviation =0.30
= PSI –Pt = 4 – 2.5 =1.5
Layer coefficients(ai):
a1 for surface
a2 for base
a3 for subbase

## Slide 10: Calculate a1 (AC surface),:
E = 450,000 psi
a1 =0.45

## Slide 11: Calculate a2(Base course), :
a2 =0.12

## Slide 12: Calculate a3(Subbase),:
a3 =0.083

## Slide 13: Definition of drainage quality and finding recommended mi values
Assume 1-5% of time pavement structure is exposed to moisture level approaching saturation quality of drainage : good
M2 =M3=1.2

## Slide 14
SN3= 4.5
SN2= 3.3
SN1= 2.5
Resilient modulus, Mr
base course =25000 psi
Subbase =12000 psi
Subgrade = 6000 psi

## Slide 15
SN = a1D1 + a2D2m2 + a3D3m3