## Slide 1: Practical 1&2 Environmental Sampling
Microbiological Sampling of Air

## Slide 2: Environmental Sampling
Environmental microbiology is not clinical microbiology(Air, water , soil, food , etc.)
Random, undirected sampling is not recommended
Sampling requires a protocol for sampling and culturing, analysis of results, and action based on the interpretation of results

## Slide 3: General Environmental Sampling
Suggested uses:
  Outbreak investigation
  Research in Environmental infection control
  Monitor a potentially hazardous situation
  Evaluate a change in environmental infection control for quality purposes
  Periodic maintenance of equipment HAC systems ( heating &air conditioning system)
  Legal issues

## Slide 4: Environmental Sampling Problems
Expensive
Time-consuming
Subject to many variables in protocol, analysis, and interpretation
Why difficult and problematic
  No baselines, no acceptable ranges
  Few protocols for conducting planned, directed environmental studies in health care settings.
  The investigator is required to minimize false negatives and false positives.

## Slide 5: Air Sampling Why do Air Sampling?
Verification of ventilation and cleanliness
  Establish baseline data
Post infection evaluation (outbreak investigation)
  Rule out ventilation as a source
  Discover source of infectious fungi (reservoir)
Construction, renovation, repair of certain buildings such as hospitals
Employee complaints

## Slide 6: Microorganisms of the air
Important Facts:
Air has no indigenous or native flora
Organisms are found temporarily suspended in air or carried on dust particles or droplets
Air is not sterile
Air does not support the growth of organisms

## Slide 7: Before Microbiological Air Sampling…
Define your objective and analytical approach
  Qualitative vs. quantitative
Compare indoor results to counts from outdoor air
Fully describe the circumstances in the area where sampling is occurring
High volume sampling most efficient

## Slide 8: Poor Ventilation
Inadequate ventilation can increase indoor pollutant levels by not bringing in enough outdoor air to dilute emissions from indoor sources and by not carrying indoor air pollutants out of the home.
High temperature and humidity levels can also increase concentrations of some pollutants.

## Slide 9: Air Sampling
To determine bacteria and fungi identities and concentration in biological aerosols
Major methods:
  Impingement in liquids
  Impaction on solid surfaces
  Sedimentation (e.g., settle plates)
Requires an understanding of what is being measured and a full description of the circumstances during sampling

## Slide 10: Compare and Contrast the Main Air Sampling Methods
Method | Principle | Suitable for Measuring | Collection Media or Surface | Points to Consider
Impingement in liquids | Air drawn in through small jet, directed against liquid surface | Viable microorganisms, water aerosols | Buffered gelatin, peptone, nutrient broth, tryptose saline | Used for Legionella spp. sampling
Impaction on solid surface | Air drawn into sampler, particles deposited on dry surface(slide, Agar) | Viable particles, viable microorganisms | Dry surfaces, coated surfaces, agar | Used for bacteria and fungal agent sampling; high volumes can be sampled
Sedimentation (settle plates) | Particles and microorganisms settle via gravity |  | Nutrient agars in plates | Simple, best suited for qualitative sampling; not used for fungal spores

## Slide 11: Types of Air Samplers*
A.
B.
C.
A. Impactor sampler
B. Glass impinger sampler
C. Sieve impactor sampler

## Slide 12: How to Sample for Viable Mold and Bacteria
Non-viable spore
  Air sampling cassette (slide) (Auto or trap–sampler)
Viable Sampling
  Active ( membrane /media)
    Surface Air Sampler (SAS)
  Passive
    Settle Plates
SAS

## Slide 13: Air sampling cassette
It is designed for the rapid collection of a wide range of airborne aerosols including mold spores, pollen, insect parts.
It collects both viable and non-viable sample specimens.
After sampling is completed, the cassettes are sent to a laboratory, where the slides are removed and direct microscopic analysis can be immediately performed.

## Slide 14: Practical work
Each 2 students will have 2 PCA plates, and should perform gravity method.
Expose one plate indoor ,and one outdoor for 1 hour .( Care taken to choose different areas)
Properly label your plates ( indoor or outdoor , name of place, time, duration, student name)
Bring to lab next day. Incubate at 37c for 48 hours, then read results with instructor.

## Slide 15: Results
It is important to compare No and type of organisms grown on plates between indoor and outdoor.
A lot of bacteria such as colored Micrococci, Actinomycetes, Bacillus , Pseudomonas , etc.
A lot of fungi ,molds and yeast.
Usually No of outdoor orgs is higher than indoor No.
If a predominant organism exist , this is not normal especially for indoor places.
High indoor No's are not normal in certain rooms.

## Slide 16: General Control of Air Borne Diseases
Good ventilation( dilutes organisms)
Avoid overcrowding especially in closed places
Isolation of patients with serious respiratory infections
Wearing masks
Spacing of beds or desks
Disinfect air ( HEPA Filters, UV hoods)
Vaccination

## Slide 17: HEPA Filter
High-efficiency particulate air filter
It removes 99.97% of all particles greater than 0.3 micrometer from the air that passes through
HEPA filters are critical in the prevention of the spread of airborne bacterial and viral organisms and infection
Medical-use HEPA filtration systems incorporate high-energy ultra-violet light units to kill off the live bacteria and viruses trapped by the filter media.

## Slide 18: HEPA Filter
It is composed of a mat of randomly arranged fibers. The fibers are typically composed of fiberglass .
These particles are trapped through a combination of the following three mechanisms: interception, impaction, diffusion.

## Slide 19
7
11
14
8
HEPA Like Air Filters
(MERV(1-20
MERV: Minimum Efficiency Reporting Value rating
These ratings are used to rate the ability of an air cleaner filter to remove dust from the air as it passes through the filter. MERV is a standard used to measure the overall efficiency of a filter. The MERV scale ranges from 1 to 20, and measures a filter's ability to remove particles from 10 to 0.3 micrometer in size

## Slide 20: Agar plates exposed to Air

## Slide 21: Actinomycetes on Agar plates
Colonies appear dry wrinkled
White colonies.

## Slide 22: Actinomycetes gram stained smear
Gram +ve branching rods

## Slide 23: Yeast stained smear

## Slide 24: Unresolved Issues and Microbiologic Air Sampling
Unknown incubation period
Infectious dose for Aspergillus spp. is unknown
Lack of standard sampling protocols
No standards or action levels for results
Variability and sensitivity of sampling devices
Lack of details :re sampling makes comparison of results with other outbreaks difficult
Lack of correlation between fungal strains in clinical specimens and those found in the environment

## Slide 26: Common biological contaminants
Include mold, dust mites, pet dander (skin flakes), droppings and body parts from cockroaches, rodents and other pests or insects, viruses, and bacteria.
Many of these biological contaminants are small enough to be inhaled. Biological contaminants are, or are produced by, living things.
Biological contaminants are often found in areas that provide food and moisture or water. For example, damp or wet areas such as cooling coils, humidifiers, condensate pans, or unvented bathrooms can be moldy. Draperies, bedding, carpet, and other areas where dust collects may accumulate biological contaminants