## Slide 1: IE 469 Manufacturing Systems 469 صنع نظم التصنيع
III- Assembly Line Tutorial

## Slide 2: Problem #1
Question 1 A feeder-selector device at one of the stations of an automatic assembly machine has a feed rate f=25 parts/min and provide a throughput of one par in four (θ =0.25). The idea cycle time of the assembly machine is 10 seconds. The low level sensor on the feed rack is set at 10 parts, and the high level sensor is set at 20 parts.
a) How long will take for the supply of parts to be depleted from higher level sensor to lower level sensor once the feeder selector device is turned off?
b) How long will take for the parts to be resupply from low level sensor to higher level sensor once the feeder selector device is turned on?
c) What proportion of the time that the assembly machine is operating will the feeder-selector devise be turned on? And Turned off?
d) For the feed rate of the machine is f=32 parts/min, recalculate a,b,c. what is your comment?

## Slide 3: Problem #1 Solution
Solution when feed rate f=25 parts/min |  |  |  |  | 
a) Time to deplete from nf2 to nf1 |  |  |  |  | 
rate of depletion = cycle rate Rc = 60/10 = 6 parts/min |  |  |  |  | 
Time to deplate = (20-10)/6 =1.667 min |  |  |  |  | 
b) Time to resupply from nf1 to nf2 |  |  |  |  | 
rate of resupply = fθ - Rc =25(0.25) - (60/10) = 0.25 parts/min |  |  |  |  | 
Time to resupply = (20-10)/0.25 =40 min |  |  |  |  | 
c) Total cycle of depletion and resupply = (40+1.667) = 41.667 min |  |  |  |  | 
proportion of time feeder-selector is on = 40/41.667 = 0.96 |  |  |  |  | 
proportion of time feeder-selector is off = 1.667/41.667 = 0.04 |  |  |  |  | 

## Slide 4: Problem #1 Solution
Solution when feed rate f=32 parts/min |  |  |  |  |  |  | 
a) Time to deplete from nf2 to nf1 |  |  |  |  |  |  | 
rate of depletion = cycle rate Rc = 60/10 = 6 parts/min |  |  |  |  |  |  | 
Time to deplate = (20-10)/6 =1.667 min |  |  |  |  |  |  | 
b) Time to resupply from nf1 to nf2 |  |  |  |  |  |  | 
rate of resupply = fθ - Rc =32(0.25) - (60/10) = 2 parts/min |  |  |  |  |  |  | 
Time to resupply = (20-10)/2 =5 min |  |  |  |  |  |  | 
c) Total cycle of depletion and resupply = (5+1.667) = 6.667 min |  |  |  |  |  |  | 
proportion of time feeder-selector is on = 5/6.667 = 0.75 |  |  |  |  |  |  | 
proportion of time feeder-selector is off = 1.667/6.667 = 0.25 |  |  |  |  |  |  | 
Comment |  |  |  |  |  |  | 
the turning rate of feed selector to the cycle rate of the assembly machine is important. |  |  |  |  |  |  | 

## Slide 5: Problem #2
Question 2 A synchronous assembly machine has 8 stations at a rate 400 completed assemblies per hour. average downtime per is 2.5 minute. When a breakdown occurs all subsystems (including the feeder) stop. The frequency of breakdowns of the machine is once every 50 parts. one of the eight stations is an automatic assembly operation that uses a feeder-selector. The components fed into the selector can have any of five possible orientations, each with equal probability, but only one of which is correct for passage into the feed track to the assembly workload. Parts rejected by the selector are fed back into the hopper. What minimum rate must the feeder deliver components to the selector during system uptime in order to keep up with the assembly machine?

## Slide 6: Problem #2 Solution
Solution |  |  | 
Tp= 60/400 = 0.15 min/assem. |  |  | 
Tp =Tc +F*Td = Tc + (1/50)*2.5 =Tc +0.05 |  |  | 
Tc= 0.15- 0.05 = 0.1 min/assem. |  |  | 
Rc= (1/Tc) = (1/0.1) =10 assem/min |  |  | 
Min fθ =0.2 f =Tc = 10 |  |  | 
Feed rate f = (10/0.2) =50 parts/min. |  |  | 

## Slide 7: Problem #3
Question 3
An automated assembly machines has four work stations. the first presents the base part, and the other 3 stations add parts to base. The production data are given Table below. Determine:
a) proportion of good product to total product coming off the line
b) production rate of good product coming off line
c) total number defect of components and Number of assemblies containing defect component given the starting components quantities of 100,000 for each of part (Base, Bracket, Pin, retainer) which are used to stock the assembly line for operation
d) total number of final assemblies produced
Table (1) |  |  |  | 
Station | Operation / part | Time, sec. | defect rate, q | jam rate of defect, m
1 | Base | 12 | 0.01 | 1
2 | Bracket | 10 | 0.02 | 1
3 | Pin | 9 | 0.03 | 1
4 | Retainer | 10 | 0.04 | 0.5
Downtime= 3 min., When a component is jammed,and putting the machine back to work |  |  |  | 
Indexing Time =3 sec., to move from station to station |  |  |  | 

## Slide 8: Problem #3 Solution
Solution |  |  |  | 
 | mq | (1-q+mq)
 | 0.01 | 1
 | 0.02 | 1
 | 0.03 | 1
 | 0.02 | 0.98
SUM | 0.08 | 0.98
Tc =12+3 = 15 sec |  | 0.25 | min |  |  | 
Tp=Tc+Σmq*Td = |  | 0.49 | min/cycle |  |  | 
a) Acceptable Ass. Yield= Pap = Π (1-q+mq) = |  |  |  |  |  | 0.98
b) Production Rate, Rp = 60/Tp = |  |  | 122.449 | assemb./hour |  | 
Production rate of good product Rap =Pap*Rp = |  |  |  |  | 120 | Good ass./hr

## Slide 9: Problem #3 Solution
c) Number of defective components given a stock quantities Q=100000 are: |  |  |  |  |  |  | 
Number of defect components for Base, Nd = Q*(1-q) = |  |  |  |  |  | 1000 | def
Number of defect components for Bracket, Nd = Q*(1-q) = |  |  |  |  |  | 2000 | def
Number of defect components for Pin, Nd = Q*(1-q) = |  |  |  |  |  | 3000 | def
Number of defect components for Retainer,Nd = Q*(1-q) = |  |  |  |  |  | 4000 | def
Hence the number of assemblies containing defect components are: |  |  |  |  |  |  | 
Number of assemblies containing Base defect = Nd*(1-m)= |  |  |  |  |  | 0 | 
Number of assemblies containing Bracket defect = Nd*(1-m)= |  |  |  |  |  | 0 | 
Number of assemblies containing Pin defect = Nd*(1-m)= |  |  |  |  |  | 0 | 
Number of assemblies containing Retainer defect = Nd*(1-m)= |  |  |  |  |  | 2000 | 
d) the total number of assembly produced=100,000*Pap= |  |  |  |  |  | 98000 | Assemblies
Number of good product = Total number produced - Number of parts produced containing defect part = |  |  |  |  |  | 96000 | Assemblies

## Slide 10: Problem #4
Question 4 A six station dial indexing machine performs four assembly operations. The base is loaded manually at the station 1; the final product is unloaded at the station 6; and a component is attached to base at stations 2 to 5. The components are delivered by a hopper feeder to selector device for proper orientation. The system is designed with operating parameter given in the table below :-
Station | Assembly Time, Sec. | Feed Rate, f /min. | Selector, θ | defect rate, q | jam rate of defect, m
1 | 4 | 32 | 0.25 | 0.01 | 1
2 | 7 | 20 | 0.5 | 0.005 | 0.6
3 | 5 | 20 | 0.2 | 0.02 | 1
4 | 3 | 15 | 1 | 0.01 | 0.7
Indexing time from station to station , Sec |  |  |  | 2 | 
When a component is jammed, it takes an average 2 min to release and start the system. The mechanical and electrical assembly machine failure is not significant and can be neglected.
It is found that the system produces assemblies far below the designed average production rate. Analyze the problem, stating any assumption to determine the following:-
a) What is the designed average production rate?
b) What is the proportion of assemblies coming off the system that contain one or more defective component?
c) What seems to be the problems that limit the assembly system from achieving the expected production rate?
d) What is the actual production rate?

## Slide 11: Problem #4 Solution
Solution |  |  |  |  | 
Td = 2 min, |  |  |  |  | 
Tc =7+2 = 9 sec. = 0.15 min |  |  |  |  | 
Cycle rate, Rc = 1/0.15 = 6.667 cycle/min |  |  |  |  | 
(a) |  |  |  |  | 
Σ(mq) = 1(0.01) + 0.6(0.005) + 1(0.02) + 0.6(0.01) = 0.04 |  |  |  |  | 
Tp = Td + Σ(mq) * Td = 0.15 + 0.04 * 2 = 0.23 min |  |  |  |  | 
Rp = 60/Tp = 60/0.23 = 260.9 assemblies/hr |  |  |  |  | 
(b) |  |  |  |  | 
Pap =Σ(1-q+mq) = (1 - 0.01 + 1 * 0.01) + (1 - 0.005 + 0.6 * 0.005) + (1 - 0.02 + 1 * 0.02) + (1 - 0.01 + 0.7* 0.01) = 1 * 0.998 * 1 * 0.997 = 0.995 |  |  |  |  | 
Pqp = 1 - Rap = 0.005 |  |  |  |  | 
Rap = Rp * Pap = 260.9 * 0.995 = 259.6 good assemblies/hr |  |  |  |  | 

## Slide 12: Problem #4 Solution
(d) |  |  |  |  | 
if the machine operates at the cycle rate that is consistent with the feed rate of station 4, then: |  |  |  |  | 
Tc = 15 sec = 0.25 min |  |  |  |  | 
Tp = 0.25 + 0.04 * 2 = 0.33 min |  |  |  |  | 
Rp = 60/0.33 = 181.8 assemblies/hr |  |  |  |  | 
Rap = 181.8 * 0.995 = 180.9 good assemblies/hr |  |  |  |  | 
(c) |  |  |  |  | 
Station 1: f θ = 32 (0.25) = 8 components/min |  |  |  |  | 
Station 2: f θ = 20 (0.50) = 10 components/min |  |  |  |  | 
Station 3: f θ = 20 (0.20) = 4 components/min |  |  |  |  | 
Station 4: f θ = 15 (1.00) = 15 components/min |  |  |  |  | 
the problem is that the feeder for station 3 is slower than machines cycle rate of 6.667 cycles/min. |  |  |  |  |