## Slide 2: What are the indications of intubations??
(1) failure to maintain or protect the airway
(2) failure of ventilation or oxygenation
(3) anticipated need for intubation based on the patient's clinical course and likelihood of deterioration.

## Slide 3
Status epilepticus
Severe multiple trauma
Certain Overdoses
Penetrating neck trauma
Certain conditions indicate the need for intubation even in the absence of airway, ventilatory, or oxygenation failure.????
Indications of Intubations

## Slide 4
ESTABLISHMENT OF AIRWAY PATENCY
Common Obstructing Agents
The tongue
Dentures
Swollen or distorted tissues
Blood
Vomitus

## Slide 5
Partial airway obstruction in the patient with a decreased level of consciousness is commonly due to posterior displacement of the tongue.
ESTABLISHMENT OF AIRWAY PATENCY

## Slide 6
  Adequacy of current ventilation
  Potential for hypoxia
  Airway patency
  Need for neuromuscular blockade (muscle tone, teeth clenching, severe obstructive pulmonary disease, or asthma)
  Cervical spine stability
  Safety of technique and skill of the operator
Qs before an airway management

## Slide 7
Airway Maneuvers
The neck-lift
head-tilt method
jaw-thrust method
chin-lift method.
lax musculature and tongue occlusion of the posterior pharynx may be overcome by a variety of A/W maneuvers
A jaw-thrust or chin-lift
maneuver should be performed
on every unconscious patient.

## Slide 8
Neck lift
Chin lift
Jaw thrust

## Slide 9
The Jaw-Thrust Maneuver
The Chin-Lift Maneuver
Airway Maneuvers
By maintaining airway patency, artificial airways may facilitate both spontaneous and bag-mask ventilation.

## Slide 10
Better tolerated in the semiconscious or conscious patient.
May cause nasal bleed
Nasopharyngeal Airways
Extreme caution is indicated in patients with a suspected basilar skull fracture or facial injury.

## Slide 11
Prevent the tongue from obstructing the airway
Prevent teeth clenching.
May cause vomiting
Oropharyngeal
May cause airway obstruction if during its placement the tongue is pushed against the posterior pharyngeal wall
All potentially unstable patients with oral or nasal pharyngeal airways should be observed constantly, because these devices are temporary measures and cannot substitute for tracheal intubation.

## Slide 12
simple and effective.
it can be difficult to perform correctly
ensure a tight mask seal in situations requiring positive-pressure ventilation.
often is used with an oropharyngeal or nasopharyngeal airway in place
BVM

## Slide 13: BVM
A tight mask seal is mandatory to prevent loss of tidal volume and to ensure oxygen delivery during ventilation.
The thumb and index finger provide anterior pressure while the fifth and fourth fingers lift the jaw
Dentures generally should be left in place to
help ensure a better seal with the mask.

## Slide 14: What are the major problems encountered with BVM ventilation??
Inadequate tidal volumes
Inadequate oxygen delivery
Gastric distention.
The foreign material may be insufflated down the trachea if it is not cleared before ventilation.
Regurgitation and Aspiration
The application of firm posterior pressure on the cricoid ring helps reduce gastric inflation during BVM ventilation

## Slide 15
30 year old f. started on ACEI on the floor, became hypoxic and started to have tongue swelling and stridor. IM epi, steroid & fluid were given without any improvement.
What do you want to do????

## Slide 16: Difficult Airway
Incorrect position of the patient.
Inadequate or improper equipment.
Unusual or abnormal anatomy.
Pathologic causes
General Causes

## Slide 17
69 y.o.male admitted to the ICU with septic shock received 3 L. of crystalloid, started in inotrpes. remain hypotensive ,ECG shows new ST depression, O2 sat. went down to 85% in 100% O2.
PMH: HTN, MI, sever RA on wheelchair on ACEI , lasix, ASA, percocet.
What do you want to do????

## Slide 18: Difficult Intubation??
  Anatomically abnormal faces
  Neck trauma Prominent incisors Receding mandible Cervical spine immobilization Short, thick neck Neck mobility

## Slide 19: Difficult Airway
There are three specific tests which when used together have almost 100% reliability in predicting airway difficulty.
The Mallampati test
The Thyromental distance
Extension at the Atlantooccipital joint.

## Slide 20: Difficult Bag/Mask Ventilation
  Edentulousness
  Obesity
  History of snoring
  Beard
  Age > 55 years
  Anatomically abnormal facies
  Facial/neck trauma
  Obstructive airways disease
  Third-trimester pregnancy

## Slide 21: Difficult Intubation and Difficult BMV??
  Anatomically abnormal faces
  Facial/neck trauma
  Morbid obesity

## Slide 22
Inspect for external markers of difficult intubation, difficult bag/mask ventilation, or both.
Assess cervical spine mobility.
Assess mouth opening (three fingers between the incisors).
Assess oral access (Mallampati scale).
Assess laryngoscopic geometry (mentum to hyoid, laryngeal prominence to floor of mandible).
Evaluate for obstruction.
Evaluation of the Difficult Airway
In Summary

## Slide 23
Difficult Airway

## Slide 24: Preparation
preparation
In airway management, failure has ominous consequences.
Mental, physical, and equipment preparation maximizes
the chances of success
preparation
preparation
preparation
preparation
preparation
preparation
preparation
preparation
preparation

## Slide 25
Difficult Airway
Airway Cart
Make your self familiar to its content before you need it

## Slide 26: Preparing for Intubation
(1) confirm that the required intubation equipment is available and functioning
(2) position the patient correctly
(3) assess the patient for difficult airway
(4) establish intravenous (IV) access, time permitting
(5) draw up essential drugs
(6) attach the necessary monitoring devices

## Slide 27: Positioning
The patient should be positioned to optimally align the oral, pharyngeal, and laryngeal axes
with the head extended on the neck and the neck slightly flexed relative to the torso.
A small towel under the occiput (to raise it 7 to 10 cm) may facilitate positioning in the adult.

## Slide 28
Positioning of the head
and
neck is a critical step
suboptimal head
positioning may be
a common reason
for intubation failures.

## Slide 29
Laryngoscopy

## Slide 30: Laryngoscope
The tip fits into the vallecula and indirectly lifts the epiglottis.
The wider, curved blades are helpful in keeping the tongue retracted from the field of vision,
more room in passing the tube in the oropharynx
generally preferred in uncomplicated adult intubations.
less forearm strength than the straight blade
Curved (MacIntosh)

## Slide 31: Straight (Miller) Laryngoscope
The tip goes under the epiglottis and lifts it directly
Pediatric patients
Anterior larynx
Long floppy epiglottis
If larynx is fixed by scar tissue.
It is less effective in Prominent upper teeth.
--laryngospasm
--advanced into the esophagus.
--The light bulb at the tip that may slightly hamper vision

## Slide 32
If the straight blade is placed too deeply, the entire larynx may be elevated anteriorly and out of the field of vision.
Gradual withdrawal of the blade should allow the laryngeal inlet to drop down into view.
If the blade is deep and posterior, the lack of recognizable structures indicates esophageal passage; gradual withdrawal should permit the laryngeal inlet to come into view.
Laryngoscopy

## Slide 33
Placing the blade in the middle of the tongue and failing to move the tongue to the left are two common errors preventing visualization of the vocal cords

## Slide 34
Laryngoscopic View Grades

## Slide 35: Laryngoscopy
The "BURP"
External laryngeal manipulation, also called bimanual laryngoscopy
places the right hand on the patient's thyroid cartilage to determine the best position of the larynx from the intubator's perspective
Levitan RM, Mickler T, Hollander JE: Bimanual laryngoscopy: A videographic study of external laryngeal manipulation by novice intubators. Ann Emerg Med 40:38, 2002.

## Slide 36: Laryngoscopy bougie tube
If the vocal cords are still not seen, a bougie tube introducer may be used
It is a long, semirigid introducer that is placed, using the laryngoscope, through the laryngeal inlet and into the trachea.
The tracheal tube is then passed over the introducer and the introducer is withdrawn.

## Slide 37: Laryngoscopy bougie tube
A curved or "coude tip" bougie is best suited for aiding in difficult intubations.
The curved tip provides tactile feedback as it passes along the tracheal rings.
If resistance is met in passing the tracheal tube, rotate the tube 90° counterclockwise and advance the tube.

## Slide 38: Crash Airway
unresponsive to direct laryngoscopy

## Slide 39: ETT
The ET tube cuff should be checked for leaks by inflating the balloon before attempting intubation
flexible stylet down the tube to increase its stiffness and enhance control of the tip of the tube.
The tube is then bent in a gradual curve with a more acute angling in the distal one-third to more easily access the anterior larynx.
The tip and cuff of the tube are lubricated with viscous lidocaine or a water-soluble gel.

## Slide 40: ETT
Adult men generally accept a 7.5 to 9.0 mm
women can usually be intubated with a 7.0 to 8.0 mm tube.
In most circumstances, tubes smaller than these should not be used because airway resistance increases as tube size decreases.
In emergency intubations, particularly if a difficult intubation is anticipated, many clinicians choose a smaller tube and change to a larger tube later.

## Slide 41: ETT
Cuff pressure should be measured and maintained at 20 to 25 mm Hg.
Capillary blood flow is compromised in the tracheal mucosa when the cuff pressure exceeds 30 mm Hg.
In emergency situations, the balloon may simply be inflated with 10 mL of air and adjusted when the patient's condition has stabilized.

## Slide 42: ETT
The tube should be introduced from the right side of the patient's mouth, advanced toward the patient's larynx at an angle, not parallel with or down the slot of the laryngoscope blade.
This way, the clinician's view of the larynx is not obstructed by the hand or the tube until the last possible moment before the tube enters the larynx.
If the patient is not chemically paralyzed, the tube should be passed during inspiration, when the vocal cords are maximally open.

## Slide 43
29 y. o. 36 week pregnant lady admitted with multiple trauma after mva
GCS is 8, O 2 sat is 85% SBP is 60.?
Any special consideration in intubation of this pt ?????

## Slide 44: Obstetric Patients
Functional residual capacity is significantly reduced causing the rapid desaturation seen in the preintubation period.
hypotension in the supine position as a result of compression of the vena cava by the gravid uterus.
Engorgement of oropharyngeal and nasal mucosa leads to easily provoked bleeding with manipulation.

## Slide 45: Obstetric Patients
The generalized edema including the airway
use smaller ET tubes (6.0 to 7.0)
Advanced gestation has been shown to correlate with higher maternal Mallampati scores.
Aspiration during emergency airway procedures.

## Slide 46
90 year old male in CHF, awake, hypoxic 84% and difficult to ventilate.
No teeth
Has a beard
How do you want to pre oxygenate him for intubation ???

## Slide 47: INTERMEDIATE AIRWAYS
Allow ventilation across the larynx but do not involve complete airway control.

## Slide 48: INTERMEDIATE AIRWAYS
Esophageal obturator airway (EOA)
Esophageal gastric tube airway (EGTA)
Laryngeal mask airway (LMA)
Esophageal-tracheal Combitube (ETC) airway (Sheridan Catheter Corp., Argyle, NY).

## Slide 49: INTERMEDIATE AIRWAYS
(EOA and EGTA), are designed to occlude only the esophagus
(LMA) seals the larynx at the hypopharynx level,
(ETC) offers the versatility of use whether placed into the esophagus or the trachea.

## Slide 50: Esophageal Obturator Airway
Protect the airway by occluding the esophagus to reduce gastric distention and regurgitation.
Ventilation from the EOA exits the airway through numerous ports in its hypopharyngeal portion.

## Slide 51: As a precaution against pressure-related complications, it is recommended that these devices be left in place for no longer than 2 hours. It must be recognized that the EOA is temporary form of airway control, most suitable for use in out-of-hospital settings.
Esophageal Obturator Airway and

## Slide 52: Esophageal Obturator Airway
Indicated when neither BVM ventilation nor tracheal intubation can be performed safely, effectively, and rapidly.
Cannot be used in the awake patient with an intact gag reflex

## Slide 53: Placement of EOA/EGTA
The head is in the neutral position.
grasps and pulls the jaw forward
insert the assembled airway with the mask attached.
tip is directed into the patient's posterior pharynx with gentle, steady pressure
advance down the esophagus until the mask rests flush against the face of the patient.
ventilated with a tight mask seal on the face, and auscultate the lungs are.
For effective ventilation, the mask seal must be tight.
Breath sounds should be audible bilaterally.

## Slide 54: Placement of EOA/EGTA
The cuff should lie in the esophagus just distal to the carina of the trachea.
The rescuer postpones inflation of the balloon until proper position is confirmed.
Tracheal intubation will result in the absence of breath sounds.
The possibility of bronchial or tracheal intubation requires removal and replacement of the airway.
Once satisfactorily placed, the esophageal balloon is inflated with 20 to 25 mL of air.

## Slide 55: Placement of EOA/EGTA
Complications
Hypercarbia
Unrecognized tracheal intubation may occur in 2.9% to 5% of patients with up to a 100% mortality due to airway occlusion.
Esophageal injury may also occur, ranging from small lacerations in 8.5% of patients to esophageal rupture.

## Slide 56: Placement of EOA/EGTA
Tracheal intubation should be performed before removal of the EOA, because vomiting often occurs following deflation of the balloon and EOA removal.
If the EOA cuff has been overinflated, it may partially occlude the trachea and make intubation difficult. In such cases, the balloon is partially deflated to facilitate tracheal intubation.

## Slide 57: Esophageal Obturator Airway Contraindication
active oropharyngeal bleeding
suspected esophageal injury
caustic ingestion
history of esophageal disease.

## Slide 58: The Laryngeal-Mask Airway
use in difficult intubations and for rescue ventilation
a temporary adjunct
The mask is intended to reside in the hypopharynx rather than on the face.
One variation, the Proseal LMA, has a parallel drainage tube attached to the airway tube that is designed to reduce gastric insufflation and allow gastric drainage by a nasogastric tube, potentially decreasing the risk of aspiration

## Slide 59: The Laryngeal-Mask Airway
Indications
for patients requiring an airway who cannot be endotracheally intubated or cannot be ventilated with a BVM.
Cant visualization of the larynx.
Contraindications
inability to open the patient's mouth
Vomiting
Need for high pulmonary inflation pressures.

## Slide 60: Placement of LMA
checked for possible air leaks
If the patient has a gag reflex, deep oropharyngeal topical anesthesia or conscious sedation must be administered.
the neck and head are held in the neutral position, as would be necessary with cervical spine immobilization.
The posterior surface of the mask is lubricated and the mask is oriented so its opening faces the tongue.

## Slide 61
With the index finger of the dominant hand placed on the proximal aspect of the mask, the mask is inserted into the mouth, firmly against the hard palate.
With one smooth motion, the mask is advanced until resistance is encountered. With the tip of the mask thus seated in the upper esophageal sphincter, the cuff is inflated. The lungs are auscultated to confirm correct placement.
Preparation for ILMA placement is similar to LMA placement.
Placement of LMA

## Slide 62: Intubating LMA
facilitate blind tracheal intubation while allowing continuous positive-pressure ventilation.
Insertion of the ILMA is easier than the standard LMA
ILMA allows for passage of a larger tracheal tube (up to 8-0).

## Slide 63
Endotracheal tube down the lumen of the LMA
Tracheal tube exchanger or bougie passed blindly down the lumen of the LMA and into the trachea.
Intubation with an LMA in place is via a fiberoptic scope.
If the LMA must be removed after a tracheal tube has been successfully placed through it, pass a tracheal tube exchanger down the tube, remove the tracheal tube/LMA combination, and replace it with a tracheal tube.

## Slide 64: The Laryngeal-Mask Airway
Complications
Aspiration is always a possibility
Laryngospasm can occur if adequate anesthesia is not achieved.
A significant air leak around the cuff may occur when
high airway pressures exist,leading to poor ventilation.

## Slide 65: The Esophageal-Tracheal Combitube
has two lumina running parallel to each other. One is perforated at the level of the pharynx and occluded at the distal end, similar to the EOA. The second lumen is open at the distal end, resembling an endotracheal tube.
has two balloons: a proximal pharyngeal balloon that occludes the oropharynx by filling the space between the base of the tongue and the soft palate and a smaller, distal cuff that serves as a seal in either the esophagus or trachea
.

## Slide 66: Combitube
The ETC is superior to the EOA because no face mask seal is necessary and the risk of complications is lower.
The ETC should be used in an unresponsive person who requires an airway when tracheal intubation is not successful or practical.
Intact gag reflex
younger than 16 years or shorter than 5 feet tall.
Indications
Contraindications
It is contraindicated in suspected caustic poisonings or proximal esophageal disorders.

## Slide 67: Combitube
The device is held in the dominant hand and gently advanced caudally into the pharynx
The tube is passed blindly along the tongue to a depth that positions the printed rings on the proximal end of the tube between the patient's teeth or alveolar ridge.

## Slide 68: Combitube
If resistance is met in the hypopharynx, the tube should be removed and bent between the balloons for several seconds to facilitate insertion.
After insertion, the pharyngeal balloon is filled with 100 mL of air, and the distal cuff is subsequently filled with 10 to 15 mL of air.
One must remember to first inflate the oropharyngeal balloon before inflating the distal balloon. Although unlikely, esophageal injury is theoretically possible with overinflation of the distal balloon.

## Slide 69: Combitube
The large pharyngeal balloon serves to securely seat the ETC in the oropharynx and to create a closed system in the case of esophageal placement.
ventilation is begun through the longer (blue plastic) connector associated with the esophageal lumen.
Chest rise and good breath sounds without gastric insufflation confirm effective placement in the esophagus.

## Slide 70: Combitube
Gastric insufflation without breath sounds and chest rise indicate a tracheal positioning of the tube and require changing the ventilation to the shorter (clear plastic) tracheal lumen.
Auscultation of breath sounds over the lateral lung fields confirms endotracheal placement of the Combitube.
If the tube is in the esophageal position, gastric suctioning can be accomplished by passing a catheter through the open lumen into the stomach while the patient is being ventilated via the other port.

## Slide 71: Combitube
attach an aspirating device to the tracheal or clear plastic shorter tube. The inability to easily aspirate air confirms esophageal placement, necessitating ventilation via the longer blue esophageal tube.
CO2 detector devices also may be useful.

## Slide 72: Bullard Laryngoscope
No manipulation of the neck is necessary
Cervical spine injury.
Found to cause less head extension and cervical spine extension than the conventional laryngoscope

## Slide 73: Lighted Stylet Intubation
a blind approach
avoide in patients with expanding neck masses and patients with airway compromise presumed due to a foreign body.
Massive obesity is the most common cause for failure with this technique because of the difficulty transilluminating the generous soft tissue

## Slide 74
CHANGING TRACHEAL TUBES

## Slide 75
65 y o in cardiac arrest, just after you intubated him the RT told you the ETCO2 is low????

## Slide 76
65 year in cardiac arrest intubated O2 sat initialy was 100 % with normal Etco2. O2 sat start to go down now to 50.

## Slide 77
In patients with spontaneous circulation and the tracheal tube cuff inflated, the sensitivity and specificity rose to 100%.
cardiac arrest
secretions can interfere with the color change.
esophageal intubation.
cardiac arrest pt. should be ventilated for a minimum of 6 breaths before taking a reading.
recent ingestion of carbonated beverages
glottic positioning of the ET tube tip.
End-Tidal CO2 Detector Devices

## Slide 78
(1) a dislodged tube, either in the esophagus or in the right mainstem bronchus
(2) Tube obstruction
(3) a tension pneumothorax
(4) equipment failure.
50 y.o.f. asthmatic intubated for respiratory failure, O2 sat. after intubation was 100% ,30 minutes later you get called for decreasing O2 saturation???

## Slide 79
Failure to achieve adequate ventilation and oxygenation is the most serious complication of tracheal intubation (hypoxia)
Irreversible cerebral anoxia.
attempts at intubation should be halted for bag-mask ventilation whenever the O2 saturation drops below 92%.
vomiting following removal of a tube from the esophagus.
Right mainstem bronchus intubation may cause hypoxia as well as unilateral pulmonary edema.
Cardiac decompensation.
Profound bradycardia or asystole
laryngospasm, bronchospasm, and apnea.

## Slide 80
Loose, missing or avulsed teeth
Broken teeth
Laceration of the mucosa of the lips, especially the lower lip, may also occur.
Tracheal or bronchial injuries are rare but serious, usually occurring in infants and the elderly as a result of decreased tissue elasticity.
Vomiting with aspiration of gastric contents is another serious complication that can occur during intubation.
Exacerbation of a cervical spine injury remains largely a theoretical concern.
a persistent air leak.
Tracheal stricture

## Slide 81
Drug: action | Indications | IV dose
Lidocaine: reduces intracranial response to laryngoscopy and bronchospastic response to laryngoscopy and intubation | Patients with elevated intracranial pressure (ICP) or penetrating globe injury who are receiving succinylcholine; reactive airway disease | 1.5 mg/kg
Atropine: mitigates bradycardic response to succinylcholine | Children under 10 years old | 0.02 mg/kg
Indications for Pretreatment Agents
Fentanyl: reduces sympathetic (heart rate, blood pressure) response to laryngoscopy and intubation | Elevated ICP, intracranial hemorrhage, berry aneurysm, ischemic heart disease, aortic dissection | 3 μg/kg

## Slide 82
Agent | Initial IV Dose | Duration of Action
Morphine | 3-5 mg | 2-3 hours
Meperidine | 25-50 mg/kg | 2-4 hours
Fentanyl | 2-3 μg/kg | 0.5-1 hours
Sufentanil | 0.1-0.4 μg/kg | 20-45 minutes
Alfentanil | 10-15 μg/kg | 30 minutes
Commonly used intravenous opioids

## Slide 83
Cricothyrotomy