## Slide 1: Exp#6 Bilirubin
Quantitative determination of bilirubin in serum using a modified Malloy-Evelyn colorimetric/Endpoint procedure

## Slide 2: Definition
Bilirubin: is the yellow breakdown product of normal haemoglobin & excreted in bile and urine.
DIRECT (Conjugated) | INDIRECT(Unconjugated)
bound to albumin and sent to the liver. In the liver it is conjugated with glucuronic acid soluble in water. | Erythrocytes damaged Hb The heme is then turned into unconjugated bilirubin in the reticulo-endothelial cells of the spleen. not soluble in water.

## Slide 3: Clinical Significance
-An increase in bilirubin conc. Is called jaundice.
High level of direct type means that the bile is not being properly excreted.
-High levels of indirect mean more Hb is being damaged.
*Elevation of total bilirubin occur due to:
Excessive hemolysis of RBC
Liver diseases e.g. hepatitis &cirrhosis
Obstruction of biliary tract e.g. gall stones

## Slide 4
-Both conjugated (direct) and unconjugated (indirect) bilirubin are increased in hepatitis.
-The relative proportion of the conjugated fraction increases with progression of the disease until eventually the liver loses its ability to carry out the conjugation reaction

## Slide 5: Principle
Bilirubin in the serum is coupled with diazotized sulfanilic acid to form azobilirubin.
The intensity of the purple color that is formed is proportional to the bilirubin concentration in the serum.
Bilirubin glucuronide(the conjugated or direct bilirubin) reacts with the diazo reagent in aqueous solution to form a colored diazo compound within 1 minute.
This is the calculation of Direct Bilirubin

## Slide 6
The subsequent addition of methanol accelerates the reaction .of unconjugated bilirubin in the serum, and a value of total bilirubin is obtained after letting the sample stand for 5 minutes.
*This is the calculation of Total Bilirubin
The total bilirubin value represents the sum of the bilirubin glucoronide (direct) and the unconjugated (indirect) bilirubin.
The color formed in the reaction is measured photometrical at 540/ 546 nm

## Slide 7: Specimen
serum
While processing samples, protect from direct light as loss of bilirubin may occur.
Bilirubin in serum is reportedly stable for 4- 7 days, when stored in the dark at 2-8°C

## Slide 8: Procedure#1
Test | Test Blank | 
1400 | 1400 | Sulfanilic Acid Rgt-µl
25 | --- | Sodium Nitrate Rgt-µl
--- | 25 | DW
Mix & let stand for 1 min, then add: |  | 
100 | 100 | Sample
Mix & let stand for 1 min, read A at 540nm against DW ( Direct Calculation) |  | 
1500 | 1500 | Methanol-µl
Mix and stand for 5 min RT |  | 
Read A for both at same wavelength (Total Bilirubin) |  | 

## Slide 9: Calculation
1.The absorbance of Bilirubin Equivalent Std represents : Direct Bilirubin = 2.5 mg/dl
Total Bilirubin = 5.0 mg/dl
2. Direct Bilirubin (1 minute reading) :
A(T)- A(test blank) x 2.5mg/dl= D.Bilirubin(mg/dl)
A(bilirubin equivalent std)

## Slide 10
3-Total bilirubin(5min):
A(T)- A(test blank) x 5.0 mg/dl = Total bilirubin A(bilirubin equivalent std)
*Normal Range:
Direct……up to 0.5 mg/dl
Total……..up to 1.0 mg/dl

## Slide 11: Procedure #2
Total bilirubin |  | Direct bilirubin |  | 
Test | Test Blank | Test | Test Blank | 
500 | 500 | 1000 | 1000 | Sulfanilic Acid Rgt-µl
20 | --- | 20 | --- | Sodium Nitrate Rgt-µl
Mix and let stand for at least 1 min |  |  |  | 
50 | 50 | 50 | 50 | Sample
After exactly 1min. read the absorbance of Test and Test Blank (of Direct bilirubin only) at 546 nm against DW |  |  |  | 
500 | 500 | --- | --- | Methanol
Mix and let stand for 5 min. at RT and read A of test and test Blank (Total Bilirubin) at 546 nm against DW |  |  |  | 

## Slide 12: Calculation
USING FACTOR(25)
1-Direct Bilirubin
(A. Test ــــ A. Test Blank) x 25 = Direct Bilirubin (mg/dL).
2.-Total Bilirubin
(A Test ــــ A Test Blank) x 25 = Total Bilirubin (mg/dL).

## Slide 13: Limitation
1-Hemolysis interferes with the reaction to give falsely decreased values
2-severe lipemia may cause loss of precision.