## Slide 1: Bioremediation
Definition: Use of living organisms to transform, destroy or immobilize contaminants
Goal: Detoxification of the parent compound(s) and conversion to products that are no longer hazardous to human health and the environment.

## Slide 2: Forms of Bioremediation
In situ Bioremediation: treating contamination at the site often used ( less movement )
  Bioventing
  biodegradation
  Biosparging
  Bioaugmentation
Ex situ Bioremediation
Remove contamination and treat elsewhere
  Land farming
  Composting
  Biopiles

## Slide 3: Forms of Bioremediation
Phytoremediation
  Phytoextraction or phytoaccumulation
  Phytodegradation or phytotransformation
  Phytostabilization
  Rhizodegradation
  Rhizofiltration

## Slide 4: In Situ Bioremediation
Bioventing
  One of the most common approaches in soil
  Supply air and nutrients via wells
  Takes advantage of indigenous microorganisms
In situ biodegradation
  Supply air and nutrients by circulating aqueous solutions through contaminated soils or groundwater
Biosparging
  Injection of air below the water table  increases groundwater oxygen concentrations and mixing in saturated zone
Bioaugmentation
  Addition of indigenous or exogenous microorganisms
  Limits to use: competition and necessity
Biostimulation
Natural Attenuation or Intrinsic Bioremediation

## Slide 5: Bioventing

## Slide 6: Biosparging

## Slide 7: Ex situ Bioremediation
Land farming
  Contaminated soil is excavated and spread over land
  Soil is periodically tilled to improve aeration
  Remediation due to indigenous microorganisms, as well as chemical and physical processes
  Generally limited to the superficial 10–35 cm of soil
  Can reduce monitoring and maintenance costs
Composting
  Combines contaminated soil with nonhazardous organic amendants (e.g. manure or agricultural wastes)
Biopiles
  Combination of landfarming and composting
  Control physical losses of contaminants
Bioreactors
  Soil and water pumped up from a contaminated plume and processed through an engineered containment system
  Degradation in a bioreactor is generally greater than in situ because the contained environment is more controllable and predictable

## Slide 8: Feasibility / Effectiveness
a function of:
  Microorganisms
  Environmental factors
  Contaminant type & state

## Slide 9: Microorganisms
Aerobic bacteria:
  Examples include: Pseudomonas, Alcaligenes, Sphingomonas, Rhodococcus, and Mycobacterium
  Shown to degrade pesticides and hydrocarbons; alkanes and polyaromatics
  May be able to use the contaminant as sole source of carbon and energy.
Methanotrophs:
  Aerobic bacteria that utilize methane for carbon and energy
  Methane monooxygenase has a broad substrate range
    active against a wide range of compounds (e.g. chlorinated aliphatics such as trichloroethylene and 1,2-dichloroethane)
Anaerobic bacteria:
  Not used as frequently as aerobic bacteria
  Can often be applied to bioremediation of polychlorinated biphenyls (PCBs) in river sediments, trichloroethylene (TCE), and chloroform
Fungi:
  Able to degrade a diverse range of persistent or toxic environmental pollutants

## Slide 10: Environmental Factors
Nutrient availability
Environmental Conditions
Metal content

## Slide 12: Phytoremediation
Phytoextraction or phytoaccumulation
  Plants used to accumulate contaminants in the roots and aboveground biomass
  Can be a relatively low cost option for a large area
  Results in biomass that must be properly disposed of or reused
Phytotransformation or phytodegradation
  Uptake of contaminants and transformation to more stable, less toxic, or less mobile forms
  Eg. metal chromium can be reduced from hexavalent to less mobile (and non-carcinogenic) trivalent chromium
Phytostabilization
  Mobility and migration of contaminants are reduced through sorption onto or into the plant
Rhizodegradation
  Breakdown of contaminants through activity of the rhizosphere
Rhizofiltration
  Water remediation technique
  Used to reduce contamination in natural wetlands and estuary areas.

## Slide 14: Five Steps of In Situ Bioremediation
Site investigation
2. Treatability studies
3. Recovery of free product and removal of the
contamination source
4. Design and implementation of the in situ
bioremediation system
5. Monitoring and performance evaluation of the in situ bioremediation system