## Slide 1: Emotion Recognition from Physiological Measurement (Biosignal)
Jonghwa Kim
Applied Computer Science
University of Augsburg
Workshop Santorini, HUMAINE WP4/SG3

## Slide 2: Overview
What is Emotion?
Biosensors
Previous Works
Experiment in Augsburg
Future Work / SG3 Exemplars

## Slide 3: What is Emotion ?

## Slide 4: What is Emotion?
.…”Everyone knows what an emotion is, until asked to give a definition”….
- Beverly Fehr and James Russell -
Emotions play a major role in:
  motivation, perception, cognition, coping, creativity, attention, planning, reasoning, learning, memory, and decision making.
We do not seek to define emotions but to understand them….

## Slide 5: Understanding Emotion
Emotion is not phenomenon, but a construct
Components of emotion: cognitive processes, subjective feelings, physiological arousal, behavioral reactions

## Slide 6: Affect, Mood, and Emotion
Emotion: a concept involving three components
  Subjective experience
  Expressions (audiovisual: face, gesture, posture, voice intonation, breathing noise)
  Biological arousal (ANS: heart rate, respiration frequency/intensity, perspiration, temperature, muscle tension, brain wave)
Affect: some more than emotions, including personality factors and moods
Mood: long-term emotional state, typically global and very variable over the time, dominates the intensity of each short-term emotional states.

## Slide 7: Emotion Models
High arousal
Low arousal
Negative
Positive
Terror
Agitation
Mournful
Bliss
Excited Anticipation
Distressed
Disgust
Relaxed

## Slide 8: Using Biosensors

## Slide 9: Why Biosignal ?
Different emotional expressions produce different changes in autonomic activity:
  Anger: increased heart rate and skin temperature
  Fear: increased heart rate, decreased skin temperature
  Happiness: decreased heart rate, no change in skin temperature
Continuous data collection
Robust against human social artifact
Easily integrated with external channels (face and speech)

## Slide 10: Sensing Physiological Information
BVP- Blood volume pulse
EMG – Muscle tension
EKG– Heart rate
Respiration – Breathing rate
Temperature
GSR – Skin conductivity
Acoustics and noise
EEG – Brain waves

## Slide 11: ECG (Electrokardiogram)
Measures contractile activity of the heart
On surface of chest or limbs
Heart rate (HR), inter-beat intervals (IBI) and heart rate variability (HRV), respiratory sinus arrhythmia
Emotional cues:
  Decreasing HR: relaxation, happy
  Increasing HRV: stress, frustration

## Slide 12: BVP (Blood Volume Pulse)
Photoplethysmography, bounces infra-red light against a skin surface and measures the amount of reflected light.
Palmar surface of fingertip
Features: heart rate, vascular dilation (pinch), vasoconstriction
Cues:
  Increasing BV- angry, stress
  Decreasing BV- sadness, relaxation

## Slide 13: EEG (Electroencephalography)
Electrical voltages generated by brain cells (neurons) when they fire, frequencies between 1-40Hz
Frequency subsets: high beta (20-40Hz), beta (15-20Hz), Sensorimotor rhythm (13-15Hz), alpha (8-13Hz), theta (4-8Hz), delta (2-4Hz), EMG noise (> 40Hz)
Standard 10-20 EEG electrode placement
Mind reading, biofeedback, brain computing
Raw
Alpha

## Slide 14: EMG (Electromyogram)
Muscle activity or frequency of muscle tension
Amplitude changes are directly proportional to muscle activity
On the face to distinguish between negative and positive emotions
Recognition of facial expression, gesture and sign- language

## Slide 15: SC (Skin Conductivity)
Measure of skin’s ability to conduct electricity
Linear correlated with arousal
Represents changes in sympathetic nervous system and reflects emotional responses and cognitive activity

## Slide 16: RESP (Respiration)
Relative measure of chest expansion
On the chest or abdomen
Respiration rate (RF) and relative breath amplitude (RA)
Emotional cues:
  Increasing RF – anger, joy
  Decreasing RF – relaxation, bliss

## Slide 17: Temp (Peripheral Temperature)
Measure of skin temperature as its extremities
Dorsal or palmar side of any finger or toe
Dependent on the state of sympathetic arousal
Increase of Temp: anger > happiness, sadness > fear surprise, disgust

## Slide 18: Previous Works

## Slide 19: General Framework of Recognition
Definition of pattern classes: supervised classification
Sensing: data acquisition using biosensors in natural or scenarized situation
Preprocessing: noise filtering, normalization, up/down sampling, segmentation
Feature Calculation: extracting all possible attributes that represent the sensed raw biosignal
Feature Selection / Space Reduction: identifying the features that contribute more in the clustering or classification
Classification / Evaluation (pattern recognition): multi-class classification

## Slide 20: Ekman et al. (1983)
Manual analysis of the biosignals (finger temperature, heart rate) w.r.t. anger, fear, sadness, happiness, disgust, and surprise
Relative emotional cues
  HR: anger, fear, sadness > happiness, surprise > disgust
  HR Acceleration: anger > happiness
  Temp: anger > happiness, sadness > fear surprise, disgust

## Slide 21: Cacioppo et al. (1993, 2000)
Provide a wide range of links between physiological features and emotional states
Anger increases diastolic blood pressure to the greatest degree, followed by fear, sadness, and happiness
Anger is further distinguished from fear by larger increases in blood pulse volume
“anger appears to act more on the vasculature and less on the heart than does fear”

## Slide 22: Gross & Levenson (1995, 1997)
Study to find most effective films to elicit discrete emotions, amusement, anger, contentment, disgust, fear, neutrality
Amusement, neutrality, and sadness were elicited by showing films
Skin conductance, inter-beat interval, pulse transit times and respiratory activation were measured
Inter-beat interval increased for all three states, the least for neutrality
Skin conductance increased after the amusement film, decreased after the neutral film and stayed the same after the sadness film.

## Slide 23: Vyzas, Picard et al. (MIT Media Lab, 2000)
Discriminating self-induced emotional states in a single subject (actress)
Dataset: 20 days x 8 emotions x 4 sensors x 1 actress
Emotion model: happiness, sadness, anger, fear, disgust, surprise, neutrality, platonic love, and romantic love
Sensors: GSR (SC), BVP, RESP, EMG
11 features for each emotion
Algorithms: SFFS (sequential forward floating search), Fisher projection, hybrid of these
Overall accuracy 81.25% by hybrid method

## Slide 24: Kim et al. (Univ. Augsburg, 2004)
“Emote to Win”: emotive game interfacing based on affective interactions between player and computer pet (“Tiffany”)
Combined analysis of two channels, speech + biosignal in online
Features
  Speech: pitch, harmonics, energy
  Biosignal: mean energy (SC/EMG), StdDeviation (SC, EMG), heart rate (ECG), subband spectra (ECG/RESP)
Simple threshold-based online classification
Hard to acquire reliable emotive information of users in online condition

## Slide 25: Why is this hard ?
Need to develop strong correlations between sensor data and emotion (robust signal processing and pattern matching algorithms)
Too many dependency variables
Skin-sensing requires physical contact, compared with camera and microphone
Need to improve biometric sensor technology
  Accuracy, robustness to motion artifacts, vulnerable to distortion
  Wireless ambulant sensor system
Most research measures artificially elicited emotions in a lab setting and from single subject
Different individuals show emotion with different response in autonomic channels (hard for multi-subjects)
Rarely studied physiological emotion recognition, literature offers ideas rather than well-defined solutions

## Slide 26: Experiment in Univ. Augsburg

## Slide 27: AuDB (Augsburger database of biosignal)
Musical induction: each participant selects four favorite songs reminiscent of their certain emotional experiences corresponding to four emotion categories
Song selection criteria
  song1: enjoyable, harmonic, dynamic, moving
  song2: noisy, loud, irritating, discord
  song3: melancholic, reminding of sad memory
  song4: blissful, slow beat, pleasurable, slumberous
3 subjects x 25 days x 4 emotions x 4 sensors (SC, RESP, ECG, EMG)
song2
song1
song3
song4
Energetic
Calm
Anxious
Happy
High arousal
Low arousal
Positive
Negative
angry
joy
bliss
sad
Music genre / Emotion

## Slide 28: AuDB Raw Signal (sample)

## Slide 29: Features
29 Features from common feature set: mean, standard deviation, slope, and frequency (rate), using rectangular window
SC: scPassMean, scPassStd, scPassDiff, scBaseMean, scBaseStd, scPassNormMean, scPassNormDiff, scPassNormStd, scBaseStd, scBaseMean
RESP: rspFreqMean, rspFreqStd, rspFreqDiff, rspSpec1, rspSpec2, rspSpec3, rspSpec4, rspAmplMean, rspAmplStd, rspAmplDiff
ECG: ekgFreqMean, ekgFreqStd, ekgFreqDiff
EMG: emgBaseMean, emgBaseStd, emgBaseDiff, emgBaseNormMean, emgBaseNormStd, emgBaseNormDiff

## Slide 30: Features : example

## Slide 31: Fisher Projection (Arousal)
High arousal : joy (song1) + angry (song2)
Low arousal : sadness (song3) + bliss (song4)

## Slide 32: Fisher Projection (Valence)
Positive : joy (song1) + bliss (song4)
Negative : anger (song2) + sadness (song3)

## Slide 33: Fisher Projection (4 Emotions)
Four emotions : joy (song1), anger (song2), sadness (song3), bliss (song4)

## Slide 34: Recognition Result 1
AuDB – no selection - reduction (Fisher) – Classification (Mahalanobis distance)

## Slide 35: Recognition Result 2
AuDB – selection (SFFS) - no reduction – classification (LDA with MSE)

## Slide 36: Recognition Result 3
MIT Dataset – UA feature calculation - MIT feature selection, reduction, classification

## Slide 37: Conclusion
Database (AuDB) collected by natural musical induction from multiple subjects
29 features proven as efficient
Compared several classification methods
Need to predict the mood for as baseline of daily emotion intense
Need to develop online training method
Need to extend number of features for person-independent recognition system
This experiment is still on going

## Slide 38: Future Work in SG3

## Slide 39: Future Work in SG3
Extension of available features in biosignal, e.g. cross- correlation features between the different biosignal types
Combining multiple classification methods depending on characteristic of pattern types and applications
Need to adapt offline algorithms into online recognition system (online training, estimating decision threshold)
Feature fusion, e.g. correlating EMG features with FAP features (SG1) and SC/RESP features with quality features in speech (SG2)

## Slide 40: Suggestion to WP4 Exemplar
Efficiently fusing recognition systems of each subgroup (audio + visual + physiological) in online/offline condition, then designing application

## Slide 41: Multisensory Data Fusion for Emotion Engine - after project: muchEROS (Univ. Augsburg)
CH4
Env. Cont.
Prediction using work histogram generated as emotion of computer
Optimization of training / Management of preferences
Feature Fusion
Selection / Reduction
Classification
CH3
Biosignal
CH2
Speech
Feature
Extraction
Feature
Extraction
CH1
Face
Feature
Extraction
Local
Classifier
Local
Classifier
Local
Classifier
stance
pleasure
arousal
Emotion Space
E (a,p,s)
Rule/Fuzzy Based
Decision
Weighted Decision
Decision Feature Set

## Slide 42: Thank you !