## Slide 1: CE417: Construction Methods and Management
Tutorial #2

## Slide 2: CH2: Earthmoving Materials and Operations
Q1\How many truck loads of hauling an average volume of 6 LCM would be required to haul million CCM of Q\4 in tutorial 1?
Load factor= 0.806 = 0.8
Shrinkage factor = 0.849 = 0.85
Bank volume==
Loose volume=
Number of trucks=

## Slide 3
Q2\Calculate the volume of excavation in bank measure required for the basement shown?
By using interpolation
second part
First part

## Slide 4
Average depth of first part =
Area of first part = 24 ×28 = 672
Volume of excavation of first part = Area × depth = 672 × 6.717 = 4513.8 BCf
Average depth of second part =
Area of second part = 45 ×26 = 1170
Volume of excavation of second part = Area × depth = 1170 × 7.442 = 8707.14 BCf
Total volume of excavation = 4513.8 + 8707.14 =13220.94 BCf
second part
First part

## Slide 5
Q3\ Elevations of the normal ground with respect to a proposed highway are as following: (Assume width of the road= 1m)
Find the following:
1-Draw the highway profile and mass diagram.
2-The total volume of a cut , fill , waste and borrow.
3- The average length of haul in the balance sections.
Distance along centerline (m) | 0 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500
Elevation(m) | 0 | -10 | 0 | 12 | 0 | -15 | 0 | 5
Volume( | 0 | -2500 | -2500 | 3000 | 3000 | -3750 | -3750 | 1250
Cumulative Volume ( | 0 | -2500 | -5000 | -2000 | 1000 | -2750 | -6500 | -5250
Distance along centerline (m) | 0 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500
Elevation(m) | 0 | -10 | 0 | 12 | 0 | -15 | 0 | 5
 | 0 | -2500 | -2500 | 3000 | 3000 | -3750 | -3750 | 1250
 | 0 | -2500 | -5000 | -2000 | 1000 | -2750 | -6500 | -5250

## Slide 6
1-Draw the highway profile and mass diagram.
Chart: 
| 0 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500
Highway Profile | 0 | -10 | 0 | 12 | 0 | -15 | 0 | 5

## Slide 7
1-Draw the highway profile and mass diagram.
.
Chart: 
| 0 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500
Mass Diagram | 0 | -2500 | -5000 | -2000 | 1000 | -2750 | -6500 | -5250
2-The total volume of a cut , fill , waste and borrow.
Total volume of cut = 7250 , Total volume of fill= 12500
Borrow= 12500-7250=5250Waste = Zero
3- The average length of haul in the balance sections.
Section 1 =916.6m
Section 2 = 166m

## Slide 8
Q4\ Elevations of the normal ground with respect to a proposed highway are as following: (Assume width of the road= 10m & Shrinkage factor is 0.85)
Find the following:
1-Draw the highway profile and mass diagram.
2-The total volume of a cut , fill , waste and borrow.
3- The average length of haul in the balance sections
Distance along centerline (m) | 0 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 | Total volume
Elevation(m) | 0 | -11 | 0 | 13 | 0 | -15 | 0 | 6 | 
Fill CCM | 0 | -27500 | -27500 |  |  | -37500 | -37500 |  | 
Fill BCM | 0 | -32353 | -32353 |  |  | -44118 | -44118 |  | -152942
Cut BCM |  |  |  | 32500 | 32500 |  |  | 15000 | 80000
Cumulative Volume ( | 0 | -32353 | -64706 | -32206 | 294 | -43824 | -87942 | -72942 | 
Distance along centerline (m) | 0 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500 | Total volume
Elevation(m) | 0 | -11 | 0 | 13 | 0 | -15 | 0 | 6 | 
Fill CCM | 0 | -27500 | -27500 |  |  | -37500 | -37500 |  | 
Fill BCM | 0 | -32353 | -32353 |  |  | -44118 | -44118 |  | -152942
Cut BCM |  |  |  | 32500 | 32500 |  |  | 15000 | 80000
 | 0 | -32353 | -64706 | -32206 | 294 | -43824 | -87942 | -72942 | 

## Slide 9
1-Draw the highway profile and mass diagram.
Chart: 
| 0 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500
Highway Profile | 0 | -11 | 0 | 13 | 0 | -15 | 0 | 6

## Slide 10
1-Draw the highway profile and mass diagram.
.
2-The total volume of a cut , fill , waste and borrow.
Total volume of cut = 80000BCM , Total volume of fill= 152942BCM
Borrow= 152942-80000=72942BCMWaste = Zero
3- The average length of haul in the balance sections.
Section 1 =940m
Chart: 
| 0 | 500 | 1000 | 1500 | 2000 | 2500 | 3000 | 3500
Mass Diagram | 0 | -32353 | -64706 | -32206 | 294 | -43824 | -87942 | -72942

## Slide 11
Q5\ Plot the highway profile & mass diagram for the given data , then find the total volume of cut , fill and waste or borrow. After that find average haul distance. : (Assume width of the road= 1m)
Distance along centerline (m) | 0 | 100 | 200 | 300 | 400 | 500 | 600
Volume( | 0 | -250 | -250 | 350 | 350 | -300 | -300
Cumulative Volume ( | 0 | -250 | -500 | -150 | 200 | -100 | -400
Elevations (m) | 0 | -5 | 0 | 7 | 0 | -5 | 0
Distance along centerline (m) | 0 | 100 | 200 | 300 | 400 | 500 | 600
 | 0 | -250 | -250 | 350 | 350 | -300 | -300
 | 0 | -250 | -500 | -150 | 200 | -100 | -400
Elevations (m) | 0 | -5 | 0 | 7 | 0 | -5 | 0

## Slide 12
1-Plot the highway profile.
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600
Highway Profile | 0 | -5 | 0 | 7 | 0 | -5 | 0

## Slide 13
1-Plot the mass diagram.
.
2-The total volume of a cut , fill , waste and borrow.
Total volume of cut = 700 , Total volume of fill= 1100
Borrow= 1100-700= 400 Waste = Zero
3- The average length of haul in the balance sections.
Section 1 =173m
Section 2 =60m
Chart: 
| 0 | 100 | 200 | 300 | 400 | 500 | 600
Mass Diagram | 0 | -250 | -500 | -150 | 200 | -100 | -400

## Slide 14: Thank You
Questions Please