## Slide 1: CE417: Construction Methods and Management
Tutorial #5

## Slide 2: CH4:Loading and hauling
Cycle time = Fixed time + Variable time
Total resistance =
Grade resistance + Rolling resistance
  Rolling resistance factor (kg/t) = 20(15)* + (6 × cm penetration)
  *For radial tires
The rolling resistance(kilograms) = Rolling resistance factor × the vehicle‘s weight in (metric tons).
  Grade resistance factor (kg/t) =10(Kg/t) × grade (%)
  Grade resistance (kg) =Vehicle weight (t) × Grade resistance factor (kg/t)
  Grade resistance (kg) =Vehicle weight (kg) x Grade
  Effective grade (%) = Grade (%) + Rolling resistance factor (kg/t) / 10
  Total resistance(kg)= Rolling resistance (kg) + Grade resistance (kg)

## Slide 3: TABLE 4-1 Typical values of rolling resistance factor

## Slide 4
Q1) A wheel tractor-scraper weighing 100 tons (91 t) is being operated on a haul road with a tire penetration of 2 in. (5 cm).
What is the total resistance (kg) and effective grade when
  (a) the scraper is ascending a slope of 5%?
  (b) the scraper is descending a slope of 5%?
  Rolling resistance factor= 20 + (6 × 5) =50 kg/t
  Rolling resistance(kg) = 50 (kg/t) × 91 (t) = 4550 kg
  a)
  Grade resistance (kg) = 91 (t) x 1000 (kg/t) × 0.05 =4550 kg
  Total resistance (kg)= 4550 (kg) + 4550 (kg) = 9100 kg
  Effective grade(%)= 5 + 50/10 = 10%
  b)
  Grade resistance (kg) = 91 (t) × 1000 (kg/t) x (-0.05) = - 4550 kg
  Total resistance (kg)= 4550 (kg) + -4550 (kg) = 0 kg
  Effective grade(%)= -5 + 50/10 = 0%

## Slide 5
Q2)A crawler tractor weighing (36 t) is towing a rubber-tired scraper weighing (45.5 t) up a grade of 4%. What is the total resistance ( kg) of the combination if the rolling resistance factor is
(50 kg/t)?
  Rolling resistance (kg) (neglect crawler) = 45.5 (t) × 50 (kg/t) =2275 kg
  Grade resistance(kg) =(36+45.5) (t) × 1000 (kg/t) × 0.04 = 3260 kg
  Total resistance(kg)= 2275 + 3260 = 5535 kg

## Slide 6
Effect of Altitude and Traction
Engine power decreases approximately 3% for each (305 m).
Turbocharged engines are more efficient at higher altitude 3050 m or more.
Derating factor (%) = (Altitude (m) - 915*)/102
The percentage of rated power available = 100 - the derating factor.
Maximum usable pull = Coefficient of traction × Weight on drivers

## Slide 7: TABLE 4-2: Typical values of coefficient of Traction

## Slide 8
Q3) A four-wheel drive tractor weighs (20000 kg) and produces a maximum rimpull of
(18160 kg) at sea level.
The tractor is being operated at an altitude of (3050 m) on wet earth.
A pull (10000 kg (total resistance) ) is required to move the tractor and its load.
Can the tractor perform under these conditions?
  Derating factor = (3050-­ 915)/102 =21%
  Percent rated power available=100 ­- 21 = 79%
  Maximum available power = 18160 × 0.79 = 14346 kg
  Coefficient of traction = 0.45 (Table 4-2)
  Maximum usable pull = 0.45 × 20000 = 9000 kg
  Because the maximum pull as limited by traction is less than the required pull, the tractor cannot perform under these conditions.
  For the tractor to operate, it would be necessary to:
    reduce the required pull (total resistance),
    increase the coefficient of traction, or
    increase the tractor's weight on the drivers.

## Slide 13: Thank You
Questions Please