## Slide 1
Chapter 1 Introduction Into Computer Network
Prepared by .AbdulRahman
2014

## Slide 2: :Computer Network
A computer network is a collection of computers and devices connected by communications channels that facilitate communication among users and allow them to share resources with other users

## Slide 3: Motivations for using computer nets are:
Higher Computation Power
Facilitating communications
Sharing files, data, and software
remote access to centralized resources (e.g. databases)
Many useful applications: WWW, e-commerce, e-learning, e-medicine, video-on-Demand and multimedia communications

## Slide 4: Computer Network consist of :
Network Edge : End Systems(host)
    Network core: Routers, circuit switching, packet switching, network structure
Access Network: the communication links such as Twisted Pair (TP), Fiber optic cable

## Slide 5: Access networks and physical media
Dial-up Modem: Uses existing telephony infrastructure , up to 56Kbps direct access to router.
DSL : telephone infrastructure up to 1 Mbps upstream (today typically < 256 kbps)
  Ethernet : Typically used in companies, universities, 10 Mbs, 100Mbps, 1Gbps, 10Gbps Ethernet

## Slide 6: :Wireless access networks
shared wireless access network connects end system to router
  via base station aka “access point”
wireless LANs:
  802.11b/g (WiFi): 11 or 54 Mbps
wider-area wireless access
  provided by Telco operator
  1Mbps over cellular system .

## Slide 7: Physical Media:
Twisted Pair (TP)
telephone wires which consist of two insulated copper wires twisted into pairs and are used for both voice and data transmission
The transmission speed ranges from 2 Mbps to 100 Mbps
use of two wires twisted together helps to reduce crosstalk .

## Slide 8: Physical Media (cont):
Coaxial cable:
copper or aluminum wire wrapped with insulating layer
Transmission speed range from 200 Mbps to more than 500 Mbps
minimize interference and distortion.
baseband:
  single channel on cable
broadband:
  multiple channels on cable

## Slide 9: Physical Media(cont):
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gps)
Fiber-optic cables are not affected by electromagnetic radiation.

## Slide 10: Radio /Wireless :
signal carried in electromagnetic spectrum
no physical “wire”
Radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., Wifi)
  10Mbps, 54 Mbps
wide-area (e.g., cellular)
such as between neighboring towns and cities
  3G cellular: ~ 1 Mbps

## Slide 11: Hub & Switch & Router :
Hub : forwards the packets arrive at one port, copied unmodified, to its all ports for transmission

## Slide 12: Hub & Switch & Router :
Switch : forwards and filters packets between ports involved in the communication based on the MAC addresses in the packets.

## Slide 13: Hub & Switch & Router :
Router : forwards packets between ports using information in protocol headers and forwarding tables (IP address) and determine the best next router for each packet

## Slide 14: Four sources of packet delay:
Processing delay
queuing delay
transmission delay
propagation delay
A
B
propagation
transmission
nodal
processing
queueing

## Slide 15: 1)Processing Delay:
processing delay is the time it takes routers to process the packet header.
  check bit errors
  determine output link

## Slide 16: 2)Queuing Delay:
Queuing delay is the wait while a router prepares and transmits packets.
  depends on congestion level of router

## Slide 17: 3)Transmission Delay:
Transmission delay is the amount of time required to push all of the packet's bits into the communication link.
This delay is proportional to the packet's length in bits,
It is given by the following formula
L=packet length (bits)
R=link bandwidth (bps)
time to send bits into link = L/R
For example: say we have a 1500 byte Ethernet packet being sent out on a 100 Mb/s link.
Solution : 1500 bytes is 12,000 bits (we will use 1 byte == 8 bits consistently). So, the transmission delay is
(12000 bits / 108 bits) = 1.2 * 10-4 seconds = .12 milliseconds

## Slide 18: 4)Propagation delay:
Propagation delay: In general it is the length of time taken for the quantity of interest to reach its destination.
d = length of physical link (meters).
s = propagation speed(which is about 2 * 108 meters/second)
propagation delay = d/s
Say we have a single wire or optical fiber running from the east coast of the US to the west coast, or around 3000 miles or 5000 km and the propagation speed is 2 * 108 meters . 5000 km is 5 * 106 meters. So, the
propagation delay is:
(5 * 106 meters / 2 * 108 meters) = (5 / 200) seconds = .025 seconds = 25 milliseconds

## Slide 19: Throughput & Bandwidth:
Throughput | Bandwidth
rate (bits/time unit) at which bits transferred between sender/receiver, and while a specific set of data is transmitted on the network | The carrying capacity of a communications circuit

## Slide 20: Network protocol:
network protocol : a protocol defines the format and the order of messages exchanged between two or more communicating entities, as well as actions taken on the transmission and/or receipt of message or other event
Communicating entities are often a client, or process in need of a service, and a server, or process providing the service
Lists of network protocols:
FTP File Transfer Protocol
SMTP Simple Mail Transfer Protocol
Telnet Telephone Network
HTTP Hyper Text Transfer Protocol

## Slide 21: Layers :
Layers: each layer implements a service
Why layering?
Simplifies the complexity of network systems
helps identify the functions and the relationships between these pieces
Assists in protocol design, because protocols that operate at a specific layer have defined information that they act upon and a defined interface to the layers above and below.
eases maintenance, updating of system
change of implementation of layer’s service doesn’t affect the rest of system

## Slide 22: The 5-Layer Model (the TCP/IP Model)
The 5-layer model serves primarily the protocols known as Transmission Control Protocol (TCP) and Internet Protocol (IP), or jointly, TCP/IP. The 5-layer model was developed along with these protocols.
Application
transport
Network
link
physical

## Slide 23: Layering( the TCP/IP Model) :
The Application Layer: governing communication between client and server processes or between peer processes ,and Provide applications services to users and programs
Simple Mail Transfer Protocol (SMTP) is used for mail delivery
Hypertext Transfer Protocol (HTTP) is used for transfer of web pages
File Transfer Protocol (FTP) is used for transferring files

## Slide 24: Layering ( the TCP/IP Model) :
Transport Layer : is responsible for delivery of information between processes on different machines on the internet , process-process data transfer.
The two protocols in the transport layer are
Transmission Control Protocol (TCP) for connection-oriented service
And provides the following transport services handshaking, Reliable data transfer , congestion control
User Datagram Protocol (UDP) for connectionless service which emphasizes low-overhead operation and reduced latency rather than error checking and delivery validation.

## Slide 25: Layering ( the TCP/IP Model) :
Network Layer : Provides network addressing and routing, and does so in such a( routing of datagram (packets) from source to destination), This makes possible the interconnection of networks that characterizes the Internet.
  IP : Its routing function enables internet networking, and essentially establishes the internet.
  routing protocols.

## Slide 26: Layering ( the TCP/IP Model) :
Data Link Layer : is responsible for delivery of information across a single link that transfers data between adjacent network nodes.
  PPP : commonly used in establishing a direct connection between two networking nodes . It can provide connection authentication , transmission encryption used over many types of physical networks including . serial cable, phone line, trunk line, cellular telephone .
Ethernet : used coaxial cable as a shared medium. Later the coaxial cables were replaced with twisted pair and fiber optic links in conjunction with hubs or switches
Physical Layer : bits “on the wire”.

## Slide 27: Layering ISO/OSI:
Presentation : Deals with syntactic representation of data and allow applications to interpret meaning of data : e.g., agreement on character code (e.g., ASCII, extensions to ASCII, Unicode), data-compression and data-encryption methods, representations of graphics
Multipurpose Internet Mail Extensions (MIME)
External Data Representation (XDR): is a standard for the description and encoding of data. It is useful for transferring data between different computer architectures

## Slide 28: Layering ISO/OSI:
Session : for opening, closing and managing a session between end-user application processes , Communication sessions consist of requests and responses that occur between applications, synchronization, checkpointing. (e.g., Microsoft Word importing a chart from Excel)
ISO-SP, OSI session-layer protocol (X.225, ISO 8327)

## Slide 29: Encapsulation:
When referring to networking, encapsulation is the process of taking data from one protocol and translating it into another protocol, so the data can continue across a network.

## Slide 30: Networks under attack: security
Worm | Virus | Trojan horse
malware computer program that replicates itself in order to spread to other computers, always cause at least some harm to the network, even if only by consuming bandwidth. infection by passively receiving object that gets itself executed | malicious software program It’s often perform some type of harmful activity on infected hosts, such as stealing hard disk space or CPU time, accessing private information, corrupting data, displaying political or humorous messages on the user's screen | A Trojan horse is a program that either pretends to have, or is described as having, a set of useful or desirable features, but actually contains a damaging payload Hidden part of some otherwise useful software

## Slide 31: Networks under attack: security
A distributed denial-of-service (DDoS) : attack is one in which a multitude of compromised systems attack a single target, thereby causing denial of service for users of the targeted system. The flood of incoming messages to the target system essentially forces it to shut down, thereby denying service to the system to legitimate users.
select target
break into hosts around the network .(botent)
send packets toward target from compromised hosts

## Slide 32: Networks under attack: security
  Packet Sniffing : is the process of capturing any data passed over the local network and looking for any information that may be useful. broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by.

## Slide 33: Networks under attack: security
IP Spoofing :used to gain unauthorized access to computers, whereby the intruder sends messages to a computer with an IP address indicating that the message is coming from a trusted host.
send packet with false source address.