## Slide 1: Polymer Formation
<number>
There are two types of polymerization
  Addition (or chain) polymerization
  Condensation (step) polymerization
Notes: <number>

## Slide 2: Addition (Chain) Polymerization
<number>
  Initiation
  Propagation
  Termination
Notes: <number>
<number>

## Slide 3: Condensation (Step) Polymerization
<number>
Notes: <number>
<number>

## Slide 4: Polymer Additives
<number>
Improve mechanical properties, processability, durability, etc.
Fillers
  Added to improve tensile strength & abrasion resistance, toughness & decrease cost
  ex: carbon black, silica gel, wood flour, glass, limestone, talc, etc.
Plasticizers
  Added to reduce the glass transition
  temperature Tg below room temperature
  Presence of plasticizer transforms brittle polymer to a ductile one
  Commonly added to PVC - otherwise it is brittle
Notes: <number>
<number>
  Polymers are almost never used as a pure material
  Migration of plasticizers can be a problem

## Slide 5: Polymer Additives (cont.)
<number>
Stabilizers
  Antioxidants
  UV protectants
Lubricants
  Added to allow easier processing
  polymer “slides” through dies easier
  ex: sodium stearate
Colorants
  Dyes and pigments
Flame Retardants
  Substances containing chlorine, fluorine, and boron
Notes: <number>
<number>

## Slide 6: Processing of Plastics
<number>
Thermoplastic
  can be reversibly cooled & reheated, i.e. recycled
  heat until soft, shape as desired, then cool
  ex: polyethylene, polypropylene, polystyrene.
Thermoset
  when heated forms a molecular network (chemical reaction)
  degrades (doesn’t melt) when heated
  a prepolymer molded into desired shape, then chemical reaction occurs
  ex: urethane, epoxy
Notes: <number>
<number>
Can be brittle or flexible & linear, branching, etc.

## Slide 7: Processing Plastics – Compression Molding
<number>
Thermoplastics and thermosets
polymer and additives placed in mold cavity
mold heated and pressure applied
fluid polymer assumes shape of mold
Fig. 17.36, Callister & Rethwisch 9e. (From F. W. Billmeyer, Jr., Textbook of Polymer Science, 3rd edition. Copyright © 1984 by John Wiley & Sons, New York. Reprinted by permission of John Wiley & Sons, Inc.)
Notes: <number>
<number>
Male & female parts to mold

## Slide 8: Processing Plastics – Injection Molding
<number>
Fig. 17.37, Callister & Rethwisch 9e. (From F. W. Billmeyer, Jr., Textbook of Polymer Science, 3rd edition. Copyright © 1984 by John Wiley & Sons, New York. Reprinted by permission of John Wiley & Sons, Inc.)
Thermoplastics and some thermosets
when ram retracts, plastic pellets drop from hopper into barrel
ram forces plastic into the heating chamber (around the spreader) where the plastic melts as it moves forward
molten plastic is forced under pressure (injected) into the mold cavity where it assumes the shape of the mold
Barrel
Notes: <number>
<number>

## Slide 9: Processing Plastics – Extrusion
<number>
Fig. 17.38, Callister & Rethwisch 9e. (Reprinted with permission from Encyclopædia Britannica, © 1997 by Encyclopædia Britannica, Inc.)
thermoplastics
plastic pellets drop from hopper onto the turning screw
plastic pellets melt as the turning screw pushes them forward by the heaters
molten polymer is forced under pressure through the shaping die to form the final product (extrudate)
Notes: <number>
<number>
  An extruder is a device that used a large screw to melt a polymer, compress it, & force it into a mold
  Extremely commonly used

## Slide 10
<number>
Blow Molding
First, a parison, or
length of polymer tubing, is extruded. While still in a semimolten state, the parison is placed in a two-piece mold having the desired container configuration. The hollow piece is formed by blowing air or steam under pressure into the parison, forcing the tube walls to conform to the contours of the mold. Of course the temperature and viscosity of the parison must be carefully regulated.

## Slide 11: Processing Plastics – Blown-Film Extrusion
<number>
Fig. 17.39, Callister & Rethwisch 9e. (Reprinted with permission from Encyclopædia Britannica, © 1997 by Encyclopædia Britannica, Inc.)
Notes: <number>
<number>

## Slide 12: Summary
<number>
• Metal fabrication techniques:
-- forming, casting, miscellaneous.
• Hardenability of metals
-- measure of ability of a steel to be heat treated.
-- increases with alloy content.
• Precipitation hardening
--hardening, strengthening due to formation of
precipitate particles.
--Al, Mg alloys precipitation hardenable.
Notes: <number>

## Slide 13: Summary (Cont.)
<number>
• Ceramic Fabrication techniques:
-- glass forming (pressing, blowing, fiber drawing).
-- particulate forming (hydroplastic forming, slip casting, powder pressing, tape casting)
-- cementation
• Heat treating procedures for ceramics
-- glasses—annealing, tempering
-- particulate formed pieces—drying, firing (sintering)
• Polymer Processing -- compression and injection molding, extrusion, blown film extrusion
• Polymer melting and glass transition temperatures
Notes: <number>

## Slide 14: ANNOUNCEMENTS
<number>
Core Problems:
Self-help Problems:
Reading:
Notes: <number>