## Slide 1: Dynamic Routing Protocols

## Slide 2: CH2 Outline
RIP
OSPF

## Slide 3: CH2 p1 Outline
Routing and Routing Protocols
Purpose of dynamic routing protocols
Main components of dynamic routing protocols
Dynamic Routing Protocol Operation
Advantages and disadvantage of dynamic routing
Convergence time.
Classification of dynamic routing protocols

## Slide 4: Introduction
<number>
Recall: There are two parts to routing IP packets:
1. How to pass a packet from an input interface to the output interface of a router (Forwarding) ?
2. How to find routes to remote networks (Routing)?
We already discussed the packet forwarding part in 306NET, here we will learn more about the routing process

## Slide 5: Routing
Process of finding a path from a source to every destination in the network.
A router can learn about remote networks in one of two ways:
  Manually - Remote networks are manually entered into the route table using static routes.
  Dynamically - Remote routes are automatically learned using a dynamic routing protocol.

## Slide 6: Purpose of Dynamic Routing Protocols
Routing Protocols
  Used to facilitate the exchange of routing information between routers to find paths to other networks.
Purpose of dynamic routing protocols includes:
  Discovery of remote networks
  Choosing the best path to destination networks
  Maintaining up-to-date routing information
  Ability to find a new best path if the current path is no longer available
Notes: <number>
<number>
7.1.1.2

## Slide 7: Components of Dynamic Routing Protocols
  Main components of dynamic routing protocols include:
  Data structures –
  Routing protocols typically use tables or databases for its operations.
Notes: <number>
<number>
7.1.1.2

## Slide 8: Components of Dynamic Routing Protocols
Routing protocol messages –
Routing protocols use various types of messages to discover neighboring routers, exchange routing information, and other tasks to learn and maintain accurate information about the network.
Algorithm –
Routing protocols use algorithms for facilitating routing information and for best path determination.

## Slide 9
Notes: <number>
<number>
7.1.1.2

## Slide 10: Dynamic Routing Protocol Operation
In general, the operations of a dynamic routing protocol can be described as follows:
The router sends and receives routing messages on its interfaces.
Routers exchange routing messages and routing information to learn about remote networks.
The router shares routing information with other routers that are using the same routing protocol.
When a router detects a topology change the routing protocol can advertise this change to other routers.
Notes: <number>
<number>
7.1.3.1

## Slide 11: Dynamic Routing Protocol Pros and Cons
Advantages of dynamic routing
  Compared to static routing, dynamic routing protocols require less administrative overhead
  Automatically share information about remote networks
  Determine the best path to each network and add this information to their routing tables
Disadvantage of dynamic routing
  Dedicate part of a routers resources for protocol operation, including CPU time and network link bandwidth
Notes: <number>
<number>
  Help the network administrator manage the time-consuming process of configuring and maintaining static routes

## Slide 12: Achieving Convergence
Convergence time: The time that routers take to share information, calculate best paths, and update their routing tables .
Network converged when all routers have complete and accurate information about the entire network. A network is not completely operable until the network has converged.
Notes: <number>
<number>
7.1.3.5

## Slide 13: Achieving Convergence
Convergence properties include:
  The speed of propagation of routing information and the calculation of optimal paths.
  The speed of propagation refers to the amount of time it takes for routers within the network to forward routing information.
Generally, older protocols, such as RIP, are slow to converge, whereas modern protocols, such as EIGRP and OSPF, converge more quickly.

## Slide 14: Types of Routing Protocols Classifying Routing Protocols
Notes: <number>
<number>
7.1.4.1

## Slide 15: IGP and EGP Routing Protocols
Wide area network is divided into autonomous systems (AS).
An AS is a set of routers and networks managed by a single administration.
Notes: <number>
<number>
7.1.4.2

## Slide 16: IGP and EGP Routing Protocols
Interior Gateway Protocols (IGP) -
Used for routing within an AS
Examples: RIP, EIGRP, OSPF, and IS-IS
Each AS can choose an IGP to handle routing inside the AS
Exterior Gateway Protocols (EGP) -
Used for routing between ASs
Usually one EGP is chosen to handle routing between ASs.
Notes: <number>
<number>
Interior Gateway Protocols (IGP): Used for routing within an AS. It is also referred to as intra-AS routing. Companies, organizations, and even service providers use an IGP on their internal networks. IGPs include RIP, EIGRP, OSPF, and IS-IS.
Exterior Gateway Protocols (EGP): Used for routing between autonomous systems. It is also referred to as inter-AS routing. Service providers and large companies may interconnect using an EGP. The Border Gateway Protocol (BGP) is the only currently viable EGP and is the official routing protocol used by the Internet.