## Slide 1: Dynamic Routing Protocols part2

## Slide 2: CH2 Outline
Dynamic Routing Protocols
Distance Vector Dynamic Routing
Link-State Dynamic Routing
RIP
OSPF

## Slide 3: CH2 p3 Outline
Link State Routing Protocols
Link-State Routing Process
Advantages and disadvantages of link state routing protocols
OSPF Routing Protocol
  Components of OSPF
  OSPF Terminologies
  OSPF Operation
  OSPF Operational State
  Dijkstra’s Algorithm

## Slide 4: Types of Routing Protocols
Notes: 4
7.1.4.1

## Slide 5: Link-State Routing Protocols
In contrast to distance vector routing protocol operation, a router configured with a link-state routing protocol can create a complete view or topology of the network by gathering information from all of the other routers.
A link-state router uses the link-state information to create a topology map and to select the best path to all destination networks in the topology
Notes: A link-state routing protocol is like having a complete map of the network topology. The sign posts along the way from source to destination are not necessary, because all link-state routers are using an identical map of the network. A link-state router uses the link-state information to create a topology map and to select the best path to all destination networks in the topology.

## Slide 6: Link-State Routing Process
Notes: 6
7.4.2.1

## Slide 7: Link and Link-State
The first step in the link-state routing process is that each router learns about its own links, its own directly connected networks.
Notes: 7
7.4.2.2

## Slide 8: Say Hello
The second step in the link-state routing process is that each router is responsible for meeting its neighbors on directly connected networks.
Notes: 8
7.4.2.3

## Slide 9: Link State Updates
The third step in the link-state routing process is that each router builds a link-state packet (LSP) containing the state of each directly connected link.
Notes: 9
7.4.2.4

## Slide 10: Flooding the LSP and Building the Link-State Database
The fourth step in the link-state routing process is that each router floods the LSP to all neighbors, who then store all LSPs received in a database.
Notes: 10
7.4.2.5

## Slide 11: Computing the Best Path
The final step in the link-state routing process is that each router uses the database to construct a complete map of the topology and computes the best path to each destination network.
Notes: 11
7.4.2.6

## Slide 12: Adding Routes to the Routing Table
The best paths are inserted into the routing table
Notes: 12
7.4.2.7

## Slide 13: Why Use Link-State Protocols?
Disadvantages compared to distance vector routing protocols:
Memory Requirements
Processing Requirements
Bandwidth Requirements
Notes: 13
7.4.3.1

## Slide 14: Protocols that Use Link-State
Only two link-state routing protocols:
Open Shortest Path First (OSPF)
  most popular
  two current versions
    OSPFv2 - OSPF for IPv4 networks
    OSPFv3 - OSPF for IPv6 networks
IS-IS
  was designed by ISO
  popular in provider networks
Notes: 14
7.4.3.3

## Slide 15: OSPF Routing Protocol
Components of OSPF
OSPF Terminologies
OSPF Operation
OSPF Operational State
Dijkstra’s Algorithm

## Slide 16: OSPF
OSPF is an IGP routing protocol.
It is a Link State routing Protocol based on SPF technology.
OSPF has fast convergence
OSPF supports VLSM and CIDR
Cisco’s OSPF metric is based on bandwidth
OSPF only sends out changes when they occur.
    periodic updates (link-state refresh) every 30 minutes.
  OSPF also uses the concept of areas to implement hierarchical routing
Notes: OSPF is link-state routing protocol
  RIP is distance-vector routing protocol, susceptible to routing loops, split-horizon, and other issues.
OSPF has fast convergence
OSPF supports VLSM and CIDR
  RIPv1 does not
Cisco’s OSPF metric is based on bandwidth
  RIP is based on hop count
OSPF only sends out changes when they occur.
  RIP sends entire routing table every 30 seconds.
  periodic updates (link-state refresh) every 30 minutes.
  OSPF also uses the concept of areas to implement hierarchical routing

## Slide 17: Link State Routing
In link state routing, each router shares its knowledge about its neighborhood with every router in the area.
The three features:
  Sharing knowledge about the neighborhood.
  Sharing with every other router.
  Sharing when there is a change.

## Slide 18: OSPF Routing Protocol
Components of OSPF
OSPF Terminologies
OSPF Operation
OSPF Operational State
Dijkstra’s Algorithm

## Slide 19: From CH2 p1
What are the components of OSPF?

## Slide 20: Components of OSPF
Notes: 20
8.1.1.3

## Slide 21: Components of OSPF
OSPF Routers Exchange Packets
These packets are used to discover neighboring routers and also to exchange routing information to maintain accurate information about the network.
Notes: 21
8.1.1.3

## Slide 22: Components of OSPF
OSPF Routers run Dijkstra’s Algorithm to compute the best path to each destination network.
Notes: 22
7.4.1.2

## Slide 23: OSPF Routing Protocol
Components of OSPF
OSPF Terminologies
OSPF Operation
OSPF Operational State
Dijkstra’s Algorithm
Link, Link State and LSDB.
Area.
OSPF Route Types
OSPF Routers Classifications.
OSPF Packets

## Slide 24: Link and Link State
Link: Interface on a router
Link state: Description of an interface and of its relationship to its neighboring routers, including:
  IP address/mask of the interface,
  The type of network it is connected to
  The routers connected to that network
  The metric (cost) of that link
The collection of all the link-states would form a link-state database (LSDB).

## Slide 25: Networks Supported by OSPF
OSPF supports the following types of physical networks

## Slide 26: Area
OSPF allows the grouping of routers into a set, called an area.
An area is a collection of networks, hosts, and routers all contained within an AS.
An AS can be divided into many different areas.
All networks inside area must be connected.

## Slide 27: Area
Routers inside an area flood the area with routing information.
This technique minimizes the routing traffic required for the protocol.

## Slide 28: Area
  The topology of an area is hidden from the rest of the AS
    Inside an area, each router has an identical LSDB.
    Each area has its own copy of the topological database.
At the border of an area, special routers called area border routers summarize the information about the area and send it to other areas.

## Slide 29: Area
Among the areas inside an AS is a special area called the backbone.
All the areas inside an AS must be connected to the backbone.
The routers inside the backbone are called the backbone routers.
  Note that a backbone router can also be an area border router.
Notes: In other words, the backbone serves as a primary area and the other areas as secondary areas.

## Slide 30: Area
Each area has an area identification.
The area identification of the backbone is zero.

## Slide 31: Area
With multiarea, routing within the AS takes place on two levels, depending on whether the route to the destination lies entirely within an area (intra-area routing) or in another area (inter-area routing).
When a packet must be routed between two areas, the backbone is used.
Notes: The packet is first routed to the Area Border Router. The packet is then routed through the backbone to another area border router acting for the destination area. The packet is finally routed through the destination area to the specific destination

## Slide 32: OSPF Route Types

## Slide 33: OSPF Routers Classifications
OSPF routers can be classified into four overlapping types:
  Internal routers,
  Area Border routers,
  Backbone routers, and
  Autonomous system boundary routers
Area 0
Area 2
Area 3
IR
ABR/BR
To another AS
ASBR

## Slide 34: OSPF Routers Classifications

## Slide 35: Types of OSPF Packets
OSPF routers exchange packets.
Notes: These packets are used to discover neighboring routers and also to exchange routing information to maintain accurate information about the network.

## Slide 36: OSPF Routing Protocol
Components of OSPF
OSPF Terminologies
OSPF Operation
OSPF Operational State
Dijkstra’s Algorithm

## Slide 37: OSPF Operation
To maintain routing information, OSPF routers complete the following generic link-state routing process to reach a state of convergence
Exchanging Hello packets
Exchanging LSAs
Creating SPF Tree
Updating routing table
1
2
3 and 4
5

## Slide 38: 1. Establish Neighbor Adjacencies
An OSPF-enabled router sends Hello packets out all OSPF-enabled interfaces to determine if neighbors are present on those links.
If a neighbor is present, the OSPF-enabled router attempts to establish a neighbor adjacency with that neighbor.
Notes: 38
OSPF-enabled routers must recognize each other on the network before they can share information.

## Slide 39: Establish Neighbor Adjacencies
OSPF creates adjacencies between neighboring routers.
The reason for forming adjacencies is to exchange topological information.
Not every router needs to become adjacent to every other router.
Adjacencies are established and maintained with hello packets.
These packets are sent periodically.

## Slide 40: 2- Exchanging Link State Advertisements
LSAs contain the state and cost of each directly connected link.
Routers flood their LSAs to adjacent neighbors.
Adjacent neighbors receiving the LSA immediately flood the LSA to other directly connected neighbors, until all routers in the area have all LSAs.
Notes: 40
8.1.1.4 After adjacencies are established, routers then exchange link-state advertisements (LSAs).

## Slide 41: 3. Build the Topology Table
After LSAs are received, OSPF-enabled routers build the topology table (LSDB) based on the received LSAs.
This database eventually holds all the information about the topology of the network.

## Slide 42: 4. Execute the SPF Algorithm
Routers then execute the SPF algorithm that creates the SPF tree.

## Slide 43: 5- Updating routing table
From the SPF tree, the best paths are inserted into the routing table.
Notes: Routing decisions are made based on the entries in the routing table.