## Slide 1: Dynamic Routing Protocols part3 B

## Slide 2: CH2 Outline
Dynamic Routing Protocols
Distance Vector Dynamic Routing
Link-State Dynamic Routing
RIP
OSPF

## Slide 3: OSPF Routing Protocol
Components of OSPF
OSPF Terminologies
OSPF Operation
OSPF Operational State
Route calculation and Dijkstra’s Algorithm

## Slide 4: OSPF Operational States
When an OSPF router is initially
connected to a network, it attempts to:
  Create adjacencies with neighbors
  Exchange routing information
  Calculate the best routes
  Reach convergence
OSPF router progresses through several states while attempting to reach convergence.
Notes: 4
8.1.3.1

## Slide 5: Establish Neighbor Adjacencies
OSPF-enabled routers must form adjacencies with their neighbor before they can share information with that neighbor.
When OSPF is enabled on an interface, the router must determine if there is another OSPF neighbor on the link.
To accomplish this, the router forwards a Hello packet that contains its router ID out all OSPF-enabled interfaces to determine whether neighbors are present on those links.
If a neighbor is present, the OSPF-enabled router attempts to establish a neighbor adjacency with that neighbor.
Notes: The OSPF router ID is used by the OSPF process to uniquely identify each router in the OSPF area.
A router ID is an IP address assigned to identify a specific router among OSPF peers.

## Slide 6: Establishing Neighbor Adjacencies
An OSPF adjacency is established in several steps and OSPF router goes through the following states:

## Slide 7: Down State
This is the first OSPF neighbor adjacency state.
It means that no information (Hellos) has been received, but Hello packets can still be sent to the neighbor in this state.

## Slide 8: Down to Init State
In the first step, routers that intend to establish an OSPF neighbor adjacency exchange a Hello packets.
* A Cisco router includes the Router IDs of all neighbors in the init (or higher) state in its Hello packets.
Notes: When OSPF is enabled, the enabled Gigabit Ethernet 0/0 interface transitions from the Down state to the Init state.
Refer to R1 in Figure 1. When OSPF is enabled, the enabled Gigabit Ethernet 0/0 interface transitions from the Down state to the Init state. R1 starts sending Hello packets out all OSPF-enabled interfaces to discover OSPF neighbors to develop adjacencies with.

## Slide 9: Init State
When a router receives a Hello packet with a router ID that is not within its neighbor list, the receiving router attempts to establish an adjacency with the initiating router.
1- adds the R1 router ID to its neighbor list
2- sends a Hello packet to R1
Notes: In Figure 2, R2 receives the Hello packet from R1 and adds the R1 router ID to its neighbor list. R2 then sends a Hello packet to R1. The packet contains the R2 Router ID and the R1 Router ID in its list of neighbors on the same interface.

## Slide 10
A router transit to Init State when
It is in Down state and it starts sending Hello packet
It receives a Hello packet with a router ID that is not within its neighbor list

## Slide 11: Init State
Init state specifies that the router has received a Hello packet from its neighbor, but the receiving router's ID was not included in the hello packet.
Notes: When a router receives a Hello from the neighbor but has not yet seen its own router ID in the neighbor Hello packet, it will transit to the Init state.
In this state, the router will record all neighbor router IDs and start including them in Hellos sent to the neighbors.

## Slide 12: 2-Way State
When the router sees its own router ID in the Hello packet received from the neighbor, it will transit to the 2-Way state.
This means that bidirectional communication with the neighbor has been established.
1- adds the R2 Router ID in its list of OSPF neighbors.
2- its own Router ID in the Hello packet
Notes: In Figure 3, R1 receives the Hello and adds the R2 Router ID in its list of OSPF neighbors. It also notices its own Router ID in the Hello packet’s list of neighbors. When a router receives a Hello packet with its Router ID listed in the list of neighbors, the router transitions from the Init state to the Two-Way state
This state designates that bi-directional communication has been established between two routers. Bi-directional means that each router has seen the other's hello packet. This state is attained when the router receiving the hello packet sees its own Router ID within the received hello packet's neighbor field.

## Slide 13
When a router receives a Hello packet with
its Router ID listed in the list of neighbors, it will transit from the Init state to the Two-Way state
its Router ID not listed in the list of neighbors, it will transit to the Init state
*The transtion to 2-Way state happens if the router is in the Init state

## Slide 14: 2-Way State
The action performed in Two-Way state depends on the type of inter-connection between the adjacent routers:
  If the link is a point-to-point link, then they immediately transition from the Two-Way state to the database synchronization phase.
  If the routers are interconnected over a multiaccess network, then a designated router(DR) and a backup designated router (BDR) must be elected.
Notes: broadcast media and non-broadcast multiaccess networks

## Slide 15: Why a DR and a BDR
Multiaccess networks can create two challenges :
  Creation of multiple adjacencies
  Extensive flooding of LSAs

## Slide 16: Why a DR and a BDR
The solution to managing the number of adjacencies and the flooding of LSAs on a multiaccess network is the DR.
On multiaccess networks, OSPF elects a DR to be the collection and distribution point for LSAs sent and received.
A BDR is also elected in case the DR fails.
All other routers become DROTHERs. A DROTHER is a router that is neither the DR nor the BDR.
Notes: On broadcast links, OSPF neighbors first determine the designated router (DR) and backup designated router (BDR) roles, which optimize the exchange of information in broadcast segments.

## Slide 17: DR and BDR
The DR and BDR act as a central point of contact for link-state information exchange on a multiaccess network.
Each router must establish a full adjacency with the DR and the BDR only.
Each router, rather than exchanging LSA with every other router on the segment, sends the LSA to the DR and BDR only.

## Slide 18: DR and BDR
DR router performs the following tasks:
Network Links Advertisement
  The DR originates the network LSA for the network.
Managing LSDB synchronization:
  The DR and BDR ensure that the other routers on the network have the same link-state information about the common segment.

## Slide 19: DR and BDR
When the DR is operating, the BDR does not perform any DR functions.
Instead, the BDR receives all the information, but the DR performs the LSA forwarding and LSDB synchronization tasks.
The BDR performs the DR tasks only if the DR fails.
When the DR fails, the BDR automatically becomes the new DR, and a new BDR election occurs.

## Slide 20: Synchronizing OSPF Databases
After the Two-Way state, routers transition to database synchronization states.

## Slide 21: Synchronizing OSPF Databases
While the Hello packet was used to establish neighbor adjacencies, the other four types of OSPF packets are used during the process of exchanging and synchronizing LSDBs.

## Slide 22: ExStart state
In the ExStart state, a master and slave relationship is created between each router and its adjacent DR and BDR.
The router with the higher router ID acts as the master for the Exchange state.

## Slide 23: Exchange state
In the Exchange state, the master and slave routers exchange one or more DBD packets.
DBD packets is an abbreviated list of the sending router’s LSDB and is used by receiving routers to check against the local LSDB.
The LSDB must be identical on all OSPF routers within an area to construct an accurate SPF tree.

## Slide 25: Exchange state
A DBD packet includes information about the LSA entry header that appears in the router’s LSDB.
The entries can be about a link or about a network.
Each LSA entry header includes information about the link-state type, the address of the advertising router, the link’s cost, and the sequence number.
The router uses the sequence number to determine the newness of the received link-state information.

## Slide 26: Loading State
When a router receives a DBD packet, it compares the information received with the information it has in its own LSDB.
If the DBD packet has a more current LSA or has an LSA that is not in its LSDB, the router transitions to the Loading state.

## Slide 27
Notes: the router adds an entry to its Link State Request list

## Slide 28: Loading State
In this state, the actual exchange of link state information occurs.
Based on the information provided by the DBDs, routers send link-state request (LSR) packets.
The neighbor then provides the requested link-state information in link-state update (LSU) packets.
During the adjacency, if a router receives an outdated or missing LSA, it requests that LSA by sending a LSR packet.
All link-state update packets are acknowledged.

## Slide 29: Full State
After all LSRs have been satisfied for a given router, the adjacent routers are considered synchronized (have identical LSDBs ) and in a full state.

## Slide 30
I am router id 172.16.5.2, and I see 172.16.5.1
I am router id 172.16.5.1, and I see no one
B
A
172.16.5.1/24
172.16.5.2/24
hello
To 224.0.0.5
Down state
Initial State
Port1
Port2
Router B neighbor List 172.16.5.1/24,in Port2
hello
Router A neighbor List 172.16.5.2/24,in Port1
Two-way State
Unicast to A
Establishing Bidirectional Communication

## Slide 31
Here is a summary of my LSDB
No, I’ll start exchange because I have a higher RID
I will start exchange because I have router id 172.16.5.1
B
A
172.16.5.1/24
172.16.5.2/24
DBD
Exstart state
exchange State
Port1
Port2
DBD
Discovering the Network Routes
Here is a summary of my LSDB
DBD
DBD

## Slide 32
Thanks for the information!
B
A
172.16.5.1/24
172.16.5.2/24
LSAck
Loading state
Full State
Port1
Port2
Adding the Link-State Entries
LSAck
I need complete entry for network 172.16.6.0/24
LSR
Here is the entry for network 172.16.6.0/24
LSU
LSAck
Thanks for the information!

## Slide 35: OSPF Routing Protocol
Components of OSPF
OSPF Terminologies
OSPF Operation
OSPF Operational State
Route calculation and Dijkstra’s Algorithm

## Slide 36: From CH2 p3 A Slides
Next slides
Previous slides

## Slide 37: Route Calculation
The router now has a complete LSDB.
Now the router is ready to create a routing table, but first needs to run the Shortest Path First (SPF) Algorithm, also called the Dijkstra algorithm, on the LSDB which will create the SPF tree.
In the SPF, the router calculations places itself as the root and creating a “tree diagram” of the network

## Slide 38: Simplified Example
In order to keep it simple, we will take some liberties with the actual process and algorithm, but you will get the basic idea!
Assume there are 5 Routers that have already established adjacency relationship:
  RouterA, RouterB, RouterC, RouterD, RouterE

## Slide 39: Exchanging LSAs and Building LSDB
RouterA LSA , which will be flooded to all other routers:
  RouterB on your network 11.0.0.0/8 with a cost of 15,
  RouterC on your network 12.0.0.0/8 with a cost of 2
  RouterD on your network 13.0.0.0/8 with a cost of 5
  Have a “leaf” network 10.0.0.0/8 with a cost of 2
All other routers will also flood their link state information. (OSPF: only within the area)
“Leaf” 10.0.0.0/8
11.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2

## Slide 40: Exchanging LSAs and Building LSDB
RouterB:
Connected to RouterA on network 11.0.0.0/8, cost of 15
Connected to RouterE on network 15.0.0.0/8, cost of 2
Has a “leaf” network 14.0.0.0/8, cost of 15
RouterC:
Connected to RouterA on network 12.0.0.0/8, cost of 2
Connected to RouterD on network 16.0.0.0/8, cost of 2
Has a “leaf” network 17.0.0.0/8, cost of 2
RouterD:
Connected to RouterA on network 13.0.0.0/8, cost of 5
Connected to RouterC on network 16.0.0.0/8, cost of 2
Connected to RouterE on network 18.0.0.0/8, cost of 2
Has a “leaf” network 19.0.0.0/8, cost of 2
RouterE:
Connected to RouterB on network 15.0.0.0/8, cost of 2
Connected to RouterD on network 18.0.0.0/8, cost of 10
Has a “leaf” network 20.0.0.0/8, cost of 2
All other routers flood their own LSA to all other routers.
RouterA gets all of this information and stores it in its LSDB.
Using the LSA from each router, RouterA runs Dijkstra algorithm to create a SPT.
RouterA’s LSDB

## Slide 41: Link State information from RouterB
from RouterB LSA :
Connected to RouterA on network 11.0.0.0/8, cost of 15
Connected to RouterE on network 15.0.0.0/8, cost of 2
Have a “leaf” network 14.0.0.0/8, cost of 15
Now, RouterA attaches the two graphs…
+
=
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
10.0.0.0/8
11.0.0.0/8
12.0.0.0/8
13.0.0.0/8
14.0.0.0/8
15.0.0.0/8
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
10.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
2
2
2
Notes: A

## Slide 42: Link State information from RouterC
from RouterC LSA :
Connected to RouterA on network 12.0.0.0/8, cost of 2
Connected to RouterD on network 16.0.0.0/8, cost of 2
Have a “leaf” network 17.0.0.0/8, cost of 2
12.0.0.0/8
16.0.0.0/8
17.0.0.0/8
2
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
10.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
+
16.0.0.0/8
17.0.0.0/8
2
=
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
10.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
17.0.0.0/8
16.0.0.0/8
Now, RouterA attaches the two graphs…
Notes: A

## Slide 43: Link State information from RouterD
From RouterD LSA :
Connected to RouterA on network 13.0.0.0/8, cost of 5
Connected to RouterC on network 16.0.0.0/8, cost of 2
Connected to RouterE on network 18.0.0.0/8, cost of 2
Have a “leaf” network 19.0.0.0/8, cost of 2
13.0.0.0/8
16.0.0.0/8
18.0.0.0/8
19.0.0.0/8
18.0.0.0/8
19.0.0.0/8
2
2
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
17.0.0.0/8
16.0.0.0/8
+
=
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
17.0.0.0/8
16.0.0.0/8
18.0.0.0/8
19.0.0.0/8
2
Now, RouterA attaches the two graphs…
10.0.0.0/8
10.0.0.0/8
Notes: A

## Slide 44: Link State information from RouterE
From RouterE LSA :
Connected to RouterB on network 15.0.0.0/8, cost of 2
Connected to RouterD on network 18.0.0.0/8, cost of 10
Have a “leaf” network 20.0.0.0/8, cost of 2
15.0.0.0/8
18.0.0.0/8
2
11.0.0.0/8
14.0.0.0/8
15.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
17.0.0.0/8
16.0.0.0/8
18.0.0.0/8
19.0.0.0/8
2
10.0.0.0/8
+
20.0.0.0/8
2
20.0.0.0/8
11.0.0.0/8
14.0.0.0/8
12.0.0.0/8
13.0.0.0/8
2
2
17.0.0.0/8
16.0.0.0/8
19.0.0.0/8
2
10.0.0.0/8
15.0.0.0/8
18.0.0.0/8
20.0.0.0/8
2
Now, RouterA attaches the two graphs…
Notes: A

## Slide 45: Topology
Using the LSDB content, RouterA has now built a complete topology of the network.
The next step for OSPF is to find the best path to each node and leaf network.
2
2
2
2
2
11.0.0.0/8
14.0.0.0/8
12.0.0.0/8
13.0.0.0/8
17.0.0.0/8
16.0.0.0/8
15.0.0.0/8
18.0.0.0/8
20.0.0.0/8
19.0.0.0/8
10.0.0.0/8
Notes: A

## Slide 46: Choosing the Best Path
Using the Dijkstra’s algorithm RouterA can now proceed to find the shortest path to each leaf network

## Slide 47: SPT Results Put into the Routing Table
RouterA’s Routing Table
10.0.0.0/8 connected e0
11.0.0.0/8 connected s0
12.0.0.0/8 connected s1
13.0.0.0/8 connected s2
14.0.0.0/8 17 s0
15.0.0.0/8 17 s1
16.0.0.0/8 4 s1
17.0.0.0/8 4 s1
18.0.0.0/8 14 s1
19.0.0.0/8 6 s1
20.0.0.0/8 16 s1
2
2
2
2
11.0.0.0/8
14.0.0.0/8
12.0.0.0/8
13.0.0.0/8
17.0.0.0/8
16.0.0.0/8
15.0.0.0/8
18.0.0.0/8
20.0.0.0/8
19.0.0.0/8
10.0.0.0/8
s0
s1
s2
e0

## Slide 48: If a link fail
When change occurs:
  Announce the change to all OSPF neighbours
  All routers run the SPF algorithm on the revised database
  Install any change in the routing table

## Slide 49: Dijkstra Algorithm
Dijkstra algorithm is a routing algorithm in which a router computes the shortest path between each pair of nodes in the network.

## Slide 50: Pesudocode

## Slide 52: Dijkstra Animated Example

## Slide 53: Dijkstra Animated Example

## Slide 54: Dijkstra Animated Example

## Slide 55: Dijkstra Animated Example
C
C
C

## Slide 56: Dijkstra Animated Example
C
C
C

## Slide 57: Dijkstra Animated Example
C
C
C
C
C

## Slide 58: Dijkstra Animated Example
C
C
C
C
C

## Slide 59: Dijkstra Animated Example
C
C
C
C
C
B

## Slide 60: Dijkstra Animated Example
C
C
C
C
C
B