## Slide 1: Frame Relay

## Slide 2: Outline
Why do we need Frame Relay?
Frame Relay Network
Frame Relay Network as a NBMA network
Virtual Circuits
DLCI
Mapping of DLCI
Frame Relay Frame
Frame Relay Topologies

## Slide 4: Why do we need Frame Relay?
Frame Relay is more complex a technology than point-to-point WAN links but also provides more features and benefits
Notes: Let’s take a simple example. Suppose you are working in a big company and your company has just expanded to two new locations. The main site is connected to two branch offices, named Branch 1 & Branch 2 and your boss wants these two branches can communicate with the main site. The most simple solution is to connect them directly (called a leased line) as shown below
To connect to these two branches, the main site router, HeadQuarter, requires two serial interfaces which a router can provide. But what happens when the company expands to 10 branches, 50 branches? For each point-to-point line, HeadQuarter needs a separate physical serial interface (and maybe a separate CSU/DSU if it is not integrated into the WAN card). As you can imagine, it will need many routers with many interfaces and lots of rack space for the routers and CSU/DSUs. Maybe we should use another solution for this problem? Luckily, Frame Relay can do it!
By using Frame Relay we only need one serial interface at the HeadQuarter to connect to all branches. This is also true when we expand to 10 or 50 branches. Moreover, the cost is much lesser than using leased-lines.

## Slide 5: Why do we need Frame Relay?
Leased lines provide permanent dedicated capacity and are used extensively for building WANs.
Disadvantages
  A fixed capacity (WAN traffic is often variable)
  Equipment costs
Notes: One disadvantage is that customers pay for leased lines with a fixed capacity. However, WAN traffic is often variable and leaves some of the capacity unused.
In addition, each endpoint needs a separate physical interface on the router, which increases equipment costs.
Any change to the leased line generally requires a site visit by the carrier personnel.

## Slide 6: Why do we need Frame Relay?
An alternative to dedicated, expensive, leased WAN lines is Frame Relay.
Frame Relay is a high-performance WAN protocol that operates at the physical and data link layers of the OSI reference model.
Frame Relay provides a cost-efficient solution for communications between multiple remote sites by using a single access circuit from each site to the provider.

## Slide 7
The capacity between any two sites can vary.
Notes: Network providers implement Frame Relay to support voice and data traffic between LANs over a WAN. Each end user gets a private line, or leased line, to a Frame Relay node. The Frame Relay network handles the transmission over a frequently changing path transparent to all end users. As shown in the figure, Frame Relay provides a solution to allow the communications between multiple sites using a single access circuit to the provider.

## Slide 8: Frame Relay Network
access switches
access switches
access switches

## Slide 9: Frame Relay Network
A Frame Relay network is made up of a large number of Frame Relay switches dispersed all over the coverage area of a Frame Relay service provider (e.g. region or country)
The switches are interconnected in a complex mesh topology.

## Slide 10: Frame Relay Network
Frame Relay switches:
  Terminate user circuits, in addition to connecting to other switches, and are called access switches.
  Other Frame Relay switches do not terminate user circuits, connecting to other Frame Relay switches only, and make the backbone of the Frame Relay network.

## Slide 11: Frame Relay Network as a NBMA network
Frame Relay networks are multiaccess networks, which means that more than two devices can connect to the network.
Unlike with LANs, Frame Relay cannot send a data as a broadcast.
Therefore, Frame Relay networks are called nonbroadcast multiaccess (NBMA) networks.

## Slide 12
On a broadcast network, multiple devices are attached to a shared network. When one device transmits frames, all nodes on the network "listen" to the frames, but only the node to which the frames are addressed actually receives the frames. Thus, the frames are broadcast.
On a nonbroadcast network multiple devices are attached, but data is transmitted directly from one computer to another over a virtual circuit or across a switching fabric. (e.g. ATM , frame relay, and X.25).

## Slide 13: Frame Relay Network
The Frame Relay network is not like the Internet where any two devices connected to the Internet can communicate.
In a Frame Relay network, before two routers can exchange information, a virtual circuit between them must be set up ahead of time by the Frame Relay service provider.

## Slide 14: DCE & DTE
In the context of Frame Relay:
  the DTE is the router or sometimes Frame Relay Access Devices (FRADs).
  The DCE is Frame Relay switch.
  The purpose of DCE equipment is to provide clocking and switching services in a network
Notes: + Data terminal equipment (DTE), which is actually the user device and the logical Frame-relay end-system
+ Data communication equipment (DCE, also called data circuit-terminating equipment), which consists of modem and packet switch
In general, the routers are considered DTE, and the Frame Relay switches are DCE.
A FRAD is a specialized device designed to provide a connection between a LAN and a Frame Relay WAN.

## Slide 15: Virtual Circuits
The connection through a Frame Relay network between two DTEs is a virtual circuit (VC) .
VC is a means of transporting data over a packet switched network in such a way that it appears as though there is a dedicated physical layer link between the 2 DTEs.
Notes: With VCs, Frame Relay shares the bandwidth among multiple users and any single site can communicate with any other single site without using multiple dedicated physical lines.

## Slide 16
CH1

## Slide 17
The circuits are virtual because there is no direct electrical connection from end to end.
Provides connection-oriented data link layer communication
A logical connection between two DTE across a Frame Relay packet-switched network
Provide a bi-directional communications path from one DTE device to another
A VC can pass through any number of intermediate devices (switches) located within the Frame Relay network
Notes: The connection is logical, and data moves from end to end, without a direct electrical circuit.

## Slide 18: VC Types
There are two types of VCs:
Frame Relay is a packet-switched, connection-oriented, WAN service.
Notes: Switched Virtual Circuits (SVC) - Established dynamically by sending signaling messages to the network (CALL SETUP, DATA TRANSFER, IDLE, CALL TERMINATION)
Note that some publications refer to PVCs as private VCs.
Note: PVCs are more commonly implemented than SVCs.

## Slide 19: VC Types
Switched virtual circuits (SVCs):
  Are temporary connections used in situations requiring only sporadic data transfer between DTE devices across the Frame Relay network.
  SVC is set up dynamically when needed.
  SVC connections require call setup and termination for each connection.
  SVCs are not very common

## Slide 20: VC Types
Permanent virtual circuits (PVCs):
PVCs are more common.
A predefined VC.
  Used for frequent and consistent data transfers between DTEs devices across the Frame Relay network.
A PVC can be equated to a leased line in concept.
The switching information for a VC is stored in the memory of the switch.

## Slide 21
A PVC between the same two DTEs will always be the same.
An SVC between the same two DTEs may change.
Path may change .
Always same Path.

## Slide 22: Multiple Virtual Circuits
The router or FRAD, connected to the Frame Relay network, may have multiple VCs connecting it to various endpoints.
Notes: Frame Relay is statistically multiplexed, meaning that it transmits only one frame at a time, but that many logical connections can co-exist on a single physical line.

## Slide 23: Multiple Virtual Circuits
Multiple VCs on a single physical line are distinguished by assigning each VC an identifier called data-link connection identifiers (DLCI) .
Notes: Keep in mind that the DLCI has only local significance and may be different at each end of a VC.

## Slide 24: DLCI
VCs are identified by DLCIs.
Frame Relay DLCIs have local significance, that means that their values are unique per router, but not necessarily in the other routers.
DLCI values typically are assigned by the Frame Relay service provider.
Notes: Frame Relay DLCIs have local significance, which means that the values themselves are not unique in the Frame Relay WAN.
A DLCI identifies a VC to the equipment at an endpoint. A DLCI has no significance beyond the single link.
Two devices connected by a VC may use a different DLCI value to refer to the same connection.

## Slide 25: Frame Relay Switch
Frame Relay creates a VC by storing input-port to output-port mapping in the memory of each switch and thus links one switch to another until a continuous path from one end of the circuit to the other is identified.

## Slide 26: DLCI

## Slide 27: Frame Relay Address Mapping

## Slide 28: Frame Relay Address Mapping
Before DLCI can be used to route traffic, it must be associated with the IP address of its remote router

## Slide 29: Frame Relay Address Mapping
The HeadQuarter will need to map Branch 1 IP address to DLCI 23 & map Branch 2 IP address to DLCI 51.
After that it can encapsulate data inside a Frame Relay frame with an appropriate DLCI number and send to the destination.

## Slide 30: Mapping of DLCI
The mapping of DLCIs to Layer 3 addresses can be handled manually or dynamically.
Manually (static): the administrators can statically assign a DLCI to the remote IP address.
Dynamic: the router can send an Inverse ARP Request to the other end of the PVC for its Layer 3 address.
Notes: We should use the “broadcast” keyword here because by default split-horizon will prevent routing updates from being sent back on the same interface it received. For example, if Branch 1 sends an update to HeadQuarter then HeadQuarter can’t send that update to Branch 2 because they are received and sent on the same interface. By using the “broadcast” keyword, we are telling the HeadQuarter to send a copy of any broadcast or multicast packet received on that interface to the virtual circuit specified by the DLCI value in the “frame-relay map” statement. In fact the copied packet will be sent via unicast (not broadcast) so sometimes it is called “pseudo-broadcast”.

## Slide 31: Inverse ARP
Once the router learns from the switch about available PVCs and their corresponding DLCIs, the router can send an Inverse ARP request to the other end of the PVC. (unless statically mapped )
1
2

## Slide 32: Inverse ARP
For each supported and configured protocol on the interface, the router sends an Inverse ARP request for each DLCI. (unless statically mapped)
In effect, the Inverse ARP request asks the remote station for its Layer 3 address.
At the same time, it provides the remote system with the Layer 3 address of the local system.
The return information from the Inverse ARP is then used to build the Frame Relay map.

## Slide 33
Now all the routers have a pair of DLCI & IP address of the router at the other end so data can be forwarded to the right destination.

## Slide 34: Frame Relay Frame
Frame Relay is a data link protocol and the customer router encapsulates each Layer 3 packet inside a Frame Relay frame comprising a header and trailer before it is sent out the access link.
The header and trailer used is actually defined by the Link Access Procedure Frame Bearer Services (LAPF) specification
Notes: The standard LAPF header is too simplistic and does not provide all the fields needed by Frame Relay routers. More specifically, there is no Protocol Type field in LAPF. Each data link layer needs such a field to define the type of Layer 3 packet carried by the data link frame. If Frame Relay uses only LAPF header, routers cannot support multiprotocol traffic because there is no way to identify the type of Layer 3 protocol.

## Slide 35: Frame Relay Frame
The simple LAPF header was extended to compensate for the absence of a Protocol Type field:
Notes: There are two Frame Relay encapsulation types: the Cisco encapsulation and the IETF Frame Relay encapsulation, which is in conformance with RFC 1490 and RFC 2427. The former is often used to connect two Cisco routers while the latter is used to connect a Cisco router to a non-Cisco router.

## Slide 36: Frame Relay Frame
Header
  DLCI ,
  fields related to congestion management
Data – Contains encapsulated upper-layer data
Trailer
  Frame Relay provides no error recovery mechanism. It only provides CRC error detection.
You should keep in mind that Frame Relay encapsulation should match on the routers at the two ends of a VC.
Notes: If you fail to match the Frame Relay encapsulation (both sides cisco or both ietf) on the two routers, the connection does not come up. However, if you have Cisco routers at both ends of the connection (a likely scenario), and you don’t explicitly configure Frame Relay encapsulation, both routers default to cisco and the connection does get established. Frame Relay switches do not care about the Frame Relay encapsulation. In Cisco IOS Software configuration, the Cisco proprietarty encapsulation is called cisco while the other one is called ietf.

## Slide 37: Frame Relay Topologies
  When more than two sites must be connected, the Frame Relay topology, or map, of the connections between the sites must be planned.
  Every network can be viewed as being one of three topology types:

## Slide 38: Star Topology (Hub and Spoke)
A star topology, also known as a hub and spoke configuration, is the most popular Frame Relay network topology because it is the most cost-effective.
Hub
Spoke
Notes: This is the least expensive topology because it requires the fewest PVCs.

## Slide 39
Each remote site has an access link to the Frame Relay cloud with a single VC.
The hub at has an access link with multiple VCs, one for each remote site.
Because Frame Relay costs are not distance-related, the hub does not need to be in the geographical center of the network.

## Slide 40: Full-Mesh Topology
A full-mesh topology suits a situation in which the services to be accessed are geographically dispersed and highly reliable access to them is required.
A full-mesh topology connects every site to every other site
Notes: Using leased-line interconnections, additional serial interfaces and lines add costs. In this example, ten dedicated lines are required to interconnect each site in a full-mesh topology. Using Frame Relay, a network designer can build multiple connections simply by configuring additional VCs on each existing link. This software upgrade grows the star topology to a full-mesh topology without the expense of additional hardware or dedicated lines. Because VCs use statistical multiplexing, multiple VCs on an access link generally make better use of Frame Relay than single

## Slide 41
used four VCs on each link
This method, although more costly than hub and spoke, provides direct connections from each site to all other sites and allows for redundancy.
In a full mesh topology, all routers have PVCs to all other destinations.

## Slide 42: Partial-Mesh Topology
For large networks, a full-mesh topology is seldom affordable because the number of links required increases dramatically.
The issue is not with the cost of the hardware, but because there is a theoretical limit of fewer than 1000 VCs per link.
In practice, the limit is less than that.
Full Mesh Topology
Number of Number of
Connections PVCs
----------------- --------------
2 1
4 6
6 15
8 28
10 45

## Slide 43: Partial-Mesh Topology
For this reason, larger networks generally are configured in a partial-mesh topology.
Partial mesh has more interconnections than are required for a star arrangement, but not as many as for a full mesh.
The actual pattern depends on the data flow requirements.

## Slide 44: Partial-Mesh Topology