## Slide 1: Frame Relay
part2

## Slide 2: Outline
LMI
Frame Relay bandwidth

## Slide 3: LMI
The Local Management Interface ( LMI ) is a set of enhancements to the basic Frame Relay specification.
It offers a number of features (called extensions) for managing complex internetworks.

## Slide 4: LMI Extensions
LMI provides a signaling or diagnostic between the DTE router and the Frame Relay switch, using several types of messages:
  Virtual circuit status messages
  Global addressing messages
  Multicasting messages

## Slide 5: LMI Extensions
VC status messages
Provide information about PVC integrity by communicating between devices, periodically reporting the existence of new PVCs and the deletion of already existing PVCs.
VC status messages prevent data from being sent into black holes (PVCs that no longer exist).
Notes:   keepalives sent between the DTE – DCE devices to inform about the status of the virtual circuit.
In addition to performing a keepalive function between the DTE and DCE, LMI status messages also signal if a PVC is active or inactive.

## Slide 6: LMI Extensions
VC status messages
The Status-enquiry messages
  from the router to the switch
  sent every 10 seconds
  allow the router to ask about the status of network.
The Status messages
  from the switch to the router
  responding to status-enquiry messages.
  signal if a PVC is active or inactive.
Notes: VC status messages
The Status messages
  In fact, the Frame Relay switch sends two types of messages:
  a status message every 10 seconds and
  a full status message instead of a status message every 60 seconds.
    contain all the information about known DLCIs and their state
Every PVC is predefined by the Frame Relay service provider, but its status can change due to network conditions like failure of trunk links in the provider network. An access link may be up and and running and keepalives may be present but one or more VCs may still be down. The reason is that a VC is an end-to-end logical connection that involves not only the access links at the two ends but also spans the core of the provider network. The router needs to know that which VCs are functional and which are not. The router learns this information as well from the Frame Relay switch through LMI status messages.
Every 10 seconds or so, the end device polls the network, either requesting a dumb sequenced response or channel status information. If the network does not respond with the requested information, the user device may consider the connection to be down. When the network responds with a FULL STATUS response, it includes status information about DLCIs that are allocated to that line. The end device can use this information to determine whether the logical connections are able to pass data

## Slide 7: LMI Extensions
VC status messages
These periodic LMI messages also serve as keepalives for both the router and the switch .
If the access link is having a problem, these keepalives will be missed and link problem will be detected.
LMI status messages act as a keepalive between the DTE and DCE

## Slide 8: LMI Extensions
VC status messages
LMI status messages combined with Inverse ARP messages allow a router to associate network layer and DCLI.
Notes: In this example, when R1 connects to the Frame Relay network, it sends an LMI status inquiry message to the network. The network replies with an LMI status message containing details of every VC configured on the access link.
Periodically, the router repeats the status inquiry, but subsequent responses include only status changes. After a set number of these abbreviated responses, the network sends a full status message.

## Slide 9: LMI Extensions
  Multicasting messages
  The multicasting extension defines multicasting as another optional LMI feature.
Allows a sender to transmit a single frame that is delivered to multiple recipients.
There is a series of four reserved DLCI values (1019 to 1022) that represent multicast groups.
Notes: The frames sent by a device using one of these reserved DLCIs are replicated by the network and sent to all destinations in the group. The LMI extension for multicasting also defines LMI messages to notify devices of the presence, addition, and deletion of multicast groups.
Multicasting supports the efficient delivery of routing protocol messages and address resolution procedures that are typically sent to many destinations simultaneously

## Slide 10: LMI Extensions
  Global addressing messages
In the basic Frame Relay specification, DLCI values are locally significant and Frame Relay addresses do not exist. Therefore, mapping must be created.
  The global addressing extension solves this problem by allowing DLCI values that are globally significant and hence can serve as addresses of individual end routers.
  The Frame Relay network with global addressing looks much like a LAN to the end routers that can use global addresses (DLCIs) as Frame Relay addresses similar to MAC addresses used in a LAN.
Notes: The basic Frame Relay specification supports DLCI values that are only locally significant. For example, the DLCI value used on the access link between a router and Frame Relay switch is significant only on the access link and does not in any way identifies the router globally. This DLCI value cannot serve as an address for the router due to its local significance. In other words, Frame Relay addresses do not exist and hence cannot be discovered by usual address resolution methods. Therefore, static maps must be created to tell a router which DLCI to use to reach a remote router. The global addressing extension solves this problem by allowing DLCI values that are globally significant and hence can serve as addresses of individual end routers. The Frame Relay network with global addressing looks much like a LAN to the end routers that can use global addresses (DLCIs) as Frame Relay addresses similar to MAC addresses used in a LAN.
  Provides connection IDs with global rather than local significance, allowing them to be used to identify a specific interface to the Frame Relay network. Global addressing makes the Frame Relay network resemble a LAN in terms of addressing, and ARPs are used as on a LAN.

## Slide 11: LMI Identifier
LMI is used to manage Frame Relay links.
Each LMI message is classified by a DLCI appearing in the LMI frame.

## Slide 12: LMI Identifier
The 10-bit DLCI field supports 1,024 VC IDs: 0 to 1,023.
The LMI extensions reserve some of these VC IDs, thereby reducing the number of permitted VCs.
LMI messages are exchanged between the DTE and DCE using these reserved DLCIs.

## Slide 13: LMI Types
There are several LMI types, each of which is incompatible with the others.
  CISCO - Original LMI extension
  ANSI - Corresponding to the ANSI standard T1.617 Annex D
  Q933A - Corresponding to the ITU standard Q933 Annex A
The LMI type configured on the router must match the type used by the service provider.
Notes: In order to deliver the first LMI services to customers as soon as possible, vendors and standards committees worked separately to develop and deploy LMI in early Frame Relay implementations.
The result is that there are three types of LMI, none of which is compatible with the others.
Cisco, StrataCom, Northern Telecom, and Digital Equipment Corporation (Gang of Four) released one type of LMI, while the ANSI and the ITU-T each released their own versions.
The LMI type must match between the provider Frame Relay switch and the customer DTE device.

## Slide 14: Frame Relay Bandwidth
Local Access Rate
Committed Access Rate (CIR)
Bursting
Discard Eligible (DE) Bit

## Slide 15: Local Access Rate
This is the clock speed or port speed of the the access link or local loop to the Frame Relay cloud.
It is the maximum transfer rate at which data travels into or out of the network, regardless of other settings
Notes: Access rate (AR) is the speed at which the access link is clocked. This is the speed of the physical connection (such as a T1) between your router and the Frame Relay switch

## Slide 16: Local Access Rate
The service provider provides a serial connection or access link to the Frame Relay network with specific rate (the access rate)
These may be 56 kb/s, T1 (1.544 Mb/s), or Fractional T1 (a multiple of 56 kb/s or 64 kb/s).
Access rates are clocked on the Frame Relay switch.
It is not possible to send data at higher than the access rate.

## Slide 17: Committed Access Rate (CIR)
CIR defines the bandwidth for the virtual circuit guaranteed by the service provider under normal conditions.
The CIR is the amount of data that the network receives from the access circuit.
The service provider guarantees that the customer can send data at the CIR. All frames received at or below the CIR are accepted.
Notes: Originally, when the world was moving from expensive private leased lines to the co-operative model of Frame Relay, customers were concerned about bandwidth because of the contention within the Frame Relay cloud with other customers for available capactity. In order to address these concerns, Frame Relay uses a concept of committed information rate (CIR). Each VC has a CIR, which is a guarantee by the provider that a particular VC would get that much bandwidth. So you can migrate from a private leased line to Frame Relay with a CIR equal to the leased line bandwidth.
Committed information rate (CIR) is the speed at which the bits can be sent over a VC, according to the service contract between the Frame Relay service provider and its customer.

## Slide 18: Committed Access Rate (CIR)
CIR is usually lower than the actual access rate of the interface.
Customers can choose the CIR that is most appropriate to their bandwidth needs, as long as the CIR is less than or equal to the local access rate.
Typically, the higher the CIR, the higher the cost of service.

## Slide 20: Bursting
A great advantage of Frame Relay is that any network capacity that is being unused is made available or shared with all customers, usually at no extra charge.
This allows customers to burst over their CIR as a bonus.

## Slide 21
an access rate on serial port S0/0/1 of router R1 to be 64 kb/s.
This is higher than the combined CIRs of the two PVCs.
Under normal circumstances, the two PVCs should not transmit more than 32 kb/s and 16 kb/s, respectively.
As long as the amount of data the two PVCs send does not exceed the CIR, it should get through the network.

## Slide 22: Bursting
Because the physical circuits of the Frame Relay network are shared between subscribers, there are often times where there is excess bandwidth available.
Frame Relay can allow customers to dynamically access this extra bandwidth and burst over their CIR for free.
Bursting allows devices that temporarily need additional bandwidth to borrow it at no extra cost from other devices not using it.
Notes: Frame Relay allows a customer and provider to agree that under certain circumstances, the customer can “burst” over the CIR.

## Slide 23
if PVC 102 is transferring a large file, it could use any of the 16 kb/s not being used by PVC 103.
A device can burst up to the access rate and still expect the data to get through.
The duration of a burst transmission should be less than three or four seconds.

## Slide 24: Discard Eligible (DE) Bit
If the customer sends information faster than the CIR on a given DLCI, the network marks some frames with a Discard Eligibility (DE) bit.
The network does its best to deliver all packets; however it discards DE packets first if there is congestion.

## Slide 25: Frame Relay Bandwidth
Several factors determine the rate at which a customer can send data on a Frame Relay network.
Foremost in limiting the maximum transmission rate is the capacity of the local loop to the provider.
In Frame Relay terminology, the speed of the local loop is called the local access rate.
If the local loop is a T1, no more than 1.544 Mbps can be sent.

## Slide 26: Frame Relay Bandwidth
Providers use the CIR parameter to provision network resources and regulate usage.
For example, a company with a T1 connection to the packet-switched network may agree to a CIR of 768 Kbps.
This means that the provider guarantees 768 Kbps of bandwidth to the customer’s link at all times.

## Slide 27: Frame Relay Bandwidth
If the CIR of the customer is less than the local access rate, the customer and provider agree on whether bursting above the CIR is allowed.
Since burst traffic is in excess of the CIR, the provider does not guarantee that it will deliver the frames.

## Slide 28: Frame Relay Bandwidth
An example is a customer buying a 9.6K CIR on a 64K access line. The customer will be guaranteed 9.6K speed but could burst up to 64K if the need arises, for which he may be charged or frames may be dropped.