## Slide 1: CHAPTER 11 METALS AND ALLOYS
قسم الهندسة الميكانيكية
Mechanical Engineering Department, King Saud University, P.O. Box 800, Riyadh 11421, Saudi Arabia
Notes: <number>

## Slide 2
<number>
OBJECTIVES...
• How are metal alloys classified and how are they used?
• What are some of the common fabrication techniques?
• How do properties vary throughout a piece of material
that has been quenched, for example?
• How can properties be modified by post heat treatment?
قسم الهندسة الميكانيكية
Mechanical Engineering Department, King Saud University, P.O. Box 800, Riyadh 11421, Saudi Arabia
Notes: <number>

## Slide 3: CLASSIFICATION OF METALS
<number>
Adapted from Fig. 11.1, Callister 7e.
Metal
Alloys
Steels
Ferrous
Nonferrous
Cast Irons
Cu
Al
Mg
Ti
<1.4wt%C
3-4.5
wt%C
Steels
<1.4 wt% C
Cast Irons
3-4.5 wt% C
Fe
3
C
cementite
1600
1400
1200
1000
800
600
400
0
1
2
3
4
5
6
6.7
L

austenite

+L

+Fe3C

ferrite

+Fe3C

+

L+Fe3C

(Fe)
Co , wt% C
Eutectic:
Eutectoid:
0.76
4.30
727°C
1148°C
T(°C)
microstructure:
ferrite, graphite
cementite
قسم الهندسة الميكانيكية
Mechanical Engineering Department, King Saud University, P.O. Box 800, Riyadh 11421, Saudi Arabia
Notes: <number>

## Slide 4: STEELS
<number>
Based on data provided in Tables 11.1(b), 11.2(b), 11.3, and 11.4, Callister 7e.
Low Alloy
High Alloy
low carbon
<0.25 wt% C
Med carbon
0.25-0.6 wt% C
high carbon
0.6-1.4 wt% C
Uses
auto
struc.
sheet
bridges
towers
press.
vessels
crank
shafts
bolts
hammers
blades
pistons
gears
wear
applic.
wear
applic.
drills
saws
dies
high T
applic.
turbines
furnaces
V. corros.
resistant
Example
1010
4310
1040
43
40
1095
4190
304
Additions
none
Cr,V
Ni, Mo
none
Cr, Ni
Mo
none
Cr, V,
Mo, W
Cr, Ni, Mo
plain
HSLA
plain
heat
treatable
plain
tool
austenitic
stainless
Name
Hardenability
0
+
+
++
++
+++
0
TS
-
0
+
++
+
++
0
EL
+
+
0
-
-
--
++
increasing strength, cost, decreasing ductility
Notes: <number>

## Slide 5: FERROUS ALLOYS
Iron containing – Steels - cast irons
Nomenclature AISI & SAE
10xx Plain Carbon Steels
11xx Plain Carbon Steels (resulfurized for machinability)
15xx Mn (10 ~ 20%)
40xx Mo (0.20 ~ 0.30%)
43xx Ni (1.65 - 2.00%), Cr (0.4 - 0.90%), Mo (0.2 - 0.3%)
44xx Mo (0.5%)
where xx is wt% C x 100
example: 1060 steel – plain carbon steel with 0.60 wt% C
Stainless Steel -- >11% Cr
<number>
قسم الهندسة الميكانيكية
Mechanical Engineering Department, King Saud University, P.O. Box 800, Riyadh 11421, Saudi Arabia
Notes: <number>

## Slide 6: CAST IRON
Ferrous alloys with > 2.1 wt% C
  more commonly 3 - 4.5 wt%C
low melting (also brittle) so easiest to cast
Cementite decomposes to ferrite + graphite
  Fe3C  3 Fe () + C (graphite)
  generally a slow process
<number>
قسم الهندسة الميكانيكية
Mechanical Engineering Department, King Saud University, P.O. Box 800, Riyadh 11421, Saudi Arabia
Notes: <number>
  So phase diagram for this system is different (Fig 12.4)

## Slide 7: FE-C TRUE EQUILIBRIUM DIAGRAM
<number>
Graphite formation promoted by
Si > 1 wt%
slow cooling
1600
1400
1200
1000
800
600
400
0
1
2
3
4
90
L

+L
 + Graphite
Liquid +
Graphite
(Fe)
Co , wt% C
0.65
740°C
T(°C)
 + Graphite
100
1153°C

Austenite
4.2 wt% C

قسم الهندسة الميكانيكية
Mechanical Engineering Department, King Saud University, P.O. Box 800, Riyadh 11421, Saudi Arabia
Notes: <number>
Cast irons have graphite

## Slide 8: TYPES OF CAST IRON
Gray iron
graphite flakes
weak & brittle under tension
stronger under compression
excellent vibrational dampening
wear resistant
Ductile iron
add Mg or Ce
graphite in nodules not flakes
matrix often pearlite - better ductility
<number>
Adapted from Fig. 11.3(a) & (b), Callister 7e.
قسم الهندسة الميكانيكية
Mechanical Engineering Department, King Saud University, P.O. Box 800, Riyadh 11421, Saudi Arabia
Notes: <number>

## Slide 9: TYPES OF CAST IRON
White iron
<1wt% Si so harder but brittle
more cementite
Malleable iron
heat treat at 800-900ºC
graphite in rosettes
more ductile
<number>
Adapted from Fig. 11.3(c) & (d), Callister 7e.
قسم الهندسة الميكانيكية
Mechanical Engineering Department, King Saud University, P.O. Box 800, Riyadh 11421, Saudi Arabia
Notes: <number>

## Slide 10: LIMITATIONS OF FERROUS ALLOYS
  Relatively high density
  Relatively low conductivity
  Poor corrosion resistance
<number>
قسم الهندسة الميكانيكية
Mechanical Engineering Department, King Saud University, P.O. Box 800, Riyadh 11421, Saudi Arabia
Notes: <number>

## Slide 11: NONFERROUS ALLOYS
<number>
Based on discussion and data provided in Section 11.3, Callister 7e.
NonFerrous
Alloys
• Al Alloys
-lower

: 2.7g/cm3
-Cu, Mg, Si, Mn, Zn additions
-solid sol. or precip.
strengthened (struct.
aircraft parts
& packaging)
• Mg Alloys
-very low

: 1.7g/cm3
-ignites easily
-
aircraft, missiles
• Refractory metals
-high melting T
-Nb, Mo, W, Ta
• Noble metals
-Ag, Au, Pt
-
oxid./corr. resistant
• Ti Alloys
-lower

: 4.5g/cm3
vs 7.9 for steel
-reactive at high T
-
space applic.
• Cu Alloys
Brass: Zn is subst. impurity
(costume jewelry, coins,
corrosion resistant)
Bronze
: Sn, Al, Si, Ni are
subst. impurity
(bushings, landing
gear)
Cu-Be
:
precip. hardened
for strength
قسم الهندسة الميكانيكية
Mechanical Engineering Department, King Saud University, P.O. Box 800, Riyadh 11421, Saudi Arabia
Notes: <number>