## Slide 1
Chapter 2
Physical Layer
Prepared by :
Dr. Adel Soudani & Dr. Mznah Al-Rodhaan

## Slide 2
Lecture 1

## Slide 3: Outline
2.1 Analog and Digital
2.2 Transmission Media
2.3 Digital Modulation and Multiplexing
2.4 Transmission Impairment
2.5 Data-rate Limits
2.6 Performance

## Slide 4
Physical layer
Main functions of the physical layer
Coding /decoding signals
Modulation/Demodulation
Adaptation of the signal to the physical medium properties

## Slide 5
2-1 ANALOG AND DIGITAL
Data can be analog or digital
Analog data refers to information that is continuous
Analog data take on continuous values
Analog signals can have an infinite number of values in a range
Digital data refers to information that has discrete states
Digital data take on discrete values
Digital signals can have only a limited number of values
In data communications, we commonly use
periodic analog signals and nonperiodic digital signals.

## Slide 6
Comparison of analog and digital signals

## Slide 7
PERIODIC ANALOG SIGNALS
Periodic analog signals can be classified as simple or composite.
A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals.
A composite periodic analog signal is composed of multiple sine waves.

## Slide 8
Signal amplitude

## Slide 9
Frequency is the rate of change with respect to time.
Change in a short span of time means high frequency.
Change over a long span of time means low frequency.
If a signal does not change at all, its frequency is zero
If a signal changes instantaneously, its frequency is infinite.
Frequency

## Slide 10
Frequency and period are the inverse of each other.
Units of period and frequency
Frequency and Period

## Slide 11
Two signals with the same amplitude, but different frequencies

## Slide 12
The power we use at home has a frequency of 60 Hz. What is the period of this sine wave ?
Examples
The period of a signal is 100 ms. What is its frequency in kilohertz?

## Slide 13
Phase describes the position of the waveform
relative to time 0
Phase
Three sine waves with the same amplitude and frequency, but different phases

## Slide 14
Wavelength and period
Wavelength = Propagation speed x Period
= Propagation speed / Frequency

## Slide 15
Time-domain and frequency-domain plots of a sine wave
A complete sine wave in the time domain can be represented by one single spike in the frequency domain.

## Slide 16
Frequency Domain
The frequency domain is more compact and useful when we are dealing with more than one sine wave.
A single-frequency sine wave is not useful in data communication
  We need to send a composite signal, a signal made of many simple sine waves.

## Slide 17
According to Fourier analysis,
any composite signal is a combination of simple sine waves with different frequencies, amplitudes, and phases.
Fourier analysis
If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies;
If the composite signal is nonperiodic, the decomposition gives a combination of sine waves with continuous frequencies.

## Slide 18
A composite periodic signal
Decomposition of the composite periodic signal in the time and frequency domains

## Slide 19
Time and frequency domains of a nonperiodic signal
A nonperiodic composite signal
  It can be a signal created by a microphone or a telephone set when a word or two is pronounced.
  In this case, the composite signal cannot be periodic
    because that implies that we are repeating the same word or words with exactly the same tone.

## Slide 20
The bandwidth of a composite signal is
the difference between the highest and the lowest frequencies contained in that signal.
Bandwidth

## Slide 21
A nonperiodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V. The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal.
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz.
Example

## Slide 22
DIGITAL SIGNALS
In addition to being represented by an analog signal, information can also be represented by a digital signal.
For example, a 1 can be encoded as a positive voltage and a 0 as zero voltage.
A digital signal can have more than two levels.
In this case, we can send more than 1 bit for each level.

## Slide 23
Two digital signals: one with two signal levels and
the other with four signal levels

## Slide 24
A digital signal has 8 levels. How many bits are needed per level?
We calculate the number of bits from the formula
Each signal level is represented by 3 bits.
A digital signal has 9 levels. How many bits are needed per level?
Each signal level is represented by 3.17 bits.
The number of bits sent per level needs to be an integer as well as a power of 2.
Hence, 4 bits can represent one level.
Examples

## Slide 25
Assume we need to download files at a rate of 100 pages per minute. A page is an average of 24 lines with 80 characters in each line where one character requires 8 bits. What is the required bit rate of the channel?
A digitized voice channel is made by digitizing a 4-kHz bandwidth analog voice signal. We need to sample the signal at twice the highest frequency (two samples per hertz). Assume that each sample requires 8 bits.
What is the required bit rate?
Examples

## Slide 26
HDTV uses digital signals to broadcast high quality video signals. There are 1920 by 1080 pixels per screen, and the screen is renewed 30 times per second. Also, 24 bits represents one color pixel.
What is the bit rate for high-definition TV (HDTV)?
The TV stations reduce this rate to 20 to 40 Mbps through compression.
Example

## Slide 27
The time and frequency domains of periodic and
nonperiodic digital signals

## Slide 28
Baseband transmission
A digital signal is a composite analog signal with an infinite bandwidth.

## Slide 29
Bandwidths of two low-pass channels

## Slide 30
Baseband transmission using a dedicated medium
Baseband transmission of a digital signal that preserves the shape of the digital signal is possible only if we have a low-pass channel with an infinite or very wide bandwidth.

## Slide 31
Bandwidth of a bandpass channel
If the available channel is a bandpass channel, we cannot send the digital signal directly to the channel; we need to convert the digital signal to an analog signal before transmission.

## Slide 32
Twisted pair (1)
  Simply two wires twisted together – thickness=1mm
  The twisting cuts down on electrical interference.
  Heavily used in the phone system
  Typical office has four pairs for phones.
  Until some Kilometers/ Some Mbps
  For Analog and Digital
2-2 TRANSMISSION MEDIA

## Slide 33: Transmission Media (2)
Twisted pair (2)
  Bandwidth depends on thickness and distance
  Need repeater for long distances
  Category 3 and 5 - with 5 having more twists and better insulation.
  Popular by UTP (Unshielded Twisted Pair)
Category 5 UTP cable with four twisted pairs

## Slide 34: Transmission Media (3)
Baseband Coaxial cable
  Used for digital transmissions (called baseband.)
  Good noise immunity.
  Data rates as high as 2 Gbps for 1 Km distance.
  Now being replaced by fiber.
Broadband Coaxial cable
  Used for analog transmissions (called broadband.)
  Can run 300 MHz for long distances.
  Analog signaling has better S/N than digital signaling.
  Interfaces must convert digital signals to analog and vice versa.
  Designed for long distances - can use amplifiers.

## Slide 35: Transmission Media (4)
Fiber Optic (1)
  Transmission of light through fiber
  Bandwidth more than 50,000 Gbps !
  But now restricted to 1Gbps!
  Reason: Electrical and optical signal conversion
  Including 3 components:
    Light source: Pulse of light=1, absence of light=0
    Transition medium: an ultra-thin fiber of glass
    detector: generate an electrical pulse when light falls on it
  Similar to coax (without braid)

## Slide 36: Transmission Media (5)
Fiber Optic (2)
  Thickness of core: 8~10 microns or 50 microns
  Two typically light sources:
    LED (Light Emitting Diode)
    response time=1ns  data rate = 1Gbps
    2. Semiconductor laser

## Slide 37
Lecture 2

## Slide 38: Transmission Media (6)
Fiber Optic (3)
  Properties include total internal reflection and attenuation of particular frequencies.
  Fiber Optic Networks - can be used for LANs and long-haul.
  A fiber-optic LAN

## Slide 39: Transmission Media (7)
Comparison of fiber optic and copper wire
Copper | Fiber | 
Lower | Higher | Bandwidth
5 Km | 30 KM | Distance between repeaters
High | Low | Interference
- | Smaller/Lighter | Physical
Bi-directional | Uni-directional | Flow

## Slide 40: Transmission Media (8)
Connector
Repeater
  Signal Regeneration
  Clean up
  Amplify
  Distance Extension
Hub
  Repeater functionality, plus...
    Concentration Point
    Signal Distribution Device
    Management Functions

## Slide 41: Wireless Transmission
The electromagnetic spectrum and its uses for communication

## Slide 42: Radio Transmission
In the VLF, LF, and MF bands, radio waves follow the curvature of the earth

## Slide 43: Radio Transmission (2)
In the HF band, they bounce off the ionosphere.

## Slide 44: Light Transmission
Convection currents can interfere with laser communication systems. A bidirectional system with two lasers is pictured here.

## Slide 45: Communication Satellites
Communication satellites, some properties, including: altitude above earth, round-trip delay time, number of satellites for global coverage.

## Slide 46: Geostationary Satellites
VSATs using a hub.

## Slide 47: Low-Earth Orbit Satellites

## Slide 48: Baseband Transmission
Line codes: (a) Bits, (b) NRZ, (c) NRZI, (d) Manchester, (e) Bipolar or AMI.
2-3 Digital Modulation and Multiplexing

## Slide 49: Passband Transmission
(a) A binary signal. (b) Amplitude shift keying. (c) Frequency shift keying. (d) Phase shift keying.

## Slide 50: Passband Transmission (2)
(a) QPSK. (b) QAM-16. (c) QAM-64.

## Slide 51: Frequency Division Multiplexing
Orthogonal frequency division multiplexing (OFDM).

## Slide 52: Time Division Multiplexing
Time Division Multiplexing (TDM).

## Slide 53: Code Division Multiplexing
Chip sequences for four stations.
Signals the sequences represent.

## Slide 54
2-4 TRANSMISSION IMPAIRMENT
Signals travel through transmission media, which are not perfect.
The imperfection causes signal impairment.
This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium.
What is sent is not what is received.
Three causes of impairment are attenuation, distortion, and noise.

## Slide 55
Attenuation

## Slide 56
Suppose a signal travels through a transmission medium and its power is reduced to one-half.
This means that P2 is (1/2)P1.
In this case, the attenuation (loss of power) can be calculated as
A loss of 3 dB (–3 dB) is equivalent to losing one-half the power.
Example

## Slide 57
A signal travels through an amplifier, and its power is increased 10 times.
This means that P2 = 10P1 .
What is the amplification (gain of power)?
57
Example

## Slide 58
One reason that engineers use the decibel to measure the changes in the strength of a signal is that decibel numbers can be added (or subtracted) when we are measuring several points (cascading) instead of just two.
A signal travels from point 1 to point 4.
In this case, the decibel value can be calculated as
Example

## Slide 59
Distortion

## Slide 60
Noise

## Slide 61
The power of a signal is 10 mW and the power of the noise is 1 μW; what are the values of SNR and SNRdB ?
Solution
The values of SNR and SNRdB can be calculated as follows:
61
Example

## Slide 62
Two cases of SNR: a high SNR and a low SNR

## Slide 63
The values of SNR and SNRdB for a noiseless channel are
We can never achieve this ratio in real life; it is an ideal.
63
Example

## Slide 64
Lecture 3

## Slide 65
2-5 DATA RATE LIMITS
A very important consideration in data communications is how fast we can send data, in bits per second, over a channel.
Data rate depends on three factors:
1. The bandwidth available
2. The level of the signals we use
3. The quality of the channel (the level of noise)
Increasing the levels of a signal may reduce the reliability of the system.

## Slide 66
For noiseless channel,
In baseband transmission, we said the bit rate is 2 times the bandwidth if we use only the first harmonic in the worst case.
However, the Nyquist formula is more general than what we derived intuitively; it can be applied to baseband transmission and modulation.
Also, it can be applied when we have two or more levels of signals.
66
Nyquist Theorem
BitRate = 2 x Bandwith x log2Levels

## Slide 67
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. What is the maximum bit rate?
Examples
Consider the same noiseless channel transmitting a signal with four signal levels (for each level, we send 2 bits). What is the maximum bit rate?

## Slide 68
We need to send 265 kbps over a noiseless channel with a bandwidth of 20 kHz. How many signal levels do we need?
Solution
We can use the Nyquist formula as
Since this result is not a power of 2, we need to either increase the number of levels or reduce the bit rate.
If we have 128 levels, the bit rate is 280 kbps.
If we have 64 levels, the bit rate is 240 kbps.
68
Example

## Slide 69
The Shannon capacity gives us the upper limit;
the Nyquist formula tells us how many signal levels we need.
69
Shannon Capacity
In reality, we can not have a noisless channel
For noisy channel,
Capacity = Bandwith x log2(1+SNR)

## Slide 70
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero.
In other words, the noise is so strong that the signal is faint. What is the channel capacity?
Solution
This means that the capacity of this channel is zero regardless of the bandwidth.
In other words, we cannot receive any data through this channel.
70
Example

## Slide 71
Let’s calculate the theoretical highest bit rate of a regular telephone line. A telephone line normally has a bandwidth of 3000. The signal-to-noise ratio is usually 3162.
What is the channel capacity?
Solution
This means that the highest bit rate for a telephone line is 34.860 kbps.
If we want to send data faster than this, we can either increase the bandwidth of the line or improve the signal-to-noise ratio.
71
Example

## Slide 72
The signal-to-noise ratio is often given in decibels.
Assume that SNRdB = 36 and the channel bandwidth is 2 MHz.
What is the theoretical channel capacity?
Solution
72
Example

## Slide 73
For practical purposes, when the SNR is very high, we can assume that SNR + 1 is almost the same as SNR.
In these cases, the theoretical channel capacity can be simplifiedto
For example, we can calculate the theoretical capacity of the previous example as
73
Example

## Slide 74
We have a channel with a 1-MHz bandwidth. The SNR for this channel is 63.
What are the appropriate bit rate and signal level?
Solution
First, we use the Shannon formula to find the upper limit.
The Shannon formula gives us 6 Mbps, the upper limit. For better performance we choose something lower, 4 Mbps, for example.
Then we use the Nyquist formula to find the number of signal levels.
74
Example

## Slide 75
2-6 PERFORMANCE
One important issue in networking is the performance of the network—how good is it?
In networking, we use the term bandwidth in two contexts
The first, bandwidth in hertz,
refers to the range of frequencies in a composite signal or the range of frequencies that a channel can pass.
The second, bandwidth in bits per second,
refers to the speed of bit transmission in a channel or link.

## Slide 76: Message Latency
Latency is the delay to send a message over a link
  Transmission delay: time to put M-bit message “on the wire”
    T-delay = M (bits) / Rate (bits/sec) = M/R seconds
  Propagation delay: time for bits to propagate across the wire
    P-delay = Length / speed of signals = D seconds
  Combining the two terms we have: Latency = M/R + D

## Slide 77: Metric Units
The main prefixes we use:
Use powers of 10 for rates, 2 for storage
  1 Mbps = 1,000,000 bps, 1 KB = 1024 bytes
“B” is for bytes, “b” is for bits
Prefix | Exp. | prefix | exp.
K(ilo) | 103 | m(illi) | 10-3
M(ega) | 106 | μ(micro) | 10-6
G(iga) | 109 | n(ano) | 10-9
Notes: From CN5E Slides #1-42

## Slide 78
The bandwidth of a subscriber line is 4 kHz for voice or data.
The bandwidth of this line for data transmission
can be up to 56,000 bps using a sophisticated modem to change the digital signal to analog.
78
Examples
If the telephone company improves the quality of the line and increases the bandwidth to 8 kHz,
we can send 112,000 bps.

## Slide 79
A network with bandwidth of 10 Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000 bits. What is the throughput of this network?
Solution
We can calculate the throughput as
The throughput is almost one-fifth of the bandwidth in this case.
79
Example

## Slide 80
What is the propagation time if the distance between the two points is 12,000 km? Assume the propagation speed to be 2.4 × 108 m/s in cable.
Solution
We can calculate the propagation time as
The example shows that a bit can go over the Atlantic Ocean in only 50 ms if there is a direct cable between the source and the destination.
80
Example

## Slide 81
What are the propagation time and the transmission time for a 2.5-kbyte message if the bandwidth of the network is 1 Gbps? Assume that the distance is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
Note that in this case, because the message is short and the bandwidth is high, the dominant factor is the propagation time, not the transmission time.
The transmission time can be ignored.
81
Example

## Slide 82
What are the propagation time and the transmission time for a 5-Mbyte message if the bandwidth of the network is 1 Mbps? Assume that the distance is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
Note that in this case, because the message is very long and the bandwidth is not very high, the dominant factor is the transmission time, not the propagation time.
The propagation time can be ignored.
82
Example