## Slide 1
Fig 28-CO, p.858
Notes: <number>
Fig 28-CO An assortment of batteries that can be used to provide energy for various devices. Batteries provide a voltage with a fixed polarity, resulting in a direct current in a circuit, that is, a current for which the charges always move in the same direction. (George Semple)

## Slide 3
A constant current can be maintained in a closed circuit through the use of a source of emf, (such as a battery or generator) that produces an electric field and thus may cause charges to move around a circuit.
One can think of a source of emf as a “charge pump.” When an electric potential difference exists between two points, the source moves charges “uphill” from the lower potential to the higher.
The emf describes the work done per unit charge, and hence the SI unit of emf is the volt.
Notes: <number>
Figure 28.1

## Slide 4
A circuit consisting of a resistor connected to the terminals of a battery.
The positive terminal of the battery is at a higher potential than the negative terminal. If we neglect the internal resistance of the battery, the potential difference across it (called the terminal voltage) equals its emf.
assume that the connecting wires have no resistance.
However, because a real battery always has some
internal resistance r, the terminal voltage is not equal to the emf for a battery in a circuit in which there is a current.

## Slide 5
As we move through the resistance r, the potential decreases by an amount Ir, where I is the current in the circuit.
ε : is equivalent to the open-circuit voltage—that is, the terminal voltage when the current is zero. The emf is the voltage labeled on a battery,….
As we pass from the negative terminal to the positive terminal, the potential increases by an amount ε.
the terminal voltage V must equal the potential difference across the external resistance R, often called the load resistance.
Notes: <number>
Active Figure 28.2 (a) Circuit diagram of a source of emf (in this case, a battery), of internal resistance r, connected to an external resistor of resistance R. (b) Graphical representation showing how the electric potential changes as the circuit in part (a) is traversed clockwise.

## Slide 6
Fig 28-2b, p.860
the changes in electric potential as the circuit is traversed in the clockwise direction
The resistor represents a load on the battery because the battery must supply energy to operate the device. The potential difference across the load resistance is
ΔV = IR
the total power output Iε of the battery is delivered to the external load resistance in the amount I 2R and to the internal resistance in the amount I 2r.
Notes: <number>
Active Figure 28.2 (b) Graphical representation showing how the electric potential changes as the circuit in part (a) is traversed clockwise.

## Slide 9
* A battery has an emf of 15.0 V. The terminal voltage of the battery is 11.6 V when it is delivering 20.0 W of power to an external load resistor R. (a) What is the value of R? (b) What is the internal resistance of the battery?

## Slide 10
When two or more resistors are connected together as are the light- bulbs, they are said to be in series.
In a series connection, all the charges moving through one resistor must also pass through the second resistor.
This relationship indicates that the equivalent resistance of a series connection of resistors is always greater than any individual resistance.
Notes: <number>
Active Figure 28.4 (a) A series connection of two lightbulbs with resistances R1 and R2. (b) Circuit diagram for the two-resistor circuit. The current in R1 is the same as that in R2. (c) The resistors replaced with a single resistor having an equivalent resistance Req = R1+R2.

## Slide 11
Now consider two resistors connected in parallel,
When the current I reaches point a in Figure 28.5b, called a junction, it splits into two parts, with I1 going through R1 and I 2 going through R2 . A junction is any point in a circuit where a current can split
Notes: <number>
Active Figure 28.6 (a) A parallel connection of two lightbulbs with resistances R1 and R2.

## Slide 12
…the equivalent resistance of two or more resistors connected in parallel is always less than the least resistance in the group.
* Household circuits are always wired such that the appliances are connected in parallel. Each device operates independently of the others so that if one is switched off, the others remain on. In addition, the devices operate on the same voltage.
Notes: <number>
Active Figure 28.4 (a) A series connection of two lightbulbs with resistances R1 and R2.

## Slide 13
(a) Find the equivalent resistance between points a and c.
(b) What is the current in each resistor if a potential difference of 42V is maintained between a and c ?
Notes: <number>
Active Figure 28.4 (b) Circuit diagram for the two-resistor circuit. The current in R1 is the same as that in R2.

## Slide 14
Three resistors are connected in parallel as shown in Figure 28.7. A potential difference of 18 V is maintained between points a and b.
(a) Find the current in each resistor.
(b) Calculate the power delivered to each resistor and the total power delivered to the combination of resistors.
Notes: <number>
Active Figure 28.4 (c) The resistors replaced with a single resistor having an equivalent resistance Req = R1+R2.

## Slide 15
(c) Calculate the equivalent resistance of the circuit.
Exercise :Use Req to calculate the total power delivered by the battery.
Answer :200 W.
Notes: <number>
Figure 28.5 (Quick Quiz 28.4) What happens when the switch is opened?

## Slide 16
Notes: <number>
Active Figure 28.6 (a) A parallel connection of two lightbulbs with resistances R1 and R2. (b) Circuit diagram for the two-resistor circuit. The potential difference across R1 is the same as that across R2. (c) The resistors replaced with a single resistor having an equivalent resistance given by Equation 28.7.

## Slide 17
- we can analyze simple circuits using the expression V IR and the rules for series and parallel combinations of resistors. Very often, however, it is not possible to reduce a circuit to a single loop.
- The procedure for analyzing more complex circuits is greatly simplified if we use two principles called Kirchhoff’s rules:
Notes: <number>
Active Figure 28.6 (b) Circuit diagram for the two-resistor circuit. The potential difference across R1 is the same as that across R2.

## Slide 18
Fig 28-14, p.870
the charge passes through some circuit elements must equal the sum of the
decreases in energy as it passes through other elements. The potential energy
decreases whenever the charge moves through a potential drop IR across a resis-tor or whenever it moves in the reverse direction through a source of emf. The
potential energy increases whenever the charge passes through a battery from the
negative terminal to the positive terminal.
Kirchhoff’s first rule is a statement of conservation of electric charge.
Notes: <number>
the charge passes through some circuit elements must equal the sum of the
decreases in energy as it passes through other elements. The potential energy
decreases whenever the charge moves through a potential drop IR across a resis-tor
or whenever it moves in the reverse direction through a source of emf. The
potential energy increases whenever the charge passes through a battery from the
negative terminal to the positive terminal.
Figure 28.14 (a) Kirchhoff’s junction rule. Conservation of charge requires that all charges entering a junction must leave that junction. Therefore, I1= I2+ I3. (b) A mechanical analog of the junction rule: the amount of water flowing out of the branches on the right must equal the amount flowing into the single branch on the left.

## Slide 19
Kirchhoff’s second rule follows from the law of conservation of energy.
Let us imagine moving a charge around the loop. When the charge returns to the starting point, the charge–circuit system must have the same energy as when the charge started from it.
The sum of the increases in energy in some circuit elements must equal the sum of the decreases in energy in other elements.
The potential energy decreases whenever the charge moves through a potential drop IR across a resistor or whenever it moves in the reverse direction through a source of emf. The potential energy increases when-ever the charge passes through a battery from the negative terminal to the positive terminal.

## Slide 20
You should note the following sign conventions when using the second rule:
• Because charges move from the high-potential end of a resistor to the low potential end, if a resistor is traversed in the direction of the current, the change in potential V across the resistor is - IR
Each circuit element is traversed from left to right
• If a resistor is traversed in the direction opposite the current, the change in potential V across the resistor is + IR
• If a source of emf (assumed to have zero internal resistance) is traversed in the direction of the emf (from - to+ ), the change in potential V is +ε.
The emf of the battery increases the electric potential as we move through it in this direction.
• If a source of emf (assumed to have zero internal resistance) is traversed in the direction opposite the emf (from + to - ), the change in potential V is - ε.
In this case the emf of the battery reduces the electric potential as we move through it.
Notes: <number>
Figure 28.15 Rules for determining the potential differences across a resistor and a battery. (The battery is assumed to have no internal resistance.) Each circuit element is traversed from left to right.

## Slide 22
Fig 28-16, p.871
(a) Find the current in the circuit. (Neglect the internal resistances of the batteries.)
Traversing the circuit in the clockwise direction, starting at a, we see that a →b represents a potential change of +ε1 , b → c represents a potential change of - IR1 , c → d represents a potential change of -ε2 , and d → a represents a potential change of -IR2 . Applying Kirchhoff’s loop rule gives
Notes: <number>
Figure 28.16 (Example 28.8) A series circuit containing two batteries and two resistors, where the polarities of the batteries are in opposition.

## Slide 23
(b) What power is delivered to each resistor? What power is delivered by the 12-V battery?
The 12-V battery delivers power Iε2. Half of this power is delivered to the two resistors, as we just calculated. The other half is delivered to the 6-V battery, which is being charged by the 12-V battery.

## Slide 24
Find the currents I1 , I2 , and I3 in the circuit
We arbitrarily choose the directions of the currents as labeled in Figure
Substituting Equation (1) into Equation (2) gives
Dividing each term in Equation (3) by 2 and rearranging gives
Subtracting Equation (5) from Equation (4) eliminates I 2 , giving
The fact that I 2 and I 3 are both negative indicates only that the currents are opposite the direction we chose for them. However, the numerical values are correct.
Notes: <number>
Figure 28.17 (Example 28.9) A circuit containing different branches.

## Slide 25
Exercise Find the potential difference between points b and c .
Answer 2 V.

## Slide 26
Fig 28-18, p.873
Notes: <number>
Figure 28.18 (Example 28.10) A multiloop circuit. Kirchhoff’s loop rule can be applied to any closed loop, including the one containing the capacitor.

## Slide 28
Fig P28-6, p.885
Notes: <number>

## Slide 29
Fig P28-11, p.886
Notes: <number>

## Slide 30
Fig P28-15, p.886
Notes: <number>

## Slide 31
Fig P28-20, p.887
Notes: <number>

## Slide 32
Fig P28-21, p.887
Notes: <number>

## Slide 33
Fig P28-24, p.887
Notes: <number>

## Slide 34
Fig P28-26, p.888
Notes: <number>

## Slide 35
Fig P28-30, p.888
Notes: <number>