## Slide 1
Fig 32-CO, p.1003
Notes: <number>
Fig 32-CO An airport metal detector contains a large coil of wire around the frame. This coil has a property called inductance. When a passenger carries metal through the detector, the inductance of the coil changes, and the change in inductance signals an alarm to sound. (Jack Hollingsworth/Getty Images)

## Slide 2
As the source current increases with time, the magnetic flux through the circuit loop due to this current also increases with time. This increasing flux creates an induced emf in the circuit.
The direction of the induced emf is such that it would cause an induced current in the loop (if a current were not already flowing in the loop), which would establish a magnetic field that would oppose the change in the source magnetic field.

## Slide 3
After the switch is closed, the current produces a magnetic flux through the area enclosed by the loop.
As the current increases toward its equilibrium value, this magnetic flux changes in time and induces an emf in the loop.
The emf set up in this case is called a self-induced emf.
Notes: <number>
Figure 32.1 After the switch is closed, the current produces a magnetic flux through the area enclosed by the loop. As the current increases toward its equilibrium value, this magnetic flux changes in time and induces an emf in the loop.

## Slide 4
Fig 32-2, p.1005
A current in the coil produces a magnetic field directed to the left.
If the current increases, the increasing magnetic flux creates an induced emf having the polarity shown by the dashed battery.
The polarity of the induced emf reverses if the current decreases.
Notes: <number>
Figure 32.2 (a) A current in the coil produces a magnetic field directed to the left. (b) If the current increases, the increasing magnetic flux creates an induced emf having the polarity shown by the dashed battery. (c) The polarity of the induced emf reverses if the current decreases.

## Slide 5
p.1005
L معامل الحث الذاتي
الحث الذاتي: القوة الدافعة الكهربية التأثيرية الذاتية المتولدة في ملف عندما تتغير شدة التيار الكهربي
بمعدل وحدة شدة التيار في وحدة الزمن (امبير لكل ثانية).
وحدة الحث الذاتي لدائرة هى هنري Henry (V/A.S-1)، والهنري و الحث الذاتي لدائرة تتولد فيها ق.د.ك
قدرها واحد فولت عندما تتغير التيار في الدائرة بمعدل امبير لكل ثانية.
Notes: <number>
Joseph Henry American Physicist (1797–1878) Henry became the first director of the Smithsonian Institution and first president of the Academy of Natural Science. He improved the design of the electromagnet and constructed one of the first motors. He also discovered the phenomenon of self-induction but failed to publish his findings. The unit of inductance, the henry, is named in his honor. (North Wind Picture Archives)

## Slide 10
32-3 الطاقة بالمجال المغناطيسي
القوة الدافعة الكهربية الذاتية التأثيرية بالملف تعمل على تأخر
وصول التيار المار بالدائرة إلى وضع الاستقرار، لذلك فأن البطارية
شغل ضد الملف (الموصل) لكي ينشأ التيار الكهربي بالدائرة.
- جزء من الطاقة المتولدة ن البطارية يفقد بالمقاومة على شكل
حرارة والجزء المتبقي يخزن بالملف.
- بناءا على مبدأ أحفاظ الطاقة،
- المعدل الزمني للطاقة المخزنة بالمجال المغناطيسي للملف
- الطاقة الكلية المخزنة بالملف هى:
Notes: <number>

## Slide 11
- كثافة الطاقة المخزنة بالمجال المغناطيسي- الطاقة لكل وحدة حجم
الطاقة المخزنة بالمجال المغناطيسي
Notes: <number>

## Slide 12
p.1005
Notes: <number>
Joseph Henry American Physicist (1797–1878) Henry became the first director of the Smithsonian Institution and first president of the Academy of Natural Science. He improved the design of the electromagnet and constructed one of the first motors. He also discovered the phenomenon of self-induction but failed to publish his findings. The unit of inductance, the henry, is named in his honor. (North Wind Picture Archives)

## Slide 15
A 40 mA current is carried by a uniformly wound air-core solenoid with 450 turns, a 15 mm diameter, and 12 cm length. Compute
the magnetic field inside the solenoid,
(b) the magnetic flux through each turn
(c) the inductance of the solenoid.
(d) What If? If the current were different,
which of these quantities would change?
L= NK = NФ/I = µonNA
----------------------------------------------------------------------------------------------------------------------

## Slide 21
Fig 32-3, p.1007
Notes: <number>
Active Figure 32.3 A series RL circuit. As the current increases toward its maximum value, an emf that opposes the increasing current is induced in the inductor.

## Slide 22
Fig P32-12, p.1025
Notes: <number>

## Slide 23
Fig P32-17, p.1026
Notes: <number>

## Slide 24
Fig P32-23, p.1026
Notes: <number>

## Slide 25
Fig P32-25, p.1026
Notes: <number>

## Slide 26
Fig P32-26, p.1026
Notes: <number>

## Slide 27
Fig P32-27, p.1026
Notes: <number>

## Slide 28
Fig P32-45, p.1027
Notes: <number>

## Slide 29
Fig P32-48, p.1028
Notes: <number>

## Slide 30
Fig P32-52, p.1028
Notes: <number>

## Slide 31
Fig P32-64, p.1029
Notes: <number>

## Slide 32
Fig P32-68, p.1029
Notes: <number>

## Slide 33
Fig P32-69, p.1029
Notes: <number>

## Slide 34
Fig P32-71, p.1030
Notes: <number>

## Slide 35
Fig P32-72, p.1030
Notes: <number>

## Slide 36
Fig P32-73, p.1030
Notes: <number>

## Slide 37
Fig P32-75, p.1030
Notes: <number>

## Slide 38
Fig P32-78, p.1031
Notes: <number>

## Slide 39
Fig P32-79, p.1031
Notes: <number>

## Slide 40
Fig P32-79a, p.1031
Notes: <number>

## Slide 41
Fig P32-79b, p.1031
Notes: <number>

## Slide 42
Fig P32-79c, p.1031
Notes: <number>