## Slide 1
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>

## Slide 2: 27-1 Electric Current
Now consider a system of electric charges in motion. Whenever there is a net flow of charge through some region, a current is said to exist.
the charges are moving perpendicular to a surface of area A,
The current is the rate at which charge flows through this surface.
average current
instantaneous current
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 3
The SI unit of current is the ampere (A):
That is, 1 A of current is equivalent to 1 C of charge passing through the surface area in 1 s.
It is conventional to assign to the current the same direction as the flow of positive charge
the direction of the current is opposite the direction of flow of electrons.
It is common to refer to a moving charge (positive or negative) as a mobile charge carrier. For example, the mobile charge carriers in a metal are electrons.
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 4: The electric current in a wire is 6 A. How many electrons flow past a given point in a time of 3 s?
I = 6 A
Example:
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 5: Example :
The quantity of charge q (in coulombs) that has passed through a surface of area 2.00 cm2 varies with time according to the equation q = 4t 3 + 5t + 6, where t is in seconds.
(a) What is the instantaneous current through the surface at t = 1.00 s?
(b) What is the value of the current density?
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 6
Microscopic Model of Current
ΔQ = number of carriers in section x charge per carrier
ΔQ = (n A Δ x)q
ΔQ = (nA vd Δ t) q
The speed of the charge carriers vd is an average speed called the drift speed.
consider a conductor in which the charge carriers are free electrons. If the conductor is isolated—that is, the potential difference across it is zero then these electrons undergo random motion that is analogous to the motion of gas molecules.
n = number of electrons/volume
N = n x A 𝚫X electrons travel distance 𝚫X = vd Δt
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>
Figure 27.2 A section of a uniform conductor of cross-sectional area A. The mobile charge carriers move with a speed vd , and the displacement they experience in the x direction in a time interval Δt is x vd Δt. If we choose t to be the time interval during which the charges are displaced, on the average, by the length of the cylinder, the number of carriers in the section of length Δx is nAvd Δt, where n is the number of carriers per unit volume.

## Slide 7
However, the electrons do not move in straight lines along the conductor. Instead, they collide repeatedly with the metal atoms, and their resultant motion is complicated and zigzag (Fig. 27.3). Despite the collisions, the electrons move slowly along the conductor (in a direction opposite that of E) at the drift velocity vd .
when a potential difference is applied across the conductor (for example, by means of a battery), an electric field is set up in the conductor; this field exerts an electric force on the electrons, producing a current.
Fig 27-3, p.834
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 8
A copper wire in a typical residential building has a cross-sectional area of 3.31x 106 m2. If it carries a current of 10.0 A, what is the drift speed of the electrons? Assume that each copper atom contributes one free electron to the current. The density of copper is 8.95 g/cm3. (Atomic mass of cupper is 63.5 g/mol.
# Recall that 1 mol of any substance contains Avogadro’s number of atoms (6.02x 1023). Knowing the density of copper, we can calculate the volume occupied by 63.5 g (≡ 1mol) of copper:
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 9
Consider a conductor of cross-sectional area A carrying a current I.
The current density J in the conductor is defined as the current per unit area. Because the current = nAqvd
the current density is
A current density J and an electric field E are established in a conductor whenever a potential difference is maintained across the conductor.
If the potential difference is constant, then the current also is constant. In some materials, the current density is proportional to the electric field:
(direction of + charge carriers)
27-2 resistance and ohm’s law
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 10
where the constant of proportionalityσ is called the conductivity of the conductor. Materials that obey Equation # are said to follow Ohm’s law
More specifically, Ohm’s law states that ;
for many materials (including most metals), the ratio of the current density to the electric field is a constant σ that is independent of the electric field producing the current.
Materials that obey Ohm’s law and hence demonstrate this simple relationship between E and J are said to be ohmic,
Materials that do not obey Ohm’s law are said to be non-ohmic
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>
Figure 27.5 A uniform conductor of length and cross-sectional area A. A potential
difference ΔV =Vb-Va maintained across the conductor sets up an electric field E,
and this field produces a current I that is proportional to the potential difference.
mass m. This can be written as

## Slide 11
We can obtain a form of Ohm’s law useful in practical applications by considering
a segment of straight wire of uniform cross-sectional area A and length
If the field is assumed to be uniform, the potential difference is related to the field through the relationship
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 12
From this result we see that resistance has SI units of volts per ampere. One volt per ampere is defined to be 1 ohm (Ω):
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 13
(a) The current–potential difference curve for an ohmic material. The curve is linear, and the slope is equal to the inverse of the resistance of the conductor.
(b) A nonlinear current–potential difference curve for a semiconducting diode. This device does not obey Ohm’s law.
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>
Figure 27.7 (a) The current–potential difference curve for an ohmic material. The curve is linear, and the slope is equal to the inverse of the resistance of the conductor.

## Slide 14: When a 3V battery is connected to a light, a current of 6 mA is observed. What is the resistance of the light filament?
Example:
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 15: What length L of copper wire is required to produce a 4 m resistor? Assume the diameter of the wire is 1 mm and that the resistivity  of copper is 1.72 x 10-8 .m .
Example :
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 16
Calculate the resistance of a rectangular strip of copper length 0.08 m. thickness15 mm and width 0.8 mm . The resistivity of copper = 1.7 x 10-8 𝜴.m
Example :
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 17
Calculate the resistance of an aluminum cylinder that is
10.0 cm long and has a cross-sectional area of 2.0x 10-4 m2. Repeat the calculation for a cylinder of the same dimensions and made of glass having a resistivity of 3x1010 Ω
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 18
(a) Calculate the resistance per unit length of a 22-gauge Nichrome wire, which has a radius of 0.321 mm.
(b) If a potential difference of 10 V is maintained across a 1.0-m length of the Nichrome wire, what is the current in the wire?
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 19
Table 27-1, p.837
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>

## Slide 20
27-3 RESISTANCE AND TEMPERATURE
Over a limited temperature range, the resistivity of a metal varies approximately linearly with temperature according to the expression
where is the resistivity at some temperature T (in degrees Celsius), ρ0 is the resistivity at some reference temperature T0 (usually taken to be 20°C), and 𝛼 is the temperature coefficient of resistivity.
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 21
For most materials, the resistance R changes in proportion to the initial resistance Ro and to the change in temperature 𝚫t.
Change in resistance:
The temperature coefficient of resistance 𝛼, a is the change in resistance per unit resistance per unit degree change of temperature.
Because resistance is proportional to resistivity
(Eq. 27.21),
(Eq. 27.11),
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 22: The resistance of a copper wire is 4.00 m at 200C. What will be its resistance if heated to 800C? Assume that = 0.004 /Co.
Ro = 4.00 mt = 80oC – 20oC = 60 Co
R = 1.03 m
R = Ro + R
R = 4.00 m + 1.03 m
R = 5.03 m
Example:
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 23: Factors Affecting Resistance
1. The length L of the material. Longer materials have greater resistance.
1 
L
2 
2L
2. The cross-sectional area A of the material. Larger areas offer LESS resistance.
2 
A
1 
2A
3. The temperature T of the material. The higher temperatures usually result in higher resistances.
4. The kind of material. Iron has more electrical resistance than
a geometrically similar copper conductor.
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 24
A resistance thermometer, which measures temperature by measuring the change in resistance of a conductor, is made from platinum and has a resistance of 50.0 Ω at 20.0°C. When immersed in a vessel containing melting indium, its resistance increases to 76.8 . Calculate the melting point of the indium.
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 25
Fig 27-10, p.844
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>
Figure 27.10 Resistivity versus temperature for a metal such as copper. The curve is linear over a wide range of temperatures, and ρ increases with increasing temperature. As T approaches absolute zero (inset), the resistivity approaches a finite value ρ0 .

## Slide 26
If a battery is used to establish an electric current in a conductor, the chemical energy stored in the battery is continuously transformed into kinetic energy of the charge carriers.
In the conductor, this kinetic energy is quickly lost as a result of collisions between the charge carriers and the atoms making up the conductor, and this leads to an increase in the temperature of the conductor.
In other words, the chemical energy stored in the battery is continuously transformed to internal energy associated with the temperature of the conductor.
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 27
Consider a simple circuit consisting of
Now imagine following a positive quantity of charge Q that is moving clockwise around the circuit from point a through the battery and resistor back to point a.
However, as the charge moves from c to d through the resistor, it loses this electric potential energy as it collides with atoms in the resistor, thereby producing internal energy. If we neglect the resistance of the connecting wires, no loss in energy occurs for paths bc and da. When the charge arrives at point a, it must have the same electric potential energy (zero) that it had at the start.
As the charge moves from a to b through the battery, its electric potential energy U increases by an amount ΔV Δ Q (where Δ V is the potential difference between b and a),
while the chemical potential energy in the battery decreases by the same amount. (Recall from Eq. 25.9 that Δ U= q Δ V).
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>
Active Figure 27.13 A circuit consisting of a resistor of resistance R and a battery having a potential difference V across its terminals. Positive charge flows in the clockwise direction.

## Slide 28
The rate at which the charge Q loses potential energy in going through the
resistor is
Note that because charge cannot build up at any point, the current is the same everywhere in the circuit.
where I is the current in the circuit. In contrast, the charge regains this energy
when it passes through the battery.
Because the rate at which the charge loses energy equals the power delivered to the resistor (which appears as internal energy), we have
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 29
A battery, a device that supplies electrical energy, is called either a source of electromotive force or, more commonly, an emf source.
(The phrase electromotive force is an unfortunate choice because it describes not a force but rather a potential difference in volts.)
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 30
An electric heater is constructed by applying a potential difference of 120 V to a Ni-chrome wire that has a total resistance of 8.0 Ω . Find the current carried by the wire and the power rating of the heater.
If we doubled the applied potential difference, the current would double but the power would quadruple because
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 31
Estimate the cost of cooking a turkey for 4 h in an oven that operates continuously at 20.0 A and 240 V.
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 32
An electric heater draws a steady 15.0 A on a 120-V line. How much power does it require and how much does it cost per month (30 days) if it operates 3.0 h per day and the electric company charges 9.2 cents per kWh?
Example:
P = IV = 1800 W. 1800 W x 3.0 h/day x 30 days = 162 kWh. At 9.2 cents per kWh, this would cost $15.
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>

## Slide 33
An aluminum wire having a cross-sectional area of 4.00 × 10–6 m2 carries a current of 5.00 A. Find the drift speed of the electrons in the wire. The density of aluminum is 2.70 g/cm3. Assume that one conduction electron is supplied by each atom.
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 34
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 35
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 36
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 37
1- A certain light bulb has a tungsten filament with a resistance of 19.0 Ω when cold and 140 Ω when hot. Assume that the resistivity of tungsten varies linearly with temperature even over the large temperature range involved here, and find the temperature of the hot filament. Assume the initial temperature is 20.0°C.
Homework:
2- Aluminum and copper wires of equal length are found to have the same resistance. What is the ratio of their radii?
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 38
4- A 0.900V potential difference is maintained across a 1.50m length of tungsten wire that has a cross-sectional area of 0.600 mm2. What is the current in the wire?
3-If the magnitude of the drift velocity of free electrons in a copper wire is 7.84 x 10-4 m/s, what is the electric field in the conductor? (for copper
n = 8.49 × 10 28 electron/m 3
ρ = 1.7 × 10−8 Ω⋅m
5- A certain toaster has a heating element made of Nichrome resistance wire. When the toaster is ﬁrst connected to a 120-V source of potential difference (and the wire is at a temperature of 20.0°C), the initial cur-rent is 1.80A. However, the current begins to decrease as the resistive element warms up. When the toaster has reached its ﬁnal operating temperature, the current has dropped to 1.53A. (a) Find the power the toaster consumes when it is at its operating temperature. (b) What is the ﬁnal temperature of the heating element?
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 39
6- A high-voltage transmission line with a diameter of 2.00cm and a length of 200km carries a steady current of 1000A. If the conductor is copper wire with a free charge density of 8.00x10 28 electrons/m3
how long does it take one electron to travel the full length of the cable?
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university

## Slide 40
7- A toaster is rated at 600W when connected to a 120V source. What current does the toaster carry, and what isits resistance?
8- If the current carried by a conductor is doubled, what happens to the (a) charge carrier density? (b)current density? (c) electron drift velocity?
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
A- same
B- double
C- double

## Slide 41
1) Ohm’s Law is obeyed since the current still increases when V increases
2) Ohm’s Law is not obeyed
3) this has nothing to do with Ohm’s Law
9- You double the voltage across a certain conductor and you observe the current increases three times. What can you conclude?
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>

## Slide 42
10- Two wires, A and B, are made of the same metal and have equal length, but the resistance of wire A is four times the resistance of wire B. How do their diameters compare?
1) dA = 4 dB
2) dA = 2 dB
3) dA = dB
4) dA = 1/2 dB
5) dA = 1/4 dB
11-Two lightbulbs operate at 120 V, but one has a power rating of 25 W while the other has a power rating of 100 W. Which one has the greater resistance?
1) the 25 W bulb
2) the 100 W bulb
3) both have the same
4) this has nothing to do with resistance
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>

## Slide 43
12 -Two lightbulbs operate at 120 V, but one has a power rating of 25 W while the other has a power rating of 100 W. Which one has the greater resistance?
1) the 25 W bulb
2) the 100 W bulb
3) both have the same
4) this has nothing to do with resistance
07/30/26
<number>
T- Norah Ali Al- moneef king Saud university
Notes: <number>