## Slide 1
A square coil of 100 loops is quickly pulled from the magnetic field as shown in 0.10 s. Calculate the change in flux.
Bfinal =0
Binitial = BAcos0
Binitial = (0.60 T)(0.050m)2(1)
Binitial = 0.0015 Wb
= Bfinal – binitial
= 0 – 0.0015 Wb = -0.0015 Wb
example
What Voltage(induced emf) and current are produced in the loop (assume resistance = 100 )
ε = -NB
t
ε = -(100)(-0.0015 Wb) = 1.5 V
0.10 s
V=ε = IR
I = ε /R = 1.5 V/100  = 0.015 A (15 mA)

## Slide 2: Ex ample
An airplane travels at 1000 km/hr in a region where the earth’s magnetic field is 5 x 10-5T (vertical). What is the potential difference between the wing tips if they are 70 m apart?
1000 km/hr = 280 m/s
E = Blv
E = (5 X 10-5T )(70 m)(280 m/s) = 1.0 V

## Slide 3: example
Blood contains charged ions. A blood vessel is 2.0 mm in diameter, the magnetic field is 0.080 T, and the blood meter registers a voltage of 0.10 mV. What is the flow velocity of the blood?
E = Blv
v = E /Bl
v = (1.0 X 10-4 V) = 0.63 m/s
(0.080 T)(0.0020m)

## Slide 4: Example
Calculate the inductance of a solenoid with 100 turns, a length of 5.0 cm, and a cross sectional area of 0.30 cm2.
L = 0N2A
l
L = (4 X 10-7 T m/A)(100)2(3 X 10-5m2)
(0.05 m)
L = 7.5 X 10-6 H or 7.5 H

## Slide 6
An AC circuit consists of a combination of circuit elements and a power source
The power source provides an alternative voltage, v
The output of an AC power source is sinusoidal and varies with time according to the following equation:
  Δv = ΔVmax sin ωt
    Δv is the instantaneous voltage
    ΔVmax is the maximum output voltage of the source
      Also called the voltage amplitude
    ω is the angular frequency of the AC voltage
The angular frequency is
  ƒ is the frequency of the source
  T is the period of the source
The voltage is positive during one half of the cycle and negative during the other half

## Slide 7
The current in any circuit driven by an AC source is an alternating current that varies sinusoidally with time
Sine waves are characterized by the amplitude and period. The amplitude is the maximum value of a voltage or current; the period is the time interval for one complete cycle.
The amplitude (A) of this sine wave is
20 V
The period is
50.0 s
A
T
If the period is 50 s, the frequency is
0.02 MHz = 20 kHz.

## Slide 8
Sine waves are characterized by the amplitude and period. The amplitude is the maximum value of a voltage or current; the period is the time interval for one complete cycle.
Sine waves
The amplitude (A) of this sine wave is
20 V
The period is
50.0 s
A
T
Notes: <number>

## Slide 9
Consider a circuit consisting of an AC source and a resistor
The AC source is symbolized by
ΔvR = Dv= Vmax sin wt
ΔvR is the instantaneous voltage across the resistor
The instantaneous current in the resistor is
The instantaneous voltage across the resistor is also given as
ΔvR = Imax R sin ωt

## Slide 10
The graph shows the current through and the voltage across the resistor
The current and the voltage reach their maximum values at the same time
The current and the voltage are said to be in phase
For a sinusoidal applied voltage, the current in a resistor is always in phase with the voltage across the resistor
The direction of the current has no effect on the behavior of the resistor
Resistors behave essentially the same way in both DC and AC circuits
Phasor Diagram
To simplify the analysis of AC circuits, a graphical constructor called a phasor diagram can be used
A phasor is a vector whose length is proportional to the maximum value of the variable it represents

## Slide 11
The vector rotates counterclockwise at an angular speed equal to the angular frequency associated with the variable
The projection of the phasor onto the vertical axis represents the instantaneous value of the quantity it represents
rms Current and Voltage
The average current in one cycle is zero
The rms current is the average of importance in an AC circuit
    rms stands for root mean square
Alternating voltages can also be
discussed in terms of rms values

## Slide 12: rms Current and Voltage
The average current in one cycle is zero
The rms current is the average of importance in an AC circuit
    rms stands for root mean square
Alternating voltages can also be discussed in terms of rms values
rms values are used when discussing alternating currents and voltages because
  AC ammeters and voltmeters are designed to read rms values

## Slide 13: Example : For a particular device, the house ac voltage is 120-V and the ac current is 10 A. What are their maximum values?
Irms = 0.707 imax
Vrms= 0.707 Vmax

## Slide 14: Example
A 60 W light bulb operates on a peak voltage of 156 V. Find the Vrms, Irms, and resistance of the light bulb.
Vrms = 110 V
Irms = 0.55 A
R = 202 
Vrms = 156 V / 2 = 110 V
Irms: P = IV  60 W = I (110V)  .55 A
P=V2/R  60 W = (110 V)2/R  R = (110V)2/60W  202 
Notes: <number>
Vrms = 156 V / 2 = 110 V
Irms: P = IV  60 W = I (110V)  .55 A
P=V2/R  60 W = (110 V)2/R  R = (110V)2/60W  202 Vrms = 156 V / 2 = 110 V
Irms: P = IV  60 W = I (110V)  .55 A
P=V2/R  60 W = (110 V)2/R  R = (110V)2/60W  202 

## Slide 15: Power
The rate at which electrical energy is dissipated in the circuit is given by
  P = i 2 R
    i is the instantaneous current
    The heating effect produced by an AC current with a maximum value of Imax is not the same as that of a DC current of the same value
    The maximum current occurs for a small amount of time
The average power delivered to a resistor that carries an alternating current is
Assume a sine wave with a peak value of 40 V is applied to a 100  resistive load. What power is dissipated?
Vrms = 0.707 x Vp = 0.707 x 40 V = 28.3 V
8 W
Example:

## Slide 16
Example 33.1 What Is the rms Current?

## Slide 17
1- A heater takes 10 A rms from the 230 V rms mains. What is its power?
A) 1630 W
2300 W
3250 W
D) 4600 W
2- The voltage output of an AC source is given by the expression :
v = (200 V) sin wt. Find the rms current in the circuit when this source is connected to a 100-Ωresistor.

## Slide 18: 33-3 Inductors in an AC Circuit
Kirchhoff’s loop rule can be applied and gives:

## Slide 19: Current in an Inductor
The equation obtained from Kirchhoff's loop rule can be solved for the current
This shows that the instantaneous current iL in the inductor and the instantaneous voltage ΔvL across the inductor are out of phase by (/2) rad = 90o

## Slide 20: Phase Relationship of Inductors in an AC Circuit
The current is a maximum when the voltage across the inductor is zero
  The current is momentarily not changing
For a sinusoidal applied voltage, the current in an inductor always lags behind the voltage across the inductor by 90° (π/2)
Phasor Diagram for an Inductor
The phasors are at 90o with respect to each other
This represents the phase difference between the current and voltage
Specifically, the current always lags behind the voltage by 90o

## Slide 21: Inductive Reactance
The factor ωL has the same units as resistance and is related to current and voltage in the same way as resistance
Because ω depends on the frequency, it reacts differently, in terms of offering resistance to current, for different frequencies
The factor XL is the inductive reactance and is given by:
  XL = ωL

## Slide 22: Inductive Reactance, cont.
Current can be expressed in terms of the inductive reactance
As the frequency increases, the inductive reactance increases
  This is consistent with Faraday’s Law:
    The larger the rate of change of the current in the inductor, the larger the back emf, giving an increase in the reactance and a decrease in the current

## Slide 23
Example 33.2 A Purely Inductive AC Circuit
In a purely inductive AC circuit, L = 25.0 mH and the rms voltage is 150 V. Calculate the inductive reactance and rms current in the circuit if the frequency is 60.0 Hz.
What if the frequency increases to 6.00 kHz? What happens to the rms current in the circuit?

## Slide 24: Example : A coil having an inductance of 0.6 H is connected to a 120-V, 60 Hz ac source. Neglecting resistance, what is the effective current(Irms) through the coil?
A
L = 0.6 H
V
120 V, 60 Hz
Reactance: XL = 2fL
XL = 2(60 Hz)(0.6 H)
XL = 226 
ieff = 0.531 A
Show that the peak current is Imax = 0.750 A

## Slide 25
The circuit contains a capacitor and an AC source
Kirchhoff’s loop rule gives:
Δv + Δvc = 0 and so
Δv = ΔvC = ΔVmax sin ωt
  Δvc is the instantaneous voltage across the capacitor
The charge is q = C ΔVmax sin ωt
The instantaneous current is given by
The current is /2 rad = 90o out of phase with the voltage
q = C V [ V=Vmax sin(wt) ]
Take derivative: ic = dq/dt = C dV/dt

## Slide 26
The current reaches its maximum value one quarter of a cycle sooner than the voltage reaches its maximum value
The current leads the voltage by 90o
Phasor Diagram for Capacitor
The phasor diagram shows that for a sinusoidally applied voltage, the current always leads the voltage across a capacitor by 90o

## Slide 27: Capacitive Reactance
The maximum current in the circuit occurs at cos ωt = 1 which gives
The impeding effect of a capacitor on the current in an AC circuit is called the capacitive reactance and is given by

## Slide 28: Voltage Across a Capacitor
The instantaneous voltage across the capacitor can be written as ΔvC = ΔVmax sin ωt = Imax XC sin ωt
As the frequency of the voltage source increases, the capacitive reactance decreases and the maximum current increases
As the frequency approaches zero, XC approaches infinity and the current approaches zero
  This would act like a DC voltage and the capacitor would act as an open circuit

## Slide 29
Consider the AC circuit in the Figure .The frequency of the AC source is adjusted while its voltage amplitude is held constant. The lightbulbwill glow the brightest at;
a)high frequencies
b)low frequencies
c)The brightness will be same at all frequencies.
Quick Quiz

## Slide 30: Example :A 2-F capacitor is connected to a 120-V, 60 Hz ac source. Neglecting resistance, what is the effective current through the coil?
Reactance:
XC = 1330 
ieff = 90.5 mA
Show that the peak current is imax = 128 mA
A
V
C = 2 F
120 V, 60 Hz

## Slide 31: Example
What are the peak and rms currents of a circuit if
C = 1.0 F and Vrms = 120 V. The frequency is 60.0 Hz.
XC = 1 = 1
2 fC 2(60 Hz)(1.0 X 10-6F)
XC = 2700 
Vrms = Vmax /√2
Vmax= Vrms√2
Vmax = (120 V)(√2) = 170 V
Imax = Vmax/XC
Imax = 170 V/2700 
Imax = 63 mA
Irms = Vrms/XC
Irms = 120 V/2700  = 44 mA

## Slide 32
An 8.00μF capacitor is connected to the terminals of a 60.0-Hz AC source whose rms voltage is 150 V. Find the capacitive reactance and the rms current in the circuit
Example A Purely Capacitive AC Circuit
What if the frequency is doubled? What happens to the rms current in the circuit?
If the frequency increases, the capacitive reactance decreases—just the opposite as in the case of an inductor. The decrease in capacitive reactance results in an increase in the current. Let us calculate the new capacitive reactance

## Slide 33: The RLC Series Circuit
The resistor, inductor, and capacitor can be combined in a circuit
The current and the voltage in the circuit vary sinusoidally with time

## Slide 34: The RLC Series Circuit, cont.
The instantaneous voltage would be given by Δv = ΔVmax sin ωt
The instantaneous current would be given by i = Imax sin (ωt - φ)
  φ is the phase angle between the current and the applied voltage
Since the elements are in series, the current at all points in the circuit has the same amplitude and phase

## Slide 35: i and v Phase Relationships – Graphical View
The instantaneous voltage across the resistor is in phase with the current
The instantaneous voltage across the inductor leads the current by 90°
The instantaneous voltage across the capacitor lags the current by 90°

## Slide 36: i and v Phase Relationships – Equations
The instantaneous voltage across each of the three circuit elements can be expressed as

## Slide 37: More About Voltage in RLC Circuits
ΔVR is the maximum voltage across the resistor and ΔVR = ImaxR
ΔVL is the maximum voltage across the inductor and ΔVL = ImaxXL
ΔVC is the maximum voltage across the capacitor and ΔVC = ImaxXC
The sum of these voltages must equal the voltage from the AC source
Because of the different phase relationships with the current, they cannot be added directly

## Slide 38: Phasor Diagrams
To account for the different phases of the voltage drops, vector techniques are used
Remember the phasors are rotating vectors
The phasors for the individual elements are shown

## Slide 39: Resulting Phasor Diagram
The individual phasor diagrams can be combined
Here a single phasor Imax is used to represent the current in each element
  In series, the current is the same in each element

## Slide 40: Vector Addition of the Phasor Diagram
Vector addition is used to combine the voltage phasors
ΔVL and ΔVC are in opposite directions, so they can be combined
Their resultant is perpendicular to ΔVR

## Slide 41: Total Voltage in RLC Circuits
From the vector diagram, ΔVmax can be calculated

## Slide 42: Impedance
The current in an RLC circuit is
Z is called the impedance of the circuit and it plays the role of resistance in the circuit, where
  Impedance has units of ohms
The right triangle in the phasor diagram can be used to find the phase angle, φ
The phase angle can be positive or negative and determines the nature of the circuit
Phase Angle

## Slide 43: Determining the Nature of the Circuit
If  is positive
  XL> XC (which occurs at high frequencies)
  The current lags the applied voltage
  The circuit is more inductive than capacitive
If  is negative
  XL< XC (which occurs at low frequencies)
  The current leads the applied voltage
  The circuit is more capacitive than inductive
If  is zero
  XL= XC
  The circuit is purely resistive

## Slide 44: Power in an AC Circuit
The average power delivered by the AC source is converted to internal energy in the resistor
  av = ½ Imax ΔVmax cos  = IrmsΔVrms cos 
  cos  is called the power factor of the circuit
We can also find the average power in terms of R
  av = I2rmsR

## Slide 45: Power in an AC Circuit, cont.
The average power delivered by the source is converted to internal energy in the resistor
No power losses are associated with pure capacitors and pure inductors in an AC circuit
  In a capacitor, during one-half of a cycle, energy is stored and during the other half the energy is returned to the circuit and no power losses occur in the capacitor
  In an inductor, the source does work against the back emf of the inductor and energy is stored in the inductor, but when the current begins to decrease in the circuit, the energy is returned to the circuit

## Slide 49
Calculate the average power delivered to the series RLC
circuit described in Example 33.5.

## Slide 50: Example
A circuit has R=25.0 , L = 30.0 mH, and C = 12.0 F. Calculate the impedance of the circuit if they are connected to a 90.0 V ac(rms), 500 Hz source. Also calculate the phase angle.
XL = 2fL
XL = 2(500 Hz)(0.030 H) = 94.2 
XC = 1/2fC
XC = 1/2(500 Hz)(12 X 10-6F) = 26.5 

## Slide 51
Z = √R2 + (XL – XC)2
Z = √(25.0)2 + (94.2  – 26.5 )2
Z = 72.2 
tan  = XL – XC
R
tan  = 94.2  – 26.5 
25.0 
 = 69.7o

## Slide 52
Calculate the rms current
V = IZ
Irms = Vrms/Z = 90.0 V/ 72.2 
Irms = 1.25 A
Calculate the voltage drop across each element
(VR)rms = IrmsR = (1.25 A)(25.0 ) = 31.2 V
(VL)rms = IrmsXL = (1.25 A)(94.2 ) = 118 V
(VC)rms = IrmsXC = (1.25 A)(26.5 ) = 33.1 V
Voltages do not add to 90.0 V (out of phase)
Calculate the power loss in the circuit
Pave = IrmsVrmscos
Pave = (1.25 A)(90.0 V)cos(69.7o)
Pave = 39.0 W

## Slide 53
Resonance occurs at the angular frequency ωo where the current has its maximum value
  To achieve maximum current, the impedance must have a minimum value
  This occurs when XL = XC
  The Resonance frequency
  Solving for the angular frequency gives

## Slide 54: Calculating Total Source Voltage

VR
VL - VC
VT
Source voltage
Treating as vectors, we find:
Now recall that:
VR = iR; VL = iXL; and VC = iVC
Substitution into the above voltage equation gives:

## Slide 55: Impedance in an AC Circuit

R
XL - XC
Z
Impedance
Impedance Z is defined:
Ohm’s law for ac current and impedance:
The impedance is the combined opposition to ac current consisting of both resistance and reactance.

## Slide 56: Example : A 60- resistor, a 0.5 H inductor, and an 8-F capacitor are connected in series with a 120-V, 60 Hz ac source. Calculate the impedance for this circuit.
A
60 Hz
0.5 H
60 
120 V
8 F
Thus, the impedance is:
Z = 122 

## Slide 57: Example : Find the effective current (Irms) and the phase angle for the previous example.
A
60 Hz
0.5 H
60 
120 V
8 F
XL = 226 XC = 332 
R = 60 Z = 122 
Irms = 0.985 A
Next we find the phase angle:

R
XL - XC
Z
Impedance
XL – XC = 226 – 332 = -106 
R = 60 

## Slide 58: Example :Find the phase angle for the previous example.
-106 

60 
Z
XL – XC = 226 – 332 = -106 
R = 60 
= -60.50
The negative phase angle means that the ac voltage lags the current by 60.50. This is known as a capacitive circuit.

## Slide 59: Example : Find the resonant frequency for the previous circuit example: L = .5 H, C = 8 F
Resonant fr = 79.6 Hz
At resonant frequency, there is zero reactance (only resistance) and the circuit has a phase angle of zero.
A
? Hz
0.5 H
60 
120 V
8 F
Resonance XL = XC

## Slide 60: Power in an AC Circuit
No power is consumed by inductance or capacitance. Thus power is a function of the component of the impedance along resistance:
In terms of ac voltage:
P =IrmsVrmscos 
In terms of the resistance R:
P = irms2R

R
XL - XC
Z
Impedance
P lost in R only
The fraction Cos is known as the power factor.

## Slide 61: Example : What is the average power loss for the previous example: V = 120 V,  = -60.50, Irms = 90.5 A, and R = 60 .
The higher the power factor, the more efficient is the circuit in its use of ac power.
A
? Hz
0.5 H
60 
120 V
8 F
Resonance XL = XC
P = i2R = (0.0905 A)2(60 
Average P = 0.491 W
The power factor is: Cos 60.50
Cos  = 0.492 or 49.2%

## Slide 62: Example:
A radio tunes in a station at 980 kHz at a capacitance of 3 F. What is the inductance of the circuit?
Xc=⅟ 2π f c
X C =1/2x3.14x980x103x3x10-6
ANS: 8.8 X 10 -9 H or 8.8 pH

## Slide 63
Homework
An AC power supply produces a maximum voltage ΔVmax = 100 V. This power supply is connected to a 24.0‐Ω resistor, and the current and resistor voltage are measured with an ideal AC ammeter and voltmeter, as shown in Figure P33.3. What does each meter read? Note that an ideal ammeter has zero resistance and that an ideal voltmeter has infinite resistance

## Slide 64
three lamps connected to a 120‐V AC (rms) household supply voltage. Lamps 1 and 2 have 150‐W bulbs; lamp 3 has a 100‐W bulb. Find the rms current and resistance of each bulb.

## Slide 65
2-A 20.0‐mH inductor is connected to a standard electrical outlet (ΔVrms = 120 V; f = 60.0 Hz). Determine the energy stored in the inductor at t = (1/180) s, assuming that this energy is zero at t = 0.
3- An inductor is connected to a 20.0‐Hz power supply that produces a 50.0‐V rms voltage. What inductance is needed to keep the instantaneous current in the circuit below 80.0 mA?
4- An inductor (L = 400 mH), a capacitor (C = 4.43 μF), and a resistor (R = 500 Ω) are connected in series. A 50.0‐Hz AC source produces a peak current of 250 mA in the circuit. (a) Calculate the required peak voltage ΔVmax. (b) Determine the phase angle by which the current leads or lags the applied voltage

## Slide 66
5- A series AC circuit contains the following components: R = 150 Ω, L = 250 mH, C = 2.00 μF and a source with ΔVmax = 210 V operating at 50.0 Hz. Calculate the (a) inductive reactance, (b) capacitive reactance, (c) impedance, (d) maximum current, and (e) phase angle between current and source voltage.
6- (a) What is the resistance of a light bulb that uses an average power of 75.0 W when connected to a 60.0-Hz power source having a maximum voltage of 170 V? (b) What If? What is the resistance of a 100-W