## Slide 1: Chapter 1: Introduction to Factory Automation
IE337 Automatic Control Systems
KSU - College of Engineering - IE Department
<number>

## Slide 2: 1.1 A hierarchical model of factory automation;
IE337 Automatic Control Systems
KSU - College of Engineering - IE Department
<number>
There are four levels of factory automation namely:
Machine level automation
Production line or work cell automation
Shop floor automation
Plant level automation .
Course objectives focus on 1st level.
Notes: <number>

## Slide 3: 1.2 Control system requirements and automatic control technologies
IE337 Automatic Control Systems
KSU - College of Engineering - IE Department
<number>
Fig. 1.1 Main types of control systems
Control system
Discrete control system
Continuous control system
Linear : e.g PID controller.
Nonlinear : e.g. MARC, Fuzzy.
Conditional: (Boolean – Expert system)
Sequential : (Temporal – Event)
Continuous: In this case the values to be controlled changes smoothly.
Discrete: The value to be controlled can be described as on or off, e.g. room light is switched on or off.
Linear systems: Linear systems can be represented using linear differential equations.
Non-linear systems: This is how the real world behaves, that will complicate the mathematical modeling of a system behavior.
Sequential systems: The logic controller depends not only on time but also on the previous logic condition

## Slide 4: Illustrated Example: Simple Elevator Problem
IE337 Automatic Control Systems
KSU - College of Engineering - IE Department
<number>
Discrete/sequential:
+ The elevator must move towards a floor when push button is used.
+ The elevator must open a door when it is at the floor level.
+ The elevator door must be closed before elevator travel.
+ The elevator door must suddenly open when the elevator door is jammed or
interrupted by the users.
+….etc.
Linear or continuous:
+ If desired level or position is updated, accelerate quickly towards the required
position
+ The elevator will slow-down or decelerate when approaching the new position.
+ …etc.

## Slide 5: Open loop systems
IE337 Automatic Control Systems
KSU - College of Engineering - IE Department
<number>
There is no link (feedback) between inputs and outputs
Controller has no feedback information on the evolution of outputs
Controller
Actuator
Controlled Process
Input Control Mechanical
Instruction Action Action
Input material Output
Figure 1.2: Block diagram of open loop control system.

## Slide 6: Closed loop systems
IE337 Automatic Control Systems
KSU - College of Engineering - IE Department
<number>
Inputs and outputs are connected with feedback loop
Controller has a feedback information on the evolution of outputs
Input
Instruction.
Output
e.g. Required
Furnace output
temperature input material
Feed back loop
Figure 1.3 Block diagram of closed loop control system.
controller
Actuator
Controlled
Process e.g. heating element power
Sensor, e.g. thermocouple

## Slide 7: Classification of systems and control systems
IE337 Automatic Control Systems
KSU - College of Engineering - IE Department
<number>
Controlled system
Controller
Linear
Non Linear
Continuous/Analog
Discrete

## Slide 8: Classification of control systems based on time and resolution
IE337 Automatic Control Systems
KSU - College of Engineering - IE Department
<number>
Time refers to how quickly it is necessary to update the information on the system state in order to affect adequate control. Furthermore, continuous updating of information is required when system states change rapidly.
Resolution refers to the precision with which it is necessary to measure the state of the system. For example, maintain the room temp +/- 1 deg, requires high resolution. Switching a lamp in room ON/OFF does not require high resolution because it is just binary information (on or off).
  Continuous control systems.
  This type of system monitors the system constantly and adjusts the parameters of the control system.
  The control system has closed loop plus short time response plus high resolution, e.g. Temp. control in heat treatment furnace problem
  Also possible: open loop (low resolution) plus short time response time. Bench mounted room heater problem.
  Discrete event control systems.
  In this control systems, the system often does not require time-critical control specifications or high-resolution measurement, but just the existence of closed loop control or even open loop control.
  e.g. Hooper filling problem can be open loop or closed loop system.

## Slide 9: Continuous and closed loop control system response system and its stability
IE337 Automatic Control Systems
KSU - College of Engineering - IE Department
<number>
Time
Steady state error
Under-shot
Over-shot
Steering time
Temperature error Er = (Tr-T)
Time
Temperature error Er = (Tr-T)
Time
(a) Stable response system
(b) Unstable system (oscillatory)
(c)Unstable system with divergence

## Slide 10: Discrete open and closed loop control systems – Illustrated Applications
IE337 Automatic Control Systems
KSU - College of Engineering - IE Department
<number>
Flow control valve
Sensor 1
Hopper Sensor 2
Figure 1.5 Hopper control through discrete event system.
Front position sensor Back position sensor
Permanent Magnet
rod cylinder
Pneumatic actuator
Figure 1. 6 Pneumatic cylinder position control problem.