## Slide 1: PLC: Programmable Logical Controller
<number>
CONTENTS
1. What is a PLC ?
2. Application examples
3. Inputs, Outputs and Commercial PLCs
4. Structure and Operating cycle of a PLC
5. How to choose a PLC ?
Notes: <number>

## Slide 2
What is a PLC?
Inputs
Outputs
PLC - Programmable Logic Controller متحكم منطقي مبرمج
A PLC is a digital (discrete) control system that continuously monitors the status of devices connected as inputs.
Based upon a user written program, stored in memory, it controls the status of devices connected as outputs.
PLC

## Slide 3
<number>
Inputs
Outputs & Power Supply
Communication
Ports (RS-485)
Schematic of a PLC

## Slide 4
Switches and Push buttons
Sensing Devices
  Limit Switches
  Photoelectric Sensors
  Proximity Sensors
Condition Sensors
  Pressure Switches
  Level Switches
  Temperature Switches
  Vacuum Switches
  Float Switches
Encoders
What are inputs?

## Slide 5
Valves
Motor Starters
Solenoids
Actuators
Control Relays
Horns & Alarms
Stack Lights
Fans
Counter/Totalizer
Pumps
Printers
What are outputs?

## Slide 6: Commercially Available PLC’s
<number>
A variety of PLCs are available on the market.
  Siemens Simatic PLCs
  Allen Bradley (AB) part of Rockwell Automation
  Modicon TSX PLCs
  …

## Slide 7: Siemens Simatic
Eng. R. L. Nkumbwa @ CBU 2010
<number>

## Slide 8: Allen Bradley
<number>

## Slide 9: Modicon
<number>

## Slide 10: An application example 1: Gate Control
<number>
PLC can:
  Sense a vehicle at the entrance or exit
  Open and close the gate automatically
Vehicle count is easily determined by programming a simple counter
Notes: <number>

## Slide 11: An application example 2: Conveyor System
<number>
PLC can be used to start/stop latching logic for motor control
Counters can be used for monitoring product amounts
Notes: <number>

## Slide 12
<number>
An application example 3:
Electric Drive (Motor) Control
2 push button switches (Start/Stop) are used to switch the motor on/off.
These switches are connected to the PLC using 2 discrete inputs.
One of the output ports (discrete output) of the PLC is used to switch the motor starter on/off, which will start/stop the electric motor.

## Slide 13
Old installations:
Wired relay logic
Modern installations:
Programmed logic
<number>
Why PLCs?

## Slide 14: Comparing traditional and programmable control systems
<number>
Notes: <number>

## Slide 15: Comparing traditional and programmable control systems
<number>
In traditional control, the switches S1, S2 and S3 must close for K1 to be turned on - the wiring makes the rule
In PLC systems, the program is written to perform the logic “when S1 is closed AND S2 is closed AND S3 is closed, THEN turn on K1” - the program makes the rule
It is
  Much simpler (complexity)
  Much easier (difficulty)
  Much more reliable (fault free)
  Much more effective (cost and time )
to change program then wiring!
Notes: <number>

## Slide 16: How does a PLC differ from a computer?
<number>
A computer is optimized for calculation and display tasks
A computer is more user focused and user friendly
Not necessarily real time
A PLC is more task/process oriented
A PLC is designed for (logic) control and regulation tasks
A PLC has to operate in real time
A PLC is well adapted to industrial environment
Notes: <number>

## Slide 17: Advantages of PLCs
<number>
PLCs have significant advantages over traditional control systems based on relay or pneumatics
They are cost-effective
They are flexible, reliable and compact
Can be used in every industry where automation is involved, from individual machines to whole processes
Notes: <number>

## Slide 18: What tasks do PLCs perform?
<number>
Logic control tasks: interlocking, sequencing, timing and counting (previously undertaken with relays or pneumatics)
A variety of calculation, communication and monitoring tasks
Notes: <number>

## Slide 19: Structure of a PLC
<number>
Notes: <number>

## Slide 20
<number>
Analog
Input
Analog
Ouput
Networking module
Modem
Structure of a PLC

## Slide 21: PLC main component: the processor
<number>
Notes: <number>

## Slide 22
PLC Operating Cycle: the scanning method
An “Executive” program tells the PLC to:
    Input Scan
       Scan the state of the Inputs
    Program Scan
       Processes the program logic
    Output Scan
       Activate/de-activate the outputs
    Housekeeping
       This step includes communications, Internal Diagnostics, etc.
The steps are continually repeated - processed in a loop
This program is stored in “non volatile” memory meaning that the program will not be lost if power is removed

## Slide 23: Data Flow in the PLC
<number>
Notes: <number>

## Slide 24
Quantity, Type and Location of I/O
  Number of Inputs and output points
  AC or DC voltage
  Analog or Discrete
  Concentrated or spread out (distributed)
Communication Requirements
  Protocol/Network used
  Devices to communicate with (HMI, other PLCs, etc)
Speed of Application
  Response time required (throughput) of the system
  How fast does the process change
What you need to know when specifying a PLC

## Slide 25
Control Architecture Philosophy
  Centralized Control, Distributed Control or combination
  Redundancy - CPUs, Power Supplies, etc
Programming Software
  IEC vs. 984
  Installed base / what is currently being used
User Logic
  Size and complexity of Program
  Feedback control used
  etc.
What you need to know when specifying a PLC