## Slide 1: Chapter 3
Number Systems and Codes In PLC

## Slide 2
3.1 Decimal Number System
Weight
Base

## Slide 3
3.1 Binary Number System
The binary system uses the number 2 as base and only two digits are used, 0 and 1.
In a digital circuit:
digit 1 or logic 1 is used for high voltage (e.g. +5Volts)
digit 0 or logic 0 is used for low voltage (e.g. 0Volts).
The Binary system is used in PLCs and computer systems.
Decimal number | Binary number
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
10 | 1010
11 | 1011
12 | 1100
13 | 1101
14 | 1110
15 | 1111

## Slide 4
3.2 Binary Number System
Weight
Base
Data in a PLC or a Computer System:
Bit: 0 or 1
Byte: 8 bits
Word: 2 Bytes = 16 bits
Double Word: 4 Bytes
least significant bit (LSB)
Most significant bit (MSB)
Lower Byte
Higher Byte
Binary

## Slide 5
3.2 Binary Number System

## Slide 6
3.3 Octal Number System
Weight
Base

## Slide 7
3.3 Octal Number System

## Slide 8
3.4 Hexadecimal Number System
The hexadecimal (Hex) numbering system provides even shorter notation than octal. Hexadecimal uses a base of 16. It employs 16 digits: number 0 through 9, and letters A through F, with A through F substituted for numbers 10 to 15, respectively, see Table 3.3.
Hexadecimal numbers can be expressed as their decimal equivalents by using the sum of weights method, as shown in the following example:

## Slide 9
3.4 Hexadecimal Number System

## Slide 10
3.5 BCD (Binary Coded Decimal) Number System
The BCD system provides a convenient means to handle large numbers that need to be input to or output from a PLC or PC computer.
The BCD system represents decimal numbers as patterns of 1’s and 0’s. This system provides a means of converting a code readily handled by humans (decimal) to code readily handled by the equipment (binary).
The BCD system uses 4 bits to represent each decimal digit. The 4 bits used are the binary equivalents of the number 0 to 9.
In BCD system, the largest decimal number that can be displayed by any four digits is 9.

## Slide 11
3.5 BCD (Binary Coded Decimal) Number System

## Slide 12
Problems