## Slide 1
10.
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Part III
Datalink Layer

## Slide 2
10.
Data link layer duties

## Slide 3
10.
Chapter 10 :Error Detection and Correction
Chapter 11 Data Link Control and Protocols
Chapter 12 Multiple Access
Chapter 13 Wired LANs: Ethernet
Chapter 15 Connecting LANs, Backbone networks and virtual LAN

## Slide 4
10.
Chapter 10
Error Detection and Correction

## Slide 5
10.
Network must be able to transfer data from one device to another with acceptable accuracy.
Data can be corrupted during transmission. For reliable communication, errors must be detected and corrected.
Note

## Slide 6
10.
Single-Bit Error
Burst Error
Types of Error

## Slide 7
10.
In a single-bit error, only one bit in the data unit has changed. (0 to 1 or 1 to 0)
Does the Single-bit error happen in parallel or serial transmission ? Why ?
Single-bit error most likely to occur in parallel transmission (eg. between CPU and memory)
Single-bit error

## Slide 8
10.
Burst burst error means that 2 or more bits in the data unit have changed
Burst error does not necessarily mean that the errors occur in consecutive bits
Most likely to happen in a serial transmission
Number of bits affected depends on the data rate and noise duration
If the data is sent at 1 kbps, a noise of 1/100 s can affect 10 bits.
If the data is sent at 1 Mbps, a noise of 1/100 s can affect 10000 bits.
error
Burst error

## Slide 9
10.
ERROR DETECTION
Error detection uses the concept of redundancy, which means adding extra bits for detecting errors at the destination.

## Slide 10
10.
Error can be detected by using block coding:
Dived the message into blocks, each of k bits, called datawords.
Add r redundant bits to each block to make the length
n = k + r.
The resulting n bits blocks are called codewords
ERROR DETECTION

## Slide 11
10.
Error Detection methods

## Slide 12
10.
parity Check
The most common and least expensive
Simple or Two Dimensional
simple parity check
a parity bit (extra bit) is added to every data unit so that the total number of 1s is even or odd (for odd-parity).

## Slide 13
10.
Figure 10.10 Encoder and decoder for simple parity-check code

## Slide 14
10.
Error Detection methods
Suppose the sender wants to send the word world. In ASCII the five characters are coded as
W o r l d
1110111 1101111 1110010 1101100 1100100
The following shows the actual bits sent
11101110 11011110 11100100 11011000 11001001

## Slide 15
10.
Error Detection methods
Now suppose the word world in Example 1 is received by the receiver without being corrupted in transmission.
11101110 11011110 11100100 11011000 11001001
The receiver counts the 1s in each character and comes up with even numbers:
(6, 6, 4, 4, 4). The data are accepted.

## Slide 16
10.
Error Detection methods
Now suppose the word world in Example 1 is corrupted during transmission.
11111110 11011110 11101100 11011000 11001001
The receiver counts the 1s in each character and comes up with even and odd numbers:
(7, 6, 5, 4, 4).
The receiver knows that the data are corrupted, discards them, and asks for retransmission.

## Slide 17
10.
Performance of Simple Parity Check
We have an even-parity data unit where the total number of 1s, including the parity bit, is 6: 1000111011.
If any 3 bits changed, the resulting parity will be odd and the error will be detected:
    1111111011: “ 9 ones”
    0110111011: “7 ones”
    1100010011: “ 5 ones”
    The same holds true for any odd number of errors
Example:

## Slide 18
10.
Performance of Simple Parity Check
Suppose 2 bits are changed:
    1110111011: ”8 ones”
    1100011011: ”6 ones”
    The number of 1s in the data unit is still even .The same holds true for any even number of errors
    The parity checker cannot detect errors when number of bits changed is even. The change cancel each other and the data unit will pass a parity check even though the data unit is damaged.
Example:

## Slide 19
10.
Simple parity check can detect all single--bit error. It can detect burst errors only if the total number of errors in each data unit is odd.
Note

## Slide 20
10.
Two-dimensional parity
Calculate the parity bit for each data unit, then organize them into table (rows and columns)
Calculate the parity bit for each column and create a new row (column parity)
A redundant row of bits is added to the whole block.

## Slide 21
10.
In two-dimensional parity check, a block of bits is divided into rows and a redundant row of bits is added to the whole block.
Note

## Slide 22
10.
Figure 10.11 Two-dimensional parity-check code
Suppose the following block is sent:
10101001 00111001 11011101 11100111 10101010
However, it is hit by a burst noise of length 8, and some bits are corrupted.
10100011 10001001 11011101 11100111 10101010
When the receiver checks the parity bits, some of the bits do not follow the even-parity rule and the whole block is discarded.( see next slide)

## Slide 23
10.
Figure 10.11 Two-dimensional parity-check code

## Slide 24
10.
Two-dimensional Performance
Increases the likelihood of detecting burst errors.
A redundancy of n-bits can detect a burst error of n bits
A burst error of more than n bits is also detected with a very high probability
One pattern of errors still elusive: If 2 bits in one data unit are damaged and two bits in exactly the same position in anther data unite are also damaged. The error will not be detected

## Slide 25
10.
Figure 10.11 Two-dimensional parity-check code

## Slide 26
10.
Figure 10.11 Two-dimensional parity-check code

## Slide 27
10.
Cyclic Redundancy Check CRC
Uses Module-2 Binary division

## Slide 28
10.
Two-dimensional Performance
In CRC generator (At sender)
A string of n 0s is appended to the data unit
The number n is 1 less than the number of bits in the divisor
Divide the data word plus appended zeros by the divisor
Use module-2 binary division:
  There is no carry when you add or subtract two digits in a column
  Addition and subtraction gives the same results
  This means: you can use XOR operation for both Addition and subtraction
The remainder resulting from the division is the CRC
The CRC of n bits replaces the appended 0s at the end of the data unit.
Appending CRC to the end of the data must make resulting bit sequence divisible by the divisor

## Slide 29
10.
Figure 10.15 Binary division in a CRC generator

## Slide 30
10.
Two-dimensional Performance
In CRC generator (At receiver)
After receiving the data appended with the CRC, it does the same module -2 division
If the remainder is all 0s the CRC dropped and the data are accepted ( the data is correct)
If the remainder is not equal zero, the received stream of bits is discarded and data must be resent ( the data is corrupted)

## Slide 31
10.
Figure 10.15 Division in CRC encoder

## Slide 32
10.
Figure 10.15 Division in CRC encoder

## Slide 33
10.
Figure 10.16 Division in the CRC decoder for two cases

## Slide 34: Using Polynomials
The divisor in CRC generator is most often represented not as string of 1s and 0s, but as an algebraic polynomial.
We can use a polynomial to represent a binary word.
Each bit from right to left is mapped onto a power term.
The rightmost bit represents the “0” power term. The bit next to it the “1” power term, etc.
If the bit is of value zero, the power term is deleted from the expression.
10.

## Slide 35
10.
Figure 10.21 A polynomial to represent a binary word

## Slide 36
10.
Figure 10.22 CRC division using polynomials

## Slide 37
10.
In a cyclic code,
If s(x) ≠ 0, one or more bits is corrupted.
If s(x) = 0, either
a. No bit is corrupted. or
b. Some bits are corrupted, but the decoder failed to detect them.
Note

## Slide 38
10.
CRC Performance
CRC is very effective error detection method:
CRC Can detect all burst errors that affect an odd number of bits.
2. CRC Can detect all burst errors of length less than or equal to the degree of the polynomial
3. CRC can detect, with very high probability, burst errors of length greater than the degree of the polynomial.

## Slide 39
10.
Figure 10.22 CRC division using polynomials
The CRC-12 x12 + x11 + x3 + x + 1 which has a degree of 12, will detect
1.all burst errors affecting an odd number of bits,
2.will detect all burst errors with a length less than or equal to 12, and
3. will detect, 99.97 percent of the time, burst errors with a length of 12 or more.

## Slide 40
10.
10-5 CHECKSUM
The last error detection method we discuss here is called the checksum. The checksum is used in the Internet by several protocols although not at the data link layer.(Checksum used for example in network layer ). However, we briefly discuss it here to complete our discussion on error checking

## Slide 41
10.
CHECKSUM

## Slide 42
10.
Data unit and checksum
The sender follows these steps:
1.The unit is divided into k sections, each of n bits.
2.All sections are added using one’s complement to get the sum.
3.The sum is complemented and becomes the checksum.
4.The checksum is sent with the data
The receiver follows these steps:
1.The unit is divided into k sections, each of n bits.
2.All sections are added using one’s complement to get the sum.
3.The sum is complemented.
4.If the result is zero, the data are accepted: otherwise, rejected

## Slide 43
10.
Example
Suppose the following block of 16 bits is to be sent using a checksum of 8 bits.
10101001 00111001
The numbers are added using one’s complement
1 0 1 0 1 0 0 1
0 0 1 1 1 0 0 1
Sum 1 1 1 0 0 0 1 0
Checksum 00011101
The pattern sent is 10101001 00111001 00011101

## Slide 44
10.
Example 7
Now suppose the receiver receives the pattern sent in Example 7 and there is no error.
10101001 00111001 00011101
When the receiver adds the three sections, it will get all 1s, which, after complementing, is all 0s and shows that there is no error.
1 0 1 0 1 0 0 1
0 0 1 1 1 0 0 1
0 0 0 1 1 1 0 1
Sum 1 1 1 1 1 1 1 1
Complement 00000000 means that the pattern is OK.

## Slide 45
10.
Example
Now suppose there is a burst error of length 5 that affects 4 bits.
10101111 11111001 00011101
When the receiver adds the three sections, it gets
1 0 1 0 1 1 1 1
1 1 1 1 1 0 0 1
0 0 0 1 1 1 0 1
Partial Sum 1 1 1 0 0 0 1 0 1
Carry 1
Sum 1 1 0 0 0 1 1 0
Complement 00111001 the pattern is corrupted.

## Slide 46
10.
Performance of checksum
Almost detects all errors involving odd numbers of bits or even.
if one or more bits of a segment are damaged and the corresponding bit or bits of opposite value in a second segment are also damaged,
then the sum of columns will not change. Receiver will not be able to detect the error