## Slide 1
10.
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Part III
Datalink Layer
Notes: <number>

## Slide 2
10.
Chapter 10 :Error Detection and Correction
Chapter 11 Data Link Control and Protocols
Chapter 12 Multiple Access
Chapter 13 Wired LANs: Ethernet
Chapter 15 Connecting LANs, Backbone networks and virtual LAN

## Slide 3
10.
Chapter 12
Multiple Access

## Slide 4
10.
Multiple-access protocols
When more than two nodes send at the same time , the transmitted frames collide.
All collide frames are lost and the bandwidth of the broadcast channel will be wasted.
We need multiple –access protocol to coordinate access to multipoint or broadcast link (Nodes or stations are connected to or use a common link)
Multiple access protocols are needed in wire and wireless LANs and satellite networks

## Slide 5
10.
Multiple-access protocols

## Slide 6
10.
Multiple-access protocols
Problem of controlling the access to the medium is similar to the rules of speaking in an assembly :
•Given everyone a chance to speak
•Don’t speak until you are spoken to
•Don’t monopolize the conversation
•Raise your hand if you have a question
•Don’t interrupt when someone speaking

## Slide 7
10.
Multiple-access protocols

## Slide 8
10.
RANDOM ACCESS
In random access or contention methods, no station is superior to another station and none is assigned the control over another. No station permits , or does not permit, another station to send .At A each instance, a station that has data to send use a procedure defined by the protocol to make a decision on whether or not to send. This decision depends on the state of the medium(idle or busy)
Random access Methodes:
ALOHA
Carrier Sense Multiple Access ; CSMA
Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA)

## Slide 9
10.
RANDOM ACCESS
Each station has the right to the medium without being controlled by any other station.
Two features gives the method its name:
There is no schedule time for a station to transmit: transmission is random among stations
Stations compete with one another to access the medium Contention method.
Collision: an access conflict occurs when more than one station tries to send, as a result the frame will be either destroyed or modified.

## Slide 10
10.
Evolution of random-access methods
ALOHA: uses MA( Multiple Access) No carrier sense
CSMA: Carrier Sense Multiple Access
CSMA/CD: Collision Detection
CSMA/CA Collision Avoidance

## Slide 11
10.
Pure ALOHA
The earliest random access method developed at the Univ. of Hawaii in the early 1970s
Designed for a radio (wireless) LAN
Simple method. Each station sends a frame whenever it has a frame to send.
Since there is only one channel to share, there is the possibility of collision between frames from different stations.

## Slide 12
10.
Pure ALOHA
Each station sends a frame whenever it has a frame to send.
It relies on acknowledgments from the receiver.
If the ACK dose not arrive after a time-out period, the station resend the frame.

## Slide 13
10.
Carrier sense Multiple Access(CSMA)
Sense the carrier before transmit :“listen before you talk”
CSMA can reduce the possibility of collision, but it can not eliminate it because of the propagation delay (a station may sense the medium and find it idle, only because the first bit of a frame sent by another station has not been received)

## Slide 14
10.
Carrier Sense Multiple Access collision detection (CSMA/CD)
Listen-while-talk ” protocol. A host listens even while it is transmitting, and if a collision is detected, stops transmitting

## Slide 15
10.
collision detection
How the station detects a collision?
Detecting voltage level on the line
Detecting energy level .
Energy in channel can have three values: zero, normal, and abnormal.
at zero level, the channel is idle
At the normal level, a station has successfully captured the channel and is sending its frame.
At the abnormal level, there is a collision and the level of the energy twice the normal level.

## Slide 16
10.
In controlled access , the stations consult one another to find which station the right to send . A station cannot send unless it has been authorized by other stations . We discuss three popular controlled access methods.
2 --CONTROLLED ACCESS
Controlled Access methods
Reservation
Polling
Token Passing

## Slide 17
10.
Reservation access method
A station needs to make a reservation before sending data.
Time is divided into intervals
A reservation frame proceeds each time interval
Number of stations and number of mini-slots in the reservation frame are equal
Each time slot belongs to a particular station
If there are N stations in the system, there are exactly N reservation mini-slots in the reservation frame

## Slide 18
10.
Polling access method
Devices are designated as a Primary station and secondary station.
All data exchange must go through the primary station
Primary station controls the link and initiates the session; the secondary station follow its instructions.
Two functions: polls and select
Poll: If the primary wants to receive data, it asks the secondary if they have anything to send.
Select: if the primary wants to send data, it tells the secondary to get ready to receive data

## Slide 19
10.
Polling access method
The select function is used when the primary has frames to send.
The primary creates and transmits a select (SEL) frame.
SEL alerts the secondary to the upcoming transmission
The primary waits for ACK to send the data

## Slide 20
10.
Polling access method
When the primary is ready to receive data, it must ask (Poll) each device in turn if it has anything to send.
When the first secondary is approached, it responds either with a NAK frame if it has nothing to send or with data if it does.
If the response is NAK, the primary polls the next secondary.
If it receives data, it sends ACK frame.

## Slide 21
10.
Token Passing method
In the token-passing, the stations are organized in a logical ring.
For each station there is a predecessor and a successor
predecessor is the station which is logically before the station in the ring
The successor is the station which is logically after the station in the ring
The current station is the one that accessing the channel now.
How is The right to access channel passed from one station to another?

## Slide 22
10.
Token Passing method
Station is authorized to send data when it receives a special frame called a token
Stations are arranged around a ring.
When no data are being sent, a token circulates the ring.
If a station needs to send data, it waits for the token.
The station captures the token and sends one or more frames (as long as it has frames to send or the allocated time has not expired), and finally it releases the token to be used by next station ( successor).
The maximum time any station can hold the token is limited.
Since there is only one token, only one station transmits at a time, and collisions never occur.

## Slide 23
10.
Token Passing method
Token management is needed for this access method:
Stations must be limited in the time they can have possession of the token
the token must be monitored to ensure it has not been lost or destroyed( if the station that is holding the token fails, the token will disappear from the network)
Assign priorities to the stations , to make low-priority stations release the token to high priority stations.
Stations do not have to be physically connected in a ring ; the ring can be logical one

## Slide 24
10.
Token Passing method
Logical ring and physical topology in token-passing access method

## Slide 25
10.
Channelization is a multiple -access method in which the available bandwidth of a link is shared in time, frequency ,or through code, between different stations .
channelization protocols:
Frequency-Division Multiple Access (FDMA)
Time-Division Multiple Access (TDMA)
Code-Division Multiple Access (CDMA)
3-CHANNELIZATION ACCESS