## Slide 1
Part III
Datalink Layer

## Slide 2
Chapter 10 :Error Detection and Correction
Chapter 11 Data Link Control and Protocols
Chapter 12 Multiple Access
Chapter 13 Wired LANs: Ethernet
Chapter 15 Connecting LANs, Backbone networks and virtual LAN

## Slide 3
Chapter 13
Wired LANs: Ethernet

## Slide 4
10.
IEEE STANDARDS
In 1985 ,the Computer Society of the IEEE started a project, called Project 802, to set standards to enable intercommunication a among equipment from a variety of manufacturers. Project 802 is a way of specifying functions of the physical layer and the data link layer of major LAN protocols.
Topics discussed in this section:
Data Link Layer
Physical Layer

## Slide 5
IEEE standard for LAN
IEEE divided the Data link layer into two sublayer:
upper layer : logical link control (LLC); flow and error control.
Lower sublayer : Multiple access (MAC); media access control.
Multiple access (MAC) :for resolving access to the shared media.
If channel is dedicated ( point to point) we do not need the (MAC); sublayer.

## Slide 6
IEEE standard for LAN

## Slide 7
LLC (Logical link control)and MAC (Media Access Control)
In IEEE project 802, flow control , error control, and part of the framing duties are collected into one sublayer called the logical link control (LLC )
LLC provides one single data link control for all IEEE LANs.
IEEE project 802 has created a sublayerMAC that defines the specific access method for each LAN. In contrast to the LLC, MAC contains a number of distinct modules: each defines the access method and the framing format specific to the corresponding LAN protocol
For example:
CSMA/CDas media access method for EthernetLANs.
Token passing method for Token Ring and Token Bus LANs
Framing is handled in both the LLC and MAC sublayer.

## Slide 8
Physical layer
Physical layer is dependent on the implementation and type of the physical media used.
IEEE define detailed specifications for each LAN implementation.
For example, although there is only one MAC sublayer for Standard Ethernet( CSMA/CD), there is a different physical layer specifications for each Ethernet implementations.

## Slide 9
ETHERNET IEEE
It is the dominant LAN technology.
Cheap
First widely used LAN technology
Simpler and cheaper than token LANs
Kept up with speed race: 10, 100, 1000 Mbps

## Slide 10
ETHERNET Evolution

## Slide 11
ETHERNET Evolution
The MAC sublayer governs the operation of the random access method
Standard Ethernet uses CSMA/CD
Ethernet dose not provide any mechanism for acknowledging received frames( unreliable medium).
Acknowledgments must be implemented at the higher layer.
It also frames data received from the upper layer and passes them to the physical layer.

## Slide 12
ETHERNET
The MAC sublayer
The MAC sublayer governs the operation of the random access method
Standard Ethernet uses CSMA/CD
Ethernet dose not provide any mechanism for acknowledging received frames( unreliable medium).
Acknowledgments must be implemented at the higher layer.
It also frames data received from the upper layer and passes them to the physical layer.

## Slide 13
ETHERNET frame
The Ethernet frame contains seven fields:
Preamble:
7bytes (56 bits); Alternating 0s and 1s, used for synchronizing
Start Frame Delimiter (SFD):
10101011 indicates the start of the frame.
Last two bits (11) alerts that the next field is destination address.
preamble and SFD are added at the physical layer and is not formally part of the frame

## Slide 14
ETHERNET frame
DA: Destination address
SA: Source Address
Length/Type:
Define the upper-layer protocol using the MAC frame. OR define the number of bytes in the data filed.
Data: minumum: 46 and maximum : 1500 bytes
CRC: error detection information:CRC-32

## Slide 15
10.
Frame length:
Minimum: 64 bytes (512 bits)
Maximum: 1518 bytes (12,144 bits
Note

## Slide 16
ETHERNET frame
Minimum frame length restriction(64 bytes) is required for the correct operation of CSMA/CD.
Min data length =64 -18 (6+-6+2+4) = 46 bytes
If the upper-layer packet is less than 46 bytes, padding is added to make up the difference.
Maximum length restriction; two historical reasons:
Memory was very expensive when Ethernet was designed.
Prevents one station from monopolizing the shared medium, blocking other stations that have data to sent.
Max data length =1518-18= 1500 bytes.

## Slide 17
Ethernet address in hexadecimal notation
Each station (PC or printer) has a network interface card (NIC) which provides the station with a 6-byte [48 bits] physical address (MAC adress)
It is written in hexadecimal notation, with a colon between the bytes

## Slide 18
Source address is always a unicast address –the frames comes from only one station.
Destination address can be:
unicast: defines only one recipient; one to one
multicast: a group of addresses; one to many
Broadcast: the recipients are all the stations on the LAN

## Slide 19
10.
The least significant bit of the first byte defines the type of address.
if the bit is 0, the address is unicast; otherwise, it is multicast.
The broadcast destination address is a special case of the multicast address in which all bits are 1s.
Note

## Slide 20
Define the type of the following destination addresses:
a.4A:30:10:21:10:1A
b.47:20:1B:2E:08:EE
c.FF:FF:FF:FF:FF:FF
Solution
To find the type of the address, we need to look at the second hexadecimal digit from the left.
If it is even, the address is unicast. If it is odd, the address is multicast .If all digits are F’s, the address is broadcast. Therefore, we have the following:
This is a unicast address because A in binary is 1010.
this is a multicast address because 7 in binary is 0111.
This is a broadcast address because all digits are F’s.
Example 1

## Slide 21
Show how the address 47:20:1B:2E:08:EEis sent out on line.
Solution
The address is sent left-to-right, byte by byte; for each byte, it is sent right-to-left( LSB first), bit by bit, as shown below
left-to-right :47→20→1B→2E→08→ EE
47 is 0100 0111 right -to-left 1110 0010
Example 2