## Slide 1
10.
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Part IV
Network layer

## Slide 2
10.
Chapter 19 :
Network Layer
Logical Addressing

## Slide 3
IPv4 ADDRESSES
An IPv4 address is a 32-bit address that uniquely
and universally defines the connection of a device
(for example, a computer or a router) to the Internet
Topics discussed in this section :
Address Space
Notations
Classful Addressing
Classless Addressing
Network Address Translation (NAT)

## Slide 4
An IPv4 address is 32 bits long
IPv4 ADDRESSES

## Slide 5
Two devices in the Internet can never have the same
address at the same time.
An address may be assigned to a device for a time period and then taken away and assigned to another device.
If a device operating at the network layer (e.g. router) has m connections to the Internet, it needs to have m IP address.
The IPv4 addresses are unique and universal.
IPv4 ADDRESSES

## Slide 6
IPv4 ADDRESSES
IPV4 has an address space: is the total number of
addresses used by the protocol.
If a protocol uses N bits to define an address, the address space is 2 n .
IPv4 uses 32-bit addresses:
The address space=232 =4,294,967,296 ( more than 4
billion)
This means, if there were no restrictions, more than 4
billion devices could be connected to the Internet.
IPv6 uses 128 bit-addresses

## Slide 7
IPv4 ADDRESSES
There are two prevalent notations to show an IPv4 address:
1. Binary notation:
Address is displayed as 32 bits.
Each octet is often referred to as byte.
IPv4 address referred to as 32-bit address or 4-byte address
Example:
01110101 10010101 00011101 00000010

## Slide 8
IPv4 ADDRESSES
Dotted-decimal notation:
More compact and easier to read
Written in decimal form with a decimal point( dot)
separating the bytes.
Example: 117.149.29.2
Each decimal value range from 0 to 255
Example:
Dotted-decimal notation and binary notation for an IPv4
address

## Slide 9
10.
IPv4 ADDRESSES
Change the following IPv4 addresses from binary
notation to dotted-decimal notation.
Example 1
10000001 00001011 00001011 11101111
11000001 10000011 00011011 11111111
Solution
We replace each group of 8 bits with its equivalent
decimal number (see Appendix B) and add dots for
separation.

## Slide 10
IPv4 ADDRESSES
Change the following IPv4 addresses from dotted-decimal
notation to binary notation.
Example 2
111.56.45.78
221.34.7.82
Solution
We replace each decimal number with its binary
equivalent

## Slide 11
IPv4 ADDRESSES
Find the error, if any, in the following IPv4 addresses.
Example 3
111.56.045.78
221.34.7.8.20
75.45.301.14
11100010.23.14.67
Solution
a. There must be no leading zero (045).
b. There can be no more than four numbers.
c. Each number needs to be less than or equal to 255.
d. A mixture of binary notation and dotted-decimal
notation is not allowed.

## Slide 12
IPv4 ADDRESSES
In classful addressing, the address space is divided into five
classes: A, B, C, D, and E.
We can find the class of an address in:
Binary notation: the first few bits define the class
Decimal-dotted notation: the first byte define the class

## Slide 13
IPv4 ADDRESSES
In classful addressing, the address space is divided
into five classes: A, B, C, D, and E.
Addresses in Classes A, B and C are uniast addresses
A host needs to have at least one unicast address to be able to send packet (Source).
Addresses in Class D are for multicast address: used only for destination.
Addresses in class E are reserved

## Slide 14
IPv4 ADDRESSES
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Example 4
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 15
IPv4 ADDRESSES
NetId and HostId
The address is divided into Netid and Hostid.
These part are of varying lengths, depending on the class.
Dose not apply to classes D and E

## Slide 16
IPv4 ADDRESSES

## Slide 17
IPv4 ADDRESSES
Class A address: designed for large organizations with a
large number of attached hosts or routers. (most of the
addresses were wasted and not used)
Class B address: designed for midsize organizations with ten
of thousands of attached hosts or routers( too large for many
organizations)
Class C address: designed for small organizations with a
small number of attached hosts or routers (too small for
many organizations)
Class D address: designed for multicasting. (waste of
addresses)
Class E address: reserved for future use (waste of addresses)

## Slide 18
IPv4 ADDRESSES
One problem is that each class is divided into fixed
number of blocks with each block having a fixed size
In classful addressing, a large part of the available addresses were wasted.

## Slide 19
Classful Addressing: Classes and Blocks
Mask (default mask)
Help us to find the NetId and HostId
Mask: 32-bit made of 1s followed by 0s.
Dose not apply to classes D and E.
CIDR(Classless Interdomain Routing): used to show the
mask in the form /n (n=8,16,24)
Class | Binary | Dotted-decimal | CIDR
A | 11111111 00000000 00000000 00000000 | 255.0.0.0 | /8
B | 11111111 11111111 00000000 00000000 | 255.255.0.0 | /16
C | 11111111 11111111 11111111 00000000 | 255.255.255.0 | /24

## Slide 20
Classful Addressing: Network address
The network address is an address that define the
network itself to the reset of the internet
The network address has the following properties:
1. All hostid bytes are 0’s
2. It is the first address in the block
3. It cannot be assigned to a host
4. Given the network address, we can find
the class of the address

## Slide 21
Classful Addressing: Network address
Find the network address for the following:
a. 132.6.17.85
b. 23.56.7.91
a. The class is B. The first 2 bytes defines the Netid. We can find the network address by replacing the hostid bytes (17.85) with 0s.
Therefore, the network address is 132.6.0.0
b. The class is A. Only the first byte defines the Netid. We can find the network address by replacing the hostid bytes (56.7.91) with 0s.
Therefore, the network address is 23.0.0.0

## Slide 22
Classful Addressing: Network address

## Slide 23
Classful addressing : subnetting
IP addresses are designed with two levels of hierarchy.

## Slide 24
A network with two levels of hierarchy

## Slide 25
Classful Addressing:
If an organization was granted a large block in classes A or B
It could divide the addresses into several contiguous groups
and assign each group to smaller networks ( subnets)
It increases the number of 1s in the mask
Number of 1s in a subnet mask is more than the number of 1s
in the corresponding mask.
To make a subnet mask , we change some of the leftmost 0s in
mask to 1s
The number of subnets is determine by the number of extra1s.
If the number of extra 1 is n, the number of subnets is 2 n.
If the number of subnets is N, the number of extra 1s is log2N
Subnetting

## Slide 26
Classful Addressing: Subnet Mask
Class B address
mask : 255.255.0.0 or /16
For 4 subnets : (log 2 4 = 2; need 2-extra bits )
Subnet mask: 255.255. 192.0 or /18
For 8 subnets: (log 2 8 = 3; need 3-extra bits )
subnet mask : 255.255.224.0 or /19
11111111 11111111 | 00000000 00000000
11111111 11111111 | 11 | 000000 00000000
11111111 11111111 | 111 | 00000 00000000

## Slide 27
Classful Addressing:
Example:
A router receives a packet with destination address 190.240.33.91. Show how it finds the network and the subnetwork address toroute the packet. Assume the subnet mask is /19
The router follows steps:
1. The router looks at the first byte of the address to find the
class. It is class B.
2. The mask for class B is (/16)The router ANDs this mask
with the address to get the network address :190.240.0.0.
3. The router applies the subnet mask (/19) to the address,
190.240.33.91.
190.240.001 00001. 91
The subnet address is 190.240.32.0.
4. The router looks in its routing table to find how to route the
packet to this destination
Subnetting

## Slide 28
Classful Addressing
Huge demand for midsize blocks.
Although class A and B addresses are almost depleted, class C addresses are still available( size of block= 256 address did not satisfy the needs).
In supernetting, an organization can combine several class C blocks to create a larger range of addresses.
Several networks are combined to create a supernetwork (
supernet). e.g. Organization needs 1000 address can be granted 4 contiguous class C blocks to create one supernetwork.
Decreases the number of 1s in the mask. E.g. The mask changes from /24 to /22 for 4 class C block
supernetting

## Slide 29
Classful Addressing: supernetting
Address Depletion
Near depletion of the available address because of the fast growth of the Internet.
Run out of classes A and B address.
Classes C block is too small for most mid size organizations.
Solution: Classless addressing
Notes: <number>
Layla Hajr

## Slide 30
Classless Addressing address Block
To overcome address depletion.
no classes, but the address are still granted in blocks.
The size of the block( the number of addresses) varies based on the nature and size of the entity.
Household: 2 addresses
Large organization: thousands of addresses.
ISP: thousands or hundreds of thousands based on the number of customers it may serve.
Notes: <number>
Layla Hajr

## Slide 31
Classless Addressing address Block
Restriction
The Internet Authorities impose three restrictions:
The address in a block must be contiguous, one after another.
The number of addresses in a block must be a power of 2 ( 1,2,4,8,…)
The first address must be evenly divisible by
the number of addresses..
Notes: <number>
Layla Hajr

## Slide 32
Example :
The Figure in the next slide shows a block of
addresses, in both binary and dotted-decimal
notation, granted to a small business that needs 16 addresses.
Notes: <number>
Layla Hajr

## Slide 33
We can see that the restrictions are applied to this block.:
• The addresses are contiguous.
• The number of addresses is a power of 2 (16 = 24)
• the first address is divisible by 16. The first address,
when converted to a decimal number( use base 256), is 3,440,387,360, which when divided by 16 results in 215,024,210.
Notes: <number>
Layla Hajr

## Slide 34
Mask: /n
32- bit
can take any value from 0 to 32, for ex /24
The n leftmost bits are 1s
32-n rightmost bits are 0s
In IPv4 addressing, a block of addresses can be defined as
x.y.z.t /n
in which x.y.z.t defines one of the addresses
and the /n defines the mask.
Example: 172.31.16.42/26
Classless Addressing Mask
Notes: <number>
Layla Hajr

## Slide 35
The address and the /n notation define the
whole block:
First address
Last address
Number of address
Classless Addressing Mask
Notes: <number>
Layla Hajr

## Slide 36
Classless Addressing
The first address in the block ( network
address) can be found by setting the
Rightmost 32 − n bits to 0s.
Notes: <number>
Layla Hajr

## Slide 37
Classless Addressing
Example :
A block of addresses is granted to a small organization.
We know that one of the addresses is 205.16.37.39/28.
What is the first address in the block?
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
205.16.37. 0010 0111
If we set 32−28 rightmost bits to 0, we get
205.16.37. 0010 0000
or
205.16.37.32.
This is actually the block shown in example 8
Notes: <number>
Layla Hajr

## Slide 38
Classless Addressing
The first address in a block is
normally not assigned to any device;
it is used as the network address that
represents the organization
to the rest of the world.
Notes: <number>
Layla Hajr

## Slide 39
Classless Addressing
The last address in the block can be
found by setting the rightmost 32 − n bits to 1s.
Notes: <number>
Layla Hajr

## Slide 40
Classless Addressing
Find the last address for the block in Example 19.6.
Solution
The address is
205.16.37. 0010 0111
If we set 32 − 28 = 4 rightmost bits to 1, we get
205.16.37. 0010 1111
or
205.16.37.47
This is actually the block shown in Example 8
Notes: <number>
Layla Hajr

## Slide 41
Classless Addressing
The number of addresses in the block
can be found by using the formula
2 32−n.
Notes: <number>
Layla Hajr

## Slide 42
Classless Addressing
Find the number of addresses in Example 19.6.
Solution
The value of n is 28, which means that number of addresses is
2 32−28 or 16.
Notes: <number>
Layla Hajr

## Slide 43
Classless Addressing
Another way to find the first address, the last address,
and the number of addresses is to represent the mask as
a 32-bit binary (or 8-digit hexadecimal) number. This is
particularly useful when we are writing a program to
find these pieces of information. In Example 19.5 the
/28 can be represented as
11111111 11111111 11111111 11110000
(twenty-eight 1s and four 0s).
Find
a. The first address
b. The last address
c. The number of addresses.
Notes: <number>
Layla Hajr

## Slide 44
Classless Addressing
Solution
a. The first address can be found by ANDing the given
addresses with the mask. ANDing here is done bit by
bit. The result of ANDing 2 bits is 1 if both bits are 1s;
the result is 0 otherwise.
Notes: <number>
Layla Hajr

## Slide 45
The last address can be found by ORing the given
addresses with the complement of the mask. ORing
here is done bit by bit. The result of ORing 2 bits is 0
If both bits are 0s; the result is 1 otherwise. The complement of a number is found by changing each1
to 0 and each 0 to 1.
Notes: <number>
Layla Hajr

## Slide 46
The number of addresses can be found by complementing the mask, interpreting it as a decimal number, and adding 1 to it.
Notes: <number>
Layla Hajr

## Slide 47
A network configuration for the block 205.16.37.32/28
Notes: <number>
Layla Hajr

## Slide 48
Classless addressing Two levels of hierarchy: No subnetting
The prefix is common to all addresses in the network; the suffix changes from one device to another
Notes: <number>
Layla Hajr

## Slide 49
Classless Addressing
Each address in the block can be considered as a two-level hierarchical structure:
the leftmost n bits (prefix) define
the network;
the rightmost 32 − n bits define
the host (suffix).
Notes: <number>
Layla Hajr

## Slide 50
The organization has its own mask : network mask
Each subnet must also have its own mask: subnet mask
Notes: <number>
Layla Hajr

## Slide 51
An organization is granted a block of addresses
17.12.40.0/26, which contains 64: (2(32-26)=24 =64) addresses.
The organization has three offices and needs to divide the
addresses into three subblocks (subnets) of 32, 16 and 16
Addresses. Design the subblocks and find the new masks.
Solution
Subnet1:
Mask n1: 2 32-n1 = 32; n1=27
Subnet2
Mask n2: 2 32-n2 =16; n2=28
Subnet3
Mask n3: 2 32-n2= 16; n3= 28
Example
Notes: <number>
Layla Hajr

## Slide 52
Configuration and addresses in a subnetted network
Notes: <number>
Layla Hajr

## Slide 53
a. In subnet 1, the address 17.12.14.29/27 can give us the subnet address if we use mask/27:
Host : 17. 12 .14 .00011101
Mask: /27
Subnet: 17.12.14.00000000 17.12.14.0
b. In subnet 2, the address 17.12.14.45/28 can give us the subnet address if we use mask/28:
Host : 17. 12. 14. 00101101
Mask: /28
Subnet: 17.12.14. 00100000 17.12.14.32
Notes: <number>
Layla Hajr

## Slide 54
c. In subnet 3, the address 17.12.14.50/28 can give us the subnet address if we use mask/28:
Host : 17. 12. 14. 00110010
Mask: /28
Subnet: 17. 12. 14. 00110000 17.12.14.48
Notes: <number>
Layla Hajr

## Slide 55
Notes: <number>
Layla Hajr