## Slide 1: Chapter 19
Construction Safety and Health

## Slide 2: Chapter 19
19-1 IMPORTANCE OF SAFETY
19-2 OSHA
19-3 SAFETY PROGRAMS
19-4 SAFETY PROCEDURES
19-5 ENVIRONMENTAL HEALTH IN CONSTRUCTION

## Slide 3: 19-1 IMPORTANCE OF SAFETY
It has been reported that construction, which consists of about 5% of the U.S. work force, accounts for some:
  20% of work fatalities and
  12% of disabling injuries.
The total annual cost (direct and indirect) of construction accidents has been estimated to exceed $17 billion.
In the United States, national concern over the frequency and extent of industrial accidents and health hazards led to the passage of the Occupational Safety and Health Act of 1970, which established specific safety and health requirements for virtually all industries, including construction.

## Slide 4: 19-1 IMPORTANCE OF SAFETY
The Occupational Safety and Health Administration (OSHA) is responsible for developing and enforcing regulations implementing this act.
the concern over OSHA regulations and penalties has tended to obscure the fact that there are at least two other major reasons for construction management to be seriously concerned about safety. These reasons are:
  humanitarian and
  financial.

## Slide 5: 19-1 IMPORTANCE OF SAFETY
Everyone is understandably distressed when a fellow employee is killed or disabled, so the humanitarian basis for safety is apparent.
many managers do not fully appreciate the financial consequences of accidents.
Worker's compensation insurance premiums, for example, are based on a firm's accident rate.
Public liability, property damage, and equipment insurance rates are also affected by accident rates.

## Slide 6: 19-1 IMPORTANCE OF SAFETY
It has been shown that a construction firm can lose its competitive bidding position simply because of the effect of high insurance premiums resulting from a poor safety record.

## Slide 7: 19-1 IMPORTANCE OF SAFETY
In addition to the visible cost of accidents represented by insurance and worker's compensation payments, there are other costs, which are difficult to estimate.
Such costs associated with an accident include:
  the monetary value of lost project time while the accident is investigated and damages are repaired,
  the time required to replace critical materials and equipment and to train replacement workers,
  as well as the effect on those portions of the project not directly involved in the accident.

## Slide 8: 19-2 OSHA
The U.S. Occupational Safety and Health Administration (OSHA) has produced a comprehensive set of safety and health regulations, inspection procedures, and record-keeping requirements.
The law has also established both civil and criminal penalties for violations of OSHA regulations.
Table 19-1 indicates the maximum penalty for major categories of violations.

## Slide 9: TABLE 19-1: Maximum penalties under OSHA

## Slide 10: 19-2 OSHA
As shown in Table 19-1, civil penalties of $7000 per day may be assessed for failure to correct a cited violation.
Under criminal proceedings, a fine of $20,000 and imprisonment for 1 year may be adjudged for a second conviction of a violation resulting in the death of an employee.
OSHA officials may also seek a restraining order through a U.S. District Court to stop work or take other action required to alleviate a condition identified as presenting imminent danger of serious injury or death.

## Slide 11: 19-2 OSHA
Under OSHA regulations employers are required to keep records of all work-related deaths, injuries, and illnesses.
  It is not necessary to record minor injuries that require only first-aid treatment.
all injuries involving medical treatment, loss of consciousness, restrictions on work or body motion, or transfer to another job must be recorded.
A special report of serious accidents resulting in one or more deaths or the hospitalization of five or more employees must be made to OSHA officials within 48 hours.

## Slide 12: 19-2 OSHA
One of the major inequities of OSHA is that only management may be penalized for safety violations.
  So, management may enforce safety regulations is to discipline or fire workers engaging in unsafe acts.
It should be pointed out that OSHA safety regulations are considered to be the minimum federal safety standards.

## Slide 13: 19-3 SAFETY PROGRAMS
All construction firms need a carefully planned and directed safety program to minimize accidents and ensure compliance with OSHA and other safety regulations.
no safety program will be successful without the active support of top management.
Job-site supervisors have traditionally neglected safety in their haste to get the job done on time and within budget.

## Slide 14: 19-3 SAFETY PROGRAMS
Only when supervisors are convinced by higher management that safety is equally as important as production will the benefits of an effective safety program be achieved.
An effective safety program must instill a sense of safety consciousness in every employee.

## Slide 15: 19-3 SAFETY PROGRAMS
some of the major elements of safety program are:
  1. A formal safety training program for all new employees.
  2. Periodic refresher training for each worker.
  3. A formal supervisory safety training program for all supervisors.
  4. A program of regular site visits by safety personnel to review and control job hazards.
  5. Provision of adequate personal protective equipment, first-aid equipment, and trained emergency personnel.
  6. An established procedure for the emergency evacuation of injured workers.
  7. Provisions for maintaining safety records and reporting accidents in compliance with OSHA requirements.

## Slide 16: 19-4 SAFETY PROCEDURES
It has been found that most serious construction accidents involve:
  construction equipment operations,
  trench and embankment failure,
  falls from elevated positions,
  collapse of temporary structures and formwork, or
  the failure of structures under construction.

## Slide 17: 19-4 SAFETY PROCEDURES
Many safety precautions for specific construction operations have been discussed in chapters 18.
In addition, the following list of major safety precautions should be helpful as a general guide.

## Slide 18: 19-4 SAFETY PROCEDURES
General
Equipment Operations
Construction Plant
Excavations
Construction of Structures
Marine or Over-Water Construction

## Slide 19: General
Good housekeeping on a project site is both a safety measure and an indicator of good project supervision.
Lumber, used formwork, and other material lying around a work area increase the likelihood of falls and puncture wounds.

## Slide 20: Equipment Operations
Require operators and mechanics to use steps and hand holds when mounting equipment.
Utilize guides or signalmen when the operator's visibility is limited or when there is danger to nearby workers.
  Backup alarms or guides must be used when equipment operates in reverse.
Exercise extreme caution and comply with safety regulations when operating near high-voltage lines.
  In case of accidental contact with a high-voltage line, the operator should attempt to move the equipment enough to break contact.
  If unsuccessful, the operator should remain on the equipment until the line can be deenergized.

## Slide 21: Equipment Operations
Make sure that machines are equipped with required safety features and that operators use seat belts when provided.
Use care when operating equipment on side slopes to prevent overturning.
When operating cranes, be extremely careful not to exceed safe load limits for the operating radius and boom position.
  Electronic load indicators are available.
Do not allow workers to ride on equipment unless proper seating is provided.

## Slide 22: Equipment Operations
Haul roads must be properly maintained.
  Items to check include:
    condition of the road surface (holes, slippery surface, excess dust),
    visibility (curves, obstacles, intersections, and dust), and
    adequate width for vehicles to pass (unless one-way).

## Slide 23: Equipment Operations
Park equipment with the brake set, blade or bowl grounded, and ignition key removed at the end of work.
  Equipment used for land clearing must be equipped with overhead and rear canopy protection.
  Workers engaged in clearing must be protected from the hazards of irritant and toxic plants and instructed in the first-aid treatment for such hazards.

## Slide 24: Equipment Operations
When hauling heavy or oversized loads on highways, make sure that loads are properly secured and covered if necessary.
  Slow-moving and over-sized vehicles must use required markings and signals to warn other traffic.
Take positive action to ensure that equipment under repair cannot be accidentally operated.

## Slide 25: Equipment Operations
Utilize blocking, cribbing, or other positive support when employees must work under heavy loads supported by cables, jacks, or hydraulic systems.
Ensure that any guards or safety devices removed during equipment repair are promptly replaced.
Shut down engines and do not allow smoking during refueling.

## Slide 26: Construction Plant
Set equipment containing hot or flammable fluids on firm foundations to prevent overturning.
  Clearly mark high-temperature lines and containers to prevent burns.
  Be especially careful of live steam.
  Provide fire extinguishers and other required safety equipment.

## Slide 27: Construction Plant
Aggregate bins and batching plants should be emptied before performing major repairs.
When electrical equipment is being repaired, shut off and tag electrical circuits.
Ensure that wire rope and cable is of the proper size and strength, well maintained, and inspected at least weekly.

## Slide 28: Excavations
The location of underground utilities and other hazards must be determined before starting an excavation.
  Contact utility companies and property owners to request that they establish the location of such installations.
  Almost all U.S. states have central One-Call telephone numbers which coordinate with utility companies to provide prompt service in locating and marking their underground lines when requested.
  When utility companies or owners cannot provide this information promptly (usually within 24 hours), the contractor may cautiously proceed with excavation.
  However, in this situation, the contractor must employ detection equipment or other acceptable means to locate and avoid underground hazards.

## Slide 29: Excavations
The sides of excavations must be properly shored or sloped to the angle of repose to prevent cave-ins.
  OSHA regulations require that banks over 5 ft (1.5 m) must be shored, cut back to a stable slope, or otherwise protected.
  Regulations also require that protective systems (sloping, benching, shoring, or shielding) for excavations over 20 ft (6.1 m) deep must be designed by a registered professional engineer.
When workers are required to enter a trench excavation 4 ft (1.2192 m) or more in depth, a stairway, ladder, ramp, or other safe means of egress must be located in such a manner as to require no more than 25 ft (7.62 m) of lateral travel by any worker in the trench.

## Slide 30: Excavations
Avoid the operation of equipment near the top edge of an excavation because this increases the chance of slope failure.
  The storage of materials near the top edge of an excavation, vibration, and the presence of water also increase the chance of slope failure.
  When these conditions cannot be avoided, additional measures must be taken to increase slope stability.
  If workers are required to enter the excavation, no spoil or other material may be stored within 2 ft (0.6 m) of the edge of the excavation.

## Slide 31: Excavations
Ensure that workers are not allowed under loads being handled by excavators or hoists.
Watch out for buried lines and containers when excavating.
  Possible hazards include toxic and flammable gases, electricity, and collapse of side slopes due to sudden release of liquids.
  If a gas line is ruptured and catches fire, get personnel and flammable material away from the fire and have the gas turned off as quickly as possible.
  Do not attempt to extinguish the fire because an accumulation of unburned gas poses a greater threat than does a fire.

## Slide 32: Construction of Structures
Properly guard all openings above ground level.
Provide guard rails, safety lines, safety belts, and/or safety nets for workers on scaffolds or steelwork.
Ensure that temporary structures are properly designed, constructed, and braced.

## Slide 33: Construction of Structures
Special caution should be exercised in high-rise concrete construction.
  Forms must be of adequate strength and properly braced.
  The rate of pour must be maintained at or below design limits.
  Shoring and reshoring must be adequately braced and not removed until the concrete has developed the required strength.

## Slide 34: Marine or Over-Water Construction
Marine or over-water construction operations present all of the usual construction hazards plus additional hazards posed by the marine environment.
These additional hazards include drowning, slippery surfaces, increased tripping and height hazards, as well as weather and wave action.
Some of the major safety precautions that should be taken are listed below.
  Unless workers can safely step onto vessels, a ramp or safe walkway must be provided.
    Access ways must be adequately illuminated, free of obstructions, and located clear of suspended loads.

## Slide 35: Marine or Over-Water Construction
  Working areas should have nonslip surfaces, be maintained clear of obstructions, and be equipped with adequate handrails.
  Workers on unguarded decks or surfaces over water must wear approved lifejackets or buoyant vests.
    Life rings and a rescue boat must also be available.
    Workers more than 25 ft (7.6 m) above a water surface must be protected by safety belts, safety nets, or similar protective equipment.

## Slide 36: 19-5 ENVIRONMENTAL HEALTH IN CONSTRUCTION
Increased governmental interest in occupational safety has been accompanied by an increased concern for occupational health and environmental controls.
The major environmental health problems encountered in construction consist of:
  noise,
  dust,
  radiation (ionizing and nonionizing),
  toxic materials,
  heat, and cold.