## Slide 1
26-1 Definition of Capacitance
26-2 Calculating Capacitance
26-3 Combinations of Capacitors
26-4 Energy Stored in a Charged Capacitor
26-5 Capacitors with Dielectrics
10/28/2011
<number>

## Slide 2: 26-1 Definition of Capacitance
Pictures from Serway & Beichner
A capacitor consists of two conductors (known as plates) carrying charges of equal magnitude but opposite sign.
A potential difference V exists between the conductors due to the presence of the charges.
What is the capacity of the device for storing charge at particular value of V?
Experiments show the quantity of electric charge Q on a capacitor is linearly proportional to the potential difference between the conductors, that is Q ~ V. Or we write Q = C V
10/28/2011
<number>

## Slide 3: Definition of Capacitance
Pictures from Serway & Beichner
The capacitance C of a capacitor is the ratio of the magnitude of the charge on either conductor to the magnitude of the potential difference between them:
SI Unit: farad (F), 1F = 1 C/V
The farad is an extremely large unit, typically you will see
microfarads (F=10-6F),
nanofarads (nF=10-9F), and
picofarads (pF=10-12F)
Capacitance will always be a positive quantity
The capacitance of a given capacitor is constant
The capacitance is a measure of the capacitor’s ability to store charge
10/28/2011
<number>

## Slide 4
Assume a spherical charged conductor
Assume V = 0 at infinity
Note, this is independent of the charge and
the potential difference
26-2 Calculating Capacitance
10/28/2011
<number>
Let’s assume that the inner sphere has charge +q and the outer sphere has charge –q
Capacitance of an Isolated Sphere
We obtain the capacitance of a single conducting sphere by taking our result for a spherical capacitor and moving the outer spherical conductor infinitely far away

## Slide 5: Parallel - Plate Capacitors
Pictures from Serway & Beichner
A parallel-plate capacitor consists of two parallel conducting plates, each of area A, separated by a distance d. When the capacitor is charged, the plates carry equal amounts of charge. One plate carries positive charge, and the other carries negative charge.
The plates are charged by connection to a battery. Describe the process by which the plates get charged up.
10/28/2011
<number>

## Slide 6
For example, a `parallel plate’ capacitor, has capacitance
10/28/2011
<number>

## Slide 7: Parallel-Plate Capacitors
Pictures from Serway & Beichner
A
d
The electric field between the plates of a parallel-plate capacitor is uniform near the center but nonuniform near the edges.
Electric field pattern of two oppositely charged conducting parallel plates.
10/28/2011
<number>
Notes: <number>

## Slide 8: example
What is the AREA of a 1F capacitor that has a plate separation of 1 mm?
10/28/2011
<number>

## Slide 9: Example: Lightning
Pictures from Serway & Beichner
Regarding the Earth and a cloud layer 800 m above the Earth as the “plates” of a capacitor, calculate the capacitance if the cloud layer has an area of 1.00 x 1.00 km2. Assume that the air between the cloud and the ground is pure and dry.
Assume that charge builds up on the cloud and on the ground until a uniform electric field of 3.00 x 106 N/C throughout the space between them makes the air break down and conduct electricity as a lightning bolt. What is the maximum charge the cloud can hold?
C= oA/d = 8.85x10-12 x (1000)2/800 = 11.1 nF
Potential between ground and cloud is
V = Ed = 3.0 x106 x 800 = 2.4 x 109 V
Q = C(V) = 26.6 C
10/28/2011
<number>

## Slide 10: Cylindrical Capacitors
Pictures from Serway & Beichner
A solid cylindrical conductor of radius a and charge Q is coaxial with a cylindrical shell of negligible thickness, radius b > a, and charge –Q. Find the capacitance of this cylindrical capacitor if its length is L.
L
10/28/2011
<number>

## Slide 11: Cylindrical Capacitors
Pictures from Serway & Beichner
Assume that L is >> a and b, neglect the end effects.
E is perpendicular to the long axis of the cylinders and is confined to the region between them.
Potential difference between the two cylinders is given by
L
Vb-Va = -
E . ds
b
a
Where E is the E field in the region a < r < b.
Our discussion on Gauss’s Law  Er = 2k/r where  is the linear charge density of the cylinder.
Note that the charge on outer cylinders does not contribute to E field inside it.
10/28/2011
<number>

## Slide 12: Cylindrical Capacitors
Pictures from Serway & Beichner
L
Vb-Va = -
Er dr
b
a
= - 2k
b
a
dr
r
= - 2kln( )
b
a
Using = Q/L , we have
C = =
Q
V
ln( )
b
a
2kQ
L
Q
C =
ln( )
b
a
2k
L
10/28/2011
<number>

## Slide 13: Cylindrical Capacitors
Pictures from Serway & Beichner
L
C =
ln( )
b
a
2k
L
What is the capacitance per unit length ?
Example
Co-axial Cable. Read the cable, typically 50 pF/m. Is this sensible ?
Typically a  0.5 mm, b  1.5 mm
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 14: The Spherical Capacitors
Pictures from Serway & Beichner
Gauss’s law  E field outside a spherically symmetric charge distribution is radial and given by Er = kQ/r2.
The potential difference between the spheres is
Vb-Va = -
Er dr
b
a
= - kQ
b
a
dr
r2
= kQ
1
b
1
a
C =
Vb-Va
Q
=
ab
k (b-a)
What happens to the capacitance of this system when the radius of the outer sphere approaches infinity?
10/28/2011
<number>

## Slide 15: Example
Pictures from Serway & Beichner
(a) If a drop of liquid has capacitance 1.00 pF, what is its radius ? (b) If another drop has radius 2.00 mm, what is its capacitance ? (c) What is the charge on the smaller drop if its potential is 100V ?
C = 4o R
R = (8.99 x 109 N · m2/C2)(1.00 x 10–12 F) = 8.99 mm
C = 4 (8.85 x 10-12) x 2.0x10-3 = 0.222 pF
Q =CV = 0.222 pF x 100 V = 2.22 x 10-11 C
10/28/2011
<number>

## Slide 16: Example
Pictures from Serway & Beichner
What is the capacitance of the Earth ?
Think of Earth spherical conductor and the outer conductor of the “spherical capacitor” may be considered as a conducting sphere at infinity where V approaches zero.
10/28/2011
<number>

## Slide 17: Combinations of Capacitors
Pictures from Serway & Beichner
Parallel Combination
The individual potential differences across capacitors connected in parallel are all the same and are equal to the potential difference applied across the combination.
10/28/2011
<number>

## Slide 18
a
b
10/28/2011
<number>

## Slide 19: Combinations of Capacitors
Pictures from Serway & Beichner
Series Combination
Start with uncharged situation and follow what happen just after a battery is connected to the circuit.
When a battery is connected, electrons transferred out of the left plate of C1 and into the right plate of C2.
As this charge accumulates on the right plate of C2, an equivalent amount of negative charge is forced off the left plate of C2 and this left plate there fore has an excess positive charge. (cont’d)
10/28/2011
<number>

## Slide 20: Capacitors in Series
a
b
10/28/2011
<number>

## Slide 21: Example
Pictures from Serway & Beichner
A 1-megabit computer memory chip contains many 60.0-fF capacitors. Each capacitor has a plate area of 21.0 x 10-12 m2. Determine the plate separation of such a capacitor (assume a parallel-plate configuration). The characteristic atomic diameter is 10-10 m =0.100nm. Express the plate separation in nanometers.
3.10 nm
10/28/2011
<number>

## Slide 22: Example: Equivalent Capacitance
Pictures from Serway & Beichner
In parallel use C=C1+C2
In series use 1/C=1/C1+1/C2
6.00 F
20.00 F
2.50 F
8.50 F
20.00 F
In series use 1/C=1/C1+1/C2
5.965 F
10/28/2011
<number>

## Slide 23: Example: Equivalent Capacitance
Pictures from Serway & Beichner
In parallel use C=C1+C2
In parallel use C=C1+C2
In series use 1/C=1/C1+1/C2
10/28/2011
<number>

## Slide 24: Example: Equivalent Capacitance 26.22
Pictures from Serway & Beichner
In series use 1/CB=1/C+1/C+1/C
In series use 1/CA=1/C+1/C
C
C/2
C/3
In parallel use Ceq=C+C/2+C/3
10/28/2011
<number>

## Slide 25: Energy stored in a charged capacitor
Consider the circuit to be a system
Before the switch is closed, the energy is stored as chemical energy in the battery
When the switch is closed, the energy is transformed from chemical to electric potential energy
The electric potential energy is related to the separation of the positive and negative charges on the plates
A capacitor can be described as a device that stores energy as well as charge
10/28/2011
<number>

## Slide 26: How Much Energy Stored in a Capacitor?
q
-q
dq
To study this problem, recall that the work the field force does equals the electric potential energy loss:
When the charge buildup is q, move a dq, the work is
This also means that when the battery moves a charge dq to charge the capacitor, the work the battery does equals to the buildup of the electric potential energy:
We now have the answer to the final charge Q:
10/28/2011
<number>

## Slide 27
When a capacitor has charge stored in it, it also stores electric potential energy that is
This applies to a capacitor of any geometry
The energy stored increases as the charge increases and as the potential difference (voltage) increases
In practice, there is a maximum voltage before discharge occurs between the plates
26-4 Energy Stored in a Charged Capacitor
10/28/2011
<number>

## Slide 28: Energy Density
Consider a Parallel Plate Capacitor:
the energy density (energy per unit volume)
10/28/2011
<number>

## Slide 29
The energy can be considered to be stored in the electric field
For a parallel-plate capacitor, the energy can be expressed in terms of the field as
U = ½ (εoAd)E2
It can also be expressed in terms of the energy density (energy per unit volume)
uE = ½ E2
Constant Q: How do (A,d,) affect V, E, U and u?
   C   V  E  U  u 
d   C   V  E  U  u 
A   C   V  E  U  u 
Constant V: How do (A,d,) affect Q, E, U and u?
   C   Q  E  U  u 
d   C   Q  E  U  u 
A   C   Q  E  U  u 
10/28/2011
<number>

## Slide 30
A dielectric is a nonconducting material that, when placed between the plates of a capacitor, increases the capacitance
  Dielectrics include rubber, glass, and waxed paper
With a dielectric, the capacitance becomes C = κCo
  The capacitance increases by the factor κ when the dielectric completely fills the region between the plates
  κ is the dielectric constant of the material Dielectric constant is a property of a material and varies from one material to another.
26-5 Capacitors with Dielectrics
10/28/2011
<number>

## Slide 31: Effect of a dielectric on capacitance
Potential difference with a dielectric
is less than the potential difference
across free space
Results in a higher capacitance.
Allows more charge to be stored before breakdown voltage.
If the dielectric is introduced while the potential difference is being maintained constant by a battery, the charge increases to a value Q =  Qo . The additional charge is supplied by the battery and the capacitance again increases by the factor .
C = 
A
d
10/28/2011
<number>

## Slide 32
For a parallel-plate capacitor, C = κεo(A/d)
In theory, d could be made very small to create a very large capacitance
In practice, there is a limit to d
  d is limited by the electric discharge that could occur though the dielectric medium separating the plates
For a given d, the maximum voltage Vmax that can be applied to a capacitor without causing a discharge depends on the dielectric strength (maximum electric field) Emaxof the material
Dielectrics provide the following advantages:
  Increase in capacitance
  Increase the maximum operating voltage
If magnitude of the electric field in the dielectric exceeds the dielectric strength, then the insulating properties break down and the dielectric begins to conduct.
10/28/2011
<number>

## Slide 33: Example values of dielectric constant
“Dielectric strength” is the maximum field in the dielectric before breakdown.
(a spark or flow of charge)
10/28/2011
<number>

## Slide 34: Example
Pictures from Serway & Beichner
26.33: A parallel-plate capacitor is charged and then disconnected from a battery. By what fraction does the stored energy change (increase or decrease) when the plate separation is doubled ?
U = Q2/2C
and C = oA/d
and d2 = 2 d1 then
C2= C1/2.
10/28/2011
<number>

## Slide 35: Types of Capacitors
Pictures from Serway & Beichner
(a) A tubular capacitor, whose plates are separated by paper and then rolled into a cylinder. (b) A high-voltage capacitor consisting of many parallel plates separated by insulating oil. (c) An electrolytic capacitor.
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 36: Question
<number>
d
A
- - - - -
+ + + +
Suppose the capacitor shown here is charged to Q and then the battery is disconnected.
Now suppose I pull the plates further apart so that the final separation is d1.
How do the quantities Q, C, E, V, U change?
How much do these quantities change?.. exercise for student!!
Q:
C:
E:
V:
U:
remains the same.. no way for charge to leave.
increases.. add energy to system by separating
decreases.. since capacitance depends on geometry
increases.. since C , but Q remains same (or d  but E the same)
remains the same... depends only on charge density
Answers:
10/28/2011

## Slide 37: Question
<number>
d
A
- - - - -
+ + + +
Suppose the capacitor shown here is charged to Q and then the battery is disconnected.
Now suppose I pull the plates further apart so that the final separation is d1.
How do the quantities Q, C, E, V, U change?
How much do these quantities change?.. exercise for student!!
Q :
C :
E :
V :
U :
remains the same.. no way for charge to leave.
increases.. add energy to system by separating
decreases.. since capacitance depends on geometry
increases.. since C , but Q remains same (or d  but E the same)
remains the same... depends only on charge density
Answers:
10/28/2011

## Slide 38
<number>
Another Question
Suppose the battery (V) is kept attached to the capacitor.
Again pull the plates apart from d to d1.
Now what changes?
d
A
- - - - -
+ + + +
V
Answers:
C :
V :
Q :
E :
U :
decreases (capacitance depends only on geometry)
must stay the same - the battery forces it to be V
must decrease, Q=CV charge flows off the plate
How much do these quantities change?.. exercise for student!!
must decrease ( , )
must decrease ( )
10/28/2011

## Slide 39
Find the capacitance of a 4.0 cm diameter sensor immersed in oil if the plates are separated by 0.25 mm.
The plate area is
The distance between the plates is
178 pF
10/28/2011
<number>
Question

## Slide 40
1- When a potential difference of 150 V is applied to the plates of a parallel-plate capacitor, the plates carry a surface charge density of 30.0 nC/cm2. What is the spacing between the plates?
2-Four capacitors are connected as shown in the Figure
Find the equivalent capacitance between points a and b.
Calculate the charge on each capacitor if ΔVab = 15.0 V.
Homework
10/28/2011
<number>

## Slide 41
3 - Find the equivalent capacitance between points a and b for the group of capacitors connected as shown in the Figure. Take C1 = 5.00 μF, C2 = 10.0 μF, and C3 = 2.00 μF.
4- A parallel-plate capacitor is charged and then disconnected from a battery. By what fraction does the stored energy change (increase or decrease) when the plate separation is doubled?
10/28/2011
<number>

## Slide 42
5- Determine (a) the capacitance and (b) the maximum potential difference that can be applied to a Teflon-filled parallel-plate capacitor having a plate area of 1.75 cm2 and plate separation of 0.040 0 mm.
6 - A parallel-plate capacitor is constructed using a dielectric material whose dielectric constant is 3.00 and whose dielectric strength is 2.00 × 108 V/m. The desired capacitance is 0.250 μF, and the capacitor must withstand a maximum potential difference of 4 000 V. Find the minimum area of the capacitor plates.
10/28/2011
<number>

## Slide 43
Pictures from Serway & Beichner
7- Consider the circuit as shown, where C1 = 6.00F and C2= 3.00 F and V =20.0V. Capacitor C1 is first charged by closing of switch S1. Switch S1 is then opened and the charged capacitor is connected to the uncharged capacitor by the closing of S2. Calculate the initial charge acquired by C1 and the final charge on each.
10/28/2011
<number>

## Slide 44
10/28/2011
<number>
8- Given a 7.4 pF air-filled capacitor. You are asked to convert it to a capacitor that can store up to 7.4 J with a maximum voltage of 652 V. What dielectric constant should the material have that you insert to achieve these requirements?
9-An air-filled parallel plate capacitor has a capacitance of 1.3 pF. The separation of the plates is doubled, and wax is inserted between them. The new capacitance is 2.6pF. Find the dielectric constant of the wax.
10- Consider a parallel plate capacitor with capacitance C = 2.00 F connected to a battery with voltage V = 12.0 V as shown. A) What is the charge stored in the capacitor?
b) Now insert a dielectric with dielectric constant  = 2.5 between the plates of the capacitor. What is the charge on the capacitor?

## Slide 45
10/28/2011
<number>
11- An isolated conducting sphere whose radius R is 6.85 cm has a charge of q=1.25 nC. a) How much potential energy is stored in the electric field of the charged conductor?
Find the equivalent capacitance
12 - If each capacitor has a capacitance of 5 nF, what is the capacitance of this system of capacitors?
13- A storage capacitor on a random access memory (RAM) chip has a capacitance of 55 nF. If the capacitor is charged to 5.3 V, how many excess electrons are on the negative plate?

## Slide 46
10/28/2011
<number>
14 - A parallel plate capacitor made from 2 squares of metal, 2mm thick and 20cm on a side separated by 1mm with 1000V between them Find:
a) capacitance b)charge per plate c) charge density d)electric field e) energy-stored f) energy density
15 -
16 - One common kind of computer keyboard is based on the idea of capacitance. Each key is mounted on one end of a plunger, the other end being attached to a movable metal plate. The movable plate and the fixed plate form a capacitor. When the key is pressed, the capacitance increases. The change in capacitance is detected, thereby recognizing the key which has been pressed.
The separation between the plates is 5.00 mm, but is reduced to 0.150 mm when a key is pressed. The plate area is 9.50x10-5m2 and the capacitor is filled with a material whose dielectric constant is 3.50.
Determine the change in capacitance detected by the computer.