## Slide 1
Capacitors
Calculating capacitance
Energy stored in a capacitor
Capacitors with dielectric materials

## Slide 2
25.2: Capacitance:
To store charge
To store energy
To control variation time scales in a circuit
Notes: <number>

## Slide 3
25.2: Capacitance:
When a capacitor is charged, its plates have charges of equal magnitudes but opposite signs: q+ and q-. However, we refer to the charge of a capacitor as being q, the absolute value of these charges on the plates.
The charge q and the potential difference V for a capacitor are proportional to each other:
The proportionality constant C is called the capacitance of the capacitor. Its value depends only on the geometry of the plates and not on their charge or potential difference.
The SI unit is called the farad (F): 1 farad (1 F)= 1 coulomb per volt =1 C/V.

## Slide 4
25.2: Charging a Capacitor:
The circuit shown is incomplete because switch S is open; that is, the switch does not electrically connect the wires attached to it. When the switch is closed, electrically connecting those wires, the
circuit is complete and charge can then flow through the switch and the wires.
As the plates become oppositely charged, that potential difference increases until it equals the potential difference V between the terminals of the battery. With the electric field zero, there is no further drive of electrons. The capacitor is then said to be fully charged, with a potential difference V and charge q.

## Slide 5
25.3: Calculating the Capacitance:

## Slide 6
1 farad Capacitor
Example1: Given a 1 farad parallel plate capacitor having a plate separation of 1mm. What is the area of the plates?
This corresponds to a square of about 10km on a side!

## Slide 7
25.3: Calculating the Capacitance; A Cylindrical Capacitor :
As a Gaussian surface, we choose a cylinder of length L and radius r, closed by end caps and placed as is shown. It is coaxial with the cylinders and encloses the central cylinder and thus also the charge q on that cylinder.

## Slide 8
25.3: Calculating the Capacitance; A Spherical Capacitor:

## Slide 9
We can assign a capacitance to a single isolated spherical conductor of radius R by assuming that the “missing plate” is a conducting sphere of infinite radius.
The field lines that leave the surface of a positively charged isolated conductor must end somewhere; the walls of the room in which the conductor is housed can serve effectively as our sphere of infinite radius.
To find the capacitance of the conductor, we first rewrite the capacitance as:
Now letting b→∞, and substituting R for a,
25.3: Calculating the Capacitance; An Isolated Sphere:

## Slide 10
Example, Charging the Plates in a Parallel-Plate Capacitor:

## Slide 11
25.4: Capacitors in Parallel:

## Slide 12
25.4: Capacitors in Series:

## Slide 13
Example, Capacitors in Parallel and in Series:

## Slide 14
Example, Capacitors in Parallel and in Series:

## Slide 15
Example, One Capacitor Charging up Another Capacitor:

## Slide 16
25.5: Energy Stored in an Electric Field:

## Slide 17
25.5: Energy Density:

## Slide 18
Example, Potential Energy and Energy Density of an Electric Field:

## Slide 19
26.5. Capacitors with Dielectrics
Dielectric is a non-conducting material, such as rubber, glass, or waxed paper. When a dielectric is inserted between the plates of a capacitor, the capacitance increases. If the dielectric completely fills the space between the plates, the capacitance increases by a dimensionless factor k , which is called the dielectric constant.

## Slide 20
26.6: Dielectrics, an Atomic View:
Polar dielectrics. The molecules of some dielectrics, like water, have permanent electric dipole moments. In such materials (called polar dielectrics), the electric dipoles tend to line up with an external electric field as in Fig. 25-14. Since the molecules are continuously jostling each other as a result of their random thermal motion, this alignment is not complete, but it becomes more complete as the magnitude of the applied field is increased (or as the temperature, and thus the jostling, are decreased).The alignment of the electric dipoles produces an electric field that is directed opposite the applied field and is smaller in magnitude.
Nonpolar dielectrics. Regardless of whether they have permanent electric dipole moments, molecules acquire dipole moments by induction when placed in an external electric field. This occurs because the external field tends to “stretch” the molecules, slightly separating the centers of negative and positive charge.

## Slide 21
October 10, 2007
What Happens When You Insert a Dielectric?
With battery attached, V=const, so more charge flows to the capacitor
With battery disconnected, q=const, so voltage (for given q) drops.

## Slide 22
October 10, 2007
What Does the Dielectric Do?
A dielectric material is made of molecules.
Polar dielectrics already have a dipole moment (like the water molecule).
Non-polar dielectrics are not naturally polar, but actually stretch in an electric field, to become polar.
The molecules of the dielectric align with the applied electric field in a manner to oppose the electric field.
This reduces the electric field, so that the net electric field is less than it was for a given charge on the plates.
This lowers the potential (case b of the previous slide).
If the plates are attached to a battery (case a of the previous slide), more charge has to flow onto the plates.

## Slide 40
Homework:
Problems 1, 2, 4, 6, 8,11,35,48
Serway Book