## Slide 1
26-1 Definition of Capacitance
26-2 Calculating Capacitance
26-3 Combinations of Capacitors
26-4 Energy Stored in a Charged Capacitor
26-5 Capacitors with Dielectrics
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 2: 26-1 Definition of Capacitance
Pictures from Serway & Beichner
A capacitor consists of two conductors (known as plates) carrying charges of equal magnitude but opposite sign.
A potential difference V exists between the conductors due to the presence of the charges.
What is the capacity of the device for storing charge at particular value of V?
Experiments show the quantity of electric charge Q on a capacitor is linearly proportional to the potential difference between the conductors, that is Q ~ V. Or we write Q = C V
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 3: Definition of Capacitance
Pictures from Serway & Beichner
The capacitance C of a capacitor is the ratio of the magnitude of the charge on either conductor to the magnitude of the potential difference between them:
SI Unit: farad (F), 1F = 1 C/V
The farad is an extremely large unit, typically you will see
microfarads (F=10-6F),
nanofarads (nF=10-9F), and
picofarads (pF=10-12F)
Capacitance will always be a positive quantity
The capacitance of a given capacitor is constant
The capacitance is a measure of the capacitor’s ability to store charge
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 4
Assume a spherical charged conductor
Assume V = 0 at infinity
Note, this is independent of the charge and
the potential difference
26-2 Calculating Capacitance
10/28/2011
<number>
Norah Ali Al-moneef king saud university
Let’s assume that the inner sphere has charge +q and the outer sphere has charge –q
Capacitance of an Isolated Sphere
We obtain the capacitance of a single conducting sphere by taking our result for a spherical capacitor and moving the outer spherical conductor infinitely far away

## Slide 5: Parallel - Plate Capacitors
Pictures from Serway & Beichner
A parallel-plate capacitor consists of two parallel conducting plates, each of area A, separated by a distance d. When the capacitor is charged, the plates carry equal amounts of charge. One plate carries positive charge, and the other carries negative charge.
The plates are charged by connection to a battery. Describe the process by which the plates get charged up.
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 6
For example, a `parallel plate’ capacitor, has capacitance
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 7: Parallel-Plate Capacitors
Pictures from Serway & Beichner
A
d
The electric field between the plates of a parallel-plate capacitor is uniform near the center but nonuniform near the edges.
Electric field pattern of two oppositely charged conducting parallel plates.
10/28/2011
<number>
Norah Ali Al-moneef king saud university
Notes: <number>

## Slide 8: example
What is the AREA of a 1F capacitor that has a plate separation of 1 mm?
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 9: Example: Lightning
Pictures from Serway & Beichner
Regarding the Earth and a cloud layer 800 m above the Earth as the “plates” of a capacitor, calculate the capacitance if the cloud layer has an area of 1.00 x 1.00 km2. Assume that the air between the cloud and the ground is pure and dry.
Assume that charge builds up on the cloud and on the ground until a uniform electric field of 3.00 x 106 N/C throughout the space between them makes the air break down and conduct electricity as a lightning bolt. What is the maximum charge the cloud can hold?
C= oA/d = 8.85x10-12 x (1000)2/800 = 11.1 nF
Potential between ground and cloud is
V = Ed = 3.0 x106 x 800 = 2.4 x 109 V
Q = C(V) = 26.6 C
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 10: Example
Pictures from Serway & Beichner
(a) If a drop of liquid has capacitance 1.00 pF, what is its radius ? (b) If another drop has radius 2.00 mm, what is its capacitance ? (c) What is the charge on the smaller drop if its potential is 100V ?
C = 4o R
R = (8.99 x 109 N · m2/C2)(1.00 x 10–12 F) = 8.99 mm
C = 4 (8.85 x 10-12) x 2.0x10-3 = 0.222 pF
Q =CV = 0.222 pF x 100 V = 2.22 x 10-11 C
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 11: Example
Pictures from Serway & Beichner
What is the capacitance of the Earth ?
Think of Earth spherical conductor and the outer conductor of the “spherical capacitor” may be considered as a conducting sphere at infinity where V approaches zero.
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 12: Combinations of Capacitors
Pictures from Serway & Beichner
Parallel Combination
The individual potential differences across capacitors connected in parallel are all the same and are equal to the potential difference applied across the combination.
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 13
a
b
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 14: Combinations of Capacitors
Pictures from Serway & Beichner
Series Combination
Start with uncharged situation and follow what happen just after a battery is connected to the circuit.
When a battery is connected, electrons transferred out of the left plate of C1 and into the right plate of C2.
As this charge accumulates on the right plate of C2, an equivalent amount of negative charge is forced off the left plate of C2 and this left plate there fore has an excess positive charge. (cont’d)
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 15: Capacitors in Series
a
b
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 16: Example
Pictures from Serway & Beichner
A 1-megabit computer memory chip contains many 60.0-fF capacitors. Each capacitor has a plate area of 21.0 x 10-12 m2. Determine the plate separation of such a capacitor (assume a parallel-plate configuration). The characteristic atomic diameter is 10-10 m =0.100nm. Express the plate separation in nanometers.
3.10 nm
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 17: Example: Equivalent Capacitance
Pictures from Serway & Beichner
In parallel use C=C1+C2
In series use 1/C=1/C1+1/C2
6.00 F
20.00 F
2.50 F
8.50 F
20.00 F
In series use 1/C=1/C1+1/C2
5.965 F
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 18: Example: Equivalent Capacitance
Pictures from Serway & Beichner
In parallel use C=C1+C2
In parallel use C=C1+C2
In series use 1/C=1/C1+1/C2
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 19: Example: Equivalent Capacitance 26.22
Pictures from Serway & Beichner
In series use 1/CB=1/C+1/C+1/C
In series use 1/CA=1/C+1/C
C
C/2
C/3
In parallel use Ceq=C+C/2+C/3
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 20: Energy stored in a charged capacitor
Consider the circuit to be a system
Before the switch is closed, the energy is stored as chemical energy in the battery
When the switch is closed, the energy is transformed from chemical to electric potential energy
The electric potential energy is related to the separation of the positive and negative charges on the plates
A capacitor can be described as a device that stores energy as well as charge
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 21: How Much Energy Stored in a Capacitor?
q
-q
dq
To study this problem, recall that the work the field force does equals the electric potential energy loss:
When the charge buildup is q, move a dq, the work is
This also means that when the battery moves a charge dq to charge the capacitor, the work the battery does equals to the buildup of the electric potential energy:
We now have the answer to the final charge Q:
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 22
When a capacitor has charge stored in it, it also stores electric potential energy that is
This applies to a capacitor of any geometry
The energy stored increases as the charge increases and as the potential difference (voltage) increases
In practice, there is a maximum voltage before discharge occurs between the plates
26-4 Energy Stored in a Charged Capacitor
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 23: Energy Density
Consider a Parallel Plate Capacitor:
the energy density (energy per unit volume)
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 24
The energy can be considered to be stored in the electric field
For a parallel-plate capacitor, the energy can be expressed in terms of the field as
U = ½ (εoAd)E2
It can also be expressed in terms of the energy density (energy per unit volume)
uE = ½ E2
Constant Q: How do (A,d,) affect V, E, U and u?
   C   V  E  U  u 
d   C   V  E  U  u 
A   C   V  E  U  u 
Constant V: How do (A,d,) affect Q, E, U and u?
   C   Q  E  U  u 
d   C   Q  E  U  u 
A   C   Q  E  U  u 
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 25
Capacitance of a parallel plate capacitor. A parallel plate capacitor consists of two
metal disks, 5.00 cm in radius. The disks are separated by air and are a distance of 4.00 mm apart. A potential of 50.0 V is applied across the plates by a battery. Find
(a) the capacitance C of the capacitor, and (b) the charge q on the plate.

## Slide 26
Find the energy stored in the capacitor
Find the energy density in the electric field between the plates of the above parallel plate capacitor.

## Slide 27
A dielectric is a nonconducting material that, when placed between the plates of a capacitor, increases the capacitance
  Dielectrics include rubber, glass, and waxed paper
With a dielectric, the capacitance becomes C = κCo
  The capacitance increases by the factor κ when the dielectric completely fills the region between the plates
  κ is the dielectric constant of the material Dielectric constant is a property of a material and varies from one material to another.
26-5 Capacitors with Dielectrics
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 28: Effect of a dielectric on capacitance
Potential difference with a dielectric
is less than the potential difference
across free space
Results in a higher capacitance.
Allows more charge to be stored before breakdown voltage.
If the dielectric is introduced while the potential difference is being maintained constant by a battery, the charge increases to a value Q =  Qo . The additional charge is supplied by the battery and the capacitance again increases by the factor .
C = 
A
d
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 29
For a parallel-plate capacitor, C = κεo(A/d)
In theory, d could be made very small to create a very large capacitance
In practice, there is a limit to d
  d is limited by the electric discharge that could occur though the dielectric medium separating the plates
For a given d, the maximum voltage Vmax that can be applied to a capacitor without causing a discharge depends on the dielectric strength (maximum electric field) Emaxof the material
Dielectrics provide the following advantages:
  Increase in capacitance
  Increase the maximum operating voltage
If magnitude of the electric field in the dielectric exceeds the dielectric strength, then the insulating properties break down and the dielectric begins to conduct.
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 30: Example values of dielectric constant
“Dielectric strength” is the
maximum field in the
dielectric before breakdown.
(a spark or flow of charge)
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 31: Example
Pictures from Serway & Beichner
26.33: A parallel-plate capacitor is charged and then disconnected from a battery. By what fraction does the stored energy change (increase or decrease) when the plate separation is doubled ?
U = Q2/2C
and C = oA/d
and d2 = 2 d1 then
C2= C1/2.
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 32: Rewiring Two Charged Capacitors
Pictures from Serway & Beichner
Two capacitors C1 and C2 (where C1 > C2) are charged to the same initial potential difference Vi, but with opposite polarity. The charged capacitors are removed from the battery, and their plates are connected as shown. (a) Find the final potential difference Vf between a and b after the switches are closed. (b) Find the total energy stored in the capacitors before and after the switches are closed and the ratio of the final energy to the initial energy.
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 33: Rewiring Two Charged Capacitors
Pictures from Serway & Beichner
Before switches are closed:
Q1i = C1 Vi and
Q2i = - C2 Vi (negative sign for plate 2)
Total Q = Q1i + Q2i = (C1-C2) Vi
After switches are closed:
Total charge in system remain the same
Total Q = Q1f + Q2f
Charges redistribute until the entire system is at the same potential Vf. And this potential is the same across both the capacitors.
Q1f = C1 Vf and Q2f = C2 Vf
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 34: Rewiring Two Charged Capacitors
Pictures from Serway & Beichner
After switches are closed (cont’d):
Q = Q1f + Q2f
Q1f / Q2f = C1/C2  Q1f = [ C1/C2 ] Q2f
Hence Q = Q1f + Q2f =[ 1+ C1/C2 ] Q2f
We have Q2f = Q
C2 + C1
C2
and
C2 + C1
C1
Q1f = Q
V1f
=
Q1f
C1
=
C2 + C1
C1
Q
C1
=
Q
C2 + C1
And
=
V2f
=
Vf
Vf
=
Q
C2 + C1
=
(C1-C2) Vi
C2 + C1
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 35: Rewiring Two Charged Capacitors
Energy
Before switches are closed:
Ui = C1 (Vi)2/2 + C2 (Vi)2/2 = ( C1 + C2 ) (Vi)2/2
After switches are closed:
Uf = C1 (Vf)2/2 + C2 (Vf)2/2 = ( C1 + C2 ) (Vf)2/2
Uf =
( C1 + C2 )
1
2
Q
C2 + C1
2
=
1
2
Q2
C2 + C1
Uf =
1
2
C2 + C1
(C1-C2)2 (Vi )2
Ui =
1
2
( C1 + C2 ) (Vi)2
We have
Uf
Ui
=
C1 - C2
C1+ C2
2
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 36: Types of Capacitors
Pictures from Serway & Beichner
(a) A tubular capacitor, whose plates are separated by paper and then rolled into a cylinder. (b) A high-voltage capacitor consisting of many parallel plates separated by insulating oil. (c) An electrolytic capacitor.
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 37: Question
<number>
d
A
- - - - -
+ + + +
Suppose the capacitor shown here is charged to Q and then the battery is disconnected.
Now suppose I pull the plates further apart so that the final separation is d1.
How do the quantities Q, C, E, V, U change?
How much do these quantities change?.. exercise for student!!
Q:
C:
E:
V:
U:
remains the same.. no way for charge to leave.
increases.. add energy to system by separating
decreases.. since capacitance depends on geometry
increases.. since C , but Q remains same (or d  but E the same)
remains the same... depends only on charge density
Answers:
10/28/2011
Norah Ali Al-moneef king saud university

## Slide 38
<number>
Another Question
Suppose the battery (V) is kept attached to the capacitor.
Again pull the plates apart from d to d1.
Now what changes?
C:
V:
Q:
E:
U:
decreases (capacitance depends only on geometry)
must stay the same - the battery forces it to be V
must decrease, Q=CV charge flows off the plate
d
A
- - - - -
+ + + +
V
How much do these quantities change?.. exercise for student!!
Answers:
must decrease ( , )
must decrease ( )
10/28/2011
Norah Ali Al-moneef king saud university

## Slide 39
<number>
Two identical parallel plate capacitors are connected to a battery, as shown in the figure. C1 is then disconnected from the battery, and the separation between the plates of both capacitors is doubled.
What is the relation between the charges on the two capacitors ?
a) Q1 > Q2 b) Q1 = Q2 c) Q1 < Q2
How does the electric field between the plates of C2 change as separation between the plates is increased ? The electric field:
a) increases b) decreases c) doesn’t change
Question
10/28/2011
Norah Ali Al-moneef king saud university

## Slide 40
<number>
Two identical parallel plate capacitors are connected to a battery, as shown in the figure. C1 is then disconnected from the battery, and the separation between the plates of both caps is doubled.
What is the relation between the voltages on the two capacitors?
a) V1 > V2 b) V1 = V2 c) V1 < V2
Question
10/28/2011
Norah Ali Al-moneef king saud university

## Slide 41
Find the capacitance of a 4.0 cm diameter sensor immersed in oil if the plates are separated by 0.25 mm.
The plate area is
The distance between the plates is
178 pF
10/28/2011
<number>
Norah Ali Al-moneef king saud university
Question

## Slide 42: Question
<number>
d
d
V
2d
2d
V
C1
C2
Two identical parallel plate capacitors are connected to a battery.
  What is the relation between the U1, the energy stored in C1, and the U2, energy stored in C2?
  C1 is then disconnected from the battery and the separation between the plates of both capacitors is doubled.
(a) U1 < U2
(b) U1 = U2
(c) U1 > U2
What is the difference between the final states of the two capacitors?
  The charge on C1 has not changed.
  The voltage on C2 has not changed.
The energy stored in C1 has definitely increased since work must be done to separate the plates with fixed charge, they attract each other.
The energy in C2 will actually decrease since charge must leave in order to reduce the electric field so that the potential remains the same.
Initially:
Later:
10/28/2011
Norah Ali Al-moneef king saud university

## Slide 43
Two parallel conducting plates, separated by a
distance d, are connected to a battery of emf .
Which of the following is correct if the plate separation is doubled while the battery remains connected?
(A) The electric charge on the plates is doubled.
(B) The electric charge on the plates is halved.
(C) The potential difference between the plates is doubled.
(D) The potential difference between the plates is halved
(E) The capacitance is unchanged.
Answer: B
Notes: <number>

## Slide 44
o
o
C
C
C
Ceq
1) Ceq = 3/2 C
2) Ceq = 2/3 C
3) Ceq = 3 C
4) Ceq = 1/3 C
5) Ceq = 1/2 C
What is the equivalent capacitance, Ceq , of the combination below?
Notes: <number>

## Slide 45
1) V1 = V2
2) V1 > V2
3) V1 < V2
4) all voltages are zero
C1 = 1.0 F
C3 = 1.0 F
C2 = 1.0 F
10 V
How does the voltage V1 across the first capacitor (C1) compare to the voltage V2 across the second capacitor (C2)?
Notes: <number>

## Slide 46
C1 = 1.0 F
C3 = 1.0 F
C2 = 1.0 F
10 V
1) Q1 = Q2
2) Q1 > Q2
3) Q1 < Q2
4) all charges are zero
How does the charge Q1 on the first capacitor (C1) compare to the charge Q2 on the second capacitor (C2)?
Notes: <number>

## Slide 47
. A 4 F capacitor is charged to a potential difference of
100 V. The electrical energy stored in the capacitor is
(A) 2 x 10-10 J (B) 2 x 10‑8 J (C) 2 x 10‑6 J (D) 2 x 10-4 J (E) 2 x 10-2 J
Answer: E
Notes: <number>

## Slide 48
1- When a potential difference of 150 V is applied to the plates of a parallel-plate capacitor, the plates carry a surface charge density of 30.0 nC/cm2. What is the spacing between the plates?
2-Four capacitors are connected as shown in the Figure
Find the equivalent capacitance between points a and b.
Calculate the charge on each capacitor if ΔVab = 15.0 V.
Homework
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 49
3 - Find the equivalent capacitance between points a and b for the group of capacitors connected as shown in the Figure. Take C1 = 5.00 μF, C2 = 10.0 μF, and C3 = 2.00 μF.
4- A parallel-plate capacitor is charged and then disconnected from a battery. By what fraction does the stored energy change (increase or decrease) when the plate separation is doubled?
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 50
5- Determine (a) the capacitance and (b) the maximum potential difference that can be applied to a Teflon-filled parallel-plate capacitor having a plate area of 1.75 cm2 and plate separation of 0.040 0 mm.
6 - A parallel-plate capacitor is constructed using a dielectric material whose dielectric constant is 3.00 and whose dielectric strength is 2.00 × 108 V/m. The desired capacitance is 0.250 μF, and the capacitor must withstand a maximum potential difference of 4 000 V. Find the minimum area of the capacitor plates.
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 51
Pictures from Serway & Beichner
7- Consider the circuit as shown, where C1 = 6.00F and C2= 3.00 F and V =20.0V. Capacitor C1 is first charged by closing of switch S1. Switch S1 is then opened and the charged capacitor is connected to the uncharged capacitor by the closing of S2. Calculate the initial charge acquired by C1 and the final charge on each.
10/28/2011
<number>
Norah Ali Al-moneef king saud university

## Slide 52
10/28/2011
Norah Ali Al-moneef king saud university
<number>
8- Given a 7.4 pF air-filled capacitor. You are asked to convert it to a capacitor that can store up to 7.4 J with a maximum voltage of 652 V. What dielectric constant should the material have that you insert to achieve these requirements?
9-An air-filled parallel plate capacitor has a capacitance of 1.3 pF. The separation of the plates is doubled, and wax is inserted between them. The new capacitance is 2.6pF. Find the dielectric constant of the wax.
10- Consider a parallel plate capacitor with capacitance C = 2.00 F connected to a battery with voltage V = 12.0 V as shown. A) What is the charge stored in the capacitor?
b) Now insert a dielectric with dielectric constant  = 2.5 between the plates of the capacitor. What is the charge on the capacitor?

## Slide 53
10/28/2011
Norah Ali Al-moneef king saud university
<number>
11- An isolated conducting sphere whose radius R is 6.85 cm has a charge of q=1.25 nC. a) How much potential energy is stored in the electric field of the charged conductor?
Find the equivalent capacitance
12 - If each capacitor has a capacitance of 5 nF, what is the capacitance of this system of capacitors?
13- A storage capacitor on a random access memory (RAM) chip has a capacitance of 55 nF. If the capacitor is charged to 5.3 V, how many excess electrons are on the negative plate?

## Slide 54
10/28/2011
Norah Ali Al-moneef king saud university
<number>
14 - A parallel plate capacitor made from 2 squares of metal, 2mm thick and 20cm on a side separated by 1mm with 1000V between them Find:
a) capacitance b)charge per plate c) charge density d)electric field e) energy stored f) energy density
15 -
16 - One common kind of computer keyboard is based on the idea of capacitance. Each key is mounted on one end of a plunger, the other end being attached to a movable metal plate. The movable plate and the fixed plate form a capacitor. When the key is pressed, the capacitance increases. The change in capacitance is detected, thereby recognizing the key which has been pressed.
The separation between the plates is 5.00 mm, but is reduced to 0.150 mm when a key is pressed. The plate area is 9.50x10-5m2 and the capacitor is filled with a material whose dielectric constant is 3.50.
Determine the change in capacitance detected by the computer.