## Slide 1
2.<number>
Chapter 2
Network Models
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Notes: <number>

## Slide 2
2.<number>
2-1 LAYERED TASKS
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.
Sender, Receiver, and Carrier Hierarchy Tasks must be done in order given in hierarchy
Services : each layer at the sending site uses the services of the layer below it.
Topics discussed in this section:
Notes: <number>

## Slide 3
2.<number>
Figure 2.1 Tasks involved in sending a letter
Notes: <number>

## Slide 4
2.<number>
Figure 2.2 Seven layers of the OSI model
Layer: A grouping of related tasks involving the transfer of information .Each layer addresses an essential networking tasks
Notes: <number>

## Slide 5
2.<number>
2-1 Internet layers
Within a single machine, each layer use services provided by layer below it and provides services for layer above it .
Ex. Layer 3 provides services to layer 4 and uses services provided by layer 2.
Peer-to-peer process : The processes on each machine that communicate at a given layer are called peer –to-peer processes
Between machines layer x communicates with layer x on another machine by protocols.
Communication between machines is peer-to-peer processing using the protocols appropriate to a given layer.
Interfaces : Between each pair of adjacent layers . It defines what information and services a layer must provide for layer above it
Notes: <number>

## Slide 6
2.<number>
2-1 Internet layers
Network support layer :
Deal with the physical aspects of moving data from one device to another such as :electrical specifications , physical connections, physical addressing, transport timing and reliability. Includes Layers 1, 2 and 3
User support layer: Application layer, presentation ,session Layers 5,6 and 7
Layer 4(transport layer) links the two subgroups to insure that what the lower layers have transmitted is in form the upper layer can use
Notes: <number>

## Slide 7
2.<number>
Figure 2.3 The interaction between layers in the OSI model
Notes: <number>

## Slide 8
2.<number>
2-2 THE OSI MODEL
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
Layered Architecture Peer-to-Peer Processes
Encapsulation
Topics discussed in this section:
Notes: <number>

## Slide 9
2.<number>
Figure 2.4 An exchange using the OSI model
Notes: <number>

## Slide 10
2.<number>
2-1 Internet layers
The layers in the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.
Layer: A grouping of related tasks involving the transfer of information .Each layer addresses an essential networking tasks
Notes: <number>

## Slide 11
2.<number>
2-2 THE OSI MODEL
At sender:
at each layer, a header can added to the data unit.
At layer 2 a trailer is added as well .
When formatted data unit passes through physical layer it is changed into an electromagnetic signal and transported along physical link.
Encapsulation:
A packet (header and data ) at level 5 is encapsulated in a packet in level 4, and so on.
The data portion of packet at level N-1 carries the whole packet (data and header/trailer) from level N.
At destination:
A data then move back up through the layer
a headers and trailers attached to data at the corresponding layer are removed (decapsulated) and action appropriate to that layer are taken. (unwrapped/decapsulated)
At layer 5 the message is again in form appropriate to the application and is made available to user.
Notes: <number>

## Slide 12
2.<number>
ISO is the organization. OSI is the model.
Note
Notes: <number>

## Slide 13
2.<number>
2-3 LAYERS IN THE OSI MODEL
In this section we briefly describe the functions of each layer in the OSI model.
Physical Layer Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
Topics discussed in this section:
Notes: <number>

## Slide 14
2.<number>
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.
Note
1. Physical layer
Notes: <number>

## Slide 15
2.<number>
Figure 2.5 Physical layer
Notes: <number>

## Slide 16
2.<number>
Physical characteristic of interfaces and media:
It defines the characteristic of the interface between devices and media. It also define the type of transmission media
Representation of bits:
The bit stream must be encoded into signals. It defines the type of representation ( how 0, 1 are changed to signal).
Data rate:
It defines the number of bits sent per second and also the duration of bits.
Synchronization of bits
The sender and receiver must be use the same bit rate also the receiver clock must be synchronized
Duties Of physical Layer
Notes: <number>

## Slide 17
2.<number>
Line configuration
Physical layer is concerned with the connection of devices to the media ( point-to point or multipoint)
Physical topology:
How devices connected to make a network
Devices can connected by using Star, mesh , bus, ring or hybrid topology
Transmission mode:
It defines the direction of transmission between two devices (simplex, half-duplex, or full duplex)
Duties Of physical Layer
Notes: <number>

## Slide 18
2.<number>
The data link layer is responsible for moving frames from one hop (node) to the next.
Note
2. Data Link Layer( hop to hop delivery)
Notes: <number>

## Slide 19
2.<number>
Figure 2.6 Data link layer
Notes: <number>

## Slide 20
2.<number>
Framing:
Divide the stream of bits received from network layer into data units called frames
Physical addressing:
It adds a header to the frame to define the sender and receiver of the frame.
If the frame for a system outside the sender’s network the receiver address: is the address of the connecting device that connects the network to next one (Router/switch).
Flow control:
It imposes a flow control mechanism , if the data rate at the receiver is less than produced by sender the data link layer imposes a flow control to avoid overwhelming the receiver
Duties Of Data Link Layer
Notes: <number>

## Slide 21
2.<number>
Error control:
Add mechanisms to detect and retransmit damaged or lost frames.
Prevent also duplication of frames.
Error control is normally achieved through a trailer added to the end of frame.
Access control:
When two or more devices than one devices are connected to the same link, data link layer protocols are necessary to determine which device has control over the link at given time.
Duties Of Data Link Layer
Notes: <number>

## Slide 22
2.<number>
Figure 2.7 Hop-to-hop delivery
Notes: <number>

## Slide 23
2.<number>
known also as the MAC or link address
Is the address of a node as defined by its LAN or WAN
It is included in the frame used by data link layer (Header)
Ethernet uses 6-bytes (48-bits) physical address that imprinted on the NIC
Physical address
Notes: <number>

## Slide 24
2.<number>
Example
A node with physical address 10 sends a frame to a node with physical address 87. The two nodes are connected by a link. At the data link level this frame contains physical addresses in the header. These are the only addresses needed. The rest of the header contains other information needed at this level. The trailer usually contains extra bits needed for error detection
Physical address
Notes: <number>

## Slide 25
2.<number>
Physical address
Notes: <number>

## Slide 26
2.<number>
The network layer is responsible for the delivery of individual packets from the source host to the destination host across multiple network.
If two system are connected to the same link (network), no need for this layer.
Note
3. Network Layer( hop to hop delivery)
Notes: <number>

## Slide 27
2.<number>
Figure 2.8 Network layer
Notes: <number>

## Slide 28
2.<number>
Logical addressing
In contrast to physical addressing implemented by data link layer handling the addressing problem locally. Net work layer adds unique identifier ( IP or logical address) to the packet.
These unique identifier( as tel. no, each tel. has unique number ) enable special devices called router to make sure the packet get to correct system.
Routing:
provide the routing mechanism for the router which route the packet to their final destination.
Routers : devices used when independent networks are connected to create an internetworking ( network of networks)
Duties Of Network Layer
Notes: <number>

## Slide 29
2.<number>
Figure 2.9 Source-to-destination delivery
Notes: <number>

## Slide 30
2.<number>
IP addresses are necessary for universal communications that are independent of physical network.
No two host address on the internet can have the same IP address
IP addresses 32-bit address that uniquley define a host connected to the Internet
Logical address (IP)
Logical address (IP) The physical addresses will change from hop to hop, but the logical addresses remain the same.
Notes: <number>

## Slide 31
2.<number>
Example2:
The following figure shows a part of an internet with two routers connecting three LANs. Each device (computer or router) has a pair of addresses (logical and physical) for each connection. In this case, each computer is connected to only one link and therefore has only one pair of addresses. Each router, however, is connected to three networks (only two are shown in the figure). So each router has three pairs of addresses, one for each connection.
Notes: <number>

## Slide 32
2.<number>
Example2:
Notes: <number>

## Slide 33
2.<number>
The transport layer is responsible for the delivery of a message from one process to another.
Note
3. Transport Layer(process to process delivery)
Notes: <number>

## Slide 34
2.<number>
Figure 2.10 Transport layer
Notes: <number>

## Slide 35
2.<number>
Port addressing (Service-point addressing)
Computer often run several process ( running programs) at the same time, so the process to process delivery means delivery from a specific process on a computer to specific process to the other.
The transport layer header must include Port address
Port address: 16-bit addresses represented by decimal number range from 0-65535 to choose among multiple processes on the destination host
Destination port No is needed for delivery
Source port No is needed for replay.
Duties Of transport Layer
Notes: <number>

## Slide 36
2.<number>
IP (logical address )and port address play different roles in selecting the final destination
IP: defines the host among the different hosts in the world
After host is selected , the port address defines one of the processes on this particular host.

## Slide 37
2.<number>
2. Segmentation and reassembly
A message is divided into small pieces (Segment), each segment containing sequence number. These number enable the transport layer to reassemble the message correctly at destination and to identify and replace segment that were lost in transmission.
3.Flow control:
Like the data link layer, transport layer responsible for flow control. Flow control at this layer is performed end to end rather than across a single link.
Duties Of transport Layer
Notes: <number>

## Slide 38
2.<number>
4. Error control
•Error control at this layer is performed process-to-process rather than across a single link
•The sending transport layer makes sure that the entire message arrives at the receiving transport layer without error (damage, loss or duplicated).
•Error correction is usually achieved through retransmission
Duties Of transport Layer
Notes: <number>

## Slide 39
2.<number>
5. Connection control
The transport layer can be either connection less or connection oriented
1. Connection oriented
Makes a connection with the transport layer at the destination machine first before delivering the packers.
When the connection established a sequence of packets from source to the destination can be sent one after another on the same path and in sequential order.
When all packets of message have been delivered, the connection is terminated
This makes the sending transport layer ensure that the message arrives at the receiving transport layer without error ( damage, loss or duplication
Duties Of transport Layer
Notes: <number>

## Slide 40
2.<number>
Duties Of transport Layer
2. Connection Less ( as Internet)
It sends the data, but does not establish and verify a connection between hosts before sending data.
Treats each packet independently, the packets in a message may or may not travel the same path to their destination.
Notes: <number>

## Slide 41
2.<number>
Figure 2.11 Reliable process-to-process delivery of a message
The network layer gets each packet to the correct computer; the transport layer gets the message to the correct processes on that computer
Notes: <number>

## Slide 42
2.<number>
Example
The following figure shows two computers communicating via the Internet. The sending computer is running three processes at this time with port addresses a, b, and c. The receiving computer is running two processes at this time with port addresses j and k. Process a in the sending computer needs to communicate with process j in the receiving computer.
Note that although physical addresses change from hop to hop, logical and port addresses remain the same from the source to destination.
Notes: <number>

## Slide 43
2.<number>
Notes: <number>

## Slide 44
2.<number>
Four levels of addresses are used in an internet employing the TCP/IP protocols: physical , logical , port and Specific addresses :
examples:
e-mail addresses ( Lhajr@yahoo.com) to define the recipient of an e-mail
URL addresses ( www.ksu.com) to find a document on the world wide web
The addresses get changed to the corresponding port and logical addresses by the sending computer
ADDRESSING
Notes: <number>

## Slide 45
2.<number>
Note
5. Session Layer
The session layer is responsible for dialog control and synchronization.
Notes: <number>

## Slide 46
2.<number>
Figure 2.12 Session layer
Notes: <number>

## Slide 47
2.<number>
1. Dialog control:
Allows two systems to enter into dialog. It allows communication between two processes in either half or full duplex.
2. Synchronization (Recovery)
Allow a process to add check points (Synchronization point) into a stream of data . So that if a failure of some sort occurs between checkpoints, the layer can retransmit all data since the last checkpoint.
Duties Of Session Layer
Notes: <number>

## Slide 48
2.<number>
The presentation layer is responsible for translation, compression, and encryption.
Note
6. Presentation Layer
Notes: <number>

## Slide 49
2.<number>
Figure 2.13 Presentation layer
Notes: <number>

## Slide 50
2.<number>
Duties Of Presentation Layer
1.Translation
At the sender it changes the information from its sender –dependent format into common format. At receiving, changes the common format into its receiver-dependent format
2. Encryption-Decryption
To ensure privacy and security
3. Compression
Data compression reduces the number of bits contained in the information. It is important in the transmission of multimedia such as audio or video
Notes: <number>

## Slide 51
2.<number>
The application layer is responsible for providing services to the user.
Note
7 . Application Layer
Notes: <number>

## Slide 52
2.<number>
Figure 2.14 Application layer
Notes: <number>

## Slide 53
2.<number>
Application Layer
The application layer is responsible for providing services to the user such as
Mail services
File transfer and access
Remote log-in Accessing the web (WWW)
•Telnet: A service that enables users on the internet to log onto remote systems from their own host system.
•HTTP: Hyper text transfer protocol used for network file transfers in WWW environment
•SMTP: Simple mail transfer protocol used to send electronic mail on the internet.
Notes: <number>

## Slide 54
2.<number>
OSI model
Notes: <number>

## Slide 55
2.<number>
Figure 2.15 Summary of layers
Notes: <number>

## Slide 56
2.<number>
2-4 TCP/IP PROTOCOL SUITE
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model. However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.
Physical and Data Link Layers Network Layer Transport Layer
Application Layer
Topics discussed in this section:
Notes: <number>

## Slide 57
2.<number>
Figure 2.18 Relationship of layers and addresses in TCP/IP
Notes: <number>

## Slide 58
2.<number>
Most local-area networks use a 48-bit (6-byte) physical address written as 12 hexadecimal digits; every byte (2 hexadecimal digits) is separated by a colon, as shown below:
Example 2.2
07:01:02:01:2C:4B
A 6-byte (12 hexadecimal digits) physical address.
Notes: <number>