## Slide 1
Chapter 3
The Data Link Layer
Prepared by :
Dr. Adel Soudani & Dr. Mznah Al-Rodhaan

## Slide 2: The Data Link Layer
  Data Link Layer Design Issues
  Error Detection and Correction
  Elementary Data Link Protocols
  Sliding Window Protocols
  Example Data Link Protocols
Notes: Gray units can be optionally omitted without causing later gaps

## Slide 3: The Data Link Layer
Responsible for delivering frames of information over a single link
  Handles transmission errors and regulates the flow of data
Physical
Link
Network
Transport
Application

## Slide 4: The Data Link Layer

## Slide 5: Data Link Layer Design Issues
  Frames »
  Possible services »
  Framing methods »
  Error control »
  Flow control »

## Slide 6
Framing

## Slide 7: Frames
Link layer accepts packets from the network layer, and encapsulates them into frames that it sends using the physical layer; reception is the opposite process
Actual data path
Virtual data path
Network
Link
Physical

## Slide 8: Framing Methods
  Byte count »
  Flag bytes with byte stuffing »
  Flag bits with bit stuffing »
  Physical layer coding violations
    Use non-data symbol to indicate frame

## Slide 9: Framing – Byte count
Frame begins with a count of the number of bytes in it
  Simple, but difficult to resynchronize after an error
Error
case
Expected
case

## Slide 10: Framing – Byte stuffing
Special flag bytes delimit frames; occurrences of flags in the data must be stuffed (escaped)
  Longer, but easy to resynchronize after error
Stuffing
examples
Frame
format
Need to escape extra ESCAPE bytes too!

## Slide 11: Framing – Bit stuffing
Stuffing done at the bit level:
  Frame flag has six consecutive 1s (01111110)
  On transmit, after five 1s in the data, a 0 is added
  On receive, a 0 after five 1s is deleted
Transmitted bits
with stuffing
Data bits

## Slide 12: Error Control
Error control repairs frames that are received in error
  Requires errors to be detected at the receiver
  Typically retransmit the unacknowledged frames
  Timer protects against lost acknowledgements
Detecting errors and retransmissions are next topics.
Notes: We’ll get to this later in the chapter (error detection/correction, and elementary data link protocols)

## Slide 13: Flow Control
Prevents a fast sender from out-pacing a slow receiver
  Receiver gives feedback on the data it can accept
  Rare in the Link layer as NICs run at “wire speed”
    Receiver can take data as fast as it can be sent
Flow control is a topic in the Data Link and Transport layers.
Notes: We’ll get to this later in the chapter (sliding window protocol) but note that flow control is mostly the responsibility of the Transport layer in practice (e.g., TCP)

## Slide 14
Lecture 2
Error Control

## Slide 15
Data Link Layer

## Slide 16
3.1 INTRODUCTION
Types of Errors Redundancy Detection Versus Correction
Detection
      Parity Check
      Cyclic Redundancy Check (CRC)
      Checksum
Corrections
  Retransmission
  Forward Error Correction
  Burst Error Correction
Topics discussed in this section:

## Slide 17
Data can be corrupted during transmission.
Some applications require that errors be detected and corrected.

## Slide 18
In a single-bit error, only 1 bit in the data unit has changed.
Types of Errors
1. Single-bit error

## Slide 19
A burst error means that 2 or more bits in the data unit have changed.
Types of Errors
2. Burst error

## Slide 20
To detect or correct errors, we need to send extra (redundant) bits with data.
Error detection uses the concept of redundancy, which means adding extra bits for detecting errors at the destination.
Redundancy

## Slide 21
Redundancy

## Slide 22
XORing of two single bits or two words

## Slide 23
We divide the message into blocks, each of m bits, called datawords. We add r redundant bits to each block to make the length
n = m + r.
The resulting n-bit blocks are called codewords.
Error Detection Error Correction
Topics discussed in this section:
3.2 Block Coding
2 r ≥ m+r+1

## Slide 24
Error Detection
Solution
Retransmission

## Slide 25
Error Correction
Solution
Forward Error Correction
Burst Error Correction

## Slide 26
Error Detection
3.3 Linear Block Coding

## Slide 27
Even-parity concept
      Simple Parity Check code
Odd-parity concept ?

## Slide 28
      Parity Check

## Slide 29
Simple parity check can detect all single-bit errors.
It can detect burst errors only if the total number of errors in each data unit is odd for even-parity.

## Slide 30
Two-dimensional parity-check code
In two-dimensional parity check, a block of bits is divided into rows and a redundant row of bits is added to the whole block.

## Slide 31
Two-dimensional parity-check code

## Slide 32
Two-dimensional parity

## Slide 33
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
Sent
Received
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 34
Two-dimensional parity-check code

## Slide 35
Two-dimensional parity-check code

## Slide 36
Lecture 3
Error Detection and Correction

## Slide 37
Hamming Code
Hamming codes provide for FEC using a “Block Parity”
  i.e, instead of one parity bit send a block of parity bits
Allows correction of single bit errors
This is accomplished by using more than one parity bit
Each computed on different combination of bits in the data
Note: Study the Hamming code from the slides.

## Slide 38
Redundancy Bits Calculation
Decimal | Binary
3 | 0011
5 | 0101
6 | 0110
7 | 0111
9 | 1001
10 | 1010
11 | 1011
    Uses four (4) parity bits
      Bit Position 1 (r1): Bits 3, 5, 7, 9, 11
      Bit Position 2 (r2): Bits 3, 6, 7, 10, 11
      Bit Position 4 (r3): Bits 5, 6, 7
      Bit Position 8 (r4): Bits 9, 10, 11
Parity Bits

## Slide 39
Redundancy Bits Calculation
Position 1: check 1 bit, skip 1 bit, ..etc. (1,3,5,7,9,11,13,15,...)
Position 2: check 2 bits, skip 2 bits, ..etc. (2,3,6,7,10,11,14,15,...)
Position 4: check 4 bits, skip 4 bits, ..etc. (4,5,6,7,12,13,14,15,20,21,22,23,...)
Position 8: check 8 bits, skip 8 bits..etc. (8-15,24-31,40-47,...)
Position 16: check 16 bits, skip 16 bits, ..etc. (16-31,48-63,80-95,...)

## Slide 40
Redundancy Bits Calculation

## Slide 41
Example
Redundancy bits calculation using even-parity ( at the sender)
So the sender will send 10011100101

## Slide 42
Error Correction using Hamming Code
At the receiver:
So the corrected data will be 10011100101

## Slide 43
Error Correction using Hamming Code
    Hamming code Increases overhead in both data transmitted and processing time

## Slide 44
Burst error correction using Hamming code

## Slide 45
Lecture 4
Cyclic codes

## Slide 46
3.4 CYCLIC CODES
In a cyclic code, if a codeword is cyclically shifted (rotated), the result is another codeword.
Cyclic Redundancy Check
Generator and Checker Polynomials Checksum
Topics discussed in this section:
Cyclic codes
  Cyclic Redundancy Check
  Checksum

## Slide 47
CRC generator and checker

## Slide 48
A CRC code with C(7, 4)

## Slide 49: Binary Division
Find the quotient and remainder when 1111101 is divided by 1101 in modulo 2 arithmetic.
  As with traditional division, we note that the dividend is divisible once by the divisor.
  We place the divisor under the dividend and perform modulo 2 subtraction.

## Slide 50: Binary Division
Find the quotient and remainder when 1111101 is divided by 1101 in modulo 2 arithmetic…
  Now we bring down the next bit of the dividend.
  We see that 00101 is not divisible by 1101. So we place a zero in the quotient.

## Slide 51: 2.8 Error Detection and Correction
Find the quotient and remainder when 1111101 is divided by 1101 in modulo 2 arithmetic…
  1010 is divisible by 1101 in modulo 2.
  We perform the modulo 2 subtraction.
Binary Division

## Slide 52: 2.8 Error Detection and Correction
Find the quotient and remainder when 1111101 is divided by 1101 in modulo 2 arithmetic…
  We find the quotient is 1011, and the remainder is 0010.
This procedure is very useful to us in calculating CRC syndromes.
Binary Division

## Slide 53
Division in CRC encoder

## Slide 54
Division in the CRC decoder for two cases

## Slide 55: At the sender side
Suppose we want to transmit the information string: 1111101.
The receiver and sender decide to use the polynomial pattern, 1101.
The information string is shifted left by one position less than the number of positions in the divisor.
The remainder is found through modulo 2 division (at right) and added to the information string: 1111101000 + 111 = 1111101111.

## Slide 56: At the receiver side
If no bits are lost or corrupted, dividing the received information string by the agreed upon pattern will give a remainder of zero.
We see this is so in the calculation at the right.
Real applications use longer polynomials to cover larger information strings.

## Slide 57
A polynomial to represent a binary word
Note:
The divisor 1101 corresponds to the polynomial: X 3 + X 2 + 1.
The divisor 1011 corresponds to the polynomial: X 3 + X 1 + 1.

## Slide 58
The divisor in a CRC is normally called the generator polynomial
or simply the generator.

## Slide 59
A good polynomial generator needs to have the following characteristics:
1. It should have at least two terms.
2. The coefficient of the term x0 should be 1.
3. It should have the factor x + 1.
polynomial generator

## Slide 60
polynomial generator
It is obvious that we cannot choose x (binary 10) or x2 + x (binary 110) as the polynomial because both are divisible by x to guarantee that all burst errors of length ≤ degree of the polynomial are detected.
However, we can choose x + 1 (binary 11) or x2 + 1 (binary 101) because it is divisible by x + 1 (binary division) to guarantee that all burst of odd numbers are detected.

## Slide 61
The CRC-12
x12 + x11 + x3 + x + 1
which has a degree of 12, will detect all burst errors affecting an odd number of bits, will detect all burst errors with a length less than or equal to 12, and will detect, 99.97 percent of the time, burst errors with a length of 12 or more.
Example 1

## Slide 62
If the generator has more than one term and the coefficient of x0 is 1, all single errors can be caught.
A generator that contains a factor of x + 1 can detect all odd-numbered errors.

## Slide 63
Standard polynomials
Name | Polynomial | Application
CRC-8 | x8 + x2 + x + 1 | ATM header
CRC-10 | x10 + x9 + x5 + x4 + x 2 + 1 | ATM AAL
CRC-16 (ITU-16) | x16 + x12 + x5 + 1 | HDLC
CRC-32 (ITU-32) | x32 + x26 + x23 + x22 + x16 + x12 + x11 + x10 + x8 + x7 + x5 + x4 + x2 + x + 1 | LANs

## Slide 64
Lecture 5
Checksum

## Slide 65
3.5 CHECKSUM
Checksum is an error detection method. The checksum is used in the Internet by several protocols although not at the data link layer. However, we briefly discuss it here to complete our discussion on error checking
Idea One’s Complement Internet Checksum
Topics discussed in this section:

## Slide 66
CHECKSUM

## Slide 67
CHECKSUM
The sender follows these steps:
The unit is divided into k sections, each of n bits.
All sections are added using one’s complement to get the sum.
The sum is complemented and becomes the checksum.
The checksum is sent with the data.

## Slide 68
CHECKSUM
The receiver follows these steps:
The unit is divided into k sections, each of n bits.
All sections are added using one’s complement to get the sum.
The sum is complemented.
If the result is zero, the data are accepted: otherwise, rejected.

## Slide 69
Example 2
Suppose the following block of 16 bits is to be sent using a checksum of 8 bits.
10101001 00111001
The numbers are added using one’s complement
10101001
00111001 ------------ Sum 11100010
Checksum 00011101
The pattern sent is 10101001 00111001 00011101

## Slide 70
Example 3
Now suppose the receiver receives the pattern sent in Example 2 and there is no error. 10101001 00111001 00011101
When the receiver adds the three sections, it will get all 1s, which, after complementing, is all 0s and shows that there is no error.
10101001
00111001
00011101
Sum 11111111
Complement 00000000 means that the pattern is OK.

## Slide 71
Example 4
Now suppose there is a burst error of length 5 that affects 4 bits.
10101111 11111001 00011101
When the receiver adds the three sections, it gets
10101111
11111001
00011101
Partial Sum 1 11000101
Carry 1
Sum 11000110
Complement 00111001 the pattern is corrupted.

## Slide 72
Example 5
If we need to send the set of numbers (7, 11, 12, 0, 6), we
1111
0000
0110
1001

## Slide 73
An error-detecting code can detect only the types of errors for which it is designed; other types of errors may remain undetected.

## Slide 74
Lecture 6
Flow Control

## Slide 75: Data Link Layer (DLL)

## Slide 76: Flow and Error Control
The most important responsibilities of the data link layer are flow control and error control. Collectively, these functions are known as data link control.
  Flow control refers to a set of procedures used to restrict the amount of data that the sender can send before waiting for acknowledgment.
  Error control in the data link layer is based on automatic repeat request (ARQ), which is the retransmission of data.

## Slide 77
Protocols

## Slide 78: Noisy Channels
We discuss three protocols in this section that use error control.
  Stop & Wait Automatic Repeat Request
  Go-Back-N Automatic Repeat Request
  Selective Repeat Automatic Repeat Request

## Slide 79: Stop-and-Wait Automatic Repeat Request
Simplest flow and error control mechanism
The sending device keeps a copy of the last frame transmitted until it receives an acknowledgement
  Identification of duplicate transmission
A damaged or lost frame is treated in the same way at the receiver.
A control variable is needed at both sides.
Timers introduced at the sender side.
Positive ACK sent only for frames received safe & sound to define the next expected frame.

## Slide 80: Stop-and-Wait

## Slide 81: Stop-and-Wait ARQ
Cases of operations:
Normal operation
The frame is lost
The ACK is lost
The ACK is delayed

## Slide 82: Stop-and-Wait ARQ Normal operation
The sender will not send the next piece of data until it is sure that the current one is correctly received
sequence number is necessary to check for duplicated packets
No NACK – when packet is corrupted – duplicate ACKs instead

## Slide 83: Stop-and-Wait ARQ Lost or damaged frame
A damaged or lost frame is treated in the same way at the receiver.

## Slide 84: Stop-and-Wait ARQ Lost ACK
Importance of frame numbering

## Slide 85: Stop-and-Wait ARQ Delayed ACK
Importance of ACK numbering

## Slide 86: Duplex Stop-and-Wait ARQ
Piggybacking
  combine data with ACK (less overhead saves bandwidth)

## Slide 87
The bandwidth-delay product defines the number of bits that can fill the link.
bandwidth-delay product = Bandwidth * Delay.
Efficiency

## Slide 88
Assume that, in a Stop-and-Wait ARQ system, the bandwidth of the line is 1 Mbps, and 1 bit takes 20 ms to make a round trip. What is the bandwidth-delay product?
If the system data frames are 1000 bits in length, what is the utilization percentage of the link?
Solution
The bandwidth-delay product is
Example
the utilization percentage of the link is
1000/20,000 = 5%

## Slide 89: Stop-and-Wait ARQ
After each frame sent the host must wait for an ACK
  inefficient use of bandwidth
To improve efficiency ACK should be sent after multiple frames
Alternatives: Sliding Window protocols
  Go-back-N ARQ
  Selective Repeat ARQ

## Slide 90
Lecture 7
Go-back-N

## Slide 91: Pipelining
One task begins before the other one ends
  increases efficiency in transmission
There is no pipelining in Stop-and-Wait ARQ

## Slide 92: Sliding Window Protocols
Sequence numbers
  Sent frames are numbered sequentially
  Sequence number is stored in the header
    if the number of bits to store the sequence number is m than sequence number goes from 0 to 2m-1
sequence numbers
frame
acknowledged frames
Sliding window
  to hold the unacknowledged outstanding frames
  In Go-back-N ARQ the receiver window size always 1

## Slide 93: Go-back-N Control variables
S- holds the sequence number of the recently sent frame
SF – holds sequence number of the first frame in the window
SL – holds the sequence number of the last frame or Sn – holds the sequence number of the next frame to be send
R – sequence number of the frame expected to be received

## Slide 94: Go-back-N

## Slide 95: Go-back-N

## Slide 96: The name of Go-back-N: why?
Re-sending frame
  when the frame is damaged the sender goes back and resends a set of frames starting from the last one acknowledged; the number of retransmitted frames is N
Example:
The window size is 4.
  A sender has sent frame 6 and the timer expires for frame 3 (ACK3 is not received). The sender goes back and resends the frames 3, 4, 5 and 6.

## Slide 97: Go-back-N normal operation
How many frames can be transmitted without acknowledgment?
ACK1 – not necessary if ACK2 is sent
  Cumulative ACK
expected sequence number

## Slide 98: Go-back-N damaged or lost frame
Damaged frames are discarded!
Why are correctly received out of order packets are not buffered?
What is the disadvantage of this?

## Slide 99: Go-back-N sender window size
sequence number

## Slide 100
In the Go-Back-N Protocol, the sequence numbers are modulo 2m,
where m is the size of the sequence number field in bits (Number of bits needed to represent one sequence number).

## Slide 101
What is the utilization percentage of the link in Example 11.4 if we have a protocol that can send up to 15 frames before stopping and worrying about the acknowledgments?
Solution
The bandwidth-delay product is still 20,000 bits. The system can send up to 15 frames or 15,000 bits during a round trip. This means the utilization is 15,000/20,000, or 75%. Of course, if there are damaged frames, the utilization percentage is much less because frames have to be resent.
Example

## Slide 102: Go-back-N
Inefficient
  all out of order received packets are discarded
This is a problem in a noisy link
  many frames must be retransmitted -> bandwidth consuming
Solution
  re-send only the damaged frames
Selective Repeat ARQ
  avoid unnecessary retransmissions

## Slide 103
Stop-and-Wait ARQ is a special case of Go-Back-N ARQ in which the size of the send window is 1.

## Slide 104
Lecture 8
Selective Repeat

## Slide 105: Selective Repeat ARQ
Processing at the receiver more complex
The window size is reduced to one half of 2m
Both the transmitter and the receiver have the same window size
Receiver expects frames within the range of the sequence numbers

## Slide 106: Selective Repeat ARQ
Sender window size
Receive window size

## Slide 107: Selective Repeat ARQ

## Slide 108: Selective Repeat ARQ lost frame
Note: retransmission triggered with NACK and not with expired timer.

## Slide 109: Selective Repeat ARQ Sender window size

## Slide 110
Piggybacking
To improve the efficiency of the bidirectional protocols
Piggybacking in Go-Back-N ARQ

## Slide 111
Lecture 9
High-level Data Link Control

## Slide 112
HDLC
High-level Data Link Control (HDLC) supports half-duplex and full-duplex communication over point-to-point and multipoint links. It implements the ARQ mechanisms we discussed in this chapter.
Configurations and Transfer Modes
  Normal respond mode (NRM)
  Asynchronous balanced mode (ABM)
Frames
Control Field
Topics discussed in this section:

## Slide 113
Normal response mode

## Slide 114
Asynchronous balanced mode (ABM)
ABM is used over point-to-point links.

## Slide 115
HDLC frames:
Information frames (I-frame).
2. Supervisory frames (S-frame).
3. Unnumbered frames (U-frame).
Frames

## Slide 116
HDLC frames
Frames

## Slide 117
HDLC frames
Frames
Flag: 8-bit ; 01111110 that identifies the beginning and end of the frame
FCS: frame check sequence is error detection field
Address: contain the address of the secondary station. It can be one byte or more . If the address is more than one bytes , all bytes end with zero except the last byte ends with ones.

## Slide 118
Control field format for the different frame types

## Slide 119
Control field format for the I-frame
N(s): Sequence number of the frame in travel
N(R): the value of ACK when piggybacking is used.
P/F: (poll/Final)

## Slide 120
Control field format for S-frame
SS=00 RR - Receiver Ready to accept more I-frames
SS=01 REJ - Go-Back-N retransmission request for an I-frame
SS=10 RNR - Receiver Not Ready to accept more I-frames
SS=11 SREJ - Selective retransmission request for an I-frame
S
S

## Slide 121
U-frame control command and response

## Slide 122
The figure in the next slide shows an exchange using piggybacking. Node A begins the exchange of information with an I-frame numbered 0 followed by another I-frame numbered 1. Node B piggybacks its acknowledgment of both frames onto an I-frame of its own. Node B’s first I-frame is also numbered 0 [N(S) field] and contains a 2 in its N(R) field, acknowledging the receipt of A’s frames 1 and 0 and indicating that it expects frame 2 to arrive next. Node B transmits its second and third I-frames (numbered 1 and 2) before accepting further frames from node A.
Example

## Slide 123
Example of piggybacking without error

## Slide 124
Its N(R) information, therefore, has not changed: B frames 1 and 2 indicate that node B is still expecting A’s frame 2 to arrive next. Node A has sent all its data. Therefore, it cannot piggyback an acknowledgment onto an I-frame and sends an S-frame instead. The RR code indicates that A is still ready to receive. The number 3 in the N(R) field tells B that frames 0, 1, and 2 have all been accepted and that A is now expecting frame number 3.

## Slide 125
The figure in the next slide shows an exchange in which a frame is lost. Node B sends three data frames (0, 1, and 2), but frame 1 is lost. When node A receives frame 2, it discards it and sends a REJ frame for frame 1. Note that the protocol being used is Go-Back-N with the special use of an REJ frame as a NAK frame. The NAK frame does two things here: It confirms the receipt of frame 0 and declares that frame 1 and any following frames must be resent. Node B, after receiving the REJ frame, resends frames 1 and 2. Node A acknowledges the receipt by sending an RR frame (ACK) with acknowledgment number 3.
Example

## Slide 126
Figure 11.31 Example of piggybacking with error

## Slide 127: Data Transparency
Bit Stuffing

## Slide 128: Bit Stuffing
≥ 15
< 15