## Slide 1
Introduction to Cisco IOS -(Internetwork Operating System)

## Slide 2
Cisco IOS:
Just like a computer a switch or router requires an operating system to support the
hardware. Cisco IOS is the operating system that you will find on the switches and routers and some other devices like wireless access points.
When you work with Cisco routers and switches you will do most of the configuration using the CLI (Command Line Interface).

## Slide 3
We need:
1- a switch
2- console cable.
3- an application to connect to serial ports

## Slide 4: Determining Which Cables to Use When Wiring Devices Together

## Slide 5
As soon as you power on the switch this is what it will do:
1. Check the hardware.
2. Locate the Cisco IOS image & load it to the RAM.
3. Locate and apply configuration (if available).
Once the switch is done you finally get to see this message:
Press RETURN to get started!
If the switch does not have a configuration, you'll see the following:
--- System Configuration Dialog ---
Would you like to enter the initial configuration dialog? [yes/no]:
If you type yes and press enter it will walk you through a wizard where you can configure
some basic settings.
Note:
we'll configure everything ourselves, so we will choose no.

## Slide 6: RAM:
Random Access Memory, also called dynamic RAM (DRAM)
RAM has the following characteristics and functions:
Stores routing tables
Holds ARP cache
Holds fast-switching cache
Performs packet buffering (shared RAM)
Maintains packet-hold queues
Provides temporary memory for the configuration file of the router while the router is powered on
Loses content when router is powered down or restarted

## Slide 7: NVRAM:
Non-Volatile RAM
NVRAM has the following characteristics and functions:
Provides storage for the startup configuration file.
Retains content when router is powered down or restarted.

## Slide 8: Flash:
Flash memory has the following characteristics and functions:
Holds the operating system image (IOS).
Allows software to be updated without removing and replacing chips on the processor
Retains content when router is powered down or restarted
Can store multiple versions of IOS software
Is a type of electronically erasable, programmable ROM (EEPROM)

## Slide 9: ROM
Read-Only Memory
ROM has the following characteristics and functions:
Maintains instructions for power-on self test (POST) diagnostics
Stores bootstrap program and basic operating system software
Requires replacing pluggable chips on the motherboard for software upgrade

## Slide 10: Interfaces
Interfaces have the following characteristics and functions:
Connect router to network for frame entry and exit
Can be on the motherboard or on a separate module
Types of interfaces:
Ethernet
Fast Ethernet
Serial
Loopback
Console
Aux

## Slide 11: IOS File System Overview

## Slide 12: Overview of Router Modes:

## Slide 13: Router Modes

## Slide 14: User Mode Commands

## Slide 15: Privileged Mode Commands
NOTE:
There are many more commands available in privileged mode.

## Slide 16: CLI Command Modes
All command-line interface (CLI) configuration changes to a Cisco router are made from the global configuration mode. Other more specific modes are entered depending upon the configuration change that is required.
Global configuration mode commands are used in a router to apply configuration statements that affect the system as a whole.
The following command moves the router into global configuration mode
Router#configure terminal (or config t) Router(config)#
When specific configuration modes are entered, the router prompt changes to indicate the current configuration mode.
Typing exit from one of these specific configuration modes will return the router to global configuration mode. Pressing Ctrl-Z returns the router to all the way back privileged EXEC mode.

## Slide 17: Configuring a Router’s Name
A router should be given a unique name as one of the first configuration tasks.
This task is accomplished in global configuration mode using the following commands:
Router(config)#hostname Tokyo Tokyo(config)#
As soon as the Enter key is pressed, the prompt changes from the default host name (Router) to the newly configured host name (which is Tokyo in the example above).

## Slide 18: Configuring a Console Password
Passwords restrict access to routers.
Passwords should always be configured for virtual terminal lines and the console line.
Passwords are also used to control access to privileged EXEC mode so that only authorized users may make changes to the configuration file.
The following commands are used to set an optional but recommended password on the console line:
Router(config)#line console 0 Router(config-line)#password <password> Router(config-line)#login

## Slide 19: Configuring Interfaces
An interface needs an IP Address and a Subnet Mask to be configured.
All interfaces are “shutdown” by default.
The DCE end of a serial interface needs a clock rate.
Router#config t Router(config)#interface serial 0/1
Router(config-if)#ip address 200.100.50.75 255.255.255.240 Router(config-if)#clock rate 56000 (required for serial DCE only) Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#int f0/0 Router(config-if)#ip address 150.100.50.25 255.255.255.0
Router(config-if)#no shutdown
Router(config-if)#exit
Router(config)#exit
Router#
On older routers, Serial 0/1 would be just Serial 1 and f0/0 would be e0.
s = serial e = Ethernet f = fast Ethernet

## Slide 20: Home work 3