## Slide 1
3.<number>
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Physical Layer
Part II
Notes: <number>

## Slide 2
3.<number>
Chapter 3: Signals
Chapter 4: Digital Transmission
Chapter 5: Analog Transmission
Chapter 7:Transmission Media
Notes: <number>

## Slide 3
3.<number>
Chapter 3
Data and Signals
Notes: <number>

## Slide 4
3.<number>
To be transmitted, data must be transformed to electromagnetic signals.
Note
Notes: <number>

## Slide 5
3.<number>
3-1 ANALOG AND DIGITAL
Data can be analog or digital. The term analog data refers to information that is continuous; digital data refers to information that has discrete states. Analog data take on continuous values. Digital data take on discrete values.
Analog and Digital Data
Analog and Digital Signals
Periodic and Nonperiodic Signals
Topics discussed in this section:
Notes: <number>

## Slide 6
3.<number>
ANALOG AND DIGITAL
Analog data :refers to information that is continuous as clock and human voice. This can be converted to analog signal or sampled and converted to digital signal
Notes: <number>

## Slide 7
3.<number>
ANALOG AND DIGITAL
Digital data: refers to information that has discrete states as digital clock and data stored in in computer memory in forms of 1 s and 0s.
This This can be converted to digital signal or modulated into an analog signal.
Notes: <number>

## Slide 8: Analog and Digital Signals
3.<number>
Signals can be analog or digital.
Analog signals can have an infinite number of values in a range.
Digital signals can have only a limited number of values.
Notes: <number>

## Slide 9
3.<number>
Figure 3.1 Comparison of analog and digital signals
Notes: <number>

## Slide 10
3.<number>
PERIODIC AND APERIODIC SIGNALS
Both digital and analog can be periodic or a periodic (non periodic) signal
Periodic signal : It consists of repeating pattern within a measurable time called a period. The competition of full pattern called cycle.
Aperiodic :changes without exhibiting a pattern or cycle repeats over time.
Notes: <number>

## Slide 11
3.<number>
PERIODIC ANALOG SIGNALS
Periodic analog signals can be classified as simple or composite.
A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals.
A composite periodic analog signal is composed of multiple sine waves.
Notes: <number>

## Slide 12
3.<number>
Figure 3.2 A sine wave
S(t)= A sin (2πft+Φ)
S: is the instantaneous amplitude
A: peak amplitude( absolute value of its highest intensity)
F: frequency
Φ: Phase shift
Notes: <number>

## Slide 13
3.<number>
Figure 3.3 Two signals with the same phase and frequency, but different amplitudes
Notes: <number>

## Slide 14
3.<number>
Frequency and period are the inverse of each other.
Note
Period and frequency
Notes: <number>

## Slide 15
3.<number>
Period and frequency
Period :amount of time in sec. a signal can complete one cycle ( amount of time signal takes for one repetition)
Frequency:no of cycles ( period s) per sec.
Notes: <number>

## Slide 16
3.<number>
Figure 3.4 Two signals with the same amplitude and phase, but different frequencies
Fa=2 Fb
Ta=1/2 Tb
Notes: <number>

## Slide 17
3.<number>
Table 3.1 Units of period and frequency
Notes: <number>

## Slide 18
3.<number>
The power we use at home has a frequency of 60 Hz. The period of this sine wave can be determined as follows:
Example 3.1
Notes: <number>

## Slide 19
3.<number>
The period of a signal is 100 ms. What is its frequency in kilohertz?
Example 3.2
Solution
First we change 100 ms to seconds, and then we calculate the frequency from the period (1 Hz = 10−3 kHz).
Notes: <number>

## Slide 20: Frequency
3.<number>
Frequency is the rate of change with respect to time.
Change in a short span of time means high frequency.
Change over a long span of time means low frequency.
Notes: <number>

## Slide 21
3.<number>
If a signal does not change at all, its frequency is zero.
If a signal changes instantaneously, its frequency is infinite.
Note
Notes: <number>

## Slide 22
3.<number>
Phase describes the position of the waveform relative to time 0.
Note
Notes: <number>

## Slide 23: Frequency
3.<number>
Phase is measured in degrees or radians
1°= 2π/360 rad &1 rad = 360/2 π°
A phase shift of 360:shift of a complete period
A phase shift of 180: one half of a period(1/2 cycle) .
A phase shift of 90: one quarter of period (1/4) cycle.
Notes: <number>

## Slide 24
3.<number>
Figure 3.5 Three sine waves with the same amplitude and frequency, but different phases
Phases starts at 0 with Zero amplitude. The amplitude increasing
Starts at time Zero with a peak amplitude. The amplitude is decreasing
starts at time Zero with a zero amplitude. The amplitude is decreasing
Notes: <number>

## Slide 25
3.<number>
A sine wave is offset 1/6 cycle with respect to time 0. What is its phase in degrees and radians?
Example 3.3
Solution
We know that 1 complete cycle is 360°. Therefore, 1/6 cycle is
Notes: <number>

## Slide 26
3.<number>
Sine wave examples
Notes: <number>

## Slide 27
3.<number>
Figure 3.7 The time-domain and frequency-domain plots of a sine wave
Time domain plot: shows changes in signal amplitude with respect to time
Frequency domain plot: is concerned only with peak value of amplitude and the frequency
Notes: <number>

## Slide 28
3.<number>
A complete sine wave in the time domain can be represented by one single spike in the frequency domain.
Note
Notes: <number>

## Slide 29
3.<number>
•An analog signal is best represented in the frequency domain .WHY?
A complete sine wave in the time domain can be represented by one single spike in the frequency domain.
•we show two characteristics of a signal ( amplitude and frequency) with only one spike
•Frequency domain is more compact and useful when we are dealing with more than on sine wave ( composite signal)
Note
Notes: <number>

## Slide 30
3.<number>
Figure 3.7 The time-domain and frequency-domain plots of a sine wave
Notes: <number>

## Slide 31
3.<number>
The frequency domain is more compact and useful when we are dealing with more than one sine wave. For example, Figure 3.8 shows three sine waves, each with different amplitude and frequency. All can be represented by three spikes in the frequency domain.
Example 3.7
Notes: <number>

## Slide 32
3.<number>
Figure 3.8 The time domain and frequency domain of three sine waves
Notes: <number>

## Slide 33: Signals and Communication
3.<number>
A single-frequency sine wave is not useful in data communications
We need to send a composite signal, a signal made of many simple sine waves.
According to Fourier analysis, any composite signal is a combination of simple sine waves with different frequencies, amplitudes, and phases.
Notes: <number>

## Slide 34: Composite Signals and Periodicity
3.<number>
If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies.
If the composite signal is nonperiodic, the decomposition gives a combination of sine waves with continuous frequencies.
Notes: <number>

## Slide 35
3.<number>
Figure 3.9 shows a periodic composite signal with frequency f. This type of signal is not typical of those found in data communications. We can consider it to be three alarm systems, each with a different frequency. The analysis of this signal can give us a good understanding of how to decompose signals.
Example 3.4
Notes: <number>

## Slide 36
3.<number>
Figure 3.9 A composite periodic signal
Notes: <number>

## Slide 37
3.<number>
Figure 3.10 Decomposition of a composite periodic signal in the time and frequency domains
Notes: <number>

## Slide 38
3.<number>
Figure 3.11 shows a nonperiodic composite signal. It can be the signal created by a microphone or a telephone set when a word or two is pronounced. In this case, the composite signal cannot be periodic, because that implies that we are repeating the same word or words with exactly the same tone.
Example 3.5
Notes: <number>

## Slide 39
3.<number>
Figure 3.11 The time and frequency domains of a nonperiodic signal
Notes: <number>

## Slide 40: Bandwidth and Signal Frequency
3.<number>
The bandwidth of a composite signal is the difference between the highest and the lowest frequencies contained in that signal.
Notes: <number>

## Slide 41
3.<number>
Figure 3.12 The bandwidth of periodic and nonperiodic composite signals
Notes: <number>

## Slide 42
3.<number>
The term bandwidth refer to
a property of a medium:
It is the difference between the highest and the lowest frequencies that the medium can satisfactorily pass
OR
The width of a signal spectrum
The signal spectrum: all frequencies contained in the signal .
Note
Notes: <number>

## Slide 43
3.<number>
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is its bandwidth? Draw the spectrum, assuming all components have a maximum amplitude of 10 V.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
Example 3.6
The spectrum has only five spikes, at 100, 300, 500, 700, and 900 Hz (see Figure 3.13).
Notes: <number>

## Slide 44
3.<number>
Figure 3.13 The bandwidth for Example 3.6
Notes: <number>

## Slide 45
3.<number>
A periodic signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all frequencies of the same amplitude.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
Example 3.7
The spectrum contains all integer frequencies. We show this by a series of spikes (see Figure 3.14).
Notes: <number>

## Slide 46
3.<number>
Figure 3.14 The bandwidth for Example 3.7
Notes: <number>

## Slide 47
3.<number>
A nonperiodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V. The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal.
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz. Figure 3.15 shows the frequency domain and the bandwidth.
Example 3.8
Notes: <number>

## Slide 48
3.<number>
Figure 3.15 The bandwidth for Example 3.8
Notes: <number>

## Slide 49
3.<number>
DIGITAL SIGNALS
In additional to being represented by an analog signal ,
information can also be represented by a digital signal.
For example , a 1 can be encoded as a positive voltage,
and a 0 as zero voltage.
A digital signal can have more than 2 levels
In this case , we can send more than 1 bit for each level
Notes: <number>

## Slide 50
3.<number>
Two digital signals: one with two signal levels and the other
with four signal levels
Send 1-bit per level
Send 2-bit per level
If a signal has L level, no of bits/level= log2L bits
Notes: <number>

## Slide 51
3.<number>
digital signal has eight levels. How many bits are needed per level?
We calculate the number of bits from the formula
no of bits/level= log28 bits= 3 bits
Each signal level is represented by 3 bits.
Example 3.8
Notes: <number>

## Slide 52
3.<number>
A digital signal has nine levels . How many bits are needed per level?
We calculate the number of bits by using the formula:
Log2 L= number of bits in each level
Log2(9)=3.17bits.
However, this answer is not realistic. The number of bits sent per level needs to be an integer as well as a power of 2.
For this example ,4bits can represent one level.
Example 3.8
Notes: <number>

## Slide 53
3.<number>
Bit rate and bit interval
Most digital signals are nonperiodic , frequency and period are not appropriate. Another terms instead of frequency is bit rate and instead of period: bit interval(bit duration)
Bit rate : number of bits per second bps
Bit interval=1/bit rate
Notes: <number>

## Slide 54
3.<number>
A digital signal has a bit rate of 2000 bps. What is the duration of each bit (bit interval)
Solution
The bit interval is the inverse of the bit rate.
Bit interval = 1/ 2000 s = 0.000500 s = 0.000500 x 106ms =500 ms
Notes: <number>

## Slide 55
3.<number>
Assume we need to download text documents at the rate of 100 pages per minute. What is the required bit rate of the channel?
Solution
A page is an average of 24 lines with 80 characters in each line .If we assume that one character requires 8bits,
The bit rate is:
100x24x80x8/60 =25.6Kbps
Example
Notes: <number>

## Slide 56
3.<number>
A digital signal is a composite analog signal with an infinite bandwidth.
Note
Digital Signal as a composite Analog Signal
Notes: <number>

## Slide 57
3.<number>
Fourier analysis can be used to decompose a digital signal
If the digital signal is periodic (rare in data communications), the decomposed signal has a frequency domain representation with an infinite Bandwidth and discrete frequencies
If it is nonperiodic , the decomposed signal still has infinite Binfinite BW , but the frequencies are continuous.
Note
Digital Signal as a composite Analog Signal
Notes: <number>

## Slide 58
3.<number>
The time and frequency domains of periodic and non periodic
digital signal
Notes: <number>

## Slide 59
3.<number>
Baseband transmission: means sending a digital signal over a channel without changing the digital signal to an analog signal
Transmission of Digital Signals
Base band transmission required a low-pass channel (channel with a B-W that starts from zero)
Notes: <number>

## Slide 60
3.<number>
The analog bandwidth of a medium is expressed in hertz;
The digital bandwidth, in bits per second.
Note
Notes: <number>

## Slide 61
3.<number>
Broadband Transmission: or modulation means changing the digital signal to an analog signal for transmission. Modulation allows use a band-pass channel (a channel with a B-W that doesn't start from Zero. This type of channel is more available than a low-pass channel.
Transmission of Digital Signals
Notes: <number>

## Slide 62
3.<number>
If the available channel is a bandpass channel, we cannot send the digital signal directly to the channel; we need to convert the digital signal to an analog signal before transmission.
Note
Notes: <number>

## Slide 63
3.<number>
TRANSMISSION IMPAIRMENT
Signals travel through transmission media, which are not perfect.
The imperfection causes signal impairment . This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium.
What is sent is not what is received. Three causes of impairment are: attenuation distortion ,and noise.
Notes: <number>

## Slide 64
3.<number>
CAUSES OF IMPAIRMENT
Notes: <number>

## Slide 65
3.<number>
when Signal travels through a medium, it losses some of its energy in overcoming the resistance of the medium.
To compensate for this loss, amplifiers are used to amplify the signal.
Attenuation ( means loss of energy)
Decibel: Measure the relative power(attenuation)
dB=10 log10 P2/P1
Notes: <number>

## Slide 66
3.<number>
Suppose a signal travels through a transmission medium and its power is reduced to one-half. This means that P2 is (1/2)P1. In this case, the attenuation (loss of power) can be calculated as
Example :
A loss of 3 dB (–3 dB) is equivalent to losing one-half the power.
Notes: <number>

## Slide 67
3.<number>
A signal travels through an amplifier, and its power is increased 10 times. This means that P2 = 10P1 . In this case, the amplification (gain of power) can be calculated as
Example :
= 10 log 10 (10) = 10 (1)= 10 dB
Notes: <number>

## Slide 68
3.<number>
One reason that engineers use the decibel to measure the change s in the strength of a signal is that decibel numbers can be added (or subtracted) when we are measuring several points (cascading) instead of just two. In the following Figure a signal travels from point 1 to point 4 .
The decibel is negative if a signal is attenuated
The decibel is positive if a signal is amplified
Notes: <number>

## Slide 69
3.<number>
In this case, the decibel value can be calculated as
dB= -3+7-3= + 1
Notes: <number>

## Slide 70
3.<number>
Distortion : means that signal changes its form or shape.
Each signal component has its own propagation speed through the medium and therefore ,its own delay in arriving final destination
DISTORTION
Notes: <number>

## Slide 71
3.<number>
Several types of noise:
Thermal noise
Induced noise
Crosstalk noise
Impulse noise
NOISE
Notes: <number>

## Slide 72
3.<number>
Thermal noise:
is the random motion of electrons in a wire which creates an extra signal not originally sent by the transmitter
•Induced noise:
Comes from sources such as motors and appliances.
•Crosstalk noise:
Is the effect of one wire on the other
NOISE
Notes: <number>

## Slide 73
3.<number>
Impulse Noise:
is a spike ( a signal with high energy in a very short time) that comes from power lines, lighting and so on.
NOISE
Notes: <number>

## Slide 74
3.<number>
SNR: ratio between signal power to the noise power
average noise power
average signal power
•A high SNR :means the signal is less corrupted by noise
•A low SNR: means the signal is more corrupted by noise .
SNR can be described in db units SNRdb SNRdb=10 log10SNR
Signal-to-Noise Ratio SNR
Notes: <number>

## Slide 75
3.<number>
Two cases of SNR : high SNR and low SNR
Notes: <number>

## Slide 76
3.<number>
Two cases of SNR : high SNR and low SNR
The power of asignal is 10 m W and the power of the noise is 1 μ W ; what are the values of SNR and SNRdB ?
Solution
The values of SNR can be calculated as follows:
SNR= 10 x 10 -3 W = 10,000
1 x 10 -6 W
SNRdb = 10 log10 10,000 = 40
Notes: <number>

## Slide 77
3.<number>
Data Rate Limits
Avery important consideration in data communications is how fast we can send data, in bits per second, over a channel.
Data rate depends on three factors:
1. The bandwidth available
2. The level of the signals we use
3. The quality of the channel (the level of noise)
Notes: <number>

## Slide 78
3.<number>
Noiseless channel
Nyquist Bit Rate :
Bit Rate = 2 x bandwidth x log2 L
L: No of signal levels used to represent data
Notes: <number>

## Slide 79
3.<number>
Noiseless channel
Ex1:Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels.
The maximum bit rate can be calculated as
Bit Rate = 2 x bandwidth x log2 L
= 2 x 3000x log 2 2
= 6000 bps
Ex2: Consider the same noiseless channel transmitting a signal with four signal levels (for each level, we send 2 bits).
The maximum bit rate can be calculated as
Bit Rate = 2 x bandwidth x log2 L
= 2 x 3000x log 2 4
= 12000 bps
Notes: <number>

## Slide 80
3.<number>
Increasing the levels of a signal may reduce the reliability of the system. .
Note
Notes: <number>

## Slide 81
3.<number>
Noisy Channel: Shannon Capacity
Shannon Capacity
Capacity= bandwidth x log2(1+SNR)
Capacity: capacity of the channel in bps ( max
In the shannon formula there is no indication of the signal level
We cannot achieve a data rate higher than the capacity of the channel. In other word the formula defines a characteristic of the channel , not the method of transmission
Note
Notes: <number>

## Slide 82
3.<number>
Noisy Channel: Shannon Capacity
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero. In other words, the noise is so strongth at the signal is faint. For this channel the capacity C is calculated as
This means that the capacity of this channel is zero regardless of the bandwidth. In other words, we can not receive any data through this channel.
Notes: <number>

## Slide 83
3.<number>
In networking, we use the term bandwidth in two contexts.
The first , band width in hertz, refers to the range of frequencies in a composite signal or the range of frequencies that a channel can pass.
The second , bandwidth in bits per second , refers to the speed of bit transmission in a channel or link.
Note
Notes: <number>

## Slide 84
3.<number>
PERFORMANCE
One important issue in networking is the performance of the network how good is it?
Bandwidth
Throughput
Latency (Delay)
Notes: <number>

## Slide 85
3.<number>
Throughput
Is a measure of how fast we can actually send data through a network
The bandwidth is potential measurement of a link; the throughput is an actual measurement of how fast we can send data
Throughput less thanB-W
Notes: <number>

## Slide 86
3.<number>
Throughput
Example:
a high way designed to transmit 1000 cars per minute, if there is congestion on the road, this figure may be reduced to 100 cars per minute .
The B-W 1000 and throughput =100
Example:
if we have a link with B-W 1Mbps, but the devices connected to the end of the link may handle only 200Kbps.
B-W=1Mbps &Throughput=200Kbps
Notes: <number>

## Slide 87
3.<number>
Throughput
A network with band width of 10Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000bits. What is the throughput of this network ?
Solution
We can calculate the throughput as
The throughput is almost one-fifth of the bandwidth in this case
Notes: <number>

## Slide 88
3.<number>
Latency (delay)
Defines how long it takes for an entire message to completely arrive at the destination from the time the first bit is sent out from the source.
Latency (Delay) = propagation time + transmission time +queuing time + processing time
Notes: <number>

## Slide 89
3.<number>
Propagation time
time required for a bit to travel from the source to the destination Propagation speed
Propagation time = Distance
Propagation speed
Propagation speed depend on the medium and on the frequency of the signal
Notes: <number>

## Slide 90
3.<number>
Example:
Notes: <number>

## Slide 91
3.<number>
Transmission time
The time required for transmission of a message .
It depends on the size of the message and the bandwidth of the channel
Transmission time = Message size
Bandwidth (bps)
Notes: <number>

## Slide 92
3.<number>
Example:
Notes: <number>

## Slide 93
3.<number>
Solution
Notes: <number>

## Slide 94
3.<number>
Queuing time
The time needed for each end device to hold the message before it can be processed.
•It changes with the load imposed on the network, if there is heavy traffic on the network , the queuing time increases
Notes: <number>