## Slide 1
CIRCULAR CURVE

## Slide 2
CIRCULAR CURVE

## Slide 3
CIRCULAR CURVE

## Slide 4
Given Δ = 32°, R = 410 m, and the PI station 1+120 . 744, compute the curve data and the station of the PT using. Compute the deflection angles at even 20-m stations.
Example 1 :
𝑃𝐶 𝑆𝑡𝑎.= 𝑃𝐼 𝑆𝑡𝑎.– 𝑇
Solution :
𝑃𝑇 𝑆𝑡𝑎.= 𝑃𝐶 𝑆𝑡𝑎.+ 𝐿
𝑇= 𝑅 tan
𝐿 =
𝑇= 410 * tan = 117.533 m
𝐿 = = 228.987 m
𝑃𝐶 𝑆𝑡𝑎.= 1120.744 – 117.566 = 1003.178 𝑚 →→ 1+ 003.178 Sta
𝑃𝑇 𝑆𝑡𝑎.= 1003.178 + 228.987 = 1232.165 𝑚 →→ 1+ 232.165 Sta

## Slide 5
The deflection angle to the P.T. is
The deflection angle to intermediate stations is proportional to the distance from the P.C.
The distance to station 1 + 020.000 is = (1020.000) – (1003.178) = 16.822 m.
𝐷𝑒𝑓𝑙𝑒𝑐𝑡𝑖𝑜𝑛 𝑎𝑛𝑔𝑙𝑒 = × = 1°10′31′′
Other deflection angles are computed similarly in the Table :

## Slide 6
A horizontal curve is to be constructed as part of a railway section with a curve length of 2100 m and a central angle of 20o. If the PI station is 1+ 430:
Determine the curve radius, external distance, middle ordinate and chord length.
Compute PC and PT stations and the deflection angle (from the first tangent) for a point on the curve located at a distance of 100 m from PC (arc length).
Example 2 :
Solution :
𝐿 =
2100 =
R = 6016.05 m

## Slide 7
Middle ordinate :
M = R ( 1- Cos )
M = 6016.05 ( 1- Cos ) = 91.25 m
External distance :
E = R (Sec -1)
E = 6016.05 (Sec -1) = 92.8 m
Chord length :
C = R Sin
C = 6016.05 Sin = 2089.35 m

## Slide 8
𝑃𝐶 𝑆𝑡𝑎.= 𝑃𝐼 𝑆𝑡𝑎.– 𝑇
𝑃𝑇 𝑆𝑡𝑎.= 𝑃𝐶 𝑆𝑡𝑎.+ 𝐿
𝑇= 𝑅 tan
𝑇= 6016.05 * tan = 1060.8 m
𝑃𝐶 𝑆𝑡𝑎.= 1430 – 1060.8 = 369.2 𝑚 →→ 0 + 369.2 Sta
𝑃𝑇 𝑆𝑡𝑎.= 369.2 + 2100 = 2469.2 𝑚 →→ 2 + 469.2 Sta
D = = 0.9523o = 0°57′8.28 ′′
Φ= = = = 0.47615 = 0°28′34.14 ′′