## Slide 1: Quantitative Determenation of Alanine aminotransferase (ALT)
CLS 431

## Slide 2: Determenation of Alanine aminotransferase (ALT)
Principle of method
Alanine + 2-oxoglutrate ALT Glutamate + Pyruvate
Pyruvate + NADH + H+ LDH Lactate + NAD+
The rate of decrease in absorbance at 340nm is proportional to the ALT activity of the sample.

## Slide 3: Enzyme distribution:
Found in highest conc. in liver and kidney.
It is considered to be the most liver specific transaminase

## Slide 4: Clinical significance of ALT
hepatic disorders, hight serum levels are found in hepatocellular disorder rather than on obstructive disorders.
Cardiac tissue contains a small amount of ALT activity but serum levels usually remain normal in AMI.

## Slide 5
Samples: serum or plasma
Procedure
Assay conditions:
Wavelength ......................... 340nm.
Cuvette ................................ 1cm. light path
constant tempreture .................. 37℃
Adjust the instrument to zero with distilled water or air.

## Slide 6: Pipette into a cuvette:
WR (ml) | 1.0
Pre-warm to 37℃, then add | 
Sample (µL) | 100
Mix, incubate at 37℃ for 1 minute and read the absorbance at 340 nm against D.W. (A1).
Take the Ab every minutes for 3 min read the absorbance(A2).

## Slide 7: ΔA/min x 1768= U/L of AST
Reference values:
ALT:
Men up to 42 U/L
Women up to 32 U/L
Calculations