## Slide 2
α-naphthylphosphate + H2O ACP/pH=5
α-naphtol + phosphate
α-naphtol + Fast Red TR(diazoted compound)
diazo dye (chromophore).
The α-naphtol released from the substrate α- naphthylphosphate by acid phosphatase is coupled with Fast Red TR to produced a colored complex which absorbs light at 405 nm.

## Slide 3
ACP activity is found the in the prostate,
bone,liver, spleen, erythrocytes and platelets.
The prostate is the richest source, with many times the activity found in other tissue.
ACP measurement has been used as an aid in the detection of prostatic carcinoma, particularly metastatic carcinoma of the prostate.

## Slide 4
Wavelength ........................405 nm.
Constant tempreture ............... 37C
A- Total Acid phosphatase: | 
Acid Phos. Regt. | 1.0 ml
Pre-warm at 37C and then add: | 
Sample | 100 (µL)
Mix, incubate at 37C for 5 min, and then read the absorbance at 405 nm against D.W. every minute for 5 min. to determine ΔA/min. | 

## Slide 5
B- Non-Prostatic Acid Phosphatase: | 
Acid Phos. Regt. / L. Tartrate reagent | 1.0 ml / 10 (µL)
Mix, warm at 37C and then add: | 
Sample | 100 (µL)
Mix, incubate at 37C for 5 min, and then read the absorbance at 405 nm against D.W. every minute for 5 min. to determine ΔA/min. | 

## Slide 6
A-Total Acid Phosphatase activity (U/L) = ΔA/min x 853
B-Non-Prostatic Acid Phosphatase activity (U/L) = ΔA/min x 860
C-Prostatic Acid Phosphatase:
The value is obtained by subtracting the result of non-prostatic acid phosphatase assay (B) from the total acid phosphatase assay (A).

## Slide 7
Total acid phosphatase: 0.0 - 12 U/L
Prostatic acid phosphatase 0.0 – 4.0 U/L