## Slide 1: Armamentarium

## Slide 2: Types of Syringes
Reusable
Breech-loading, metal, aspirating,cartridge
Breech-loading, plastic, aspirating,cartridge
Breech-loading, metal, self-aspirating
Pressure type
Jet injector
Disposable
“Safety” syringe

## Slide 3: ADA Criteria
Durable, able to withstand sterilization
Accept wide variety of cartridges & needles
Simple, easy to use, lightweight, self-contained, and inexpensive
Effective and easily visualized aspiration

## Slide 4: Advantages - reusable syringe
One-handed aspiration
Visible cartridge
Autoclavable and rust-resistant
Durable with proper maintenance

## Slide 5: Disadvantages - reusable
Weight
Size
Possibility of cross-infection with
improper care

## Slide 7: Advantages - plastic
Lightweight
Lower cost
Rust free

## Slide 8: Disadvantages - plastic
Size
Deteriorates with repeated autoclaving
Possibility of cross-infection with
improper care

## Slide 9: Self-aspirating Syringe
Advantages
Easier to aspirate with small hands
Volume indicator
Disadvantages
Feeling of insecurity
Finger must be moved
Weight

## Slide 10: Advantages - pressure type
Dose is measured
Overcomes tissue resistance
Cartridge is protected

## Slide 11: Disadvantages - pressure type
Cost
May inject too rapidly
Gun-like appearance

## Slide 17: Advantages - jet injector
No “sharp” needle
Delivers small volumes
Use in lieu of topical

## Slide 18: Disadvantages - jet injector
“Jolt” of injection
Inadequate for pulpal or regional blocks
May damage periodontal tissue

## Slide 19: Advantages - disposable syringe
Sterile, no chance of cross contamination
Lightweight

## Slide 20: Disadvantages - disposable
Cannot use dental cartridge
Cannot aspirate single-handedly
Awkward to use intraorally

## Slide 21: Advantages - safety syringes
Disposable
Sterile
Lightweight
Needle covers automatically

## Slide 22: Disadvantages - safety syringe
Increased cost
Feels awkward during learning process

## Slide 23: Syringe Maintenance
Brush harpoon, clean syringe and
autoclave after each use
Do not throw out needle adaptor
Sharpen or replace harpoon periodically

## Slide 24: Needles
Stainless Steel
Platinum
Ruthenium-Platinum alloy

## Slide 25: Maintenance problems
Surface deposits
Dull or bent harpoon
Excess wear

## Slide 26: Parts of a Needle
Bevel
Shank
Hub
Syringe adaptor
Syringe-penetrating end

## Slide 27: Gauge
Measure of the diameter of the needle’s lumen
Size number is inversely proportional to the diameter
Usual dental needle guages are 25,27, & 30

## Slide 28: Length
Long - approximately 40mm or 1 5/8 in
Short - approximately 25 mm or 1 in

## Slide 29: Needle Handling
Single pt. use, change after several injections
Cap between uses, dispose of in “sharps” container
Check for barbs if pain on withdrawal
Never force against resistance
Never insert a needle to the hub

## Slide 30: Problems related to improper use
Pain on insertion
Pain on withdrawal
Needle breakage
Needle stick injury

## Slide 31: Needle size vs. comfort
Patients cannot differentiate between 23, 25, 27, or 30 guage needles.
Hamburg, H. L. 1972

## Slide 32: Advantage of larger needles
Less deflection
Less chance for breakage
More reliable aspiration

## Slide 34: Cartridge
1.8 cc volume
Glass tube
Rubber stopper
Aluminum cap with diaphragm

## Slide 36: Contents of Cartridge
Anesthetic
Vasoconstrictor
Preservative for vasoconstrictor
Sodium chloride
Distilled water

## Slide 37: Preservative for Vasoconstrictor
Sodium Bisulfite
Most common antioxidant (burning)
Prolongs shelf life to aprox. 8 mos.

## Slide 38: Handling of Cartridges
Should not be:
autoclaved
stored in alcohol or disinfectant
Should be:
kept in original container
kept in dark place

## Slide 39: Handling of Cartridges
No need for:
Cartridge warmer
Sterilization prior to injection
- may wipe with alcohol if not in original container

## Slide 40: Problems with Cartridges
Bubble in cartridge
Small - N2 which is normal
Large(>2mm) - freezing
Extruded stopper
Freezing, or uptake of holding solution

## Slide 41: Problems with Cartridges
Burning on injection
Normal response to pH of drug
Response to preservative
Diffusion of holding solution
Overwarmed cartridge

## Slide 42: Problems with cartridges
Leakage during injection
Eccentric penetration of diaphragm
Stopper sticks
Rare, may be cold
(check that needle has penetrated diaphragm)

## Slide 43: Problems with Cartridges
Cap
Corrosion - cold sterilizing solutions
Rust - leakage in container
Broken cartridge
Rough handling
Excessive force to engage harpoon

## Slide 44: Additional Armamentarium
Topical antiseptic ?
Topical anesthetic
Cotton tip applicator
Guaze
Hemostat

## Slide 47: Preparation of Armamentarium

## Slide 48: Loading the Syringe

## Slide 53: Attaching the Needle

## Slide 56: Recapping the Needle
“Scoop” Technique

## Slide 59: Unloading the Syringe

## Slide 66: Needle Sticks
Avoid by capping needle when not in use
Notify employer
Blood samples from pt. and person exposed
Health care evaluation - consider Hep B vaccination or other prophylactic coverage