## Slide 1
86
57.6
56.6
100
99
9.6
9.4
25.5
25.4
36
34
41.3
41.1
20.00 - 20.13
0.14
A
C
B
M42 X 1.5 - 6g
0.1 M B M
0.06 A
6.6
6.1
9.6
9.4
44.60
44.45
0.08 M A
C
A
0.02
31.8
31.6
0.1
B
8X 7.9 - 8.1
8X 45°
0.14 M
A C M
IE-352 Manufacturing Processes – 2 Spring - 2016 Lecture (2) Coordinate Dimensioning and Tolerancing
Ahmed M. El-Sherbeeny, PhD
Industrial Engineering Department
King Saud University

## Slide 2: Outline
Introduction
Basic Hole System
Basic Shaft System
American National Standard Fit Tables

## Slide 3: Introduction - Basic Hole and Basic Shaft Systems
The Basic Hole and Basic Shaft Systems are procedures for calculating and placing mating part dimensions and tolerance information on the drawing. This will assure that if the parts are manufactured according to the specifications on the drawing, they will fit together and function as intended.
Four basic parameters must be known to use these systems: Basic Size, Allowance, Hole Tolerance, and Shaft Tolerance.
  Basic size is the hole or shaft at maximum material condition (MMC). All tolerance values are generated from that value.
  Allowance (the intentional difference between mating parts) is the minimum clearance or maximum interference. It can be positive (clearance) or negative (interference).

## Slide 4: Introduction - Basic Hole and Basic Shaft Systems
BASIC HOLE SYSTEM – Allowance based on the hole at MMC
  1. The basic size is always equal to the minimum hole size (Hole MMC).
  2. Subtract the allowance from the basic size to get the maximum shaft size (Shaft MMC).
  3. Apply the appropriate tolerances to the hole and to the shaft (Hole & Shaft lower material condition (LMC)).
BASIC SHAFT SYSTEM – Allowance based on the shaft at MMC
  1. The basic size is always equal to the maximum shaft size.
  2. Add the allowance to the basic size to get the minimum hole size.
  3. Apply the appropriate tolerances to the shaft and the hole.

## Slide 5: BASIC HOLE SYSTEM

## Slide 6: Basic Hole System
Using the Basic Hole System and the following data, complete the drawing by placing the appropriate dimensions on both the shaft and the hole.
Nominal Size = 9/16”
Allowance = .0006
Shaft Tolerance = .0009
Hole Tolerance = .0010

## Slide 7: Basic Hole System
The basic size is determined by converting the nominal size into its decimal equivalent. The basic hole system always establishes the basic size as the minimum hole size. Remember, the smallest size limit always goes on the bottom in a stacked limits form.
.5625
Basic Size = .5625
Allowance = .0006
Shaft Tolerance = .0009
Hole Tolerance = .0010

## Slide 8: Basic Hole System
Subtract the allowance from the basic size to obtain the maximum shaft size (Shaft MMC). Place the value as the upper limit of the shaft dimension.
.5625
Basic Size = .5625
Allowance = .0006
Shaft Tolerance = .0009
Hole Tolerance = .0010
.5625
–.0006
Basic Size
Allowance
Shaft MMC

## Slide 9: Basic Hole System
Subtract the allowance from the basic size to obtain the maximum shaft size (Shaft MMC). Place the value as the upper limit of the shaft dimension.
.5625
Basic Size = .5625
Allowance = .0006
Shaft Tolerance = .0009
Hole Tolerance = .0010
.5625
–.0006
.5619
Basic Size
Allowance
Shaft MMC
Shaft MMC
.5619

## Slide 10: Basic Hole System
Apply the tolerances to both the hole and the shaft to complete the dimensions; add the hole tolerance to the hole lower limit, and subtract the shaft tolerance from the shaft upper limit. Do the arithmetic and apply the values.
.5625
Basic Size = .5625
Allowance = .0006
Shaft Tolerance = .0009
Hole Tolerance = .0010
.5625
–.0006
.5619
Basic Size
Allowance
Shaft MMC
Shaft MMC
.5619
Shaft Hole
.5619 .5625
– .0009 +.0010

## Slide 11: Basic Hole System
Apply the tolerances to both the hole and the shaft to complete the dimensions; add the hole tolerance to the hole lower limit, and subtract the shaft tolerance from the shaft upper limit. Do the arithmetic and apply the values.
Basic Size = .5625
Allowance = .0006
Shaft Tolerance = .0009
Hole Tolerance = .0010
.5625
–.0006
.5619
Basic Size
Allowance
Shaft MMC
Shaft MMC
Shaft Tol Hole Tol
.5619 .5625
– .0009 +.0010
.5610 .5635
-.0006
-.0015
+.0010
-.0000
.5625
.5625
Values Referenced to Basic Size:
.5619
.5610
.5635
.5625
Shaft Hole

## Slide 12: Basic Hole System
For the values of the hole-shaft system given below, find the hole and shaft sizes using the basic hole system. Express the results in reference to the basic size and in the stacked format.
Basic Size = 1-1/8”
Allowance = .0025
Shaft Tolerance = .0015
Hole Tolerance = .0020

## Slide 13: Basic Hole System
Nominal Size = 1-1/8”
Basic Size = 1.1250
Allowance = .0025
Shaft Tolerance = .0015
Hole Tolerance = .0020
1.1270
1.1250
1.1225
1.1210
Hole Shaft
1.1250 Basic Size 1.1225
-.0025 Allowance – .0015
1.1225 Max Shaft 1.1210
-.0025
-.0040
+.0020
-.0000
1.1250
1.1250
Values Referenced to Basic Size:
Values expressed in
The stacked format:
Shaft Hole

## Slide 14: BASIC SHAFT SYSTEM

## Slide 15: Basic Shaft System
Nominal Size = 9/16”
Allowance = .0004
Shaft Tolerance = .0008
Hole Tolerance = .0010
Using the Basic Shaft System and the following data, complete the drawing by placing the appropriate dimensions on both the shaft and the hole.

## Slide 16: Basic Shaft System
The basic shaft system establishes the basic size as the maximum shaft size. Remember, the upper size limit always goes on top in a stacked tolerance expression.
Nominal Size = 9/16”
Basic Size = .5625
Allowance = .0004
Shaft Tolerance = .0008
Hole Tolerance = . 0010
.5625

## Slide 17: Basic Shaft System
The minimum hole size (Hole MMC) is obtained by adding the allowance to the basic shaft size. Do the addition and place the dimension as the lower limit of the hole size.
Nominal Size = 9/16”
Basic Size = .5625
Allowance = .0004
Shaft Tolerance = .0008
Hole Tolerance = .0010
.5625
.5629
.5625
+.0004
.5629
Hole MMC

## Slide 18: Basic Shaft System
The process is completed by applying the tolerances to the respective components by subtracting the shaft tolerance from the shaft upper limit, and adding the hole tolerance to the hole dimension lower limit. Apply your results to the drawing.
Nominal Size = 9/16”
Basic Size = .5625
Allowance = .0004
Shaft Tolerance = .0008
Hole Tolerance = .0010
.5625
.5617
.5639
.5629
Shaft Hole
.5625 .5629
–.0008 +.0010
.5617 Shaft LMC .5639 Hole LMC

## Slide 19: Basic Hole compared to Basic Shaft System
.5635
.5625
.5619
.5610
Basic Hole System
.5625
.5617
.5639
.5629
Basic Shaft System
The same basic size (.5625)
was used for both calculations.
Compare the two results for
actual sizes of the shaft and
the hole.

## Slide 20: STANDARD FITS

## Slide 21: American National Standard Fit Tables
Tremendous advantages have been gained by standardizing fits, and publishing them in tables. They are the means for establishing tolerances for any given size, type, or class of fit. Each of the possible fit options within the tables are prescribed according to their intended function.
If the designer or engineer knows the functional requirements for the fit, a match can easily be found that conforms to the specific need. The standard provides choices for a series of types and classes of fits on a unilateral hole basis such that the fit produced by mating parts in any one class will produce approximately similar performance throughout the entire range of sizes.
The standard fit tables are consistent with the basic hole system. It is important that you understand how the tables themselves can be used to satisfy functional specifications and provide dimensional data to be used on engineering drawings.
The tables reflecting standard fits between mating parts may be found in virtually any design handbook, Machinery’s Handbook, and in any reputable drafting manual.

## Slide 22: American National Standard Fit Tables
Standard fits fall into 3 major categories and 5 basic types of fits. Within each of these divisions there are several classifications of fits.
  The first category, Running and sliding fits, for instance, has nine different classifications of this specific type of fit.
  The second category, Location fits, is a broad category of standardized fits, within which there are 3 major sub-categories: clearance, transition, and interference fits.
  Finally, there is a category for Interference, or Force fits consisting of 5 different classifications.
The five divisions of standard fits are designated by letters:
Category Type Classification
Sliding RC = Running/Sliding (Rotational or Reciprocal Motion) Clearance Fits (RC 1 - RC 9)
LC = Location Clearance Fits (LC 1 - LC 11)
Location LT = Location Transition Fits (Clearance through Interference) (LT 1 - LT 6)
LN = Location Interference Fits (LN 1 - LN 3)
Force FN = Force or Shrink Fits (FN 1 - FN 5)
The specification is complete when the category and the classification are combined, such as RC 3 or FN 5, and coupled with a specific diameter size.

## Slide 23: Running and Sliding Fits* -- American National Standard
RC 1 Close sliding fits are intended for the accurate location of parts which
must assemble without perceptible play.
RC 2 Sliding fits are intended for accurate location, but with greater maximum
clearance than class RC 1. Parts made to this fit move and turn easily but
are not intended to run freely, and in the larger sizes may seize with small
temperature changes.
RC 3 Precision running fits are about the closest fits which can be expected to
run freely, and are intended for precision work at slow speeds and light
pressures, but are not suitable where appreciable temperature
differences are likely to be encountered.
RC4 Close running fits are intended chiefly for running fits on accurate
machinery with moderate surface speeds and pressures, where
accurate location and minimum play are desired.
RC 5
RC 6
Medium running fits are intended for higher running speeds,
or heavy pressures, or both.

## Slide 24: Running and Sliding Fits* -- American National Standard
*From ANSI B4.1--1967 (R 1987).
Larger diameters and RC 7 through RC 9 not included in this presentation.
Class RC 1
Limits of
Clearance
Standard
Limits
Hole
H5
Shaft
g4
Class RC 2
Limits of
Clearance
Standard
Limits
Hole
H6
Shaft
g5
Class RC 3
Limits of
Clearance
Standard
Limits
Hole
H7
Shaft
f6
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
Class RC 5
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
e7
Class RC 6
Limits of
Clearance
Standard
Limits
Hole
H9
Shaft
e8
Nominal
Size Range
in
Inches
0 - 0.12 0.1 + 0.2 - 0.1 0.1 + 0.25 - 0.1 0.3 + 0.4 - 0.3 0.3 + 0.6 - 0.3 0.6 + 0.6 - 0.6 0.6 + 1.0 - 0.6
0.45 - 0 - 0.25 0.55 - 0 - 0.3 0.95 - 0 - 0.55 1.3 - 0 - 0.7 1.6 - 0 - 1.0 2.2 - 0 - 1.2
0.12 - 0.24 0.15 + 0.2 - 0.15 0.15 + 0.3 - 0.15 0.4 + 0.5 - 0.4 0.4 + 0.7 - 0.4 0.8 + 0.7 - 0.8 0.8 + 1.2 - 0.8
0.5 - 0 - 0.3 0.65 - 0 - 0.35 1.12 - 0 - 0.7 1.6 - 0 - 0.9 2.0 - 0 - 1.3 2.7 - 0 - 1.5
0.24 - 0.40 0.2 + 0.25 - 0.2 0.2 + 0.4 - 0.2 0.5 + 0.6 - 0.5 0.5 + 0.9 - 0.5 1.0 + 0.9 - 1.0 1.0 + 1.4 - 1.0
0.6 - 0 - 0.35 0.85 - 0 - 0.45 1.5 - 0 - 0.9 2.0 - 0 - 1.1 2.5 - 0 - 1.6 3.3 - 0 - 1.9
0.40 - 0.71 0.25 + 0.3 - 0.25 0.25 + 0.4 - 0.25 0.6 + 0.7 - 0.6 0.6 + 1.0 - 0.6 1.2 + 1.0 - 1.2 1.2 + 1.6 - 1.2
0.75 - 0 - 0.45 0.95 - 0 - 0.55 1.7 - 0 - 1.0 2.3 - 0 - 1.3 2.9 - 0 - 1.9 3.8 - 0 - 2.2
0.71 - 1.19 0.3 + 0.4 - 0.3 0.3 + 0.5 - 0.3 0.8 + 0.8 - 0.8 0.8 + 1.2 - 0.8 1.6 + 1.2 - 1.6 1.6 + 2.0 - 1.6
0.95 - 0 - 0.55 1.2 - 0 - 0.7 2.1 - 0 - 1.3 2.8 - 0 - 1.6 3.6 - 0 - 2.4 4.8 - 0 - 2.8
1.19 - 1.97
1.97 - 3.15
Basic hole system. Limits are in thousandths of an inch.

## Slide 25: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
Using the standard fit tables, determine the limits for a nominal 9/16 (.5625) inch diameter RC 4 fit between a shaft and a hole. Place the dimensions on the drawing using stacked limits form.

## Slide 26: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
First, identify the size range in the left-most column in the fit table for RC fits. The row that identifies the size range that will include the designated diameter in the problem have been highlighted. Note that this column is specified in inches. All other columns in the table are specified in thousandths of an inch.
Nominal
Size Range
in
Inches
0 - 0.12
0.12 - 0.24
0.24 - 0.40
0.40 - 0.71
0.71 - 1.19
1.19 - 1.97
1.97 - 3.15

## Slide 27: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
Next, read across the table on the row that is highlighted to identify the parameters for an RC 4 fit. Because of the lack of space, the columns for fits other than the RC 4 are excluded.
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
0.3 + 0.6 - 0.3
1.3 - 0 - 0.7
0.4 + 0.7 - 0.4
1.6 - 0 - 0.9
0.5 + 0.9 - 0.5
2.0 - 0 - 1.1
0.6 + 1.0 - 0.6
2.3 - 0 - 1.3
0.8 + 1.2 - 0.8
2.8 - 0 - 1.6
Nominal
Size Range
in
Inches
0 - 0.12
0.12 - 0.24
0.24 - 0.40
0.40 - 0.71
0.71 - 1.19
1.19 - 1.97
1.97 - 3.15

## Slide 28: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
The first column for a class RC 4 fit establishes the limits of clearance. The number on top is the allowance at MMC. Converted to inches (by moving the decimal 3 places to the left), this number would be .0006, six tenths of one-thousandth, or six ten-thousandths. The number below (2.3) is the maximum clearance at LMC, or twenty-three ten-thousandths (.0023).
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
0.3 + 0.6 - 0.3
1.3 - 0 - 0.7
0.4 + 0.7 - 0.4
1.6 - 0 - 0.9
0.5 + 0.9 - 0.5
2.0 - 0 - 1.1
0.6 + 1.0 - 0.6
2.3 - 0 - 1.3
0.8 + 1.2 - 0.8
2.8 - 0 - 1.6
Nominal
Size Range
in
Inches
0 - 0.12
0.12 - 0.24
0.24 - 0.40
0.40 - 0.71
0.71 - 1.19
1.19 - 1.97
1.97 - 3.15

## Slide 29: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
Notice that the Hole size, at its lower limit, reads “- 0”. Therefore, use the basic size (nominal 9/16 inch, converted to its decimal equivalent, .5625) as the lower limit for the dimension of the hole.
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
0.3 + 0.6 - 0.3
1.3 - 0 - 0.7
0.4 + 0.7 - 0.4
1.6 - 0 - 0.9
0.5 + 0.9 - 0.5
2.0 - 0 - 1.1
0.6 + 1.0 - 0.6
2.3 - 0 - 1.3
0.8 + 1.2 - 0.8
2.8 - 0 - 1.6
Nominal
Size Range
in
Inches
0 - 0.12
0.12 - 0.24
0.24 - 0.40
0.40 - 0.71
0.71 - 1.19
1.19 - 1.97
1.97 - 3.15
.5625

## Slide 30: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
For the upper size limit for the hole you will notice that the value on the chart is +1.0. This value when converted into inches equals one thousandth of an inch — or ten ten-thousandths. Add the required .0010 to the basic size for the upper limit of the hole (.5625 + .0010 = .5635). This is the upper size limit of the hole, which can now be added to the drawing. It is added to the basic size value.
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
0.3 + 0.6 - 0.3
1.3 - 0 - 0.7
0.4 + 0.7 - 0.4
1.6 - 0 - 0.9
0.5 + 0.9 - 0.5
2.0 - 0 - 1.1
0.6 + 1.0 - 0.6
2.3 - 0 - 1.3
0.8 + 1.2 - 0.8
2.8 - 0 - 1.6
Nominal
Size Range
in
Inches
0 - 0.12
0.12 - 0.24
0.24 - 0.40
0.40 - 0.71
0.71 - 1.19
1.19 - 1.97
1.97 - 3.15
.5625
.5635

## Slide 31: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
To determine the upper size limit of the shaft, we must subtract (note the sign in the table for the upper size limit of the shaft) 0.6 thousandths (or six ten-thousandths) from the basic size. The result will be .5619 (.5625 - .0006 = .5619). Add this value to the drawing as the upper size limit on the shaft.
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
0.3 + 0.6 - 0.3
1.3 - 0 - 0.7
0.4 + 0.7 - 0.4
1.6 - 0 - 0.9
0.5 + 0.9 - 0.5
2.0 - 0 - 1.1
0.6 + 1.0 - 0.6
2.3 - 0 - 1.3
0.8 + 1.2 - 0.8
2.8 - 0 - 1.6
Nominal
Size Range
in
Inches
0 - 0.12
0.12 - 0.24
0.24 - 0.40
0.40 - 0.71
0.71 - 1.19
1.19 - 1.97
1.97 - 3.15
.5625
.5635
.5619

## Slide 32: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
Finally, determine the lower limit of the shaft diameter by subtracting 1.3 thousandths (or thirteen ten-thousandths) from the basic size, and include the value in the drawing.
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
0.3 + 0.6 - 0.3
1.3 - 0 - 0.7
0.4 + 0.7 - 0.4
1.6 - 0 - 0.9
0.5 + 0.9 - 0.5
2.0 - 0 - 1.1
0.6 + 1.0 - 0.6
2.3 - 0 - 1.3
0.8 + 1.2 - 0.8
2.8 - 0 - 1.6
Nominal
Size Range
in
Inches
0 - 0.12
0.12 - 0.24
0.24 - 0.40
0.40 - 0.71
0.71 - 1.19
1.19 - 1.97
1.97 - 3.15
.5625
.5635
.5619
.5612

## Slide 33: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
Now, look back to the column labeled “Limits of Clearance”. These values reveal the total amount of variation that can be allowed on a 9/16” RC 4 fit--when the parts are at maximum material condition and at least material condition.
On the drawing, compare the dimensions diagonally.
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
0.3 + 0.6 - 0.3
1.3 - 0 - 0.7
0.4 + 0.7 - 0.4
1.6 - 0 - 0.9
0.5 + 0.9 - 0.5
2.0 - 0 - 1.1
0.6 + 1.0 - 0.6
2.3 - 0 - 1.3
0.8 + 1.2 - 0.8
2.8 - 0 - 1.6
Nominal
Size Range
in
Inches
0 - 0.12
0.12 - 0.24
0.24 - 0.40
0.40 - 0.71
0.71 - 1.19
1.19 - 1.97
1.97 - 3.15
.5625
.5635
.5619
.5612
Min Clearance Max Clearance
.0006 .0023

## Slide 34: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
At maximum material condition (MMC — largest shaft; smallest hole), the difference is .0006, or 0.6 thousandths.
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
0.3 + 0.6 - 0.3
1.3 - 0 - 0.7
0.4 + 0.7 - 0.4
1.6 - 0 - 0.9
0.5 + 0.9 - 0.5
2.0 - 0 - 1.1
0.6 + 1.0 - 0.6
2.3 - 0 - 1.3
0.8 + 1.2 - 0.8
2.8 - 0 - 1.6
Nominal
Size Range
in
Inches
0 - 0.12
0.12 - 0.24
0.24 - 0.40
0.40 - 0.71
0.71 - 1.19
1.19 - 1.97
1.97 - 3.15
.5625
.5635
.5619
.5612

## Slide 35: Using the Standard Fit Tables to Assign Dimensions to Mating Parts
At least material condition (LMC — smallest shaft; largest hole), there is a clearance of .0023, or 2.3 thousandths.
Class RC 4
Limits of
Clearance
Standard
Limits
Hole
H8
Shaft
f7
0.3 + 0.6 - 0.3
1.3 - 0 - 0.7
0.4 + 0.7 - 0.4
1.6 - 0 - 0.9
0.5 + 0.9 - 0.5
2.0 - 0 - 1.1
0.6 + 1.0 - 0.6
2.3 - 0 - 1.3
0.8 + 1.2 - 0.8
2.8 - 0 - 1.6
Nominal
Size Range
in
Inches
0 - 0.12
0.12 - 0.24
0.24 - 0.40
0.40 - 0.71
0.71 - 1.19
1.19 - 1.97
1.97 - 3.15
.5625
.5635
.5619
.5612
-.0006
-.0013
+.0010
-.0000
.5625
.5625
Values Referenced to Basic Size:

## Slide 36: Web Sites for Fits and Tolerances
http://www.cobanengineering.com/Tolerances/ANSILimitsAndFits.asp (very good)
http://www.mech.uq.edu.au/courses/mech2110/standard_fits/index.html