## Slide 1: Preparation & microscopic examination of a direct fecal smear
Amal Almuhana
2012

## Slide 2: Introduction
Direct fecal smears
Direct fecal smears can be used as a quick screening test to check for any intestinal parasite.

## Slide 3: Advantages &Disadvantages
Advantages:-
Useful for detecting motile organisms.
Protozoa are often detected via a direct fecal smear.
Quick process.

## Slide 4: 2) Disadvantages
Small size of the sample limits its usefulness.
You may get inaccurate results.
If your examination finds no evidence of a parasite but the patient actually harbors the parasite, then the results are called a false negative result. False negative results are common with direct fecal smears.

## Slide 5: Fecal collection
When collecting
- Fecal sample from animal in question.
- Relatively fresh
- May preserve in refrigerator if exam not immediate.
- Free from debris
Storage
Plastic or glass jar/ vial
Plastic cup
Plastic bag

## Slide 6: Preparing direct fecal smears (procedure):-
Put small amount of feces on glass slide.
Mix with drop of saline.
Place cover slip on mixtures.
Observe under microscope.
Note:- If the feces is already in a liquid state because the animal has diarrhea, obviously no fluid is needed to spread the feces over the slide.

## Slide 7
feces+ saline on the slide
Mix until it is dispersed
Examine under microscope

## Slide 8: Direct fecal smear cont.
Direct fecal smears may be examined as :
A wet mount, or can be
Dried and stained.

## Slide 9: Wet mount technique
The fecal smear may be examined in its wet state by simply placing a cover slip over the drop of wet fecal material.
This method is most useful looking for trophozoites which can be observed by their characteristic movement and appearance.

## Slide 10: Staining
A drop of stain can be added before the cover slip is placed or after having examined the unstained preparation.
The stain will diffuse and then you can examine it.
The iodine will stain the organisms a dark orange brown color.
If you use new methylene blue instead, you will see organisms contrasted against a blue background.
WITHOUT STAINING

## Slide 11
Note:- You can choose to look at the unstained preparation first for motile forms, and then add stain by applying it at the edge of the coverslip.
Methylene blue stain at the edge of the cover slip with a Pasteur pipette.
Stain will diffuse
Application of iodine stain

## Slide 12: 2) Dry mount technique
The fecal smear may be examined in a dry state and stained.
Prepare the slide as for a wet mount, but instead of placing a cover slip, let it dry so that only a thin film is visible on the slide.
It should be heat fixed by passing it over a flame for a few seconds.
Then you can stain it.
A thin fecal smear is prepared and dried

## Slide 13: Staining
The stains most commonly used are the Diff Quik or acid fast stain.
If you are trying to rule out Cryptosporidium spp., then the acid fast stain is the stain of choice.

## Slide 14: Importance of direct fecal smear
Parasitic diseases such as ascariasis, hookworms, whipworms, etc.., can be diagnosed by examining stools under a microscope for the presence of worm larvae or eggs.
Some bacterial diseases can be detected with a stool examination.
Quick screening test to check for any intestinal parasite.

## Slide 15: Under microscope
Schistosoma spp egg
Protozoa appear
Iodine stain. an Entamoeba coli trophozoite