## Slide 1
Basic ElectroCardiogram
(ECG)
Prepared by
Ms: Alwah M. Alkathiri
Mr. Hamza Ratrout
Revised by:
Dr. Irene Roco

## Slide 2
        Outline of lecture;
Definition of ECG
Cardiac Conduction System
Reasons for Performing ECG
Types of Leads ( 12, 15, 18 Leads)
Types of ECG (Stress ECG, Continuous ECG
Important Clinical Consideration
Preparation
Placement of electrodes
References

## Slide 3: Electrocardiography (ECG or EKG*)
the process of recording the electrical activity of the heart over a period of time using electrodes placed on a patient's body.

## Slide 4: Electrocardiography (ECG or EKG*)
These electrodes detect the tiny electrical changes on the skin that arise from the heart muscle depolarizing during each heartbeat.

## Slide 5: Cardiac Conduction System
(From: Yanowitz, FG. The Alan E Lindsay ECG Learning Centre in Cyberspace [homepage on the Internet]. c2012. Available from: http://library.med.utah.edu/kw/ecg/index.html.)
(Marquette Electronics, 1996)
Anatomical orientation:
Figure 1:

## Slide 6: Electrical Conduction System
Depolarization that starts with pacemaker cells in the sinoatrial node,
spreads out through the atrium, atrioventricular
node Bundle of His
Right and Left Bundle Branches
Purkinje fibers spreading down and to the left throughout the ventricles.

## Slide 8: ECG Graph Paper
y
x
Voltage (millivolts; mV)
Time (seconds; s)
y’
x’
(1  1) mm2
0.04 seconds
0.1 mV
Question: What would the bigger square, i.e. the (5  5) mm2, represent?
Answer: 0.2 seconds.

## Slide 9: Electrocardiography (ECG or EKG*)
In a conventional 12 lead ECG, ten electrodes are placed on the patient's limbs and on the surface of the chest recorded over a period of time (usually 10 seconds).
A typical ECG tracing is a repeating cycle of three electrical entities:
a P wave (atrial depolarization)
a QRS complex (ventricular depolarization)
a T wave (ventricular repolarization).

## Slide 10
1. Standard 12 Lead
Most commonly used tool to diagnose:
Dysrhythmias
Conduction abnormalities
Enlarged heart chambers
Myocardial ischemia or infarction
High / low calcium and Potassium level
Effects of some medications
Types of Leads used in Obtaining ECG

## Slide 11
2. 15 Lead ECG
3 chest leads are added across the right precordium
A valuable tool for early diagnosis of Right ventricular and posterior left ventricular infarction
Types of Leads used in Obtaining ECG

## Slide 12
3. 18 Lead ECG
3 chest leads are added from the 15 lead ECG
Early detection of Myocardial Ischemia and injury
Types of Leads used in Obtaining ECG

## Slide 13: ECG measures the following:
rate and rhythm of heartbeats
the size and position of the heart chambers
the presence of any damage to the heart's muscle cells or conduction system
the effects of cardiac drugs
the function of implanted pacemakers.

## Slide 14: Reasons for performing electrocardiography include:
Suspected heart attack
Suspected pulmonary embolism
A third heart sound, fourth heart sound, a cardiac murmur or other findings to suggest structural heart disease
Perceived cardiac dysrhythmias

## Slide 15: Reasons for performing electrocardiography include:
5. Fainting or collapse
6. Seizures
7. Monitoring the effects of a heart medication
8. Assessing severity of electrolyte abnormalities, such as hyperkalemia

## Slide 16: Types of ECG
Stress Electrocardiography
Uses ECG to assess the client’s response to an increased cardiac workload during exercise using treadmill or stationary bicycle

## Slide 17: Stress Electrocardiography
Goal of this test: to increase the heart rate to the target rate
Client with Coronary artery disease may develop chest pain and characteristic ECG changes during exercise

## Slide 18: When to Terminate Stress Test
When Target heart rate is achieved
When patient experiences symptoms / complications:
Chest pain
Extreme fatigue
Decrease in BP/ PR
Serious dysrhythmia or ST segment
changes in ECG

## Slide 19: Nursing Responsibility for Stress Electrocardiography
Monitor :
Two or more ECG leads for HR, rhythm and ischemic changes
BP
Skin temperature
Physical appearance
Perceived exertion
Symptoms ( chest pain, dyspnea, dizziness, leg cramping, fatigue)

## Slide 20: 2. Continuous Electrocardiographic Monitoring
Standard for patients who are at risk for dysrhythmias
Patients should be informed that this monitoring will not detect symptoms such as dyspnea or chest pain, therefore, patients need to be advised to report symptoms to the nurse whenever they occur

## Slide 21: Important clinical considerations
Correct lead-placement and good skin contact are essential.
Avoid electrical interference (machine to be earthed).
Compare serial tracings, if available.
Relate any changes to age, gender, clinical history, etc.
Consider co-morbidities and intercurrent illnesses that may have an effect on the ECG.
Obtain a photocopy for future reference.
Interpret the ECG systematically to avoid errors.
Notes: 21

## Slide 22
Ensure that the client did not receive any medication
Ask your pt to remove all jewelry and to wear a hospital gown
Usually ECG is taken while the patient is resting so ask your pt to lie down
Areas such as the chest where the adhesive electrodes will be placed may need to be shaved first, then skin is cleaned
Preparation

## Slide 23
Avoid oily or greasy skin creams and lotions the day of the test. They interfere with the electrode-skin contact
Avoid full-length hosiery, as electrodes need to be placed directly on the legs.
Wear a shirt that can be easily removed to place the leads on the chest.
Preparation

## Slide 24
Placement of electrodes
Ten electrodes are used for a 12-lead ECG.
The electrodes usually consist of a conducting gel, embedded in the middle of a self-adhesive pad onto which cables clip. Sometimes the gel also forms the adhesive. They are labeled and placed on the patient's body
Proper placement of the limb electrodes, color-coded
The limb electrodes can be far down on the limbs or close to the hips/shoulders, but they must be even (left vs right)

## Slide 25
Electrode label | Electrode placement
RA | On the right arm, avoiding thick muscle.
LA | In the same location where RA was placed, but on the left arm.
RL | On the right leg, lateral calf muscle.
LL | In the same location where RL was placed, but on the left leg.

## Slide 27
Instruct patient to be calm and no movement, Then print the result
The test is completely painless and takes less than a minute
to perform once the leads are in position.
After the test, the electrodes are removed & clean the skin

## Slide 28: References
Brunner & Suddarth’s Medical Surgical Nursing. 10th ed
Kozier & Erbs’ Fundamentals of Nursing . Eighth ed. 2008