## Slide 1: Determination of bicarbonate in blood

## Slide 2: Introduction:

## Slide 3: Introduction:

## Slide 4: Back titration
is an analytical chemistry technique that allows the user to Determine the concentration of an analyte by reacting it with a known number of moles of excess reagent. The excess reagent is then titrated with a second reagent.
The concentration of the analyte in the original solution is then related to the amount of reagent consumed.

## Slide 5: purposes of using back titration
Back titration is designed to resolve some of the problems encountered with forward or direct titration. Possible reasons for devising back titration technique are :
1- The analyte may be in solid form .
2- The analyte may contain impurities which may interfere with direct titration.
3- The analyte reacts slowly with titrant in direct or forward titration.
4- Weak acid – weak base reactions can be subjected to back titration for analysis of solution of unknown concentration.

## Slide 6: Advantages of doing back titration
1- Useful if the endpoint of the reverse titration is easier to identify than the endpoint of the normal titration.
2- Useful when trying to work out the amount of an acid or base in a non-soluble solid.

## Slide 7: Disadvantages of back titration
1- Needs skill and practice for effective results
2- Instruments have to be properly calibrated since it will give affected the final result.
3- Reactivity of the elements to be titrated should be well researched since this may affect the end point.
4- Time consuming if done manually.

## Slide 8: Principle
The HCO3¯ concentration is determined by :
1- Adding an excess of 0.001M HCL, to volatilize the HCO3 ( Weak Base) as CO2, swirling to allow the CO2 to escape.
2- Back-titrating the excess HCL (strong Acid) with 0.001M NaOH (Strong Base).

## Slide 9: Principle
HCO3¯ + excess HCL H2O + CO2 + CL¯
Excess HCL + NaOH NaCL + H2O ( back titration)

## Slide 10: Procedure
A) Comparison Solution:
1- In Erlenmeyer flask mix the following:
6 ml 1% saline
0.1 ml sample (NaHCO3)
2 drops phenol red
Important (Shake after each addition).
2- rotate gently to mix the contents until get pink color (end point) .
N.B.: if you use blood sample , the transition range of this indicator is pH 8.4-6.7 (yellow to red).

## Slide 11
B) Titration of the Sample :
A) First reaction:
1- In Erlenmeyer flask mix the following:
4 ml 1% saline .
0.1 ml sample (NaHCO3).
10 ml HCL (0.001 M) (excess)
2- Shake after each addition to allow the (CO2) to escape.
3- add 2 drops phenol red .

## Slide 12
B) Second reaction:
1) Titrate with NaOH (0.001 M) until you get pink color (end point).
2) Record the volume used.

## Slide 13: Comparison solution

## Slide 14: First step before titration

## Slide 15: After addition of thefirst drop of NaOH

## Slide 16: End point

## Slide 17: Result

## Slide 18: Calculation
1- HCO3- = {(M= ?) , (V=0.1 ml)}.
HCO3- + Excess HCL (known molarity,known volume) H2O + CO2 + CL- .
Remember ! Weak Base + acid = No great pH = hard to detect end point.
HCO3- + ( Excess HCL = strong acid)
titrated with NaOH (strong base) = sharp end point .

## Slide 19: How to work out HCO3- Concentration?
HCL + NaOH NaCL + H2O
0.001 M 0.001 M
ml = ? 7 ml
Number of moles of NaoH = Number of moles of Hcl
C Hcl X V Hcl = C NaOH X V NaOH
V Hcl = (0.001X7)/ 0.001 = 7 ml.

## Slide 20
HCL (Supplied) – HCL (Left over) = HCL (reacted).
10 ml – 7 ml = 3 ml reacted with HCO3-.
HCO3- + HCL H2O + CO2 +CL-.
= 0.1 ml, ? M + 3 ml , 0.001 M.
Number of moles of HCO3- = Number of moles of Hcl
C HCO3 X V HCO3= C Hcl X V Hcl
C HCO3 = 0.001 X 3/0.1=0.03 M