## Slide 1
Block 4: Sustainable Management of the Industry
Forum 20: HSE and Operations Integrity – Keeping Pace
Engineering Management and Inspection Schedule of Petroleum Well Integrity
Musaed N. J. AlAwad
Professor
King Saud University, Riyadh, Saudi Arabia
Hawwas A. Mohammed, KACST, Riyadh, Saudi Arabia
1
Notes: <number>

## Slide 2
Forum 20: HSE and Operations Integrity – Keeping Pace
Poster Title: Engineering Management and Inspection Schedule of Petroleum
Well Integrity
Abstract
Oil and gas supply the world with energy by approximately 60% of all available energy sources. The global hydrocarbon well inventory accounts for at least 1.8 million wells, more than 870,000 wells of these wells are active. Wells must be designed to ensure well integrity, i.e. that the fluids stay contained within the wellbore, and that the surrounding subsurface layers, including aquifers, are protected. Well integrity is a result of technical, operational and organizational barriers applied, with the intention to contain and control the reservoir fluid and well pressures. Failure to obtain and maintain adequate well integrity (barriers) could lead to catastrophic events, like demonstrated in the Gulf of Mexico in 2010, with the Deepwater Horizon incident. For an oil/gas well to maintain its integrity and be produced effectively and economically, it is pertinent that a complete zonal isolation is achieved through out the life of the well. This complete zonal isolation, however, can be compromised due to factors that come into play during the operative life of the completed well.
2

## Slide 3
Forum 20: HSE and Operations Integrity – Keeping Pace
Poster Title: Engineering Management and Inspection Schedule of Petroleum
Well Integrity
Abstract (cont.)
In this study, the typical well integrity primary and secondary barriers are outlined in details. Examples of Worldwide incidents due to well integrity failure are presented. An appreciable statistical data on well integrity failures worldwide are presented and analyzed. Furthermore, risks associated with different types of well integrity failure issues and how to reduce/mitigate them are discussed. Procedures, roles and responsibilities of personnel involved in the well lifecycle towards well integrity are presented. Finally, a holistic Well Integrity Barriers Inspection Schedule for use by the oil and gas producing companies worldwide are developed. This paper provides the oil industry society with a clear picture on the elements of petroleum well integrity; a general well integrity inspection schedule; and a risk based inspection and maintenance matrix.
3

## Slide 4
Introduction
Well integrity problems are seriously facing the oil and gas industry worldwide. For example, 45%, 34%, and 18% of the wells in Gulf of Mexico, North Sea UK, and North Sea Norway, respectively are suffering from well integrity failures (Decoworld, 2014).
According to the Society of Petroleum Engineers (SPE, 2016), over the next decade, the oil industry will drill more wells than they have in the last 100 years and that of the world's current inventory of 1.8 million wells, roughly 35% have integrity problems (Viableopposition, 2013).
In the Middle East, over 50% of all wells have integrity issues with 10-15% of these being critical (Well Integrity Conference, 2015).
Furthermore, the rise in extended reach wells and other high risk characteristics, such as HP/HT wells, shale formations, corrosion, scale, and sour service fields in the Middle East, are increasing the spotlight on well integrity.
4

## Slide 5
Introduction
The most common definitions of “well integrity” are based on the concept of constantly retaining two intact barriers between the reservoir and the external environment.
The NORSOK D-010, 2004 standard, developed by the Norwegian petroleum industry, provides the following definitions:
  Well Integrity (WI): “Application of Technical, Operational and Organizational Solutions to Reduce Risk of Uncontrolled Release of Formation Fluids throughout the Life Cycle of a Well”.
  Well Barrier (WB): “Envelope of one or several dependent barrier elements preventing fluids or gases from flowing unintentionally from the formation, into another formation or to surface”.
  Well Barrier Element (WBE): “An object that alone cannot prevent flow from one side to the other side of itself”.
5

## Slide 6
Primary Well Barrier Elements
Formation /cap rock above reservoir
Cement
Casing
Production packer
Completion string (below the DHSV)
Subsurface safety valve (DHSV)
    Gas Lift Valve (GLV)
    Chemical injection line (CIL)
Secondary Well Barrier Elements
Formation above production packer
Cement
Casing with seal assembly
Tubing hanger with seals
Annulus access line and valve
Production tree (X-mas tree) with X-mas tree connection
6
Notes: <number>

## Slide 7
Well Integrity Management
Well integrity management is an art of managing the well to reduce risk applying technical, operational and organizational solutions (Sanjiv, 2014; James, 2011), and it is divided into four distinct stages:
7
Well design stage,
Well construction stage,
Well integrity monitoring (production) stage, and
Well abandonment stage .

## Slide 8
Well integrity problems occur because of a wide range of circumstances. Many different types of failures can lead to loss of well integrity with varying degree of severity. The obvious consequences of loss of well integrity are:
blowouts or leaks that can cause material damage,
personnel injuries,
loss of production, and
environmental damages resulting in costly and risky repairs.
Well integrity depends not only on equipment robustness, but on the total process, the competence and resources of the organization and the competence of the individuals.
After Dickson, 2013
8

## Slide 9
Study Objectives
Extensively review and analyze well integrity case studies worldwide in order to:
  Understand the concept of well integrity and the corresponding regional standards and regulations.
  Understand the different stages from well operations, design and construction, to production and its impact on well integrity.
  Identify risks associated with different types of well integrity failure issues and how to reduce/mitigate them.
  Define procedures, roles and responsibilities of personnel involved in the well lifecycle towards well integrity.
Develop a universal “well integrity barriers inspection schedule” for use by the oil and gas producing companies Worldwide.
9

## Slide 10
Methodology
A comprehensive search was conducted to compile a worldwide well integrity statistical data based on the type of barrier failure with age.
Data collections were collected through several regional publications, journals, reports, conference proceedings and corporate web sites of interest.
The summary of findings from published statistics on well barrier and well integrity failure are presented at the following sources:
Hawwas Abdullah Mohammed (December 2015), “Engineering Management of Petroleum Well Integrity”, Master Thesis, Petroleum and Natural Gas Engineering Department, College of Engineering, King Saud University, Saudi Arabia.
Musaed N. J. Al-Awad and Hawwas A. Mohammed (June 2016): “Engineering Management and Inspection Schedule of Petroleum Well Integrity”, Journal or Emerging Technologies in Engineering and Applied Sciences, Volume 7, No. 3, p. 109-117.
10

## Slide 11
Methodology
In this study wells are categorized into seven groups based on their barrier failure frequency with age as shown in Table 2. Classification criterion shown in Table 2 is used to analyze well integrity failures using the survey of the literature available data performed in this study. The statistical data of well barriers failure frequency with age was excluded wells with unknown age.
11
Well integrity classification criterion

## Slide 12
Results and Discussion
It is difficult to come up with a mathematical model for well integrity failure likelihood. Most well integrity failure modes can occur anytime in the well life. However, magnitude of well integrity failure due to specific barrier can be predicted.
Well integrity barriers failure occurring frequency based on the data analyzed (more than 15000) in this study are as follows:
Cement failure (12446 incidences).
Casing failure (2421 incidences).
Production tubing failure (643 incidences).
Formation failure (109 incidences).
Wellhead failure (78 incidences).
Other barriers (Minor indecencies).
12

## Slide 13
Well integrity barriers failure occurring frequency
13

## Slide 14
  Well Integrity Barriers Failure Rate
Tending of failure rate against time can help to determine inspection frequencies for certain equipment and influence future replacement and selection.
The expected well components failure rate across time are divided into three categories as follows:
Early life (decreasing failure rate), when failure
is attributed to components quality.
Useful life (constant failure rate), when failure
is due to normal service stresses.
Wear out (increasing failure rate), when failure
is due to wear and tear.
14
After IAOGP Draft 116530-2, 2012

## Slide 15
  Risk Analysis of Well Integrity Barriers Failure
Rates of well integrity failure categories:
Remote Failures: within 20 years or more.
Occasional Failures: within 4 to 5 years.
Likely Failures: within 2 to 3 years.
Frequent Failures: within 1 year or less.
Severity categories of well integrity failures:
Catastrophic Failures: major system damage, system loss, death or disability.
Critical Failures: the failure will degrade the system beyond acceptable limits, so that deaths or injuries may occur if no further action is taken (assuming there is time available to do so).
Major Failures : the failure will degrade the system beyond acceptable limits, but adequate countermeasures are available to control the possible unwanted effects of the failure.
Minor Failures: the failure does not degrade the overall performance beyond acceptable limits.
15

## Slide 16
For easier recognition of the risk magnitude, color coding is normally used:
Red Color: represents extremely high hazard (EHH).
Pink Color: represents high hazard (HH).
Yalow Color: represents medium hazard (MH).
Green Color: represents low hazard (LH).
16

## Slide 17
A holistic Risk based Inspection and Maintenance Matrix
17

## Slide 18
  Conclusions
  An inspection program should be set for oil and gas production assets focuses on the following six primary well integrity surveys:
  Wellhead valves integrity inspection.
  2) Surface and Subsurface Safety Valves (SSV & SSSV) and Emergency Shut-Down (ESD) System
  functionality and integrity testing.
  Annuli Survey.
  Temperature Survey.
  5) Corrosion Logging.
  The developed well integrity inspection schedule and the risk based inspection and maintenance matrix is a generalized guide for use when specific data is not available. However, for more accurate results, the history data of the area under consideration should be used.
  More data is needed to improve the developed well integrity inspection schedule.
  A more specific inspection schedule is required based on environmental specifications differences, i.e. for HP/HT, Geothermal and highly corrosive fluids situations.
18

## Slide 19
Musaed N. J. AlAwad
Professor, COE Vice Dean for Development and Quality
King Saud University, Riyadh, Saudi Arabia
PHOTO HERE
Musaed N. J. AlAwad is a professor in the Petroleum and Natural Gas Engineering Department and the College of Engineering Vice Dean for Development and Quality at King Saud University, Riyadh, Saudi Arabia.
He obtained his B.Sc. in 1987 and M.Sc. degrees in 1990 in Petroleum Engineering both from King Saud University, Riyadh, Saudi Arabia and Ph.D. degree in 1994 in Petroleum Related Rock Mechanics from Heriot-Watt University, Edinburgh, United Kingdom.
Professor Musaed published more than 85 papers and numerous research projects reports and delivered several industry short courses in Sand Control and Management, Wellbore Instability, Rock Mechanics, Clay Mineralogy, and Oil and Gas Well Drilling Engineering.
19