## Slide 1: Cosmetic products for face
1. Face Powder:
Loose face powder.
Compact Face Powder.
2. Lipstick

## Slide 2: Face Powders
A face powders is basically a cosmetic product which its function is the complement skin color.
It should enhance the appearance of the skin by masking the shine due to secretion of sebaceous and sweat glands.
A powder should achieve its effect by being opaque enough to mask minor blemishes but it must not impart a mask like effect.

## Slide 3
It must possess reasonable lasting properties, so that, frequent re-powdering is unnecessary.
Since there is no one ingredient that possesses all the properties desired in a face powder, a blend of constituents is employed.

## Slide 4: Essential characteristics of a good product:
Covering power and Playtime:
Covering power is calculated from the refractive indices.
Materials of high refractive index and relatively small particle size are referred in the preparation of face powders.
Playtime: is the amount of time that the make up can be moved on the face prior to sitting.

## Slide 5
2. Slip:
It is the quality of easy spreading and application of powder.
3. Adhesiveness:
How well the powder will cling to the face.
4. Absorbency:
Eliminate shiny skin in certain facial areas by absorbing sebaceous secretion and perspiration.
5. Bloom:
Ability to impart a velvety peach like finish to the skin.

## Slide 6: 1. Loose face powder
The primary consideration in the manufacture of face powder is the selection of the raw materials.
1. Talc:
The first and foremost ingredient to be considered in the formulation and manufacture of face powder.
Easy slip and low covering.
Particle size of a talc at least 98% should pass through a 200-mesh.

## Slide 7
2. Kaolin (China clay ):
Good covering power and adhesion.
Grease-resistant and perspiration-absorbent properties.
Remove the shine of talc.
Has soothing effects on the skin.
It is used in formulation to adjust fluffiness and control bulk.
The color of the Kaolin used should be as light as possible.

## Slide 8
3. Precipitated Chalk (Calcium Carbonate):
Reduces the shine of talc and has good covering power.
It helps to absorb the perfume.
Grease-resistant and perspiration-absorbent.
Developing the bloom effect when face powder is applied.
When this raw material is used in excess, the powder may acquire a dry feel, but moderate usage is most helpful to face powder formulas.

## Slide 9
4. Magnesium Carbonate:
Has fine absorbent properties and distributing perfume.
Should be employed in moderation, since use in excess may result in a drying effect on the skin.
5. Metallic Stearates:
The most important characteristics of zinc and magnesium stearates are their adhesive and waterproofing properties.
Also possesses a soothing quality.
Use in moderate amounts 4 to 15%.

## Slide 10
6. Zinc Oxide:
Has certain therapeutic properties and help to clear up minor skin disorders.
It possesses moderate adhesive properties.
To avoid any drying effect and yet allow for sufficient coverage, a formulation may consist of as much as 25%.

## Slide 11
7. Titanium Dioxide:
Is three to four times better as a covering agent than zinc oxide.
It has less adhesion and does not blend well.
Used alone or in conjunction with zinc oxide, 10 to 15 % titanium dioxide will allow for sufficient covering.
8. Rice starch:
It is an ideal nutrient for bacteria.
The bloom and absorbent properties that were contributed by the use of the rice starch are now provided by calcium carbonate and other materials.

## Slide 12
9. Silica and Silicates:
Maintain free flowing characteristics.
perfume carriers.
Use of silicates such as magnesium trisilicate they have extremely high water-and-oil absorption properties.

## Slide 13
The synthetic pigment bismuth oxychloride was developed to replace guanine.
Metallic powders (mica, aluminum, bronze) are used to formulate powders with a sheen.
The luster is harsher than that produced by the pearl. The cost is very much lower than the synthetic pearl.
Mother-of-pearl (thin layers of calcium carbonate which are bound together) produce the frosted effect.
Synthetic pearl, Mother-of-pearl and mica must not be milled, since milling would destroy their optical lustrous effects.

## Slide 14
Color in Face powder Preparation
The quantity of color required depends to a great degree on the type of base used in the formula.
The use of fine quality inorganic blended with a smattering of organic lakes allows for a broad variety of face powder shades.

## Slide 15
The following organic lakes commonly used in face powder formulation:
Red | 
D & C Red No. 7 | Calcium lake
D & C Red No. 9 | Barium lake
D & C Red No. 12 | Barium lake
D & C Red No. 13 | Strontium lake
D & C Red No. 19 | Aluminum lake
D & C Red No. 21 | Aluminum lake
D & C Red No. 36 | Barium lake
Orange | 
D & C Orange No. 4 | Aluminum lake
D & C Orange No. 17 | Barium lake
Yellow | 
D & C Yellow No. 5 | Aluminum lake

## Slide 16
Perfume in Face powder Preparation
Perfume used be non-irritating, stable to mildly alkaline condition and not undergo oxidation or volatilize too easily.
The fragrance must be compatible with all of the powder ingredients since problem with rancidity, heterogeneity of odor, and discoloration may result from improper odor selection.
0.2 And 1% is a reasonable perfume rang in a face powder.

## Slide 17
Example of Preparation for Loose face powder
Rx:
Talc 75%
Zinc oxide 10
Rice starch 10
Zinc stearate 5
Perfume and color q.s.

## Slide 18: 2. Compact Face Powder
A Compact Face Powder which has been compressed into a cake and is usually applied with a powder puff.
Raw Materials:
There are 2 characteristics for pressed powder:
Binding ability
Payoff.
Binding Agent:
There are 5 basic types of binders used:
Dry binders.
Oil binders.
Water-soluble binders.
Water-repellent binders.
Emulsion binders.

## Slide 19
1. Dry binders: such as metallic stearates ( zinc or magnesium stearate).
2. Oil binders: such as mineral oil, isopropyl myristate, and lanolin derivatives.
3. Water-soluble binders: solution of gums : such as tragacanth, karaya, and Arabic.
Synthetic: such as PVP ( polyvinylpyrollidone), methyl cellulose, and carboxymethyl-cellulose.
Preservative is essential, this type to present bacteriological growth problem.

## Slide 20
4. Water-repellent binders: mineral oil, fatty esters of all types, and lanoline derivatives used and are mixed with a considerable quantity of water, preservative and wetting agent.
5. Emulsion binders: soaps: such as triethanolamine stearate and nonionic emulsifiers in mineral oil-water combination.
Preservatives: p-hydroxybenzoate-type essential in compact powders.

## Slide 21
Method Of Preparation Compact Face Powder
Compression Method
There are 3 general procedures:
The wet molding process:
The mixture is made paste like with water and cast into molds.
The upper surface of the paste is coated with an adhesive, then pressed down by properly shaped metal or glass plates to which the tablets adhered.
The tablets are then allowed to dry and are withdrawn from the molds.

## Slide 22
2. The damp compressing method:
The mixture is wetted down with a liquid binder, then blended until the proper plasticity of the mass has been attained.
The powder is then screened and passed to compression machines the finished tablets are dried at elevated temperature.
3. The dry compressing method:
The mixture are milled and the milled powder may moistened with binder, the mixture is then thoroughly blended and the powder is pressed. This method is prefer since very little binding agent is required.

## Slide 23
Example of Preparation for Compact face powder
Rx:
Mineral oil 1%
Polyoxyethylene stearate 2
Water 97
Preservative q.s.

## Slide 24: Evaluation of Face Powder
Laboratory Tests:
Shade control:
The color of the powder is checked by:
Spreading the powder out and flattened on a white background.
By applying the powder to the skin.
The color of the pressed powder in the correct container is assessed.
In each case the sample being assessed is compared for shade to the standard.

## Slide 25
b. Dispersion of color:
Color dispersion is checked by spreading the powder onto a white surface and examining under magnification.
c. Pay off:
It is the transfer of powder from the container to the puff. Pay off should be assessed on the skin using the correct applicator.

## Slide 26: Lipsticks
Lipstick is a cosmetic product containing pigments, oils, waxes, and emollients that applies color, texture, and protection to the lips.
The prime duty of lip care preparation is, to prevent drying and cracking of the lips.

## Slide 27
A lipstick should have the following storage characteristics:
A smooth and shiny appearance.
Freedom from sweating.
A suitable degree of firmness during reasonable variations of climatic temperature.
Retain plasticity without any tendency to dry-out or crumble.

## Slide 28: Composition
To consider the formulation of lipsticks the basic raw materials are conveniently classified as follows:
Wax mixture
Oil mixture
Bromo mixture
Colors
Preservatives and other additives.

## Slide 29
a. Wax and oils:
Best results are obtained by using a mixture of waxes of different melting points and adjusting the final melting point of the stick by adding a sufficient quantity of a high melting point.
Formulation which contain a high concentration of a single high melting point wax should be avoided.

## Slide 30
White Beeswax:
A useful material to bind oils and higher melting point waxes.
The molten wax shrinks slightly on cooling.
Higher concentrations give a dull waxy appearance and cause the stick to crumble during use.
2. Ozokerite wax:
Sticks containing more than 10% Ozoketrite tend to crumble during application.

## Slide 31
3. Candelilla wax:
Gives a smooth and glossy appearance to a lipstick if used at a slightly higher dosage concentration than the proportion of beeswax.
4. Paraffin wax:
Show strong oil adsorption properties.
5. Cetyl alcohol:
Binding agent between polar and non-polar ingredients.

## Slide 32
6. Lanolin:
Offer adhesion due to its plasticizing as well as luster.
7. Isopropyl lanolate:
Disperse pigments well and has convenient fusing properties to other ingredients.
8. Cetyl lactate & myristyl lactate:
Has a wax like consistency at room temperature but melts on contact with the skin, giving the product a soft effect.

## Slide 33
9. Castor oil:
Is used in nearly all lipstick preparation because of its property as a wetting agent for pigments.
It has a thick consistency which provides stability.
10. Paraffin oil:
Serve as lubricant for application and also add luster.

## Slide 34
The color system:
Permitted colors must be used.
The color is panted to the lips in 2 ways:
By staining the skin with staining dyes.
These are dye stuff in solution capable of penetration the outer surface of the lips e.g. acid eosin, and other halogenated derivatives of fluorescein known as (bromoacids).

## Slide 35
Disadvantage:
Difficulty of uniform dispersion of these dye in the lipstick mass which resulting in shade variation.
So Amine salts of bromo acid dyes, dissolve in a mixture of waxes and oils can be more uniformly dispersed.
2. By covering the lips with a colored layer:
The color is produced by insoluble dyes and pigments, which make the film more opaque.
Both inorganic, organic pigments & metallic lakes are used.

## Slide 36
Titanium dioxide:
The most effective white pigment used to obtain pink shades and opaque film on the lips. Protecting them from the aging effect of the sun.
Metallic Lakes:
Ca, Barium and Aluminum lakes of many D&C color.
A mix of staining dyes pigments and Tio2 (Titanium dioxide ) is usually used in lip stick preparation.

## Slide 37
Example for Preparation of Lipstick
Rx:
Carnuba wax 10%
Bees wax 15
Lanoline 5
Cetyl alcohol 5
Castor oil 65

## Slide 38
Evaluation of Lipstick
Physical appearance:
Color dispersions are controlled microscopically.
B. Disintegration Time:
Erweka dissolution tester type DT was adapted to suit the test and the time needed for the stick to melt completely is to observed.
C. Hardness:
Use Erweka hardness tester model SBT which used to measure the suppository hardness.

## Slide 39
2. Hardness may be assessed by using a penetrometer.
d. Melting Range:
Is determined by using the capillary tube immersion technique in glass water bath.
e. Softening Point:
It is the temperature at which the stick will become unusable.
Softening point is determined as following:
Mount the sticks vertically in petri dishes and put into an incubator with an inner glass door. The sticks are observed as the temperature is slowed raised until the sharp edges of the tip and sides being to melt or round off.