## Slide 1: Sewage treatment

## Slide 2
Sewage is the mainly liquid waste containing some solids produced by humans, typically consisting of washing water, urine, feces, laundry waste, and other material that goes down drains and toilets from households and industry

## Slide 3: Sewage treatment
is the process of removing contaminants from wastewater and sewage. It includes physical, chemical and biological processes to remove physical, chemical and biological contaminants. Its objective is to produce a waste stream and a solid waste or sludge suitable for discharge or reuse back into the environment.

## Slide 4
Sewage is created by residences, institutions, hospitals and commercial and industrial establishments.
It can be treated close to where it is created (in septic tanks), or collected and transported via a network of pipes and pump stations to a municipal treatment plant.

## Slide 5: Sewage Treatment Systems
Rural and suburban areas – septic tank
Urban areas – wastewater treatment plants
  Primary treatment – physical process
  Secondary treatment – biological process
  Chlorination – bleaching and disinfection

## Slide 6: Septic tank
common in areas with no connection to main sewage pipes
It is 4000 - 7500 litres in size
The five parts of a sewage disposal system are:
(1) the house plumbing,
(2) the sewer line from house to septic tank,
(3) the septic tank,
(4) the septic tank outlet sewer pipe,
(5) the final soil treatment unit, which may be a soil absorption unit

## Slide 7
The material in the septic tank separates into three distinct layers:
A top layer of floating scum
A middle liquid zone
A bottom layer of sludge

## Slide 10
keep the septic tank and soil absorption unit at least 100 feet away from any private well that is less than 100 feet deep, and at least 50 feet away from wells more than 100 feet deep.

## Slide 11: Sewage treatment plant
Grit removal
Pre-treatment may include a sand or grit channel or chamber where the velocity of the incoming wastewater is adjusted to allow the settlement of sand, grit, and stones

## Slide 12: Primary treatment
Settle solids for 2‑3 hours in a static, unmixed tank, commonly called "primary clarifiers" or "primary sedimentation tanks". The tanks are used to settle sludge while grease and oils rise to the surface and are skimmed off
Sludge is directed towards the base of the tank where it is pumped to sludge treatment facilities.

## Slide 14: Secondary Treatment
Sludge from the sedimentation tanks is digested anaerobically in large tanks, In the sludge digesters the sludge is kept at 37oC and mechanically mixed to ensure optimum operation.
When the sludge leaves the digesters it has undergone a 50% volume reduction

## Slide 15: Liquids
The liquids are either sent directly to open-air oxidation ponds

## Slide 16
Aeration tank, activated sludge

## Slide 17
In the pond, algae use solar energy to produce oxygen from carbon dioxide and water, and bacteria use oxygen to break down the remaining organics to simple molecules such as carbon dioxide and ammonia. The sun also destroys pathogenic bacteria, while the wind ensures even mixing so that all parts of the ponds are aerobic.

## Slide 18
After secondary treatment all effluent, both solid and liquid, is sufficiently safe to be released into the environment.

## Slide 19
Fig. 11-29, p. 255
Disposed of in
landfill or ocean or applied to cropland,
pasture, or rangeland
Sludge drying bed
Sludge
Activated sludge
Secondary
Raw sewage
from sewers
Air pump
(kills bacteria)
To river, lake,
or ocean
Sludge digester
Chlorine
disinfection tank
Settling tank
Aeration tank
Settling tank
Bar screen
Grit chamber
Primary
Notes: Figure 11.29: Solutions: primary and secondary sewage treatment.
Question: What do you think should be done with the nutrient-rich sludge produced by sewage treatment plants?