## Slide 1: STATICS (ENGINEERING MECHANICS-I)
Beams-External Effects
بسم الله الرحمن الرحيم
Notes: This is a title slide.

## Slide 2: Beams-External Effects
Beams: Structural members which offer resistance to bending due to applied loads are known as Beams.
Most beams are long prismatic bars, and the loads are usually normal to the axes of the bars.
Prismatic: In the shape of a prism.
Prism: a solid figure with ends that are parallel and of the same size and shape, and with sides whose opposite edges are equal and parallel.

## Slide 3: Beams: External Effects
5- 3
Beam - structural member designed to support loads applied at various points along its length.
Beam design is two-step process:
  determine shearing forces and bending moments produced by applied loads
  select cross-section best suited to resist shearing forces and bending moments
Beam can be subjected to concentrated loads or distributed loads or combination of both.
ENGINEERING MECHANICS : STATICS

## Slide 4: Types of Beams
Statically Determinate Beams: Beams supported in such a way that their external support reactions can be calculated by the equations of equilibrium alone are called statically determinate beams.
Statically Indeterminate Beams: A beam that has more supports than are necessary to provide equilibrium is said to be statically indeterminate.
  For such beams it is necessary to consider the load-deformation properties of the beam in addition to the equations of statical equilibrium to determine the support reactions.

## Slide 5: Various Types of Beams
5- 5
Beams are classified according to way in which they are supported.
Reactions at beam supports are determinate if they involve only three unknowns. Otherwise, they are statically indeterminate.

## Slide 6: Distributed load Resultant
The distributed loads can be reduced to equivalent concentrated (or point) loads. The magnitude and point of application of this equivalent load is computed as follows.
Magnitude: The equivalent concentrated load R is represented by the area formed by the intensity w (force per unit length of the beam) and the length L over which the force is distributed.
Point of Application: The resultant passes through the centroid of this area.

## Slide 7: Distributed Loads on Beams
5 - 7
A distributed load is represented by plotting the load per unit length, w (N/m) . The total load is equal to the area under the load curve.
A distributed load can be replace by a concentrated load with a magnitude equal to the area under the load curve and a line of action passing through the area centroid.

## Slide 9: Support Reactions (for a coplanar 2D structures)
Fixed Support: 3 Reactions
Pin or Hinge Support: 2 Reactions
Roller Support: 1 Reaction
Note: Reaction develops in that direction in which movement/displacement is obstructed.

## Slide 10: Problem 1
Determine the equivalent concentrated load(s) and external reactions for the simply supported beam which is subjected to the distributed load as shown.
Assume for given loading there are no horizontal reactions at the supports.

## Slide 11: Solution

## Slide 12: Sample Problem 2
5 - 12
A beam supports a distributed load as shown. Determine the equivalent concentrated load with its location and also the reactions at the supports.
SOLUTION:
The magnitude of the concentrated load is equal to the total load or the area under the curve.
The line of action of the concentrated load passes through the centroid of the area under the curve.
Determine the support reactions by summing moments about the beam ends.
ENGINEERING MECHANICS : STATICS

## Slide 13: Sample Problem 2 - Continued
5 - 13
The magnitude of the concentrated load is equal to the total load or the area under the curve.
The line of action of the concentrated load passes through the centroid of the area under the curve.

## Slide 14: Sample Problem 2 - Continued
5 - 14
Determine the support reactions by summing moments about the beam ends.

## Slide 15
5- 15
ENGINEERING MECHANICS : STATICS
Sample Problem 3

## Slide 16
5- 16
ENGINEERING MECHANICS : STATICS
Sample Problem 3 - Continued

## Slide 17
5- 17
ENGINEERING MECHANICS : STATICS
Sample Problem 3 - Continued
_

## Slide 18: STATICS (ENGINEERING MECHANICS-I)
Beams-Internal Effects
بسم الله الرحمن الرحيم
Notes: This is a title slide.

## Slide 19: Beams-Internal Effects
The design of any structural or mechanical member requires an investigation of both the external loads and reactions acting on the member and the loading acting within the member – in order to be sure the material can resist this loading.
How to determine the Internal Loadings:
  The internal loadings can be determined using the method of sections.
  The idea is to cut an imaginary section through the member so that the internal loadings (of interest) at the section become external on the free body diagram of the section.
  Use equations of equilibrium and find the required internal forces.

## Slide 20
5- 20
ENGINEERING MECHANICS : STATICS

## Slide 21: Internal forces
N: Normal force; V: Shear force; M: Bending moment.
If the member is subjected to a coplanar system of forces, only. N (Normal force), V (shear force) , and M (bending moment) act at the section.
Note: N will induce when applied loading is oblique.

## Slide 22: Sign Convention
The directions shown for N, V and M are in a positive sense. The easy way to remember this sign convention is to isolate a small segment of the member and note that:
Positive normal force tends to elongate the segment.
Positive shear tends to rotate the segment clockwise.
Positive bending moment tends to bend the segment concave upward, so as to hold water.

## Slide 23: Effect of Bending and Shear

## Slide 24: Shear Force and Bending Moment in a Beam
5- 24
To determine bending moment and shearing force at any point in a beam subjected to concentrated and distributed loads.
Determine reactions at supports by treating whole beam as free-body.
Cut beam at C and draw free-body diagrams for AC and CB. By definition, positive sense for internal force-couple systems are as shown.
From equilibrium considerations, determine M and V or M’ and V’.

## Slide 25: Shear-force and Bending-moment diagrams
The variation of shear-force and bending moments plotted against distance along the beam give the shear-force and bending moment diagrams for the beam.

## Slide 26: Shear Force and Bending Moment Diagrams
5- 26
Variation of shear and bending moment along beam may be plotted.
Determine reactions at supports.
Cut beam at C and consider member AC,
Cut beam at E and consider member EB,
For a beam subjected to concentrated loads, shear force is constant between loading points and bending moment varies linearly.
+
+
+
_

## Slide 27: NOTE
The part of the beam which involves the smaller number of forces, either to the right or to the left of the arbitrary section, usually yields the simpler solution.
Avoid using a transverse section that coincides with the location of a concentrated load or couple, as such this position represents a point of discontinuity in the variation of shear or bending moment.

## Slide 28: Problem-1
Determine the shear and moment values in the simple beam at three sections: 1.5 m, 2.5 m and 4 m from the left support.
1 m
A
1 m
1 m
2 kN/m
2.8 kN.m
1 m
4 kN
B
1 m

## Slide 29: Solution
Reactions:
1 m
1 m
1 m
2 kN/m
2.8 kN.m
1 m
4 kN
B
1 m
A

## Slide 30: SF and BM calculations
2.8 kN.m
1.5
A
2 kN/m
2 m
2.8 kN.m
2.5
A

## Slide 31: SF and BM calculations
A
2 kN/m
1 m
1 m
2.8 kN.m
1 m
4 m
1 m
1 m
2.8 kN.m
1 m
4m
2 kN/m
BM is the same under the point load but SF changes from 0.36 kN to -3.64 kN.
4kN

## Slide 32
5- 32
ENGINEERING MECHANICS : STATICS
Sample Exam Question

## Slide 33
5- 33
ENGINEERING MECHANICS : STATICS
Sample Exam Question